## Slide 1: Landsat Data Continuity Mission Overview
Landsat Ground Station
Sioux Falls, SD
Representative IC
Canada
Gilmore Creek Ground Station
Fairbanks, AK
TDRSS
Atlas V
VAFB
LDCM Orbit
705 km circular
sun sync, 10am DNLT
16-day repeat
NASA NEN
Wallops Island, VA
LDCM Observatory
(OLI, TIRS)
Launch Readiness Date: February 11, 2013
Svalbard Ground Station
Svalbard, Norway

## Slide 2: LDCM Overview
  Mission Objectives
Provide continuity in the multi-decadal Landsat land surface observations to study, predict, and understand the consequences of land surface dynamics
  Land cover/use change
  Human settlement and population
  Ecosystem dynamics
  Landscape scale carbon stocks
  Resource management/societal needs
LDCM Data Needed to Address Earth Science Focus Areas, Questions, and Applications
Carbon Cycle, Ecosystems, & Biogeochemistry
Water & Energy Cycle
What are the changes in global land cover and land use, and what are their causes?
How do ecosystems, land cover & biogeochemical cycle respond to and affect environmental change?
What are the consequences of land cover and land use change for human societies and the sustainability of ecosystems ?
- What are the consequences of increased human activities on coastal regions?
Focus Areas
Science Questions
Earth Surface & Interior
Landsat 7 data used to aid Indonesian government with tsunami
relief efforts (David Skole, Michigan State University)
  Mission Team
NASA Goddard Space Flight Center
Dept. of the Interior’s United States Geological Survey (USGS)
NASA Kennedy Space Center
Instruments
Operational Land Imager – BATC
Optional Thermal Infrared Sensor – GSFC
Spacecraft
Orbital Sciences Corp (OSC)

## Slide 3: LDCM Project Master Schedule

## Slide 4: LDCM Post-launch Checkout
Day
1
15
30
60
45
Launch thru Deployment
Sep, Bus Init, ACS Acq, SA Deploy
Subsystem Initialization
EPS, ACS, TCS, C&DH, RF Comm
ACS Calibration
TIRS Activation - power on
and dryout, cryocooler deploy
OLI Activation -Electronics &
Htrs On, Shutter, Dryout
OLI Activation – FPA
Cooldown
Launch
75
OLI Characterization and Commissioning
90
Orbit Maneuvers, ascent burns
TIRS Activation – cooldown
and Diagnostics check
Deploy Earth shield
TIRS Characterization and Commissioning
Close shutter
Notes: 3/7/12 timeline WG slides
<number>

## Slide 5: Spacecraft/Observatory Size
113.7”
(or 9.5 ft)
10’
32 ft
19 ft.

## Slide 6: LDCM Observatory
OLI
TIRS
Solar Array
Drive Assembly
Reaction Wheels

## Slide 7: Operational Land Imager (OLI)
Instrument description
  Eight multi-spectral bands ranging in wavelength from 433 nm to 1390 nm with spatial resolutions of 30 meters
  One panchromatic visible band with a spatial resolution of 15 meters
  Pushbroom VIS/SWIR sensor
  Four-mirror telescope with front aperture stop
  Focal Plane Assembly (FPA) consisting of 14 sensor chip assemblies, passively cooled
  Absolute radiometric accuracy < 4%
  Mass: 450Kg
  Operational Power: 160 W
  Size: 1.8 m x 2 m x 1 8 m
A reflective-band multi-channel earth-imaging instrument
  Provides imagery to detect and quantitatively characterize changes on the global land surface at a scale where natural and man-made causes of change can be detected and differentiated.
  OLI design draws on 35+ years of Landsat imaging experience plus Worldview/Quickbird and ALI heritage

## Slide 8: Thermal InfraRed Sensor (TIRS)
A thermal infrared earth-imaging instrument
  Complementary to the reflective bands sensed by OLI for detecting and quantitatively characterizing land surface change
  Continues the record of earth monitoring in the thermal portion of the electromagnetic spectrum currently sensed by Landsats 5 and 7
Instrument description
  GSFC In House Build
  Two spectral bands at 10.8 and 12 micrometers
  Ground sampling distance, both in-track and cross track, of 100m.
  Pushbroom LWIR sensor
  Four-lens telescope
  FPA consisting of three 2-dimensional QWIP sensor chip assemblies
  Mechanically cooled focal plane; BATC provided cryo cooler
  NEdT @ 300K < 0.4
  Mass: 240 Kg
  Operational Power: 380 W
  Size: 80 cm x 76 cm x 43 cm (with earth shield deployed)

## Slide 9: Ground System

## Slide 10
Operational Land Imager Bands

## Slide 11: New LDCM Capabilities
Spectral band improvements
  Landsat 7 offered 8 spectral bands (3 VIS, 1 NIR, 2 SWIR, 1 TIR, and pan band)
  LDCM has 11 spectral bands (4 VIS, 1 NIR, 3 SWIR, 2 TIR, and a pan band)
    New VIS “coastal aerosol” band allows detection of water column constituents (e.g., chlorophyll, suspended materials, etc.)
    New SWIR “cirrus” band will improve overall image quality because of better cloud screening
    Addition of a 2nd thermal band will improve the accuracy and precision of temperature measurements. Note, however, that TIR resolution decreases from 60m to 100m.
    Changes in panchromatic band spectral range will increase the overall use of this band for image sharpening and other applications.
Detection, quantification, and mapping of surface (land and water) characteristics will improve because of:
  5x improvement of signal-to-noise ratios of spectral measurements
  12 bit quantization of spectral signals (Landsat 7 was 8 bit)
Limited off-nadir imaging capability will allow viewing adjacent path rows.

## Slide 12
T-150 days and
counting…
LDCM is almost
ready for launch!!