## Slide 1: European Space Agency Frank Martin Seifert Earth Observation Programme ESRIN, Frascati, Italy Email: Frank.Martin.Seifert@esa.int
Space Data Coordination Group Meeting 2
Reston (VA), USA. 13-14 September 2012
Forest Carbon Tracking
Global Forest Observations Initiative

## Slide 2
GMES Sentinel Missions
Free and open data policy!
2013 (A), 2014+ (B)
Sentinel 1 – SAR imaging
All weather, day/night applications, interferometry
2014 (A), 2015+ (B)
Sentinel 2 – Multispectral imaging
Land applications: urban, forest, agriculture,..
Continuity of Landsat, SPOT
2014 (A), 2015+ (B)
Sentinel 3 – Ocean and global land monitoring
Wide-swath ocean colour, vegetation, sea/land
surface temperature, altimetry
2018
Sentinel 4 – Geostationary atmospheric
Atmospheric composition monitoring, trans-
boundary pollution
2014 (5P), 2019
Sentinel 5 and Precursor – Low-orbit atmospheric
Atmospheric composition monitoring
We care for a safer world
Notes: Complemented by national missions: SPOT, TerraSAR-X, CosmoSkym, DMC, Rapid Eye, Pleiades

## Slide 3
  Sentinel-1
We care for a safer world

## Slide 4: Sentinel–1: C-band SAR mission
GMES C-band radar imaging mission for ocean, land and emergency services
Data continuity of ERS and ENVISAT missions
Applications:
  monitoring sea ice zones and the arctic environment
  surveillance of marine environment (e.g. oil spill monitoring)
  maritime security (e.g. ship detection)
  wind, wave, current monitoring
  monitoring of land surface motion (subsidence, landslide, tectonics, volcanoes, etc.)
  support to emergency / risk management (e.g. flooding, etc.) and humanitarian aid in crisis situations
  mapping of land surfaces: forest, water and soil, agriculture, etc.
The Sentinel-1 mission is based on a constellation of 2 satellites
Sentinel-1A to be launched in October 2013
Sentinel-1B launch date is 2014 + (TBC)
We care for a safer world

## Slide 5: Sentinel–1 SAR operational modes Data recording / transmission capabilities
SAR operation modes:
Default modes:
• Interferometric Wide Swath 250 km swath; level-1 product
(IWS): best res.: 20 m
• Wave (WV): sampled images of 20x20 km at 100 km along
the orbit, alternating into 2 incidence angles
level-1 product best resolution: 50 m
Additional modes:
• Extra Wide Swath (EWS): 400 km swath; level-1 product best res.: 50 m
• Strip Map (SM): 80 km swath, 6 possible incidence angles;
(exceptionally use only) level-1 product best resolution: 9 m
SAR Duty cycle:  up to 25 min/orbit in high rate acquisition modes
Data recording / transmission capabilities :
• On-board data storage capacity of 1400 Gbit
• Two X-band RF channels of 260 Mpbs each
Equipped with an Optical Communication Terminal for GEO laser link with European Data Relay System
We care for a safer world

## Slide 6
We care for a safer world
During Full Operational Capability Operations
Systematic (or very frequent) mapping of tectonic / subsidence / landslides / volcano areas to support operational services and “operational science” based on INSAR
 Need to provide pairs in both ascending / descending passes
Regular mapping of areas prone to risks to acquire strategic background data (e.g. for flood)
Regular mapping of areas to support GMES security services (e.g. G-Mosaic)
Regular mapping or ice sheets (Greenland, Antarctica), polar coastal regions and of relevant areas for glacier and snow monitoring (based on season)
Regular global coverage of all land areas (frequency TBD), supporting among others forest mapping (e.g. REDD), soil moisture, land cover change, crop monitoring, etc. based on seasonal requirements
 Baseline mode of operations: IWS, if possible in dual-polarisation (HH+HV) Single polarisation HH however sufficient for INSAR applications
High Level Strategy to fulfill Observation Requirements for Services Over Land
Notes: Simulations: 4 times a year full w2w cover of forested areas
ASAR for GEO FCT: VV+VH

## Slide 7: Sentinel-1 Simulations
  Build up requirement data base
    from GMES services
    national requirements from ESA member states
  Initial Simulation
    4 times a year full coverage of world forest areas  autumn 2012
  Other possible simulation scenarios
    Increase to 6, 8 or 12 times a year globally
    Restrict to tropical belt but 10 or 15 times a year
We care for a safer world

## Slide 8
We care for a safer world
CSA-ESA discussions on-going to explore synergies between Sentinel-1 and Radarsat Constellation Mission (RCM) and in view of a certain level of interoperability between the missions
RCM – Sentinel-1 interoperability would bring strong benefits to users
The following interoperability items are explored:
  Joint / integrated pre-defined observation plans (complementarities in observations / modes, increased revisit, etc.)
  Level 1 Product format
  Harmonisation of catalogue interface
  Development of common tools
  Harmonised communication, joint publications etc.
A joint calibration working group is being set up
In addition, cooperation to support international activities should be continued (example of the International Polar Year, GEO FCT/GFOI), setting up complementary observations (e.g. sharing of Arctic / Antarctic coverage).
Synergy Sentinel-1 / RCM

## Slide 9
  Sentinel-2
We care for a safer world

## Slide 10: Sentinel–2: Multispectral Optical Mission
We care for a safer world
2 satellites in twin formation, launch Jun 2014 (and Q2 2015)
Orbit: Sun-synchronous at 786 km (14+3/10 revs/day), with LTDN 10:30 AM
Revisit: 5 days at equator (with 2 satellites) under same viewing conditions;
Multispectral Instrument: pushbroom with 13 bands in the visible, near infra-red (VNIR) and short wave infra-red (SWIR) part of the spectrum
  High spatial resolution: 10m, 20m and 60m;
  Wide field of view: 290 km
  Duty cycle: average 17 min/orbit, maximum 32 min /orbit
  Lifetime: 7.25 years, extendable to 12 years
  Onboard mission data storage: 2.4 Tbits
Geographical Coverage:
  All land masses 56° S bis 83° N incl. major islands (>100 km2)
  All EU islands < 20 km off the coast
  All Mediterranean
  Inland waters and all closed seas

## Slide 11: Sentinel–2: 13 Spectral Bands
We care for a safer world
Continuity with SPOT5 multispectral

## Slide 12: Sentinel–2: Swath
  High revisit time assured by twin satellite observations performed over a very large swath
SPOT4 60 x 60 km x 2
IRS P6 LISS III 141x141 km
Landsat ETM+ 180 x 172 km
Sentinel-2 290 x 290 km
290Km
We care for a safer world
Notes: Systematic observations over land
<number>

## Slide 13
Sentinel-2 simulated repeat rates – in summer with 2 Satellites
days
Maximum effective coverage time for SC1 and SC2 (days) (<15% cloud cover with 68% confidence)
We care for a safer world
Notes: <number>

## Slide 14: Sentinel Observation Scenario
We care for a safer world
Operational funding not yet secured
  Full deployment of four core ground stations
  Ramp-up phase of 1.5 – 2 years
Priorities for the preparation of pre-defined observation scenarios
  First priority: GMES use and National utilisation by Participating States in accordance with the GMES Space Component Programme Declaration
  Second priority: other data use
  EC confirmed ESA’s baseline assumptions and decentralised concept, whereby the dissemination of Sentinel data should primarily be towards the identified GMES services

## Slide 15
  Backup on Sentinel-1 Scenario
We care for a safer world

## Slide 16: Sentinel-1 Observation Scenario
We care for a safer world
  The Sentinel-1 observation scenario is
  currently under definition.
  High level strategy
  optimum use of SAR duty cycle (25 min/orbit), taking into account the various constraints (e.g. limitation in the number of X-band RF switches, mode transition times, …)
  Wave Mode continuously operated over open oceans, with lower priority w.r.t. the other high rate modes
  IWS or EWS modes operated over pre-defined geographical areas:
     Over land: pre-defined mode is IWS
     Over seas and polar areas, and ocean relevant areas: pre-defined mode is either IWS or EWS
  In exceptional cases only, emergency observation requests may alter the pre-defined observation scenario, with e.g. the use of the Strip Map mode

## Slide 17: Initial Sentinel-1 Observation Scenario & Evolution
  From Commissioning Phase to Full Operational Capability (FOC)
    a very basic observation / operations scenario will support the Commissioning phase
    Ramp-up phase: the scenario will gradually evolve from initial operations up to Full Operational Capability of the first satellite.
  Evolution during GSC operational phase, to cope in particular with:
    The inclusion of the 2nd Sentinel-1 satellite leading to the Full Operational Capacity of the missions with the 2-satellite constellation during the EU Operational Programme (2015+)
    The gradual use of the EDRS system to improve the data download capacity
    The evolution of the requirements from the services, the evolution of the “perimeter” of the GMES services as defined by the EC
    The constraints on the space and ground segment resources (e.g. core and collaborative ground station networks)
    The contribution of (and interoperability with) RCM
   It is planned to set up a procedure for a regular (e.g. yearly) update of the S-1 observation plan during routine operations
We care for a safer world