## Slide 1
CBERS-3 Updates
Julio Dalge – INPE
Guo Chaohui – CRESDA
SDCG Meeting – Reston, USA 2012
Notes: <number>

## Slide 2
CBERS 3 & 4 – 2nd generation series
Parameter | CBERS 1, 2, 2B | CBERS 3, 4
Total mass | 1,450 kg | 2,020 kg
Power | 1,100 W | 2,300 W
Data rate | 100 Mbit/s | 305 Mbit/s
Design lifetime | 2 years | 3 years
Notes: <number>

## Slide 3
CBERS 3 & 4 – 2nd generation series
Sun-synchronous orbit
Altitude = 778 km
Inclination = 98.5º
Nodal period = 100.26 minutes
Repeat cycle = 26 days
Descending node at 10h30 local time
Notes: <number>

## Slide 4
CBERS 3 & 4 – payloads
Payloads | MUXCam | PanMUX | IRS | WFI-2
Manufacturer | Brazil | China | China | Brazil
Type | Pushbroom | Pushbroom | Scanner | Pushbroom
Revisit time | 26 days | 52 days (nadir operation) side looking ability (±32 degrees) | 26 days | 5 days
Quantization | 8 bits | 8 bits | 8 bits | 10 bits
Compression | -- | 2:1 pan band | -- | --
Notes: <number>

## Slide 5
CBERS 3 & 4 – payloads
Payloads | MUXCam | PanMUX | IRS | WFI-2
Band 1 | 0.45 - 0.52 µm | 0.51 - 0.85 µm | 0.50 - 0.89 µm | 0.45 - 0.52 µm
Band 2 | 0.52 - 0.59 µm | 0.52 - 0.59 µm | 1.55 - 1.75 µm | 0.52 - 0.59 µm
Band 3 | 0.63 - 0.69 µm | 0.63 - 0.69 µm | 2.08 - 2.35 µm | 0.63 - 0.69 µm
Band 4 | 0.77 - 0.89 µm | 0.77 - 0.89 µm | 10.4 - 12.5 µm | 0.77 - 0.89 µm
Spatial Resolution | 20 m | 5 m(Band1), 10 m(Band 2、3、4） | 40 m(Band 1、2、3), 80 m（Band 4） | 73 m
Swath width | 120 km | 60 km | 120 km | 866 km
Notes: <number>

## Slide 6
Data transmitters and onboard storage
Data | Carrier frequency | Data rate
5 m PAN data | 8.208 GHz | 67 Mbps
10 m MUX data | 8.108 GHz | 100 Mbps
IRS data | 8.034 GHz | 17 Mbps
MUX CAM data | 8.365 GHz | 68 Mbps
WFI data | 8.290 GHz | 53 Mbps
Solid state onboard data recorder with 274 Gbits (15 minutes’ recording capability) |  | 
Notes: <number>

## Slide 7
CBERS-3 will be launched in December 2012
Long-March 4 launching rocket will be used
Notes: <number>

## Slide 8
Thank you!
Notes: <number>