## Slide 1: CEOS Data Acquisition Plan – Global Baseline strategy (Level 1) BAU plans and (first cut) Mitigation proposals
Space Data Coordination Group (SDCG)
John Faundeen, USGS
Ake Rosenqvist, for NSC
Frank-Martin Seifert, ESA

## Slide 2
BAU plans and Mitigation props
Core missions
Notes:   Cloud predictions to avoid acquisitions of “relatively cloudy data” likely to amplify gaps in regions with severe cloud cover
   Action on USGS to assess impact of relaxing the cloud threshold in LTAP (noting that pixel mining techniques present new situation where all data can be used)
  Central Africa potential problem area: Few GS available to accommodate increased observation frequency by direct downlink.
   USGS to assess potential to increase LTAP observation plan over African key regions

## Slide 3
  BAU plan
  For Landsat 7, at least 4 scenes are planned for every ground locale every year for the vast majority of land areas of the world. Smaller Caribbean and Pacific islands have recently been added to the plan. If cloud cover prevents a previous acquisition from being successfully acquired, a higher priority weighting is assigned for that area for the next acquisition opportunity. If too long a time passes between successful acquisitions, a specific acquisition request may be established.
  With the successful launch of LDCM, it is anticipated that most land areas of the world will have at least 8 scenes acquired annually. This will be accomplished by LDCM taking the previous Landsat 5 orbit, which provides an eight-day revisit cycle.
Landsat 7 & LDCM

## Slide 4
  Key Points
  • Key sensors for Category A and B
  Near-global land coverage planned:
  • 4 observations/year with L-7 - probably insufficient due to scanline error (at least 2 observations required for gap-free coverage) and cloud cover.
  • Improvement with launch of LDCM  8 obs/year.
  • Every pass observations in South America within INPE Ground Station (GS) mask.
  Potential for increased observation frequency over other regions with GS
  • Cloud predictions avoid acquisitions of “relatively” cloudy data
Landsat 7 & LDCM

## Slide 5
  Suggested actions for gap mitigation
  Cloud predictions to avoid acquisitions of “relatively cloudy data” likely to amplify gaps in regions with severe cloud cover
   Action on USGS to assess impact of relaxing the cloud threshold in LTAP (noting that pixel mining techniques present new situation where all data can be used)
Landsat 7 & LDCM
Notes:   Central Africa potential problem area: Few GS available to accommodate increased observation frequency by direct downlink.
   USGS to assess potential to increase LTAP observation plan over African key regions

## Slide 6
  BAU plans
  Brazil and China will always be first priority. Everything captured in the masks of the INPE (Cuiaba ) and the CRESDA (Miyun, Sanya and Kashi ) ground stations will be processed and made available in the INPE and CRESDA cataloges.
  CBERS for Africa is an ongoing initiative and acquisitions over existing CBERS ground stations in Africa are planned to continue. The stations in Africa will need to be upgraded in order to receive CBERS-3 data.
  All four instruments on CBERS-3 (MUXCam, PanMUX, IRS, WFI-2) can be acquired and downlinkled simultaneously. Use of the CBERS-3 OBR (on board data recorder) is also planned to provide acquisitions whenever possible and needed.
  Duty cycle: 15 min/orbit
CBERS-3

## Slide 7
  CBERS-3 ground stations
CBERS-3

## Slide 8
  Key points
  • High temporal frequency coverage over areas within GS masks.
  • Good potential to support Category A and B products with CBERS-3 (IRS sensor includes SWIR bands)
  • Remaining gaps: (1) northern fringe of South America (N Venezuela, N Colombia, Ecuador, (2) Central America, (3) southern SE-Asia (S&W Indonesia, Sri Lanka, PNG, Pacific islands) and (4) Africa (planned coverage needs to be confirmed).
  • Good potential to support Category C2 product (near-real time forest change indicators) within GS masks with the WFI-2 instrument.
CBERS-3

## Slide 9
  Suggested actions for gap mitigation
  INPE and CRESDA to assess feasibility to, within 15 min duty cycle, use the OBR to cover key regions immediately outside the national GS:
    South America (N Venezuela, N Colombia, Ecuador, forested areas in S Argentina and S Chile)
    Central America,
    southern SE-Asia (S&W Indonesia, Sri Lanka, PNG, Pacific islands)
  In case of Svalbard GS utility, develop plan for high temporal frequency coverage over key GFOI RIO in Africa
  In case of resource constraints, SDCG to suggest mitigation plan with operations of selected sensors only (not all four)
CBERS-3

## Slide 10
  BAU plans
  Priority order: (1) Europe, (2) Africa, (3) Rest of the world
  The four core ground stations for Sentinel-2 are anticipated to become gradually available 1.5–2 years from the launch of Sentinel-2A (mid 2014)
  Sentinel-2B launched and commissioned once the four core stations are operational (early~mid 2016)
  When full operational setup is reached, Sentinel-2A and 2B will systematically cover all land masses between S56 – N83.
  10 days repeat frequency with one satellite, 5 days repeat with two satellites.
   36 scenes/year (at Equator) with one satellite, 73 scenes/year with 2 satellites (!!!)
Sentinel-2

## Slide 11
  Key point
  Every pass acquisitions over all land masses (sensor always on) when in full operation
  Suggested actions for gap mitigation
  Clarification from ESA – above interpretation correct?
    If no – please indicated expected number of annual observations per region
    If yes – No mitigation plan suggested (cannot improve anything perfect!)
    During ramp up phase, focus on GFOI ROI
Sentinel-2

## Slide 12
  BAU
  Plans and capacity of Amazonia-1 still TBC.
  Anticipated main operations within the Cuiaba GS mask.
  Good potential to support Category C2 product (near-real time forest change indicators) within mask area.
  Suggested actions for gap mitigation
  INPE to clarify plans and capacityfor use of Amazonia-1 (1) within Cuiaba GS mask, (2) outside ditto.
Amazonia-1

## Slide 13
  BAU
  Will use same core GS as Sentinel 2. Once the full operational setup is reached (when? S1:2015 vs. S2: early/mid 2016), Sentinel-1A and -1B is tentatively planned to systematically cover all land masses in Interferometric Wide-Swath (IWS) mode.
  3-4 global w2w coverages/year.
  Polarisation mode (single vs. dual polarisation) TBC
  Potential for Category B3 (forest change) and possibly C1 (Degradation) products. Requires dense time series observations and dual polarization, which Sentinel-1A and -1B could provide.
  In supplement to optical and/or L-band SAR, provides additional info to Cat B1 (Forest Types)
Sentinel-1

## Slide 14
  Suggested actions for gap mitigation
  FMS to clarify when Sentinel primary “core” GS are expected to be fully operational (resolve current S1/S2 information discrepancy).
  Suggested actions for gap mitigation
  During ramp-up phase, and in case of resource constraints, focus “global coverage attempt” to include GFOI key countries, alt. reduce temporal repeat from 3-4 to 1-2 (TBC)
  ESA to consider importance of IWS mode with dual-polarisation as default when over global forested regions
  ESA to assess feasibility of (approx) monthly observations over deforestation/degradation hot spot regions within GFOI ROI (during simulations, add a few representative dummy regions. as part of Level-2 strategy, jointly developed with GFOI country)
Sentinel-1

## Slide 15
  BAU
  The first priority for SAOCOM is acquisitions over Argentina.
  A Global Background Mission is under development for the remaining capacity with focus on pan-tropical coverage in dual-polarisation mode 2 times/year.
  Key points:
  Important L-band core mission coverage
  Potential to support Category A, B and D products.
SAOCOM-1A

## Slide 16
  Suggested actions for gap mitigation
  In case of duty cycle resource scarcity, focus Global Background Mission (GBM) acquisitions (annual dual-season pantropical coverage) to GFOI country regions, in particular to areas with persistent cloud cover.
  Consider feasibility to use beam mode with shallow off-nadir angle for GBM
  CONAE and NRS to assess feasibility to use Svalbard GS for downlink of SAOCOM-1A/B data
SAOCOM-1A
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 17
  BAU
  RCM will feature largely preprogrammed acquisitions to meet clearly defined user needs. CSA is currently conducting capacity assessment for domestic use and excess capacity. Prelaunch requests from the SDCG in support of GFOI may be possible to integrate with the concept of operations currently under development.
Radarsat Constellation Mission

## Slide 18
  Suggested actions for gap mitigation
  Action on SDCG to provide CSA with basic observation requirements for initial simulations
    Geographical focus: GFOI ROI
    Observation mode:
      At least dual-polarisation (key req)
      Shallow off-nadir viewing preferred (conf. R-2 WB3)
      Spatial resolution (GSD): 25m, or better
      Wide Swath
    Temporal repeat: 2 obs/year (dual-season) or better
  Request CSA to assess feasibility of every 12-day cycle observations over deforestation/degradation hot spot regions within GFOI ROI (during simulations, add a few representative dummy regions. as part of Level-2 strategy, jointly developed with GFOI country)
Radarsat Continuity Mission
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 19
BAU plans and Mitigation props
Other Data Streams of Interest
Notes:   Cloud predictions to avoid acquisitions of “relatively cloudy data” likely to amplify gaps in regions with severe cloud cover
   Action on USGS to assess impact of relaxing the cloud threshold in LTAP (noting that pixel mining techniques present new situation where all data can be used)
  Central Africa potential problem area: Few GS available to accommodate increased observation frequency by direct downlink.
   USGS to assess potential to increase LTAP observation plan over African key regions

## Slide 20
  BAU
  Systematic observation plan for annual coverage of the Congo Basin and Madagascar during the period 2010-2014.
  Key points:
  • Regional, selected area, wall-to-wall acquisition plan for 2010-2014.
  • These regional data are provided free of charge for REDD+ purposes (special user agreement required).
  • Potential to support Category A and B products over Congo Basin and Madagascar.
  SPOT 4 to be decommissioned June 2013
  SPOT 5 to be decommissioned June 2014 (TBC)
SPOT 4/5

## Slide 21
  Suggested actions for gap mitigation
  Continue efforts for acquisitions over cloudy areas in Congo Basin Initiative countries and Madagascar
  CNES, DLR and KSAT are encouraged to coordinate SPOT and RapidEye data acquisition planning over the Congo Basin and Madagascar
SPOT 4/5
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 22
  BAU
  Annual global observation plan implemented for the RapidEye system. The five -satellite systems facilitates frequent observations and reduction of the impact of cloud cover. Observations within the range of +/- 20 degrees viewing angle. Details of the RapidEye acquisition plan (temporal repeat, regional focus areas) TBC. Forested areas a priority in acquisition planning.
  Key points:
  • Five-satellite system observations improves chances for cloud-free acquisitions.
  • Data available on commercial basis.
  • Potential to support Category A, B and C products.
RapidEye

## Slide 23
  Suggested actions for gap mitigation
  RapidEye are encouraged to consider the outcome of the SDCG gap analysis in their acquisition planning
  RapidEye are encouraged to continue provision of data for GFOI R&D activities
  CNES, DLR and KSAT are encouraged to coordinate SPOT and RapidEye data acquisition planning over the Congo Basin and Madagascar
RapidEye
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 24
  BAU
  Wall-to-wall acquisitions continue to be undertaken over selected GEO FCT National Demonstrator countries (Mexico/partial, Colombia, Peru, Guyana, and Indonesia/partial) during 2012 and the data are provided for free (CSA special terms of use for GEO FCT)..
  Key points:
  Data over FCT ND countries provided for free under special terms until 2012.
  Data over other areas available on commercial basis.
  Potential to support Category B and C products.
Radarsat-2

## Slide 25
  Suggested actions for gap mitigation
  CSA/MDA are encouraged to consider the outcome of the SDCG gap analysis in their acquisition planning
  CSA/MDA are encouraged to continue provision of data for GFOI R&D activities
  To ensure access of Radarsat-2 critical data sets within the operational implementation process of GFOI it is recommended that the SDCG (via KSAT) initiate discussions with CSA and MDA within the context of the discussion framework to access key commercial data sets to meet the GFOI objectives.
Radarsat-2
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 26
  BAU
  The acquisition plan for the TerraSAR-X/TanDEM-X, dual satellite system is designed for collection of two global single-pol coverages of X-band SAR data at 12m resolution within the 2011-2013 time period for the generation of a global Digital Elevation Model.
  The X-band intensity data (and other derivatives) that were used as base for the DEM generation is available on a commercial basis.
  Continuity of global acquisitions beyond 2013 unknown at this time.
TerraSAR-X/TanDEM-X

## Slide 27
  Suggested actions for gap mitigation
  DLR to clarify plans for TSX 2013+
  DLR is encouraged to better link existing work with X-band SAR on forestry with GFOI R&D activities
  Continued provision of data for GFOI R&D to improve understanding of potential of X-band SAR
  DLR is encouraged to consider repeat observations over FCT National Demonstrator Validations Sites to assess new 200km mode
TerraSAR-X/TanDEM-X
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.

## Slide 28
  BAU
  Global acquisition strategy is under development for ALOS-2 SAR to assure continuity with ALOS-1 PALSAR global acquisitions.
  Forest monitoring defined as one of key objectives for ALOS-2
  Acquisition plan compliant with GFOI information requirements
  The data policy for ALOS-2 is yet to be decided.
  • Potential to support Category A, B, C and D products.
ALOS-2

## Slide 29
  Suggested actions for gap mitigation
  No technical suggestions. ALOS-2 strategy compliant with GFOI priorities.
  Inclusion of ALOS-2 as a core mission would be of significant benefit for the Global Baseline Strategy.
ALOS-2
Notes:   SDCG suggested modifications to BAU observation plan:
  • If capacity is scarce, focus pan-tropical acquisitions over UNREDD/REDD+ pilot and/or observer countries.