## Slide 1: SDS-3 Session 3 Baseline implementation approach
Ake Rosenqvist

## Slide 2: Section 4: Approach to implementation of the baseline strategy
Summarising the combined core mission “business as usual” (BAU) coverage plans;
Assessing the capacity of the combined BAU plans and the impact of clouds;
Suggesting alterations to the BAU plans to better meet GFOI data requirements;
Providing early input to mission teams of key future systems; and
Providing general suggestions on how non-core systems could be employed to augment or fill critical data gaps.

## Slide 3: Roles foreseen for the core data streams
Global BAU
Regional BAU
Selected country focus - on request (Element-2)

## Slide 4: “Global coverage” group
Landsat-7, Landsat-8, and Sentinel-2A will provide more than adequate frequency of coverage for GFOI requirements when fully operational in 2016, for all regions of the world other than those worst affected by persistent cloud cover. Prior to availability of the Sentinel-2A data stream, there will be a dependence on Landsat-7 and -8 in the transition to global coverage.
Mission key relevance to GFOI target products [DRAFT feed-back pls]

## Slide 5: Landsat-7, Landsat-8
BAU:
LTAP global by definition already now [spatially].
Approx 10 observations per year (random country outside
Every opportunity observation (max 23/year) over USA, Brazil (Cuiaba) and Australia (Alice Springs) GS
L-8 in operation from April/May 2013
L-7 and L-8 the only core sensors for 2013 period.

## Slide 6: Sentinel-2
BAU
Fully global in both spatial and temporal sense when PDGS in full operations, currently expected 2016.
2014 period – early ramp-up phase: Africa inofficially prio 2, but no details available on geographical priorities within Africa, temporal repeat and start of observations. Further details expected after ESA consultation with member countries (in time for SIT-28? How to treat in SDCG doc for SIT-28?)
2015 period: Details on 2015 BAU plan not urgent in current plan. Can be updated for SIT-29 report.

## Slide 7: “Regional focus and gap filling” group
CBERS-3/4 and SAOCOM-1 not intended for full global-scale operations, but have the capacity to fulfil regional/semi-continental scale observations consistent with GFOI objectives.
ResourceSat AWiFS and CBERS WFI-2 (56-64 m GSD, ~750 km swath, ~ weekly sub-cycle repeat). Potential for regional-scale gap filling for Landsat and Sentinel-2 and near-real time forest change

## Slide 8: CBERS-3/4
BAU:
CBERS-3 operational by 2014(?)
Brazil and China territory first priority.
INPE and CRESDA have confirmed every opportunity observations within full Cuiaba and 3 China GS masks. Several GFOI countries covered.
Simultaneous operation of all 4 instruments

## Slide 9: SAOCOM-1A/1B
BAU:
In operation 2016.
Pan-tropical coverage consistent with SDCG goals for L-band SAR (dual-season).
Open issues:
    data policy
    ground segment capacity to meet global need?
    Use of Svalbard GS

## Slide 10: ResourceSat-2 AWiFS

## Slide 11: “Selected National Wall-to-Wall Coverage”
Sentinel-1A/1B
Radarsat Constellation:
High temporal repeat (monthly or better) required to optimise usefulness of C-band SAR for GFOI. Recommended to focus such intensive observations over a number of selected countries on demand (Element-2) – potentially in countries with expertise in SAR and technical resources to handle large data amounts.
Mission key relevance to GFOI target products [DRAFT feed-back pls]

## Slide 12: Sentinel-1A/1B
BAU:
A preliminary and indicative observation scenario for the first 6 months of the Sentinel-1 exploitation phase - where only two core ground stations (Matera and Svalbard) will be available - is being defined.
Highest priority is given to GMES services and use, as well as to national services and use by ESA/EU Member States. Coverage of Europe, European waters, and North Pole remain the priority areas for Sentinel-1 operations.
Outside of Europe operations a campaign to support forest monitoring international activities is foreseen with some observations over some of the highly cloud covered REDD participating countries in IWS.

## Slide 13: Roles for non-core missions
While the global baseline coverage for GFOI (Element 1) relies on core data streams, non-core systems that can make valuable contributions to providing coverage, either as gap-filling observations in areas where core data are insufficient, or by providing new thematic information not available on the core missions.
In most cases, this will be national level coverage and therefore will be implemented under strategy element 2

## Slide 14: Roles for non-core missions
Mission key relevance to GFOI target products [DRAFT feed-back pls]

## Slide 15: GAP ANALYSIS [2013]
# coverages foreseen by Landsat-7 and -8 in 2013. Yellow = 10; dark green = 30
Non-core mission operators to consider the countries designated as priorities for GFOI (16 countries in 2013).

## Slide 16: GAP ANALYSIS [2013] DRAFT suggestions for augmentation to BAU
Non-core mission operators:
Recommended to consider GFOI priority countries for 2013
Landsat 7, Landsat 8:
Modify LTAP to optimise performance over “relatively cloudy regions”
Intensify observations over GFOI priority countries for 2013 (FCT ND & GFOI “pilots” – 16 countries)
  Alt 1: every opportunity throughout full year
  Alt 2: every opportunity during time windows of less cloudiness based on LTAP archive analysis

## Slide 17: GAP ANALYSIS [2014]
# coverages foreseen by L-7 and -8, CBERS-3 in 2014. Yellow = 15; light green = 24; dark green = 35; purple = 50

## Slide 18: GAP ANALYSIS [2014] DRAFT suggestions for augmentation to BAU
Non-core mission operators:
Recommended to consider GFOI priority countries for 2014
Landsat 7, Landsat 8:
Same as for 2013, PLUS
Intensify observations over GFOI priority countries for 2014 (UN-REDD Pilots, WB-FCPF Partic. – 16+28 countries)
CBERS-3:
Focus on all GFOI 2014 prio countries within GS masks
Use On-board recorder – focus on GFOI prio countries in Africa

## Slide 19: GAP ANALYSIS [2015]
# coverages foreseen by L-7 and -8, CB-3 and S-2A in 2015. Yellow = 15; light green = 24; dark green = 35; purple = 50; blue = ?

## Slide 20: GAP ANALYSIS [2015] DRAFT suggestions for augmentation to BAU
Non-core mission operators:
Recommended to consider GFOI priority countries for 2015
Landsat 7, Landsat 8:
Same as for 2014, PLUS
Intensify observations over GFOI priority countries for 2015 (16+28+16 countries)
Sentinel-2
Observation over GFOI priority countries for 2015
CBERS-3:
Focus on all GFOI 2015 prio countries within GS masks
Use On-board recorder – focus on GFOI prio countries in Africa