## Slide 1
ESA activities in measuring GHGs
Yasjka Meijer for ESA
18 June 2018

## Slide 2
Copernicus Space Component

## Slide 3: Copernicus Sentinel missions
S-1
Radar
A
3 Apr. 2014
B
25 Apr. 2016
S-2
High Resolution Optical
A
23 Jun. 2015
B
6 Mar. 2017
S-3
Medium Resolution Optical & Altimetry
A
16 Feb. 2016
B
25 Apr. 2018
S-4
Atmospheric Chemistry (GEO)
A
2021
B
2027
S-5P
Atmospheric Chemistry (LEO)
A
13 Oct. 2017
S-5
Atmospheric Chemistry (LEO)
A
2021
B
2027
S-6
Altimetry
A
2020
B
2025
Notes: Note S-1 – S-3 are series of satellites to provide operational continuity in monitoring the components of the Earth‘s system over time – through 2030 and beyond.

## Slide 4: The Atmospheric Sentinels
Sentinel-4
Hosted on MTG-S
Sentinel-5
Hosted on EPS-SG
Sentinel-5 Precursor
Sentinel CO2 Mission (Phase A)
Notes: “EUMETSAT” deleted, as funded 1/3 though ESA MS, to be kept neutral

## Slide 5: Sentinel-5p: Improved Spatial Resolution
GOME
GOME-2
OMI
S5P/TROPOMI
SCIAMACHY
Po valley, Italy (Google)
S-5P vs SCIAMACHY, GOME-2, OMI:
Smaller pixels: 3.5x7 km2 and 7x7 km2
Larger swath-width (2600 km)  daily global coverage
~1.5 million spatial samples/orbit

## Slide 6: Sentinel-5p: Improved Spatial Resolution
S5P/TROPOMI
Pixel
3.5 km
7 km
Ispra and Lago Maggiore (Google)
S-5P vs SCIAMACHY, GOME-2, OMI:
Smaller pixels: 3.5x7 km2 and 7x7 km2
Larger swath-width (2600 km)  daily global coverage
~1.5 million spatial samples/orbit
Notes: Beijing Airport

## Slide 7: Sentinel GHG & Its Related Products
TEMPO
Sentinel-5P
Sentinel-4
GEMS
Product | Spatial | Temporal
CH4 | 7 x 7 km2 | Daily revisit
CO | ” ” | ” ”
NO2 | 3.5x7 km2 | ” ”
Vegetation SIF | ” ” | ” ”
Sentinel-5 Precursor:
From 2017 – on-going
Product | Spatial | Temporal
CH4 | 7x7 km2 | Daily revisit
CO | ” ” | ” ”
NO2 | ” ” | ” ”
Vegetation SIF | ” ” | ” ”
Sentinel-5 on MetOp-SG (EUM):
Launch readiness in 2021
Product | Spatial | Temporal
NO2 | 8x8 km2 | Hourly Europe
Vegetation SIF | ” ” | ” ”
Sentinel-4 on MTG-S (EUM):
Launch readiness in 2022
CEOS
Virtual
Constellation
Solar zenith angle [°]

## Slide 8: Sentinel-5P: Nitrogen Dioxide NO2 Ship Tracks
Strait of Gibraltar
on 20 Feb. 2018
(KNMI/NSO/ESA)
Notes: Highlight Shiptracks

## Slide 9: Sentinel-5P: Methane Preliminary Results
Nov/Dec 2017
No glint processing to date
Planned data release in October
CH4 anomalies in Africa from biomass burning & wetland emissions

## Slide 10: GHG-CCI: Satellite observation of CO2 growth rates
Michael Buchwitz1, Maximilian Reuter1, Oliver Schneising1, Stefan Noël1, Bettina Gier1,2, Heinrich 5 Bovensmann1, John P. Burrows1, Hartmut Boesch3,4, Jasdeep Anand3,4, Robert J. Parker3,4, Peter Somkuti3,4, Rob G. Detmers5, Otto P. Hasekamp5.
Computation and analysis of atmospheric carbon dioxide annual mean growth rates from satellite observations during 2003-2016
+9%
in just 15 years time
© ESA CCI / Planetary Visions, 21 Feb. 2018
Notes: Computation and analysis of atmospheric carbon dioxide annual mean growth rates from satellite observations during 2003-2016
This study estimate by how much the impact of ENSO (El Niño Southern Oscillation) dominates the impact of fossil fuel burning related emissions in explaining the variance of the atmospheric CO2 growth rate.
In this study, we analyze a new satellite XCO2 data set covering 14 years (2003-2016), this new data set confirms record large growth rates around 3 ppm/year in 2015 and 2016, which are attributed to the 2015/2016 El Niño.
Anthropogenic emissions of CO2, primarily from fossil fuel combustion, have increased the atmospheric CO2 mixing ratios at the surface by more than 40% since pre-industrial times
On average less than half of the emitted CO2 remains in the atmosphere but this “airborne fraction” varies substantially from year to year : years having higher temperatures during the vegetation growing season are
associated with larger growth rates in atmospheric CO2 at northern mid-latitudes.
The time series for the three latitude bands shown in have very similar slopes but differ in the amplitude of the seasonal cycle, which reflects the latitudinal dependence of uptake and release of atmospheric CO2 by the terrestrial biosphere
The searchers conclude that the human emissions explain 27% of the variance of the growth rate and that ENSO,as quantified by the
25 SOI, explains 41%
This analysis shows that the ENSO impact on CO2 growth rate variations dominates over that of human emissions throughout the period 2003-2016
Twitter post suggestion
“The GHG XCO2 data reveals suprising result on the correlation between El Nino southern Oscillation (ENSO) and atmospheric CO2 growth rate “

## Slide 11
CSC Expansion

## Slide 12: High Priority Candidate Missions (HPCMs)
Anthropogenic CO2 | Monitoring Anthropogenic CO2 Emissions in support of GHG Monitoring and Verification
High Spatial/Temporal Res. Land Surface Temperature | Monitoring Emissivity and Evapotranspiration to support Agricultural productivity and Water Resource Management
Polar Ice & Snow Topography | Land & Sea Ice Thickness Change (incl. sea, river and lake level) in support of C3S and CMEMS
Passive Microwave Imaging | Sea Ice Concentration and Sea Surface Temp. (others incl. soil moisture and Snow Water Equivalent) in support of operational ice/marine services and EU Arctic Policy
Hyperspectral Imaging | Agriculture/food security, forestry, raw materials, soil properties and biodiversity (others incl. water quality)
L-band SAR | Forestry, Natural Hazards, Crop type & Precision Farming, Sea ice type, ice motion (others incl. soil moisture and InSAR water extraction)

## Slide 13: Candidate Copernicus Expansion Mission End-to-end System requirements to monitor CO2
Detection of emitting hot spots such as megacities or power plants.
Monitoring the hot spot emissions to assess emission reductions/increase of the activities.
Assessing emission changes against local reduction targets to monitor impacts of the NDCs.
Assessing the national emissions and changes in 5-year time steps to estimate the global stock take.
Accuracy
Space & Time
200-400 t/year
km &
daily scales
Notes: The CO2 monitoring and verification system follows as modus operandus the following 4 steps "1) detection of hot spot, 2) quantification of hot spot emission and monitoring this over time, 3) assessing the sum of the changes of the hot spot emissions belonging to a given country (allowing to follow implemented measures on the largely emitting facilities), 4) monitoring the change in emission pattern to identify potential shifts or new hot spots and evaluate the trend of the country emissions (most challenging). While the first step requires high resolution to resolve the hot spot emissions (km, daily), the last step requires large coverage and no longer high spatial and temporal resolution. On the contrary, the accuracy needed to measure the changes in emissions are becoming more demanding for step 3 and 4 when covering all emissions for an entire country, which is not only composed of hot spots. To measure the emission changes of a European country (in average only 1% relative change per year, mounting to an averaged 10% change over 5 year), the system needs to distinguish a few hunderd ton of CO2 emissions per year for the gridcells/pixels composing the country.
200 tons per yr for the grid cell area of 0.1degx0.1deg corresponds to a change of 1% of the total inventory of Belgium, which is the expected change of the Belgian inventory over 5 yr.
Added IASAI prototype CO2… advantage is that it is based on IASI which is the L1 reference instrument for IR L1.

## Slide 14: CO2 Monitoring – Space Segment Requirements 1/2
Mission requirements for XCO2:
Spatial resolution 4 km2
Revisit around 2–3 days (poleward of 40 deg) XCO2 precision: 0.5 – 0.7 ppm
Systematic bias < 0.5 ppm
MRD
CO2M
2x2 km2
OCO-2 &
TanSat

## Slide 15: CO2 Monitoring – Space Segment Requirements 2/2
Auxiliary data:
NO2 plumes for CO2 plume location, height,
and to select best wind field for inversion
 more & better CO2 emission estimates
Spatial resolution 4 km2 (as for CO2)
NO2 precision: 1–2·1015 molec/cm2
Multi-angle polarimeter for light path correction
Cloud imaging
India (Tropomi) Locations of power plants
Credits: WUR, KNMI
Simulated plume rise of XCO2
Credits: EMPA
Simulated NO2 plumes
Credits: EMPA
MRD

## Slide 16: Sentinel GHG & Its Related Products (candidate)
Product | Spatial | Temporal
CO2 | 4 km2 | 2–3 day revisit
CH4 | 4 km2 | 2–3 day revisit
NO2 | 4 km2 | 2–3 day revisit
Vegetation SIF | 4 km2 | 2–3 day revisit
CO2 Monitoring Mission :
Objective is start in 2025
CEOS Virtual Constellation options for CO2M:
Add CO2 imagers in constellation  Increase coverage
Add CO2 lidar in constellation  calibrate imagers
Contribute with in-situ
Contribute with radiometric calibration
Exploit data

## Slide 17
Thank you