## Slide 1: Progress on Chinese FY Meteorological Satellite Programs
WEI Caiying ZHANG Jiashen FAN Jinglong
National Satellite Meteorological Center ,CMA
CEOS Plenary, Organisational Issues Session
Tromsø, Norway 28-30 October 2014

## Slide 2: FengYun Satellite Observation Network
FY GEO: FY-2 satellites provide 30 min. interval full disc image and 6 min. interval regional rapid scan service
FY LEO: FY-3 satellites provide global observation for weather, climate and environment
DB service and near real-time data dissemination via CMACast ,internet…
National Satellite Meteorological Center ,CMA
FY-2D
86.5
FY-2E
105
FY-2F
112
FY-3B
FY-3A
/FY-3C

## Slide 3: New membler: FY-3C
FY-3C, as the first operational one of new generation of CMA polar-orbiting satellite, is the successor of experimental satellites FY-3A/B working in orbit
ok
Launched on 23, Sept. 2013，Operation since June, 2014

## Slide 4
FY-3 OPERATIONAL SATELLITE INSTRUMENTS | FY-3C
MERSI – Medium Resolution Spectral Imager (I, II) | √(I)
MWTS – Microwave Temperature Sounder (I, II) | √(II)
MWHS – Microwave Humidity Sounder (I, II) | √(II)
MWRI – Microwave Radiation Imager | √
WindRAD - Wind Radar | 
GAS - Greenhouse Gases Absorption Spectrometer | 
HIRAS – Hyperspectral Infrared Atmospheric Sounder | 
OMS – Ozone Mapping Spectrometer | 
GNOS – GNSS Occultation Sounder | √
ERM – Earth Radiation Measurement (I, II) | √(I)
SIM – Solar irradiation Monitor (I, II) | √(II)
SES – Space Environment Suite | √
IRAS – Infrared Atmospheric Sounder | √
VIRR – Visible and Infrared Radiometer | √
SBUS – Solar Backscattered Ultraviolet Sounder | √
TOU – Total Ozone Unit | √
FY-3C instruments(12)
Major Improvements compared with FY-3A/B
A GNSS Occultation Sounder added for GPS sounding
MWTS sounding channels increased from 4 to 13, while spatial resolution from 70Km to 20Km
MWHS sounding channels increased from 5 to 15, with 118GHz O2 absorbing band new added
Auto solar-tracking capability for SIM to improve measurement accuracy
Better performance for at least 60% of instrument specifications
Longer design life, more reliable for operational guarantee

## Slide 5
FY3C_MERSI_Scandinavian Peninsula 20140915

## Slide 6
2013-12-04
6
Tibet Plateau from MERSI/FY-3C (Dec. 3, 2013)

## Slide 7
FY-3C MERSI: Arabian Peninsula

## Slide 8
As seen from the images, only eye area of SEPAT scatters in low frequency channel(10GHz) , with the frequency increasing, the features of typhoon structure become more and more clear.
Tropical Cyclone SEPAT by FY-3C MWRI, 30 Sept. 2013

## Slide 9
NEdT from FY3A/B/C MWRI (K)
Channel | 89V | 89H | 36V | 36H | 23V | 23H | 18V | 18H | 10V | 10H
FY3A | 0.67 | 0.58 | 0.31 | 0.33 | 0.38 | 0.44 | 0.43 | 0.43 | 0.43 | 0.43
FY3B | 0.55 | 0.64 | 0.26 | 0.24 | 0.36 | 0.35 | 0.35 | 0.37 | 0.30 | 0.31
FY3C | 0.41 | 0.41 | 0.27 | 0.27 | 0.33 | 0.39 | 0.40 | 0.42 | 0.31 | 0.29

## Slide 10
Stability of NEdT: 2013.12.1-30d (MWTS-2)
channels
Red line: specification; dot: on-orbit
On-orbit is better than specification
supposed to be good enough for NWP

## Slide 11
Standard deviation of o-b similar to ATMS after bias correction
FY-3C MWHS-2 compared to ATMS
FY-3C MWTS-2/MWHS-2 compared to ATMS

## Slide 12
Improved FengYun Satellite Data Assimilation
CMA/NSMC (Agency) Basic and general support
CMA/NWPC(User)
Feedback
UKMO(User)
Feedback
ECMWF(User)
Feedback
Closer collaborations among four centers
for FengYun satellite data assimilation is underway.
Share; early evaluation; preparation before launch
ECMWF starts using FY-3B data in the operational forecasting system on 29 September 2014

## Slide 13
Satellite Monitoring Analysis Remote-sensing Toolkit (SMART) - for FY-3
Multi-source data reading and displaying
Reading and displaying Satellite data
Reading and displaying GIS data
Customizable color palette for data displaying
Common toolkit in image processing
Multiple functions of color adjustment
Multiple image adjustment functions
Multiple auxiliary tools including magnetic lasso etc.
Source
image
Objective
image
Matched
image
Specialized toolkit in remote sensing
map projections in multiple windows
Image geometrical correction
Image split or and mosaic
Thematic products analyzing
Analyzing and processing of environmental change monitoring
Temporal analysis function of monitoring products
Thematic products generation
Customization of thematic map templates
Label for thematic map
Public service
Thematic products
Statistic table
Operational reports, etc.
Notes: Toolkit software package is very important to promote the product utilization. Through the product the utilization, the quality of product can be feedback.
This is the FY-3 data toolkit software package which focus on environment and disaster monitoring more.

## Slide 14
Data Delivery Services
1) Web-based Service（register user）
2) FTP Push （important user）
3) FTP Pull （register user）
4) Manual Service （emergency）
5) CMACAST （register user）
6) DB Users （register user）

## Slide 15
FY-3 DB Users – free access to
5 Instruments available
  MERSI, VIRR, MWTS, MWHT, IRAS
Hardware recommended
  CPU: Intel Pentium Duo Core processor (>3.0Ghz)
  Hard disk: >200GB
Operating system tested
  RedHat Fedora Linux 6.0/8.0/10.0
Software packages released
  FY3L0pp: unpack raw data in both X/L bands to generate level-0 data from the 5 instruments
  FY3L1pp: processes level-0 data to generate corresponding level-1 data respectively.
FY-3 International Pre-processing Packages
http://satellite.cma.gov.cn

## Slide 16
FUTURE CMA LEO SATELLITES
07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26
FY-3A
FY-3B
FY-3C
FY-3D/pm
FY-3E/am
FY-3G/am
FY-3RM
Following FY-3C, FY-3D/E/F/G will be launched at the pace of one satellite every two years. The life time for each satellite is 5 years. Also, CMA is developing plan for rain observation satellite, FY-3RM. The first scheduled launch of FY-3RM is in 2019, life time 5 years.

## Slide 17
FY-3 Early Morning 6:00 AM
Metop-A 9:30 AM
NPP 13:30 PM
To optimize the current global polar constellation
Orbital Option: Metop+NPP+FY-3
Recognizing that global even distribution of sounding data is of great significance for the 6 hour NWP assimilation window, one approach is to constitute a three orbital fleet including Metop (Mid. Morning) + NPP (Afternoon) + FY-3 (Early Morning).

## Slide 18
1. Potential User Workshop
  Beijing, March 11, 2013
  CMA Headquarter, NWPC, NNWPC, NCC, CAMS
2. Engineering Feasibility Seminar
  Shanghai, Nov. 8, 2012
  Shanghai, Jan. 10, 2013
  Beijing, March 12, 2013
  SAST/CAST
3. Financial Support Discussion
  Jan., 2013
  CMA, CNSA, NDRC
4. Tiger Team Meeting
  April,2013
  CMA
Investigating Possibility for FY-3 Early-morning Orbit

## Slide 19
Summary
FY-3C has been improved with good performance
Closer collaborations from UKMO、ECMWF、CMA is ongoing to improve data assimilation of FY-3C in NWP
FY-2G is scheduled for launch in December this year