## Slide 1: WSIST Water Contellation FS report
JAXA
CEOS Plenary 2016
Agenda Item 2.3
Brisbane, Australia
1st – 2nd November 2016
Committee on Earth Observation Satellites

## Slide 2
The GEOSS Water Strategy renews the observational component of the community’s efforts to communicate the needs of the Water community within the framework of GEOSS.
CEOS Water Strategy Implementation Study Team (WSIST) prepared the CEOS Water Strategy to the GEOSS Water strategy recomendations.
CEOS Plenary 2016, Kyoto, decided on extention of WSIST for one year to implement the CEOS Water Strategy actions including the water constellation FS.
CEOS Water Strategy
and Water Constellation FS
IGOS Water Theme report
April 2004
GEOSS 10 Year
Implementation Plan
February 2005
GEOSS Water
Strategy
January 2014
CEOS Water
Strategy
October 2015
CEOS Water
Constellation FS
October 2016
Notes: Slide page 2 shows how GEOSS Water Strategy evolved from IGOS Water Theme to GEOSS 10 year IP and then GEOSS Water Strategy for more than 10 years with a single goal of realizing global water cycle observing system.

## Slide 3
Sendai Framework for Disaster Risk Reduction 2015-2030
  understanding global/regional/local risks
  support access to multi-hazard EWS particularly for floods and droughts
2030 Agenda for Sutainable Development
  Goal 6: Clean water and sanitation
  UN High Level Panel on Water agreed on an action plan for the SDG 6 including use of satellite based data (Sep 2016)
Paris Agreement
  Article 7 (Adaptation) calles for systematic observation of climate system and early warning systems
Linkage with
major int’l agreements

## Slide 4
Water Constellation FS
GEO Water Strategy Recommendation C1:
The feasibility of developing a Water-Train satellite constellation should be assessed. This suite of satellites would be modelled after the A-Train, providing a space segment of an observation system that would capture all fluxes and stores of the water cycle using a diverse suite of platforms and instruments. This system would operate as a Virtual Water Cycle Constellation.
The A-Train
Notes: Page 7 GEOSS Water Strategy recommendations are quire articulate as to how FS can be made.
This is the study on feasibility of developing a Water-Train satellite constellation. It should modeled after A-Train. It provides satellite observation system to capture all flexes and stores of water cycle using diverse suite of platforms and instruments. It would operate as a Virtual Water Constellation.

## Slide 5
Integrated Water Observation System
Courtesy: Toshio. Koike
Notes: Page 15 is Prof. Koike’s integrated water observation system diagram.
Land Assimilation Model combines all the parameter data.
Prof. Koike considers the benefits of integrated observation system can be demonstrated for flood and drought prediction.

## Slide 6
Requirements
Most recent user requirements “US-09-01a: Critical Earth Observations Priorities-Water Societal Benefit Area” were reviewed.
In addition, GCOS-ECV requirements and WMO Statement of Guidance (WMO-SOG) were reviewed.
Table 1.1. GEO Water SBA requirements for precipitation
Area | Horizontal Resolution | Time Resolution | Accuracy | Latency
Local | 1 km | 1 hour, or 0.08-0.5 hour | 0.1-1 mm/hour or 0.5-3 mm/hour | 0.1-6 hours or 3-24 hours
Regional | 10 km | 3 hour, or 1-12 hours | 0.5-5 mm/day | 1-2 days
Global | 50-100 km to 500 km | 1 day, or 1-3 days | 2-10 mm/day | 7-30 days
 | Also variably stated as 5-50 km |  | Also stated to be 0.1 mm or 5% of the amount | Also variably stated as RT or DT, depending on the application

## Slide 7: Water Cycle observation status: requirements vs existing/future capabilities
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L:1km R:10km G:50 to 100 km | L: 1hr R:3hr G:1d | N/A | 0.1mm/5% | 0.1h to 6hr
Precipitation
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L:0.1km to 1km R: 10km G:50 to 100km | L/R: 1 to 6 hrs R:1d to 3d G:1 to 30d to 3 months | 10cm Res. to 1m depth; | 0.02m3/m3 | NRT or 0.5d to 1d
Evaporation/ET
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L:1km R:10km G:50 to 100km | L:1 to 6 hrs R:1d G:1d to 1m | Surface(E), and LS veg cover or canopy ht f | 0.1mm or 5%. | RT
Groundwater
Soil Moisture
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L/R:1km-10km R/G:50km to 100km | 1m to 3m to 1year | 0.1km;Variable--depth | 5%-7％(Depth to W-table) | 1m to 3m Also stated as TBD-
River discharge
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L:1km-10km G: 50 km-200km | L:1 to 6 hrs R/G:1d-10d, | N/A | 5%10%;Units:m**3/sec. | Hourly to daily (NRT)
Surface water storage
Horizontal Resolution | Time Resolution | Vertical Resolution | Accuracy | Latency
L/R:1km-40km G:50km to 100km | 1wk to 1m Or 30d to 90d | N/A | 10cm-20cm(level);Or 5%. | L/R: 1w-1m R/G: 30d to 90d
Green: satisfied
yellow: marginal
red: not satisfied

## Slide 8
MWI Mission Timeline

## Slide 9
Sampling Analysis
Figure 3.1.2 Precipitation observation sampling analysis in 2016 and 2021.
2016
2021
MWI
MWI＋MWS

## Slide 10
Precipitation (P)
  Very closely connected with soil moisture and evapotranspiration (ET)
  provides input to river discharge(RD), surface water storage(ST) and groundwater (GW)
Soil moisture (SM)
  Observation at 6 AM is ideal because of low land surface temperature
  37GHz MW data is critical to retrieve soil moisture from L/C/X band data
Evapotranspiration (ET)
  Indirectly observed by soil moisture and land surface temperature
  Pairs of cloud-free land surface temperature images are required
River discharge (RD)
  SWOT has a potential to provide river water level at major rivers
  Optical sensor and SARs are useful for flood extent monitoring
Surface water storage (ST)
  SWOT plans to monitor water levels of lakes and reservoirs.
Groundwater (GW)
  GW are connected with SM and ET in data assimilation
Synergies among Variables

## Slide 11
Sensors and technologies’ synergies |  | P | SM | ET | RD | ST | GW
 | P |  | Irrigation water allocation and scheduling | Water balance Irrigation water allocation and scheduling | Water allocation and treatment | Water allocation Dam operation | Water Recharge
 | SM | Radar LST MWI |  | vegetation growth | Discharge predict for allocation | Leakage from reservoirs | Aquifer water availability
 | ET | High res LST | High res LST LC Maps |  | TBD | Storage water loss | Aquifer water availability
 | RD | Radar | Radar | TBD |  | Storage change and refill strategy | In mountains, GW discharge
 | ST | Radar | Soil Type and profile map | Surface temp | Altimetry water level DEM |  | Aquifer recharge
 | GW | TBD | Data assimilation | Soil type and profile map | Soil type and profile map | Data assimilation | 
 | Observe vation synergies | Radar, High res LST, MWI | High res LST, LC Maps, Radar, Soil maps, Data assimilation | Surface temp/LST, LC maps, Soil maps, | Radar, Altimetry Soil type and profile map | Radar, soil maps, Surface temp. Data assimilation Altimetry | Data assimilation, soil maps
Observation Synergies for
Water Resource Management
User needs benefitting from synergies

## Slide 12
 | PR | MWI | MWS | TIR GEO/ LEO | OPS MODIS/Landsat | Radar L/C/X band | Alti meter | Gravity | Remarks
P | 〇 | 〇 | 〇 | 〇 |  |  |  |  | MWI is strongly preferred than MWS and TIR.
SM |  | 〇 37GHz is critical |  | 〇 |  | 〇 Lband preferred |  |  | MWI+TIR, MWI+Radar can improve accuracy, resolution.
ET |  | 〇 |  | 〇 | 〇 |  |  |  | Pairs of cloud-free TIR images are needed.
RD |  | 〇 |  |  | 〇 | 〇 | 〇 |  | Improvement of altimeter revisit time is needed.
ST |  |  |  | 〇 | 〇 | 〇 | 〇 |  | ditto DEM is required to estimate water volume
GW |  |  |  |  |  |  |  | 〇 | SM and ET are closely related with GW in data assimilation.
Proposed Water Constellation
Instruments requirement for observing a water variables considering synergies of other variable observations are shown in the following.
Instrument
Variable

## Slide 13
Necessary components for water constellation already exist in existing and future plans.
    MWI constellation is a key component for retrieving precipitation, soil moisture and ET. Prospective gaps of FO missions of AMSR-2, DMSP/SSMI, SMOS and SMAP need to be addressed.
    Next-generation precipitation radar and synergistic observation with EarthCARE should be made to study the process of aerosol, cloud and precipitation.
    TIR, optical and L/C/X band radars can be optimized for data aquisition and product generatio to contribute to observations of SM, ET, RD and ST.
    Revisit time of altimeter missions need to be improved for monitoring river discharge and surface water storage.
    GRACE type missions should be continued for groundwater monitoring.
    Data assimilation systems should be developed to use actual data in a more optimal way.
      It is recommended that CEOS maintain some form or a water activity or advisory group to ensure that the benefits of these studies are incorporated into future CEOS discussions and plans.
Proposed Water Constellation (con’d)

## Slide 14
It is recommended that the 30th CEOS Plenary decides;
‐to endorse the CEOS Water Constellation FS report - to consider next steps by the April 2017 CEOS SIT meeting to address recommendations of the water cycle FS and remaining CEOS Water Strategy actions (C2 to C9)
Recommendations for
CEOS Plenary Decision

## Slide 15
Proposed Major CEOS actions
Out of 55 recommendations of GEOSS Water Strategy, CEOS takes the lead in addressing “Advancing satellite data acquisition”.
C1: FS on Water Constellation
C2. C3 : participation in GEO water vapor and cloud activity
C4, C5: participation in the development of precipitation white paper
C6: coordinate LST missions toward improved ET estimation
C7, C8, C9 : CEOS agency activities already cover these.
C10: FS on hyperspectral satellite mission on water quality measurement
CEOS supports external activities, including:
E5: define soil texture map requirements and communicate them to IGWCO
E8: participate in GEO activities to define a global framework for surface water storage monitoring
Notes: Out of 24 recommendations, the CEOS leads addressing C1 to C10 “Advancing satellite data acquisition” recommendations.
Two FS are included C1 for Water Constellation FS and C10 for hyperspectral satellite water quality measurement mission.