## Slide 1: Surface Water & Ocean Topography (SWOT) Mission Pre-Launch Update Program scientist/manager : Nadya Vinogradova-Shiffer (NASA) Annick Sylvestre-Baron (CNES) Project Scientist : Lee-Lueng Fu (JPL/NASA), Hydrology Leads : Tamlin Pavelsky (UNC), Jean-Francois Ctrétaux (LEGOS/CNES) Ocean Leads : Tom Farrar (WHOI), Rosemary Morrow (LEGOS/UT3)
Rosemary Morrow,
LEGOS/University Toulouse III
1.2 # 2022 CEOS Plenary
Biarritz, France
Nov. 29 – Dec. 1

## Slide 2
SWOT is a pathfinder mission addressing fundamental questions on the Earth’s water cycle and ocean energy and heat transport
SWOT will use SAR interferometry to make global measurements of water elevation over ocean & hydrology surfaces
SWOT will cover the world between 78N and 78S every 21 days
SWOT follows 30 years of nadir altimetry cooperation between NASA and CNES.
Image Credit : K. Wiedman

## Slide 3: SWOT Science & Societal Objectives
SWOT will provide valuable data and information that will benefit society in two critical areas; freshwater on land, and the oceans’ role in a changing climate.
Surface Water : observations of the amount and variability of water stored in global lakes, reservoirs, wetlands, and derived estimates of river discharge. SWOT will also provide critical information necessary for water management, particularly in international hydrological basins.
Ocean Topography : measure sea surface height at improved resolution to better understand the ocean energy & its transport of heat, carbon and nutrients, for improved understanding of the ocean’s response to climate variations.
Coastal/estuarine regions : SWOT will improve coastal observations for societal impacts in coastal regions, such as navigation, erosion and pollutant dispersion

## Slide 4
SWOT -2D data : A technological revolution
Image Credit : K. Wiedman
Ka-band SAR interferometric (KaRIn) system with 2 swaths, 50 km wide
Produces all-weather heights & co-registered imagery
Conventional Jason-class altimeter for nadir coverage, 2-horn radiometer, and GPS/DORIS/LRA for POD
Daily data downlink volume : 8 Tb/day
Over Land : Full resolution within land mask
Over Oceans : Onboard Processor performs initial SAR-Interferometry processing : reduces data download volume (resolution 250x250m )
2 orbit phases :
Calibration orbit 857 km, 77.7° incl, 1 day repeat : 6 months
Science orbit : 891 km, 77.6° incl, 21-day repeat : 3 years
Flight system : 2400 kg; 2100 W
Launch Vehicule : SpaceX Falcon 9
Mission Architecture
Launch Date : Mid December 2022
Notes: 15 Tb/day transferred between CNES & JPL

## Slide 5: SWOT & hydrology
Studies of the global water cycle
Data assimilation in models
Freshwater Inputs to oceans, groundwater
Water Catchment hydrodynamics
  Water levels and extent in lakes, reservoirs and floodplains > 250 x 250 m
  River Levels, slopes and width > 100 m wide
  21-day cycle
SWOT will mesure
SWOT will produce
SWOT will allow
  Water storage changes in lakes and reservoirs
  River discharge
New applications
Demonstrator of an operational downstream service for river monitoring
Improvement of flood prediction models
Flood probability mapping
Notes: Planche assez facile à commenter car bcp de texte. L’idée c’est de dire qu’il y a des mesures, hauteurs étendues tous les 21 jours, que ca va servir à générer des produits avancés (débits rivieres et stocks lacs et plaines inondées) et que grâce à cela on va améliorer la connaissance du cycle de l’eau à travers plusieurs aspects: (‘SWOT va permettre’).
Dire que dans le cycle de l’eau les lacs et les rivières jouent un rôle qui est essentiel: stock l’eau, et écoulement vers l’aval. SWOT va donner les informations sur les stocks et sur les débits, mais aussi indirectement sur l’evapo-transpiration via la cartographie des plans d’eau.
Dire enfin qu’il y a aussi des applications non scientifiques et les citer (dernier bloc de la planche)
C’est la première fois qu’avec une seule mission on aura accès à ces informations et donc qu’on avancera sur la connaissance du cycle de l’eau, qui est fortement impacté par ailleurs par les changements climatiques mais aussi les usages

## Slide 6
SWOT Ice-Free River Observations Per Year
Altenau et al., WRR, 2021
H & W every 200 m
H, slope, et mean discharge over 10 km sections
120,000 sections >100m wide over 10 km
  River Levels, slopes and width > 100 m wide
Notes: Rivers – also going from 2D to 3D. Going from a patchwork of some coverage in some regions, but most of the world has no data available. With SWOT we are going to a universal baseline

## Slide 7
February 15, 2019
?
?
?
?
?
?
SWOT will give us the first 3-D images of floods, which will help us better predict and track damages
Notes: Flood monitoring … image of EXTENT from a Landsat image … SWOT allows us to go from 2D (extent) to 3D (including depth)

## Slide 8
“Lakes are sentinels, regulators and integrator of climate change” and contribute to global water cycle
Today > 10 km2
SWOT > 250 x 250 m2
Today we can piece together 10000 lakes > 10 km2.
SWOT will observe millions – 2 orders of magnitude in terms of coverage
Lakes observed by SWOT
  SWOT : Water levels and extent in lakes, reservoirs & floodplains > 250 x 250 m2

## Slide 9
AF
76,714 lakes
AR
1,924,503 lakes
NA
1,544,599 lakes
SA
250,161 lakes
EU
509,449 lakes
SI
1,126,371 lakes
AS
450,911 lakes
AU
58,615 lakes
GR
41,220 lakes
Distribution of Lakes Observed from SWOT
Based on work from Yongwei Sheng’s group at UCLA based on Landsat, compiled and validated by CNES scientists.
Total: 5,982,543 Lakes >0.01 km2
Notes: Lakes : if we could download water levels from all sources – today we can piece together 10000 lakes. SWOT will observe millions – 2 orders of magnitude in terms of coverage
Canada : partenaire : un des pays où il y a le plus de lacs non suivis
Requirement : 250x250m ; goal : 100x100m
With SWOT, we don’t need the extent from imagery, we can use the surface roughness images from the interferometry calculation

## Slide 10
Current imaging satellites can track the area of all of the world’s reservoirs, which is useful for science but not directly useful for management.
SWOT will measure changes in water volume over time for tens of thousands of reservoirs, which water managers can use to understand available resources.

## Slide 11
SWOT Ocean Objectives
SWOT will measure :
Smaller ocean eddies > 10 km diameter to enhance ocean currents & fill the gap 10-100 km.
Orbit chosen to measure ocean tides, and internal tides - > mixing and energy dissipation
Global ocean observations at 250m x 250m or 2x2 km posting, up to the coast and high latitudes (78°)
Today’s 2D gridded nadir altimetry maps resolve mesoscale eddies to 100 km in diameter
10-100 km eddies
Internal tides
Why scales < 100 km ?
Most of the ocean’s energy is transported and mixed at scales < 100 km
These scales dominate in coastal and regional seas and at high latitudes
Eddy interaction along ocean fronts drives vertical pumping of heat, carbon, nutrients
Impact on air-sea interactions and biomass transport

## Slide 12
Most of the kinetic energy in the oceans is in the “mesoscale eddy” field
Today we observe eddies > 100 km, we want to observe > 10 km
(Ocean current speed from a high-resolution global simulation)
Notes: Global 1/48° ocean + sea ice MITgcm simulation
.75–2.3 km horizontal grid spacing, 90 z levels
Forced by .14° ECMWF analysis + tidal potential
14 months of hourly output has been saved

## Slide 13
Zoom shows turbulent structures downstream of Kerguelen Island.
To observe these requires 2D observations of sea surface height & slope/gradients
100 km eddy
10 km eddy & front
Most of the vertical fluxes in the ocean come from the smaller scale dynamics
(Gradients of ocean currents - Ocean vorticity from a high-resolution global simulation)
Notes: We can continue to zoom in to see more structures in these turbulent field. The level of turbulence continuum is not a surprise in theory, but the features we see are beyond the conventional picture painted by the wavenumber spectrum in the context of energy cascade. These are coherent structures, that will benefit from a two dimensional view from satellite measurements

## Slide 14: Current gradients driving vertical velocities vary seasonally
Winter
Summer
Model reconstruction of ocean strain rate observed by mapped nadir altimetry today, and nadir + SWOT swath coverage

## Slide 15: Ocean Applications
High-latitude SSH/Currents in leads & Sea Ice Freeboard & snow thickness (Ka/Ku)
2D open ocean geoid & Bathymetry at 250 m
Finer-scale 2D currents & derived vertical currents
Biodiversity structure
Ocean tides & internal tides
Notes: Deep-ocean floor has more than 90% of active volcanoes, and millions of sea-mounts. The swath mapping capabilities of SWOT will improve our mapping of the marine geoid by a factor of 5 compared to todays marine geoid maps

## Slide 16: SWOT coastal/ estuaries/deltas/wetlands
SWOT objectives:
quantify the water exchanges
between the different compartments
river
estuary
wetlands
ocean
Diverse & complex environments 
large variations of water level connected to hydro-meteo-marine phenomena:
offshore currents, tides, waves, storm surges, river flow, sea level rise
Flow reversals due to tides – non-harmonic tides
Multi-hazard zones : Flooding (sea level, storm surge, river flood), erosion, pollution

## Slide 17
SWOT science teams since 2008
 | US | France | International | All
Open Ocean | 9 | 12 | 9 | 30
Coastal | 1 | 3 | 4 | 8
Hydrology | 7 | 7 | 6 | 20
Total | 17 | 22 | 19 | 58
Selection by a joint NASA/ROSES & CNES/TOSCA call. NASA selects & funds US projects, CNES/TOSCA selects international projects & selects and funds French projects
Multiple international partners & co-operation for global observations
Since 2020 (Covid) SWOT Science Team conducts monthly working group meetings.
Current Science Team : 2020-2024

## Slide 18
23 hydro
18 open-ocean
11 coastal
Strong ST implication in in-situ & airborne CalVal in 2023 (ocean research campaigns, river and lake validation, … )

## Slide 19
SWOT represents a scientific and technical breakthrough in
oceanography & hydrology
First global observations of Earth’s water ressources in SAR-interferometry
First estimate of the flows of all rivers > 50-100 m
Complete inventory of lakes, reservoirs and floodplains > 250m x 250 m and their spatio-temporal dynamics
First observations of the 2D ocean circulation at fine scale (10 km), and their interactions with the tides
2D observations of coastal / estuarine/ wetland regions : their water storage, discharge & connectivity
Conclusions

## Slide 20
Perspectives
SWOT will contribute to OST Virtual Constellation
Development of high resolution databases => ocean and hydrology
Applications and Early SWOT Adopters in the 3 domains: oceanic, hydrological, coastal
Improvement of dynamic and climate models for reanalysis of long series and ocean and hydrological forecasting
Launch 15 Dec 2022
Go SWOT !
Perspectives