## Slide 1: 37th CEOS Plenary GEMS Status 2023
Goo Kim, NIER
Agenda Item 3.1.2
37th CEOS Plenary
15 - 16 November 2023
Chiang Rai, Thailand
Hosted by GISTDA

## Slide 2: Launch of GEMS and its spec.
GEMS
GK-2B
Launch on 19 February 2020 (the Guiana Space Center)
GEMS overview
Main Targets | O3, SO2, NO2, HCHO, Aerosol and so on
Mission Period | 10 years
Scan Area | 5,000km x 5,000km(5°S – 45°N, 75°E – 145°E)
Spatial Resolution | 3.5km x 8km (Ozone Profile & CHOCHO: 14x32km, SO2: 7x16km)
Time Resolution | 8 times on average (30min scanning, 30min stand-by)
Spectral Resolution | UV-VIS, 300-500nm
Obit/Height/Longitude | Geostationary satellite/36,000km/128°E
Environmental Satellite Center

## Slide 3: GEMS observation plan
Scan Regions
Countries in GEMS domain (20)
China
Vietnam
Japan
Mongolia
Singapore
S. Korea
Malaysia
Thailand
Indonesia
Cambodia
Philippines
Laos
Brunei
Palau
Bangladesh
Bhutan
India
Nepal
Sri Lanka
Myanmar

## Slide 4: GEMS observation plan
Monthly observation plan

## Slide 5: GEMS data release
Normal Products (Level2) Total: 21types
Aerosol optical depth
NO2
Total ozone
Effective cloud fraction
SO2
Plant response index
Tropospheric NO2
DNA damage index
Vitamin D index
Single scattering albedo
UV aerosol index
Visible aerosol index
Cloud pressure
Background Relectance
Cloud radiance fraction
UV index
HCHO
CHOCHO
Aerosol Effective Height
Stratospheric Ozone
Tropospheric Ozone

## Slide 6: GEMS data release
NO2-Daily-Average(NO2-Trop-daily)
PM10 surface conc.
PM2.5 surface conc.
Aerosol mass flow rate
NO2-Monthly-Average(NO2-Trop-daily)
SO2 mass flow rate
NO2 surface conc.
(Jun.2023~) Average Products (Level3)
Value Added Products (Level4)
New

## Slide 7: GEMS data release
Level | No. | Product Group | Product | Unit
L3 | 1 | Average | Tropospheric Nitrogen dioxide (daily average) | molec/cm2
2 | Tropospheric Nitrogen dioxide (monthly average) | molec/cm2
L4 | 3 | Flow Rate | Aerosol Mass Flow Rate | Mg/hour
4 | Sulfur dioxide Mass Flow Rate | Mg/hour
5 | Estimated Surface | PM2.5 Surface | ㎍/㎥
6 | PM10 Surface | ㎍/㎥
7 | NO2 Surface | ppb
Normal Products (Level2)
Application Products (Level3, 4)
Serviced since 2023
Serviced since 2022
Serviced since 2021
☯ Ratio between NO2 and △XCO2 product will open from this year(TBD)
- Only image files will be displayed through gems homepage
Level | No. | Product Group | Product | Unit
L2 | 1 | Aerosol | Aerosol Optical Depth | -
2 | Sing Scattering Albedo | -
3 | UV Aerosol Index | -
4 | VIS Aerosol Index | -
5 | AEH | Aerosol Effective Height | Km
6 | Cloud | Effective Cloud Fraction | DU
7 | Effective Cloud Pressure | DU
8 | Cloud Radiance Fraction | DU
9 | BSR | Background Surface Reflectance | -
10 | O3 | Ozone Total | hPa
11 | Tropospheric Ozone Profile | -
12 | Stratospheric Ozone Profile | -
13 | VOCs | Formaldehyde | molec/cm2
14 | Glyoxal | molec/cm2
15 | NO2 | Tropospheric Nitrogen dioxide | molec/cm2
16 | Stratospheric Nitrogen dioxide | molec/cm2
17 | SO2 | Sulfur dioxide | molec/cm2
18 | UVI | UV Index | -
19 | Plant Response Index | -
20 | DNA Damage Index | -
21 | VitaminD Synthesis index | -
New

## Slide 8: GEMS data release
(May. 2023~) Homepage design updates
☯ GEMS data can be easily accessed through Website
☯ Website Address : https://nesc.nier.go.kr
New

## Slide 9: GEMS data release
1. Download from the ESC website (nesc.nier.go.kr)
- Anyone can download GEMS data without logging in.
- Up to 20 GB and 40 files
2. SFTP service (A written application form required)
- User’s public IP address, which is allowed to pass
through the ESC’s Web Application Firewall (WAF).
- Submit an account(to connect SFTP server and download data)
※please refer to “How to Access GEMS data” page
(https://nesc.nier.go.kr/en/html/cntnts/91/static/page.do)
3. GEMS Open-API (need to request API Key through ESC website)
- GEMS Open-API is an interface that enables users to more easily access
and use GEMS images and data products to serve their own purposes
such as developing web services or mobile applications
※please refer to “Open-API Key Issuance” page
(https://nesc.nier.go.kr/en/html/svc/openapi/insert.do)
Data service summary
(Application form)
ESC
Servers
User
(1) Request with application form
(2) Approved
(3) Connect to serves
New

## Slide 10: GEMS data release
(Jun. 2023~) GEMS Application Tool (GEMSAT)
- GEMSAT is an intuitive software that provides specialized and dedicated functionality of plotting, visualizing, and analyzing
space-based air quality data so that users can easily leverage satellite measurements to meet their specific needs.
New