## Slide 1: AC-VC GHG White Paper
Atmospheric Composition Virtual Constellation
SIT Tech Workshop 2017 Agenda Item #
Side Meeting “UNFCCC/IPCC Engagement”
CEOS Strategic Implementation Team Tech Workshop
ESA/ESRIN, Frascati, Italy
13th-14th September 2017
Committee on Earth Observation Satellites
Prepared by David Crisp,
Jet Propulsion Laboratory,
California Institute of Technology
Copyright 2017 California Institute of Technology. Government sponsorship acknowledged

## Slide 2
The primary focus of the AC-VC Greenhouse Gas (GHG) effort since the CEOS SIT-32 meeting has been the development of the GHG White Paper.
Community contributions to the White Paper were solicited at the following meetings:
6-8 June: IWGGMS-13, Helsinki, Finland
  Discussion of Requirements of Future GHG missions
11-16 June: CGMS Jeju Korea
  WG-II/WG-III GHG joint session on carbon observations
  CGMS Plenary Session G: Carbon Observations
28-30 June: CEOS he AC-VC-13 in Paris, France
  Devoted the afternoon session to a discussion of the AC-VC GHG White Paper
Progress since the CEOS SIT-32

## Slide 3
Contributions from participants at the CGMS and CEOS AC-VC meeting were incorporated into the White Paper structure:
Chapter 1: Need for space-based measurements of CO2 and CH4
Chapter 2: Existing space-based GHG Satellites and near term plans
Chapter 3: Lessons Learned from GOSAT and OCO-2
Chapter 4: Integrating Near-term Missions into a Virtual Constellation
Chapter 5: Defining GHG Constellation Requirements
Chapter 6: Candidate Constellation Architectures
Chapter 7: Ongoing studies of operational GHG constellations: the Copernicus CO2 Sentinels
Chapter 8: The Transition from Science to Operations
Chapter 9: Conclusions
White Paper Chapters

## Slide 4
Reduce uncertainty in fossil fuel emission inventories and their time evolution
  Review origin, content, and limitations of present GHG inventories
  New requirements from UNFCCC Paris agreement (e.g. “global stocktaking”)
  Summarize challenges of discriminating and quantifying anthropogenic emissions in context of natural carbon cycle
Monitoring and predicting changes in the natural carbon cycle associated with climate change and human activities
  Deforestation, degradation, fire
  Changes in CO2 and CH4 associated with drought, temperature stress, melting permafrost
  Ocean thermal structure and dynamics
Need for space-based measurements of CO2 and CH4

## Slide 5
Existing space-based GHG Satellites and near term plans
EnviSat SCHIAMACHY
2002-2012
TanSAT
2016 …
GOSAT
2009 …
OCO-2
2014 …
PAST
PRESENT
2020’s*
GOSAT-2
2018
2018
OCO-3/ISS
NEAR FUTURE
Sentinel 5p
2017
Gaofen 5
2017
Feng Yun
3D
2017
Most existing and planned GHG missions are “science” missions, designed to identify optimal methods for measuring CO2 and CH4, not “operational” missions designed to deliver policy relevant GHG products focused on anthropogenic emissions
2022
GeoCarb*
MERLIN
2021
Sentinel 7
2025
MicroCarb
2020
GOSAT-3
2023
2025
CO2 Only
CO2 + CH4
CH4 Only
CO2 + CH4 + CO
* Pre-decisional, for planning and discussion purposes only.

## Slide 6
High accuracy and low bias are both essential
High spatial resolution (footprint area < 4 km2)
  Critical for quantifying emissions from compact sources
    XCO2 anomaly associated with a given CO2 injection is inversely proportional to the area of the footprint
  Critical for gathering data in presence of patchy clouds
Imaging rather than sampling the CO2 and CH4 field
  Critical for tracking emission plumes and resolving anthropogenic emission sources from the natural background
High resolution transport models for flux inversion
  Critical for quantifying at the scale of cities
  Needed for resolving anomalies associated with CO2/CH4 “weather” from local sources and sinks
Proxies (SIF, CO, and NO2) may be needed for attribution
Lessons learned from GOSAT and OCO-2
OCO-2 track through patchy clouds
GEOS-5 XCO2 Weather

## Slide 7
A multi-satellite GHG constellation could
Exploit the benefits of observations from low Earth orbit (LEO), geostationary orbits (GEO), and Highly Elliptical Orbits (HEO)
Reduce revisit times in the presence of optically-thick clouds
Improve spatial coverage without requiring very broad swaths that
  Are technically difficult and expensive to implement
  Large atmospheric path lengths at the swath edges are more likely to be contaminated by clouds
Collect coincident observations of proxies (CO, NO2, SIF) to facilitate the interpretation of the measurements
Provide resiliency to the loss/degradation of individual satellites
Facilitate data quality improvements through cross calibration and cross validation
Partnerships will help realize these objectives
Integrating Near-term Missions into a Virtual Constellation

## Slide 8
Existing studies indicate that different approaches can be combined to define the measurement requirements needed to meet the demanding GHG flux requirements
  Point source mass balance methods show the sensitivity needed to quantify localized sources (cities, individual power plants)
  Signal detection experiments provide insight into the amplitude of XCO2 and XCH4 anomalies associated with persistent flux changes and their dependence on wind speed at local to global scales
  Realistic, end-to-end OSSEs are adequate for assessing flux uncertainties associated with sensor precision, resolution, and coverage in the presence of realistic transport and clouds
  Flux inversion experiments combining data from in situ, TCCON, GOSAT and OCO-2 are being validated against “withheld data” (from aircraft or surface stations) to provide insight into the impact of biases in concentration measurements and transport
Defining Constellation Requirements

## Slide 9
The coverage, resolution, and precision requirements could be achieved with a constellation that incorporates
A constellation of (3 or more) satellites in LEO with
  A broad (~200) km swath with a mean footprint size < 4 km2
  A single sounding random error near 0.5 ppm, and vanishing small regional scale bias (< 0.1 ppm) over > 80% of the sunlit hemisphere
  One (or more) satellites carrying ancillary sensors (CO, NO2, CO2 and/or CH4 Lidar)
A constellation with 3 (or more) GEO satellites
  Monitor diurnally varying processes (e.g. rush hours, diurnal variations in the biosphere)
  Stationed over Europe/Africa, North/South America, and East Asia
One or more and one or more HEO satellites to monitor carbon cycle changes in the high arctic
A Candidate GHG Constellation Architectures

## Slide 10
The high-level monitoring system objectives are to
provide policy-relevant information (trends, impacts of measures),
support national emission inventories,
observe strong point & area sources (e.g., power plants and cities)
  As part of an integrated system comprising: satellite - in-situ – modelling - emission inventory components, for provision of timely input to policymakers
In view of the above system objectives, the following mission objective of the space component has been tentatively formulated:
  The CO2 mission shall monitor anthropogenic CO2 emissions using high spatial resolution imaging of total column CO2
Ongoing studies of operational GHG constellations: the Copernicus CO2 Sentinels

## Slide 11
With the exception of the Sentinels, all of the existing and planned GHG missions are “science” missions, designed to identify optimal methods for measuring CO2 and CH4, not “operational” missions designed to deliver policy relevant GHG products focused on anthropogenic emissions
Following the model developed by the operational meteorological satellite constellation, future GHG constellation will also need to focus on orbit and mission coordination, data distribution, data exchange, and data format requirements
To fully exploit the information collected by future GHG constellations, the missions will also have to invest in training and capacity building as well as public outreach
CEOS should exploit the experience of CGMS and other organizations to foster the development of these capabilities
Moving Forward from “Science” to “Operational” GHG Missions

## Slide 12
Data from a future, coordinated GHG constellation that combines LEO, GEO, and HEO vantage points could meet the measurement accuracy, precision, resolution, and coverage requirements
To provide reliable, verifiable constraints on GHG inventories as well as the response of the natural carbon cycle to climate change, advances are needed in:
  Laboratory measurements of gas absorption cross sections
  pre-launch and on-orbit calibration capabilities,
  GHG retrieval algorithms
  flux inversion algorithms
  GHG concentration and flux validation techniques
Open data policies that encourage the cross-calibration of sensors, the cross validation and free exchange of space based data products will accelerate the development of these capabilities and the acceptance of their results by scientists and policy makers
Conclusions

## Slide 13
Rapid progress was made in May and June, but summer vacations and other commitments slowed progress during July and August.
We are still targeting an end-to-end draft of the white paper by the end of calendar year 2017
The target due date for publication is the 2018 CEOS SIT plenary
White Paper Status and Schedule