## Slide 1: SDG: 14.1.1a Sub-team Updates
Emily Smail (NOAA)
with contributions from COAST and SDG AHT
CEOS SIT Technical Workshop 2020
Session and Agenda Item #2.1
Virtual Meeting
9 September 2020
Committee on Earth Observation Satellites

## Slide 2
14.1.1 has two indicators:
  14.1.1a (index of coastal eutrophication potential)
  14.1.1b (plastic debris density)
14.1.1a sub-indicators are organized into three levels
Level 1: Proposed global indicators
  Indicator for Coastal Eutrophication Potential (based on Nitrogen and Phospahte loadings)
  Chlorophyll-a deviations and anomalies
Level 2: Proposed national indicators
  Chlorophyll-a concentration
  National modelling of coastal eutrophication potential
  In-situ concentration of nitrogen, phosphate and silica
Level 3: Supplementary indicator
  The indicators proposed to match methods presented in SDG 6.3.2
Presenter Guidance: SDG Focus

## Slide 3
Led by NOAA in collaboration with CEOS COAST, GEO Blue Planet and GEO AquaWatch
Structure: Collaborative effort between CEOS COAST and a joint GEO Blue Planet/GEO AquaWatch working group on eutrophication
Main deliverables in preparation for the Plenary and Status:
  Requirements Table on 14.1.1a
  EO Support Sheet
Sub-team organisation and Status
Agency/GEO Initiative | Individual’s name
NOAA/GEO Blue Planet | Emily Smail (UMD)
JAXA | Chu Ishida
NASA | Laura Lorenzoni
CSIRO | Flora Kerblat
NOAA/GEO AquaWatch | Steve Greb (Univ. Wisconsin)
GEO Blue Planet | Frank Muller-Karger (USF)
GEO Blue Planet | Karina von Schuckman (Mercator Ocean)

## Slide 4
Simplified Requirements
 | How ? |  | When ? | Where ? |  | 
SDG Requirement | Spatial Resolution | Measurement Type | Observation Frequency | Sampling Type | Comments | Mission Classes
Level 1 Sub-indicators |  |  |  |  |  | 
Chlorophyll a deviations in EEZs | 4km | Optical | Monthly blended product | Global | The ESA Ocean Colour CCI (OC_CCI) project, led by Plymouth Marine Laboratory (PML) is used as the default global data set. The product is a merged chlorophyll-a product from SeaWiFS, MODIS, MERIS and VIIRS, spanning 1997 to 2018 | 1
Chlorophyll a anomalies in the EEZ | 2km | Optical | Monthly blended product | Global | The NOAA VIIRS chlorophyll a anomoaly product is used as the default global dataset. The anomaly product is defined as the daily Chlorophyll value subtracted from the baseline mean value for the chlorophyll product over 61 days. The daily chlorophyll a value subtracted from the baseline mean value for the chlorophyll product over 61 days. | 1
Level 2 Sub-indicators |  |  |  |  |  | 
Regional potential eutrophic zones (coastal chlorophyll a) | 100 - 1000m | Optical | Near real time | Regional (regional seas programmes) | This sub-indicator will be based on eutrophication based on regionally defined values of chlorophyll-a limits and interannual trend. The indicator data will be derived using regionally tuned algorithms for satellite-derived chlorophyll-a. | 1,2
Level 3 Sub-indicators |  |  |  |  |  | 
TBA |  |  |  |  |  | 

## Slide 5
Main findings
  Many countries lack in situ data required for monitoring eutrophication
  Satellite data is crucial for providing some information about 14.1.1a
KEY MESSAGES FOR THE CEOS AGENCIES
  Capacity development for level 2 and level 3 sub-indicators will be needed for many of the regional seas programmes
Summary of the EO Support Sheet

## Slide 6
Thank you
We will happily respond to your question sin the Q&A session at the end of the sub-teams reporting
Co-leads Contact details:
Emily.Smail@noaa.gov
THANKS