## Slide 1: An Atmospheric CO2 Gap Analysis for CEOS CEOS SIT-25 Meeting Tokyo, Japan April 12-15, 2010
Brian Killough CEOS Systems Engineering Office (SEO)

## Slide 2
Systems Approach to Climate
Systems taxonomy for organization
Strategy for collaboration and action
Information products & services
Decision Makers
Science Knowledge & Models
Measurements
Instruments and Missions
Capabilities
Gap Assessments
Requirements
Agency Action
Societal Benefit and Policy Decisions
Applications
Process and Forecasting
Space Hardware
What are the user requirements and corresponding measurement needs ?
What are current and planned assets in space and their capabilities ?
What are the measurement or user requirement gaps ?
How can space agencies collaborate and act to fill gaps and critical needs ?

## Slide 3
Starting Point… the CEOS Databases
www.ceos.org
CEOS MIM Database
Search for CEOS missions that measure CO2 … you will find only 4 on the “official” agency MIM list. We know there are many more …
Further web searches found valid CO2 data products produced by 19 CEOS missions.

## Slide 4
General Mission Timeline Results
NO GAPS ???
  Timelines from the expanded mission list (above) DO NOT accurately reflect gaps.
  Gap analyses must consider instrument types (measurement approach), atmospheric layers, and detailed requirements (accuracy, spatial resolution, temporal resolution).
  Automation of the detailed gap analysis process using existing CEOS databases is not currently possible … maybe in the future.

## Slide 5
CEOS Systems Database
www.ceos-sysdb.org
Next… Search the Systems Database for Requirements
www.ceos.org
Requirements
Search for CO2 measurement requirements from GCOS, EUMETSAT, and WMO.
Examples: Spatial resolution, vertical resolution, repeat cycle, accuracy, spectral resolution, atmospheric layers.

## Slide 6
What are the Detailed Requirements ?
  GCOS Climate requirements are the most restrictive. For example, objectives of 4-ppm accuracy, 10-km spatial resolution and 3-hour repeat cycle are required in the lower troposphere.
Source: WMO GOS Dossier Volume-5 compiled for WMO by B. Bizzarri.

## Slide 7
What are the Detailed Mission Capabilities ?
Detailed mission capability information is not currently available in the MIM or Systems Databases so this step requires extensive web searches. Hopefully, in the future this level of detail will exist in the databases so this process can be automated.

## Slide 8
Which Missions Meet the Requirements ?
Largest issue is temporal sampling (repeat cycle) near the surface …
Limited LEO missions do not allow adequate sampling to achieve desired threshold requirement of 24-hr (one-day) repeat cycle. GOSAT is best at 3-days due to its wide (790-km) crosstrack scanning capability, but it does not make constant measurements across the swath width.

## Slide 9
Detailed Timeline Analysis
GAP
Detailed timeline analysis takes into consideration the instrument type and atmospheric layer.
Largest issue is the potential time gap beyond OCO-2.
It is unlikely that ENVISAT and GOSAT will last beyond 2015. OCO-2 has fuel for 8-years (till 2020). ASCENDS is uncertain for a 2020 launch and may be later.
OCO-2 may be the only near-surface CO2 mission in 2015 with limited repeat cycle (16 days) and spatial coverage (swath width 10-km).

## Slide 10
Gap Analysis Results
  Atmospheric CO2 measurements in the lower troposphere (near surface), critical for measuring sources and sinks, have a time gap beyond 2016. – see TIMELINE ANALYSIS
  Temporal sampling (repeat cycle) requirements are not met for all lower troposphere missions and most mid-troposphere missions. GCOS threshold requirements are 12 hours (lower trop) and 6 hours (middle trop), which requires multiple coordinated LEO satellites with wide swath capabilities. – see REQUIREMENTS ANALYSIS
  Accuracy requirements (< 4-ppm) are met for all middle-troposphere instruments and most lower-troposphere instruments (exception is SCIAMACHY). Most future low-troposphere instruments expect ~1-ppm accuracy, which will significantly improve our knowledge of sources and sinks. - see REQUIREMENTS ANALYSIS

## Slide 11
Lessons Learned and the Future
Lessons Learned
  Future gap analyses efforts will require detailed assessments of timelines and requirements to reach valid conclusions. Online automation of the gap analysis process is not yet possible.
The full CO2 Gap Analysis report is available on the CEOS website.
Future Work
  Capabilities need to be updated in MIM database. Agencies need to provide more accurate and complete data for the 2010 MIM data request.
  Plan to review existing requirements and add more space-based measurement requirements for CO2 and other climate ECVs.
  Consider adding data availability or quality indicators to instrument-measurement combinations.
  Conduct a CH4 gap analysis. Significant discussion at the recent ACC-5 meeting included several new mission concepts for Methane (CH4).
  Conduct a coverage analysis for CO2 to determine the relationship between repeat cycle, swath width and the number of satellites to support solution options for the CO2 measurement gap.

## Slide 12
Backup Charts

## Slide 13
Near-term Potential Solutions
  Extend existing missions: Utilize the full mission capacity of ENVISAT and GOSAT to make total column CO2 measurements in the lower troposphere at least until OCO-2 is launched.
  Future mission lifetimes: Consider designing future space missions with more capacity for extended operations. This “research to operations” concept may extend science missions from 3-5 years to beyond 10 years.
  Adjust new missions: Optimize time overlap of current and future missions by adjusting launch schedules or adjusting orbits to maximize coverage or sampling.
  Add new missions: Consider new missions focused on near-surface (lower troposphere) atmospheric CO2 measurements with a direct benefit to studies of sources and sinks. This requires absorption spectrometers or lasers focused in the near-IR. For example, a JAXA GOSAT follow-on, ESA Earth Explorer CarbonSat 2018 concept, NASA OCO-3 instrument (Mission of Opportunity), Micro-Carb (CNES).
Are there others ???

## Slide 14
Long-term Potential Solution: Constellation Concept
  A constellation of CEOS satellites dedicated to CO2, requires careful consideration of requirements and must be coordinated with in-situ and ground resources.
  Repeat cycle must be considered along with accuracy (ppm), spatial sampling (single sample) and swath coverage.
Example: GOSAT: 3-day repeat, 4-ppm accuracy, 10.5-km/sample, 790-km swath * High repeat cycle achieved with large swath width. OCO-2: 16-day repeat, 1-ppm accuracy, 1.3-km/sample, 10-km swath * Narrow swath width and sample size to optimize cloud-free scenes.
  Other new mission concepts are being considered internationally, but it is uncertain whether a single satellite, or a constellation of coordinated satellites can meet the full set of space-based requirements.