## Slide 1
Carbon products: Calibration and validation approaches

## Slide 2
TANSO is the only FTS for GHG measurements from space
2
SCIAMACHY (2002 - 2012) | GOSAT (2009 - ) | OCO-2 (2014-) OCO-3 (2018) |  | GHGsat (2016-)
TanSat (2016-) | TROPOMI (2017-) | GOSAT-2 (2018-) | MERLIN (2020) | GeoCARB
MicroCarb (2020) | ASCENDS (2021) | CarbonSat (2022) | GOSAT-3 | G3E
 |  |  | Lab model test | 

## Slide 3
Japanese GOSAT and US OCO-2 have different observation strategies.
TANSO-FTS onboard GOSAT has wide spectral coverage from SWIR to TIR and an agile pointing system at the expense of spatial context, while OCO-2 targets CO2 with higher spatial resolution using imaging grating spectrometers.
Since the early phase of the two projects, both teams have worked in calibration and validation to demonstrate the effectiveness of satellite greenhouse gases observation.
International effort to demonstrate the effectiveness of satellite GHG observation.

## Slide 4: Inter-comparison between GOSAT and OCO-2
2008 2009 2010 2011 2012 2013 2014 2015 2016 2017
Radiometric calibration
Prelaunch
X-CAL
CO2 & CH4 profile
XCO2 & XCH4
Coincident Target
Annual Vicarious Calibration at the desert playa in Nevada
In situ CO2 and CH4 on AJAX
Column with EM-27 FTS
Retrieved Parameter
Comparison over match up points
Calibrated GOSAT and OCO-2 radiance spectra agrees within 5% for all bands.
Retreived XCO2 bias is much less than 0.5ppm over match up observations points.
4

## Slide 5
Calibration, Retrieval, and Validation
Common standards
GOSAT/TANSO-FTS and OCO-2 observe sunlight reflected from the Earth’s surface and retrieve atmospheric carbon dioxide (CO2) with different observing geometries and ground track repeat cycles.
Most measured spectral radiances (Level 1) agree within 5% for all bands shared by the two instruments
Retrieved CO2 densities also agree within +/- 4ppm (1%).
Measurement
Level 1
Level 2
Level 1: spectra
Level 2: retrieved CO2
H2O
CO2
CH4
Should be calibrated and validated in each level.

## Slide 6: Intercomparison GOSAT/ACOS –OCO2 Level 2 XCO2
● Temporal : GOSAT – OCO2 time difference : +/- 1 hour ● Spatial : Select OCO2 data within
10.5 km GOSAT footprint
[Data period] 2014/09～2016/02 ; Level2 matchup : 715 points
⊿XCO2 (ACOS-OCO2) error bar: ⊿XCO2 deviation within GOSAT-FOV
Sep2014
Feb2016

## Slide 7: Common Standards and Data for Calibrations and Retrieval
 |  | Common standards and data | Notes
Calibration | Prelaunch | Cross-calibrate radiometers | Viewing common radiometric standard
 | Onboard | Solar data | 
 | Vicarious | CEOS site (RRV etc.) | Annual campaign
Retrieval Algorithm | Parameters | Molecular spectroscopy A priori model (Aerosol) | 
 | Input | Calibrated spectra at 0.76, 1.6, 2.0μm Observation geometry and condition | Level 1
 | Output | Retrieved column amount GHG Simultaneously retrieved parameters (aerosol optical depth, Solar-induced plant chlorophyll fluorescence (SIF)) | Level 2
Validation | Ground Site | High resolution spectrometer mobile spectrometer | TCCON
 | Air plane | In situ measured data | CONTRAIL etc.
 | Match up | Land type and Ocean | Viewing Common sites

## Slide 8: Data products Different satellite data are available from the same site
https://co2.jpl.nasa.gov/

## Slide 9: Long term data should be easy to use CO2, CH4 ,4 Aerosol Optical Depth with type classification Solar-induced plant chlorophyll fluorescence (SIF)
http://www.eorc.jaxa.jp/GOSAT/CO2_monitor/index.html