## Slide 1: AC-VC – GHG Constellation
Report to CEOS SIT
April 2017
David Crisp (JPL/Caltech)
AC-VC GHG Lead
Committee on Earth Observation Satellites

## Slide 2
GEO Carbon Report developed in June 2010 by team led by Ciais et al. (GCP).
CEOS Strategy for Carbon Observations from Space–written in response to above, completed in March 2014 –Wickland et al.
Deliveries:
  Merged CARB AI 16+18: AC-VC to support the organization of yearly IWGGMS (FMI (Helsinki, Finland) on 6-8 June 2017
  Merged CARB AI 17+19+23: AC-VC will prepare a white paper within 2 years
  CARB AI 20: AC-VC will write a Technical Note within 2 years
CEOS Carbon activity
-History and Background

## Slide 3
In February 2017, the AC-VC received a formal request from the CEOS Chair, Frank Kelly
  Included specific guidance on the content of the GHG White Paper
  Requests interim reports be provided at forthcoming CEOS SIT meetings, SIT Technical Workshops, and the 2017 CEOS Plenary
  Requests a final report to be provided at the 32nd CEOS Plenary to be held in the 4th quarter of 2018
  Invited CGMS asking them to nominate, if they wish, additional people to participate in development of the report
14 February 2017 Letter from the CEOS SIT

## Slide 4
Mandate for Satellite Carbon report content, undertaken by AC-VC
Based on existing requirements, define the key characteristics of a global architecture for carbon (CO2, CH4) measurements from space.
Consider observational needs for both composition and fluxes, natural and anthropogenic
Include known plans and considerations from space agencies worldwide in overall system architecture to ensure global consistency of design
Incorporate potential observations from both GEO and LEO potential missions in an optimal system, and consider optimal acquisition strategies across the system including orbits, equator crossing times, sensor characteristics etc.
Include instrument on-orbit calibration and geophysical validation aspects
Build on work already undertaken by AC-VC in response to the CEOS Carbon Strategy
Provide a reference architecture against which individual agencies can develop their plans to optimise joint implementation.
Report at Plenary 2017, with interim report SIT (April 2017)

## Slide 5
Define the key characteristics of a global architecture for carbon (CO2, CH4) measurements from space
The CEOS perspective
  Facilitate coordination of ongoing efforts by member agencies
  Focus on calibration and validation of space-based data and products
  Emphasize value of an open data policy and common product formats
  Foster use of space-based greenhouse gas (GHG) observations
  Consolidate data requirements for next-generation GHG satellites
Scope of the White Paper

## Slide 6
Verifying fossil fuel emission inventories and their time evolution
  Review origin, content, and limitations of present GHG inventories
  New requirements from UNFCCC Paris agreement (e.g. “global stocktaking”)
  Summarize challenges of discriminating and quantifying anthropogenic emissions in context of natural carbon cycle
Monitoring and predicting changes in the natural carbon cycle associated with climate change and human activities
  Deforestation, degradation, fire
  Changes in CO2 and CH4 associated with drought, temperature stress, melting permafrost
Introduction: Need for space-based measurements of CO2 and CH4

## Slide 7
Develop a sound-scientific, measurement-based approach that:
reduces uncertainty of national emission inventory reporting,
identifies large and additional emission reduction opportunities, and
provides nations with timely and quantified guidance on progress towards their emission reduction strategies and pledges (Nationally Determined Contributions, NDCs)
Contribution from satellite community
Improved national inventory reporting by making use of atmospheric measurements for all countries –Satellite observations can help with “closing the budget” by measurement over ocean and over areas with poor data coverage
  requires reduced uncertainty
Supporting success of post-COP21 actions to reduce climate-disrupting GHG emissions (IG3IS Perspective)
Adapted from Decola et al. October 2016 AC-VC Meeting

## Slide 8
  Measurements of CO2 and CH4 and solar induced chlorophyll fluorescence (SIF) from a constellation of GEO and LEO satellites with the accuracy, precision, resolution, coverage, and continuity needed to detect and quantify emission sources and natural sinks on local (10 km x 10 km) to national (500 km x 500 km) scales over the globe
  Precise, accurate, ground- and aircraft base measurements of atmospheric CO2, CH4, for validating the space based concentrations and fluxes with respect to internationally recognized standards
  Ground-based measurements of key isotopes (i.e. 14C) and proxy gases (CO, NO2, ethane) for attribution
  Modeling architecture for inferring CO2 and CH4 fluxes from the space based and ground based observations
    Observing System Simulation Experiments (OSSEs)
    Flux inversion models (global, regional, and local scales)
Elements of a space based top-down GHG monitoring system

## Slide 9
Deriving column-averaged CO2 and CH4 dry air mole fractions from measurements of reflected Sunlight
Retrieve variations in the column averaged CO2 and CH4 dry air mole fractions [XCO2, XCH4] over sunlit hemisphere
Record spectra of CO2 , CH4, and O2 absorption in reflected sunlight
Validate measurements against available standards to ensure XCO2, XCH4 accuracy
Flask
FTS
GOSAT and OCO-2
Tower
Aircraft
Initial Surf/Atm
State
Revised Surf/Atm State
XCO2
Radiative Transfer Model
Instrument
Performance Model
Inverse Model

## Slide 10
A multi-satellite GHG constellation could
Exploit the benefits of observations from low Earth orbit (LEO), geostationary orbits (GEO), and Highly Elliptical Orbits (HEO) vantage points
Reduce revisit times in the presence of clouds
Improve spatial coverage without requiring very broad swaths that
  are technically difficult and expensive to implement, and will limit sensitivity (spectral resolution, SNR, low scattered light …)
  Introduce larger atmospheric path lengths at the edges the swath that are more likely to be contaminated by clouds
Collect coincident observations of proxies (CO, NO2, SIF) to facilitate the interpretation of the measurements
Provide redundancy in the case of the loss of a single satellite
Provide opportunities for cross calibration and cross validation
Partnerships will help realize this objective
Advantages of GHG Constellations

## Slide 11
High spatial resolution imaging observations from broad-swath instruments on LEO platforms
Can collect measurements over nearly the entire globe at high spatial resolution at weekly to monthly intervals
Use a single sensor, reducing sensor-to-sensor calibration biases
Allows “glint” observations for adequate signal over ocean
Platforms in LEO orbits facilitate the combined use of passive spectrometers and active LIDAR measurements
Passive sensors provide high spatial resolution and coverage across the sunlit hemisphere
Active sensors complement these measurements with sampling of high latitudes and the night side
A combination of passive and active LEO sensors can reduce bias spatially-coherent biases, which affect the sensors differently
Principal disadvantage of LEO platforms
relatively long repeat cycles (weeks)
Benefits of LEO Observations

## Slide 12
Continuous imaging of XCO2 and XCH4 from GEO platforms
Captures spatial and temporal context, resolving transport, boundary conditions and local sources and sinks
Resolves emissions from localized sources in the context of CO2/CH4 “weather” and synoptic variability (clouds, fronts)
Explicitly resolves variations in XCO2, XCH4, SIF from dawn to dusk
Reduces temporal sampling bias – does not miss flux events
GEO platform disadvantages:
Clouds limit coverage beyond ± 50 of sub-satellite point
  Observations from satellites in Highly Elliptical Orbits (HEO) would provide high time resolution coverage of high latitudes
Glint observations extremely limited, precluding observations over oceans
Multiple satellites needed to cover major continents
  Places additional demands calibration and validation capabilities
Benefits of GEO Observations

## Slide 13
Existing GHG satellites: GOSAT, OCO-2, and TanSat
  Evolution of measurement capabilities: precision, accuracy, resolution, coverage, data availability
  Progress toward a constellation: cross calibration of measurements and cross validation of products against internationally recognized standards
Near-term Missions: S5P, Gaofen 5, Feng-Yun 3D, GOSAT-2, OCO-3, MERLIN
  Launch schedules, prime mission durations, orbits, sampling times
  New measurement capabilities and challenges
Missions in formulation: MicroCarb, GeoCarb, GOSAT-3, Sentinels
  Launch schedules
  New measurement capabilities and challenges
All of these are “science” missions, designed to assess how to best measure CO2 and CH4, not “operational” missions designed to deliver policy relevant products
Existing space-base GHG Satellites and near term plans

## Slide 14
Evolving Carbon Measurement Capabilities
EnviSat SCHIAMACHY
2002-2012
TanSAT
2016 …
GOSAT
2009 …
OCO-2
2014 …
PAST
PRESENT
TanSat Successfully Launched on 22 Dec 2016
NASA Earth Ventures GeoCarb Selected
CNES MicroCarb Approved for Implementation
2022
GeoCarb
MERLIN
2021
Sentinel #
2025
MicroCarb
2020
ASCENDS
202X…
LATER
GOSAT-3
2023
GOSAT-2
2018
2018
OCO-3/ISS
NEAR FUTURE
Sentinel 5p
2017
Gaofen 5
2017

## Slide 15
Even for the existing GHG science missions, there are numerous benefits of integrating data across the constellation
  Improving coverage in the presence of clouds
  Covering more of the day-lit portion of the diurnal cycle
  Maintaining data continuity if one satellite is lost
Coordinating measurement capabilities during mission formulation
  Trade-offs in precision, accuracy, resolution, coverage
  Maximizing benefits of LEO, GEO, and HEO vantage points
Cross calibration of measurements
  Pre-launch calibration measurements using common standards
  On orbit calibration (on-board, astronomical, and vicarious)
Cross validation of retrieved CO2 and CH4 concentrations
  Current role of TCCON and aircraft
  Future needs
Benefits of integrating data across the constellation

## Slide 16
Pre Launch:
  Cross calibration of pre-launch radiometric standards
  Exchange of gas absorption coefficient and solar databases
  Retrieval algorithm development/intercomparison
  Validation system development (TCCON + Tsukuba FTS?)
  Dual/multi-Satellite OSSE’s – what do you gain with truly coordinated observations
Post Launch:
  Cross calibration of solar/lunar/Earth(vicarious: RRV+?) observations
  Including exchange of solar and lunar (ROLO) standards
  Cross validation: TCCON, validation campaigns
  Continued retrieval algorithm development/intercomparisons
  Intercomparisons of flux inversions
Examples of collaborative activities needed to exploit combined data sets

## Slide 17
High spatial resolution (footprint area < 4 km2)
  Critical for quantifying emissions from compact sources
    XCO2 anomaly associated with a given CO2 injection is inversely proportional to the area of the footprint
  Critical for gathering data in the presence of patchy clouds
Imaging rather than sampling the CO2 and CH4 field
  Critical for tracking emission plumes and resolving anthropogenic emission sources from the natural background
High resolution transport models for flux inversion
  Critical for quantifying at the scale of cities
  Needed for resolving anomalies associated with CO2/CH4 “weather” from local sources and sinks
Proxies such as SIF, CO, and NO2 may be needed for attribution
Lessons learned from GOSAT and OCO-2 CO2 and CH4 Measurements
OCO-2 track through patchy clouds in NE U.S.
GEOS-5 XCO2 Weather

## Slide 18
High precision and coverage needed to characterize compact sources
drawdown counters emissions
50km
Los Angeles Basin
Winter and summer OCO-2 tracks across the Los Angeles basin and the Antelope Valley to the north of the San Gabriel mountains show XCO2 anomaly across the megacity [Schwandner et al, Submitted 2017] .
4.4 ppm
6.1 ppm
Direct OCO-2 overpasses or close flybys clearly detect emission plumes from individual, moderate sized power plants, yielding flux accuracies of 8 to 50% [Nassar et al. 2017].

## Slide 19
OMI NO2 Anomalies
OCO-2 XCO2 Anomalies
Proxies useful for CO2 emissions source attribution:
  CO traces both moderate (biomass burning) and high temperature (fossil fuel) combustion
  NO2 traces high temperature (fossil fuel) combustion
  SIF traces spatial distribution of CO2 uptake by the land biosphere
What proxies are needed for discriminating CH4 sources?
Proxies and other Coincident measurements needed
OCO-2 XCO2 and OMI NO2 anomalies over Europe (fossil fuel combustion) but not over central Africa (biomass burning) [Hakkarainen et al., GRL 2016]
OCO-2 SIF is more intense over corn fields than over Des Moines, Iowa
[Frankenberg et al., 2016]

## Slide 20
Apply best practices (lessons learned) for spectrometer calibration, characterization, and validation
  Share calibration/characterization plans and invite cross participation in reviews of such plans
  Develop longer term recommendations for common post-launch cal/val strategies (e.g. cal/val instrumentation round-robins, joint vicarious calibration campaigns, joint airborne campaigns)
Radiometric consistency
  Pre-launch: highest priority is per-instrument calibration/characterization as completely as possible (common absolute radiance calibration is secondary)
  Post-launch: (eg LEO vicarious intercalibration, lunar calibration, solar calibration)
Sharing and consistency of data products (format, content, metadata)
  Share specification documents
  Share instrument characterization/calibration databases and Level 1-b data, in a common format, to allow wide application of algorithms to all datasets
  Identify and produce common constellation data products (may differ from standard products)
Consistency in retrieval algorithms
  Cross participation in ATBD reviews
  Jointly improve retrieval algorithms by conducting inter-comparisons on common spectra
Consistency of laboratory spectroscopy
Support scientific collaboration among teams
Open Data Policy and Common Cal/Val Standards: Recommendations
Adapted from Atmospheric Composition Constellation Meeting ACC-11, Frascati, Italy, 28-30 April 2015

## Slide 21
GOSAT and OCO-2 data were validated against the Total Column Carbon Observing Network (TCCON)
TCCON is validated against the WMO standards profiles from in situ instruments on aircraft
Other standards, including aircraft campaigns (HIPPO, ACT-America, Atom) also used
These validation methods may have to be expanded to support future observations from LEO, GEO and HEO platforms
Validating space-based measurements against international standards
Example of comparisons between OCO-2 and a wide array of TCCON stations. After applying a bias correction, the global bias is reduced to < 0.5 ppm and the station-to-station biases reduced to ~1.5 ppm

## Slide 22
Efforts to trace requirements on the space based CO2 and CH4 concentration measurements to the desired improvements in inventories use numerical models of increasing sophistication:
  Signal detection experiments use carbon tracer transport models (CTTMs) to simulate atmospheric the impact of atmospheric transport on GHG concentration changes associated with specified changes in surface fluxes (i.e. doubled CO2 emissions from East Asia or CH4 injections from a broken pipeline or melting permafrost)
  End-to-end Observational System Simulation Experiments (OSSEs) combine CTTMs with remote sensing retrieval models and instrument models to assess observing system and retrieval algorithm trade in “realistic” conditions
  Flux inversion experiments using existing space-, aircraft-, and ground based data provide an end-to-end test of accuracy, precision, resolution, and coverage of existing observing systems for a wide range of conditions
Tools for deriving Constellation measurement requirements

## Slide 23
All 3 approaches need improvements to derive requirements for a constellation of satellites for anthropogenic GHG measurements
  Signal Detection experiments provide insight into sensitivity, resolution, and coverage needs as a function of source/sink scale, but provide no information about correlated errors or systematic biases
  OSSEs are good for identifying impact of random errors in concentration or transport or limitations of coverage, but are generally not adequate for assessing the impact of systematic biases in transport or measured concentration
  Flux inversion experiments show that spatially-dense space based data pose special problems
    Limitations in coverage and biases in transport and measured concentration can all introduce significant uncertainties in fluxes
    These sources of uncertainty play different roles in local (city scale), national (500 km x 500 km), and global scale flux inversion experiments
Challenges in deriving Constellation Measurement Requirements

## Slide 24
While existing studies have identified a number of challenges in defining traceable measurement requirements, they have also indicate that different approaches can be combined to define different requirements
  Signal detection experiments provide insight into the amplitude of XCO2 and XCH4 anomalies associated with persistent flux changes and their dependence on wind speed at local to global scales
  Realistic, end-to-end OSSEs are adequate for assessing flux uncertainties associated with different sensor precision, resolution, and coverage in the presence of realistic transport
  Flux inversion experiments combining data from in situ, TCCON, GOSAT and OCO-2 are being validated against “withheld data” (from aircraft or surface stations) to provide insight into the impact of biases in concentration measurements and transport
A path forward for defining Constellation requirements

## Slide 25
To monitor anthropogenic emissions on the scale of medium sized countries (e.g. France), we need to
Resolve and discriminate anthropogenic emissions from contributions from the natural biosphere and ocean
“Image” the majority (~80%) of Earth’s surface at high spatial resolution on hourly (cities) to weekly (natural biosphere) intervals
A number of international organizations have recommended requirements on space-based GHG measurement precision, accuracy, resolution, coverage, and repeat frequency
Examples: GEO Carbon Strategy Report (Ciais et al. 2010)
CEOS Strategy for Carbon Measurements from Space
GCOS (4ppm, 10 km, 3-hour repeat cycle)
Many of these requirements were recorded before space based GHG measurements were providing useful constraints on the carbon cycle
Existing Space-based GHG Measurement Requirements

## Slide 26
The next generation of GHG satellite measurements needs to provide high accuracy measurements of CO2 and CH4 with high spatial resolution (1-2 km) to observe and attribute surface fluxes and, to minimize cloud contamination.
A daily repeat-frequency is required.
  Lower repeat cycles are valuable but clearly lose information on the variability of surface fluxes, whether natural or anthropogenic in origin.
Continuity of the time series of space-based planetary boundary layer CO2 and CH4 measurements, ideally in a GHG-satellite constellation.
  managed within the international system of operational meteorological satellites or by a dedicated organization.
A strategy for easy access to GHG satellite observations should be developed.
A coordinated planning effort towards the next generation of a constellation of GHG satellite observations is also required.
Requirements from GEO Carbon Strategy Report

## Slide 27
A coordinated constellation of passive and active XCO2 and XCH4 remote sensing instruments in Low Earth Orbit (LEO), with
  retrieved, single-sounding measurement accuracy of 0.1 to 0.2% for XCO2 and XCH4
  Spatial resolution of 1-2 km
  Temporal sampling yielding daily coverage of the entire globe.
A coordinated constellation of passive XCO2 and XCH4 remote sensing instruments in geostationary orbit (GEO)
  To cover all longitudes at a spatial resolution of 1-2 km
  Retrieved, single sounding measurement accuracy of 0.1 to 0.2% for XCO2 and XCH4 over continents
  Temporal sampling interval of 20 minutes to 1 hour.
These missions should be considered in the context of the added value to be derived from coordinated mission planning and associated data compilation activities (spaceborne and in situ/aircraft) both in the future and by exploiting archive data.
Requirements from CEOS Strategy for Carbon Observations from Space

## Slide 28
Can the the coverage, resolution, and precision requirements would be to fly a constellation that incorporates
3 (or more) satellites in low Earth orbit (LEO) with
  A broad (~200) km swath with a mean footprint size < 4 km2
  A single sounding random error near 0.5 ppm, and vanishing small regional scale bias (< 0.1 ppm) over > 80% of the sunlit hemisphere
  One (or more) satellites carrying ancillary sensors (CO, NO2, CO2 and/or CH4 Lidar)
A constellation with 3 (or more) geostationary satellites
  Monitor diurnally varying processes (e.g. rush hours, diurnal variations in the biosphere)
  Stationed over Europe/Africa, North/South America, and East Asia
A Candidate Constellation Architecture

## Slide 29
25-28 May: CEOS SIT, Paris, France
  Present a report on the GHG White Paper progress and plans
6-8 June: IWGGMS-13, Helsinki, Finland
  AC-VC participation in Organizing Committee and opportunities to enlist participation in GHG White Paper among space-based GHG measurement and modeling communities
11-16 June: GHG report to the CGMS-45, Jeju Korea
  Opportunity to solicit input on GHG White Paper from operational agencies
28-30 June: CEOS VC-AC, CNES HQ, Paris, France
  Breakout session to harmonize mission requirements (GEO, GCOS, CEOS)
  Finalize GHG White Paper outline and writing assignments
21-25 August, ICDC10, Interlaken, Switzerland
  First drafts of all chapters due
11-14 September, 2017 SIT Technical Workshop, Frascati, Italy
  Present a report on the GHG White Paper scope and contents
Milestones for GHG White Paper Development