## Slide 1
Use of ozone retrievals in the CAMS system and steps to include new datasets
Antje Inness (ECMWF)

## Slide 2: What the Copernicus Atmosphere Monitoring Service has to offer
The CAMS portfolio includes Earth Observation based information products about:
past, current and near-future (forecasts) global atmospheric composition;
the ozone layer;
air quality in Europe;
emissions and surface fluxes of key pollutants and greenhouse gases;
solar radiation;
climate radiative forcing.
Quarterly validation reports of global and regional outputs.
https://atmosphere.copernicus.eu

## Slide 3: Why is CAMS needed?
Example: NO2 tropospheric column from Copernicus Sentinel-5P (31/10/2018)
Observations are essential, but direct use is generally limited:
gaps in space and time
observed quantities may not be directly relevant (vertical column vs surface concentration)
can be complex and numerous
What CAMS does:
blend observations (satellite and non satellite) with model to provide a consistent 3D state
forecasts, a few days ahead
reanalyses over past years or decades

## Slide 4: Ozone data used in CAMS NRT system
CAMS uses Earth Observation data from many satellites for atmospheric composition and weather.
S5p
GOME-2C
TROPOMI
OMPS NPP
GOME-2B
GOME-2A
SBUV NOAA-19
OMI
MLS
2015 2016 2017 2018 2019 2020 2021
NRT O3 retrievals

## Slide 5: Ozone data used in the CAMS reanalysis
Limb profile data MLS and MIPAS
Reanalysis data set going back to 2003
GOME-2C
TROPOMI
OMPS NPP
GOME-2B
MIPAS
SCIAMACHY
GOME-2A
SBUV NOAA-19
SBUV NOAA-18
SBUV NOAA-17
SBUV NOAA-16
SBUV NOAA-14
OMI
MLS

## Slide 6: Preparation for new data
Sentinel-5
Sentinel-4, GEMS, TEMPO
From https://nesc.nier.go.kr/product/view
Example of GEMS TCO3
New experience to use geostationary data
Data volume/ resolution will be a challenge
Already some experience with super-obbing for S5P

## Slide 7: Observation data flow
EUMETCast
internet
GTS
Acquisition (ECPDS)
Ingestion & processing
(SAPP)
Analysis & forecast
(CCA/CCB)
Data storage (DHS)
Converter: Read S5P netcdf data and convert into BUFR
Include the S5P BUFR data into CAMS model
S5p monitoring statistics and feedback to retrieval teams
Converter can already be prepared with test data (important to have final data format)

## Slide 8: Examples of monitoring plots
Analyse observations and departures (obs-model)
Timeseries (area-mean and Hovmoeller plots)
Geographical plots
Scatter plots
Histograms

## Slide 9: Example 1: Maps of analysis departures
Feb-April 2018
Sep-Nov 2018
Shown are obs – analysis
Early S5P TCO3 NRT data in 2018
Looking at departures allowed CAMS to identify problems in the data related to the surface albedo climatology used in the NRT retrievals
The retrieval has since been improved
Inness et al., 2019, ACP https://doi.org/10.5194/acp-19-3939-2019
TROPOMI O3 analysis departures
[DU]
[DU]

## Slide 10: Example 2: Timeseries of departures
90-70N
Departures
Stdv(dep)
Obs, an, fg
Numbers
TROPOMI TCO3 Algorithm upgrade to V2.1.3 on 16 July 2020
Area averaged timeseries 1-28 July 2020
Monitoring of TROPOMI TCO3 data shows reduced bias at high northern latitudes after upgrade.
Benefit of assimilation system:
  Departures show differences that are not clearly visible in absolute values
  We can build up statistics quickly and globally

## Slide 11: Example 3: GOME-2 NO2 retrievals
Monitoring allows us to check consistency between retrievals from different instruments
Here: GOME-2C NO2 values are higher than GOME-2AB and give different departures
GOME-2C
GOME-2A
GOME-2B
Unit: 1015 molec/cm2

## Slide 12: CAMS routine monitoring page
https://atmosphere.copernicus.eu/charts/cams_monitoring/
Monitoring plots are
routinely displayed on the CAMS website
give us and the data producers timely information about any changes in the data

## Slide 13: The Atmosphere Data Store (ADS)
Based on CDS
https://atmosphere.copernicus.eu/data
All CAMS data are freely available
https://atmosphere.copernicus.eu