## Slide 1: Monitoring air quality from geostationary satellite: Perspectives from modeling and ground-based measurements to understand the AOD-PM2.5 relationship at sub-daily time scale
Mian Chin | NASA GSFC
Huisheng Bian | UMBC / NASA GSFC
Alex Coy | Cornell University (was at Montgomery Blair High School)
Qian Tan | BAER Inc. / NASA Ames
Tianle Yuan | UMBC / NASA GSFC
Xiaohua Pan | ADNET / NASA GSFC
Hongbin Yu | NASA GSFC
Zhining Tao | USRA / NASA GSFC
Dongchul Kim | USRA / NASA GSFC
Gao Chen | NASA LaRC
Acknowledgement: NASA Earth Science Program support, AERONET and surface PM2.5 network observations

## Slide 2: Collocated AOD and PM2.5 observations
Fresno:
AERONET AOD: Fresno_2
EPA PM2.5: Fresno
(0.1 km apart)
Houston:
AERONET AOD: U. Houston
EPA PM2.5: Harris County
(2.9 km apart)
GSFC:
AERONET AOD: GSFC
EPA PM2.5: PG County
(3.9 km apart)
Column AOD: AERONET, hourly mean during the day
Surface PM2.5: EPA sites over the US, China Enviornmental Monitoring Center over China,hourly mean day and night
Co-location criteria: AOD and PM2.5 sites < 4 km apart
Sites are chosen for at least having one-year AOD and PM2.5 observations available
Beijing:
AERONET AOD: CAMS
CEMC PM2.5: Guanyuan
(1 km apart)

## Slide 3
Fresno, 2013:
Total available days: 225
19% ( 42): R ≥ 0.7
19% ( 42): 0.5 ≤ R < 0.7
11% ( 26): 0.3 ≤ R < 0.5
20% ( 46): 0.0 ≤ R < 0.3
31% ( 69): R < 0.0
Fresno, CA, 2013
R (AOD-PM2.5)
GSFC, 2012:
Total available days: 207
16% ( 33): R ≥ 0.7
15% ( 32): 0.5 ≤ R < 0.7
13% ( 26): 0.3 ≤ R < 0.5
14% ( 30): 0.0 ≤ R < 0.3
42% ( 86): R < 0.0
GSFC, 2012
R (AOD-PM2.5)
Houston, 2012:
Total available days: 181
15% ( 27): R ≥ 0.7
7% ( 13): 0.5 ≤ R < 0.7
8% ( 14): 0.3 ≤ R < 0.5
21% ( 38): 0.0 ≤ R < 0.3
49% ( 89): R < 0.0
Houston, TX, 2012
R (AOD-PM2.5)
Beijing, AOD-PM2.5, 2015:
Total available days: 254
36% ( 92): R ≥ 0.7
14% ( 35): 0.5 ≤ R < 0.7
10% ( 25): 0.3 ≤ R < 0.5
15% ( 38): 0.0 ≤ R < 0.3
25% ( 64): R < 0.0
Beijing, China, 2015
R (AOD-PM2.5)
At the U.S. sites, AOD and PM2.5 are correlated with R ≥ 0.7 only in 15-20% days but are anticorrelated in 30-50% days.
In Beijing, 36% days they are correlated with R ≥ 0.7 and 25% days they are anticorrelated.
In Beijing, 36% days they are correlated with R ≥ 0.7 and 25% days they are anticorrelated.
Observations and model simulations show that column AOD and surface PM2.5 are poorly correlated on diurnal time scales, meaning that it is not feasible to directly use the geostationary satellite observed AOD for estimating surface PM2.5

## Slide 4: GEOS model simulation of AOD and PM2.5 at 3-hourly output also show poor correlations between them at diurnal time scale
Because the consistent processes determining the AOD and PM2.5 in the model, we examine the GEOS output for “good” and “bad” AOD-PM2.5 correlation days to explain their relationship
We use several variables from the GEOS model to perform multi-variable regression to estimate the 3-hourly PM2.5 concentrations from AOD and compare them with model simulated “true” values

## Slide 5: Examination of aerosol compositions, vertical profiles, and some meteorological fields to explain the AOD-PM2.5 relationship in two different days, one with R= -0.90 and one with R = +0.98, GEOS simulation
Aerosol compositions of PM2.5 and AOD are quite different
~30% of total AOD below 3 km with different temporal variation from aerosols aloft -> AOD variations are not in-sync with PM2.5
Aerosol compositions of PM2.5 and AOD are similar
55-80% of AOD below 3km -> both AOD and PM2.5 temporal variations are controlled by the aerosol below 3 km
OA
BC
NH4+
SO4=
NO3-
DU
SS
Total
05:30
08:30
11:30
14:30
17:30
20:30
22:30
02:30
05:30
08:30
11:30
14:30
17:30
20:30
23:30
02:30
1. GSFC, 2012-01-03 (RAOD-PM2.5= -0.90)
PM2.5 composition
AOD composition
Aerosol extinction vertical profile
PBL height
Surface layer RH
Column water vapor
(a)
(b)
(c)
(d)
(e)
(f)
2. GSFC, 2012-08-29 (RAOD-PM2.5= +0.98)
PM2.5 composition
AOD composition
Aerosol extinction vertical profile
PBL height
Surface layer RH
Column water vapor
(a)
(b)
(c)
(d)
(e)
(f)
+1
+1
+1
+1
+1
+1
+1
+1
+1
+1

## Slide 6: Select several “observable” variables from the GEOS model for multi-variable regression to estimate the 3-hourly PM2.5 concentrations from AOD and compare them to the “true” simulated PM2.5 values at different places with various aerosol regimes
Multivariable regression of 3-hour GEOS output for 2012: | Multivariable regression 3-hourly GEOS output for 2012:
1 | PM2.5 = f (AOD)
2 | PM2.5 = f (AOD, CWV)
3 | PM2.5 = f (AOD, CWV, AE)
4 | PM2.5 = f (AOD, CWV, AE, RHs)
5 | PM2.5 = f (AOD, CWV, AE, RHs , PBLH)
6 7 | PM2.5 = f (AOD, CWV, AE, RHs, PBLH, ALHe) PM2.5 = f (AOD, CWV, AE, RHs, PBLH, ALHe, MEEs)
Estimate accuracy increases
Observability decrease
Satellite
Ground weather station
Ground ceilo-meter
Satellite
Publicly available reanalysis
CWV = column water vapor; AE = Angstrom exponent; RHs = relative humidity at surface; PBLH = planetary boundary layer height; ALHe = effective aerosol layer height; MEEs = mass extinction efficiency at surface
AOD, CWV, and AE are available from AERONET and mostly available from satellite retrievals
Surface RHs can be obtained from local weather stations
PBLH can be obtained from ceilometer or lidar data, although limited
ALHe (or similar quantity) can be retrieved from satellite (e.g., O2-A or O2-B)
MEEs is rarely observed, but may obtained from publicly accessible reanalysis data
Note: estimated PM2.5 is from the multivariable linear fitting, although in reality the relationships are not linear

## Slide 7: Estimated PM2.5 from multi variable fitting vs. GEOS-calculated PM2.5 at US sites
DJF
MAM
JJA
SON
PM2.5 =
DJF
MAM
JJA
SON
DJF
MAM
JJA
SON
1 f(AOD)
2 f(AOD, CWV)
3 f(AOD, CWV, AE)
4 f(AOD, CWV, AE. RHs)
5 f(AOD, CWV, AE. RHs,
PBLH)
6 f(AOD, CWV, AE. RHs,
PBLH, ALHe)
7 f(AOD, CWV, AE. RHs,
PBLH, ALHe, MEEs)

## Slide 8: How does the multi-variable regression fitting work in different aerosol regimes in various places in the world? – It is generally robust spatially, temporally, although sensitivities to different variables vary
R
a
b
y = a + bx
USA, pollution
Europe, pollution
Mexico, pollution
India, pollution
China, pollution
Korea, pollution
Brazil, smoke
Zambia, smoke
Niger, dust
PM2.5 = f (1 AOD, 2 CWV, 3 AE, 4 RHs , 5 PBLH, 6 ALHe, 7 MEEs)

## Slide 9: Conclusions
Observations from collocated AOD and PM2.5 measurements shows that it is not feasible to directly convert geostationary satellite observed diurnal AOD to diurnal PM2.5
However, our modeling analysis suggests that it is possible to “retrieve” diurnal PM2.5 from GEO satellite diurnal AOD data with much improved accuracy if additional ancillary variables (observable) are included in the retrieval (e.g., via multi-variable regression fitting)
  Additional variables included in our analysis: CWV, AE, RHs, PBLH, ALHe, MEEs
Such method seems to be temporally and spatially robust across seasons and aerosol regimes, although sensitivity to different variables varies