## Slide 1: GEMS Status
CEOS AC-VC, College Park, MD, Oct 15-18, 2024
Jhoon Kim,
Yonsei Lee Youn Jae Fellow Professor of Atmospheric Science,
Yonsei University, Korea
M-H Ahn, R. Park, H. Lee, J. H Kim, Y.-S. Choi, S. S. Park, C. H. Song, K.-M. Lee, K. Han, C.-K. Song, U. Jeong, S.-W. Kim, Y. Jung,
M.S. Yoo, D. Lee, W.-J. Lee, J. Yoon, H. Hong, W. Choi, L. Chang, Y. Kim, K.-J. Moon;
D. H. Ko, S.-H. Lee; Y. Cho, H. Chong, S. Go, H. Cha,
Y. Chai, S. Lee, M. Kang, M. Eo, J. Bak, K. Baek, D.S. Choi; H.-A. Kwon, J. Yang, J. Park, K. M. Han, H. Choi, E. Lee, G. Kim, Y. Cha;
X. Liu, K. Chance, D. Jacob, B. Lefer, J. Al-Saadi, S. Kondragunta,
P.K. Bhartia, M. Newchurch,
J.P. Veefkind, B. Veihelmann, A. Richter, N. They, C. Zehner, R. Lutz, GEMS Science Team, and Cal/Val Team

## Slide 2: GEO Constellation of Air Quality Observation
(2020- )
(2023-)
(2025-)
Kim et al.(BAMS 2020)
+ ABI
+ AMI + GOCI-2
UVN
+ FCI
Background image:
10-year average NO2
column density
from OMI (2005-2014)
CEOS AC-VC (2019)

## Slide 3
GEMS – Air Quality Observation over Asia in High Spatio-temporal Resolution
SO2
NO2
CHOCHO
HONO
Clouds
(ECF, CCP)
NIER/KARI
GEMS
(2020-present)
Daily operation since Nov 2020
Ver.2 data release in Nov., 2022
Updated ver. data release in 2024
H2O
BrO
System Attributes | Requirements
Lifetime | >10 years
Field of Regard | N/S rng: 45N-5S E/W rng: 75E-145EOrbital pos.: 116.2E - 128.2E
Ground Sampling Distance | 3.5 km  7.7 km (N/S  E/W) at Seoul, Korea
Spectral range | 300 to 500 nm
Spectral Resolution | < 0.6 nm
Products | AOD, AEH, AI-UV & Vis, O3, NO2, SO2, HCHO, CHOCHO, Cld (CRF, ECP), Surface, UVI, BrO, H2O, HONO

## Slide 4: GEMS Data Products
Trop Ozone
Urban Emission
Ship Track Emission
Coal PP & Smelters
Dust & Wildfires
Wildfires
Volcanic Eruption
UV Aerosol Index
Aerosol Optical Depth

## Slide 5
Update to version 3 (some prod in v 2.1)
Prod | V2 Issue | Update details | TROPOMI V2 V3 Val | Remark
Trop O3 | Overestimation | Fitting window, Optimize L1 cal Data (Spectroscopy, Met, Solar Ref) |  | 
Total O3 | Underestimation | LUT Data (CLD) |  | v2.1
NO2 | Overestimation Profile shape Tropopause height | AMF S-T separation smoothing Data (AOD, O3T, CLD, BSR) |  | 
SO2 | Stripe (High conc) Noise (Low conc) | Slit Function (2x2 pixel binning) SO2 profile |  | v2.1
HCHO | average model conc Underestimation(West) | Variable background correction Data (BSR) |  | 
CHO CHO | average model conc | Background correction Data (BSR, CLD) |  | 
AOD | Underestimation ALH at 2km | Extend LUT, Background AOD, AI Min LER composite to 3 years |  | v2.1
CLD | ECF: Overestimation CCP: lower-layer | LUT, interpolation Clear sky CCP as sfc P, Data (SFC) |  | 
SFC | Underestimation <400nm Overestimation @380nm | Interpolation in rad & irr Option handling for IRR, Modification |  | 

## Slide 6
HCHO v3 [x1016]
Slope =0.52
R=0.60
TROPOMI HCHO VCD
[molec. cm-2]
TROPOMI SO2 VCD [DU]
GEMS v2.1 SO2 VCD
O3 v2.1
GEMS v2.1 O3 TCO
TROPOMI TCO [DU]
Slope=0.90
R=0.99
NO2 v3
TROPOMI NO2 VCD [x1016 molec. cm-2]
GEMS v3 NO2 VCD
2023/12
2023/06
Slope =1.06
R=0.90
Slope =1.56
R=0.92
GEMS v3 HCHO VCD
CHOCHO v3 [x1015]
GEMS v2.1 HCHO VCD
TROPOMI CHOCHO VCD
[molec. cm-2]
OMI SO2 VCD [DU]
OMPS SO2 VCD [DU]
SO2 v2.1
Slope =1.33
R=0.83
Slope =1.40
R=0.83
Gas Products Validation
Presentation by L. Chang; R. Lutz
Prod. Lead: Jae Kim
Prod. Lead: H. Lee
Prod. Lead: R. Park
Notes: CHOCHO) TROPOMI와 2023년 1년 전체 검증, R은 v2.0에 비해 감소(0.72->0.64), NMB는 증가(-9.48%->-1.82%)
O3) TROPOMI와 2023년 0445 UTC 데이터만 검증
NO2) TROPOMI와 2023년 12월과 6월 데이터 검증
HCHO) GEMS(varying background concentration). 2023년 3월 11:45 ~ 15:45 KST
SO2) 2022년 1월~ 12월 데이터 검증

## Slide 7
Aerosol, Cloud & SFC Validation
AOD v2.1
SSA v2.1
TROPOMI ECF
R=0.77 ~ 0.70
RMSE: 0.16 ~ 0.20
GEMS v3 ECF
TROPOMI DLER
GEMS Cloud v3
AERONET SSA [443nm]
GEMS SSA [443nm]
AERONET AOD [443nm]
GEMS AOD [443nm]
GEMS ALH
ALH v2.1
GEMS AEH v2.1
GEMS BSR v3
BSR 440nm
BSR 380nm
R=0.832
RMSE: 0.317
Presentation by L. Chang; R. Lutz
Notes: AOD) 2023년 1월 1일~ 2024년 5월 31일
SSA) 2023년 1월 1일 ~ 2024년 5월 31일
AEH) 2023년 1년 데이터를 통해 TROPOMI ALH와 비교 검증시, v2.1에서 더욱 정규분포에 가까운 모습을 보임
BSR) 23년 3, 6, 9, 12월 자료 유효운량의 과소산출 440nm과 380 nm에서 검증
ECF) GEMS v2와 TROPOMI 검증 결과에서 크게 개선되지 않음, 다만 23년 3, 6, 9, 12월 자료를 사용하면서 v3에서는 유효운량의 과소산출을 확인할 수 있고 ECF<0.2인 경우 그 정도가 더 큼

## Slide 8: GEMS Total NO2 V2.0 and V3.1 vs. TROPOMI
December 1-15,
2023
June 1-15,
2023
GEMS (V3.1)
GEMS (V2.0)
TROPOMI
Total NO2 VCD [1016 molec/cm2]
GEMS
(04:45)
Difference [%]
(V2.0-TROPOMI)
Difference [%]
(V3.1-TROPOMI)
Difference (GEMS-TROPOMI) of Total NO2
[1015 molec/cm2]
Prod. Lead: Hanlim Lee / Y. Jung

## Slide 9: GEMS NO2 V2.0 and V3.1 vs. TROPOMI
Filtering criteria :
SZA<70º, VZA<70º, CF<0.3
GEMS Total NO2 VCD [1016 molec/cm2]
Slope (R) | 2023/03 |  | 2023/06 |  | 2023/09 |  | 2023/12 | 
 | V2.0 | V3.1 | V2.0 | V3.1 | V2.0 | V3.1 | V2.0 | V3.1
Total NO2 | 1.58 (0.93) | 0.89 (0.92) | 1.30 (0.90) | 0.78 (0.88) | 1.58 (0.88) | 0.87 (0.88) | 1.88 (0.93) | 1.10 (0.94)
TROPOMI Total NO2 VCD [1016 molec/cm2]
V3.1
V2.0
V3.1
V2.0
Jun
1-15,
2023
Dec
1-15,
2023
N=2626629
Y=1.30-0.17
R=0.90
RMSE=0.14
N=2716762
Y=0.78+0.01
R=0.88
RMSE=0.13
N=22788818
Y=1.88+1.27
R=0.93
RMSE=0.51
N=2518470
Y=1.10X-0.08
R=0.94
RMSE=0.18
V3.1
V2.0
Tropospheric NO2
(Dec 1-15, 2023)
GEMS Tropo NO2 VCD[1016 molec/cm2]
V3.1
V2.0
Stratospheric NO2
(Dec 1-15, 2023)
N=2652771
Y=0.22X+0.01
R=0.79
RMSE=0.15
N=2715898
Y=2.01-0.23
R=0.80
RMSE=0.05
N=2166546
Y=1.44X+0.09
R=0.90
RMSE=0.43
N=2655970
Y=0.91X+0.02
R=0.91
RMSE=0.18
Slope (R) | 2023/03 |  | 2023/06 |  | 2023/09 |  | 2023/12 | 
 | V2.0 | V3.1 | V2.0 | V3.1 | V2.0 | V3.1 | V2.0 | V3.1
Tropo- sphere | 1.25 (0.87) | 0.70 (0.89) | 1.16 (0.79) | 0.42 (0.71) | 1.37 (0.78) | 0.47 (0.64) | 1.44 (0.90) | 0.91 (0.91)
Strato- sphere | 0.22 (0.88) | 1.49 (0.89) | 0.27 (0.94) | 1.42 (0.95) | 0.24 (0.89) | 1.63 (0.92) | 0.22 (0.79) | 2.01 (0.80)
TROPOMI Tropo NO2 VCD [1016 molec/cm2]
Updated fitting
S/T separation
GEMS prod use
Prod. Lead: Hanlim Lee / Y. Jung

## Slide 10
Aerosol – post-processing
V2.1
[Cho et al., AMT, 2024]
Post-processing
AOD
SSA
ALH
V2.1
Post-processing
GEMS-AERONET
ML
GEMS AOD, SSA
VZA,
Z,
UVAI,
RAA,
SZA…
Corrected
GEMS

## Slide 11
GEMS
TROPOMI
TCWV [kg m-2]
TCWV [kg m-2]
New products of GEMS
H2O
Nishinoshima
Fukutoku-Okanoba
Taal
BrO
HONO
TROPOMI
GEMS

## Slide 12
 | Stripe issue | Overestimation/Underestimation | Note
O3 Total | X | - | The negative bias has shifted to a positive bias Absolute value of the bias has decreased
O3 Profile | O | overestimation | Stripe issue in the 10-30° N If the irradiance offset is not applied, it results in an overestimation of tropospheric O3
SO2 | O | - | The stripe issue has increased in the ranges of 15-30° N and around 0° N
NO2 | O | - | The stripe issue still exists NO2 VCDs have decreased over high NO2 areas
HCHO | X | - | Increase in HCHO VCDs of over 8% in Jan and Fab is expected to improve the underestimated winter values Decrease in HCHO VCDs in the south and increase in the north
CHOCHO | O | overestimation | Stripe issue Increase in winter, where there was an issue of CHOCHO overestimation
AOD | X | bias | Overestimation of AOD due to a degradation issue
AEH | X | - | Overestimation of AEH has decreased AEH output range is more stable
SFC | X | - | The stripe issue that occurred when using KNMI has been reduced The low BSR calculated with KNMI has stabilized to reliable values when using BTDF IRR
CLD | O | - | Stripe issue does not occur with ECF, but occurs with CCP Stripe issue in CCP mainly occurs in the lower layers and appears regardless of latitude
After applying BTDF-corrected Irradiance
Notes: GEMS irr 사용보다 BTDF-corrected IRR을 사용했을 때 더 좋은 결과를 보이는 산출물에
연두색 표시를 했습니다.

## Slide 13
NO2
SO2
HCHO
CHOCHO
O3
HONO
aerosols
hv
H2O
BrO
Diurnal variations - Temporal
Validations
Long-term trends for AM, noon, & PM
2.0
0.0
[1016 molecules/cm2]
3.0
08:45 (LT)
09:45 (LT)
10:45 (LT)
11:45 (LT)
12:45 (LT)
13:45 (LT)
14:45 (LT)
07:45 (LT)
15:45 (LT)
Seoul
Diurnal variations – Conc & Spatial
Urban
Industry
Rural
in successful operation
since 2020
Fire
Air Quality
Summary
Park et al.(submitted)

## Slide 14
Acknowledgements
Thank you
for all your contribution,
dedication,
and
support !

## Slide 15: Plan of GK series for Atmospheric Composition
Environmental |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
AQ |  |  |  |  |  |  |  |  |  |  | GEMS (UV-VIS 1000 ch, 3.5x 7.7 km, 1 hr) |  |  |  |  |  |  |  |  |  |  | GEMS 2 (UV-NIR 2000 ch, 4.5 x 4.97 km, 1 hr) |  |  |  |  |  |  |  |  | 
GHG |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | GHG(L, x5) 1.6 um FPI |  |  |  |  |  |  |  |  |  |  |  |  | 
Meteorological |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Imag | MI (5 ch, 1/4 km, 1hr) |  |  |  |  |  |  |  |  | AMI (16 ch, 0.5/2 km, 10 min) |  |  |  |  |  |  |  |  |  |  |  | AMI 2 (18 ch, 0.25/1 km, 2 min) |  |  |  |  |  |  |  |  | 
IRS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | IR Sounder |  |  |  |  |  | 
Oceanic |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
OC | GOCI (412 – 865 nm, 8 ch, 500 m, 1 hr) |  |  |  |  |  | GOCI 2 (380 – 865 nm, 13 ch, 250 m, 1 hr) |  |  |  |  |  |  |  |  |  |  | GOCI 3 (380 – 1030 nm, 16 ch, <250 m, < 1 hr) |  |  |  |  |  |  |  |  | 
 | ‘10 |  |  |  | ‘15 |  |  |  | ‘20 |  |  |  | ‘25 |  |  |  | ‘30 |  |  |  | ‘35 |  |  | ‘40