## Slide 1
Tropospheric Emissions:
Monitoring of Pollution
TEMPO: Overview and Status
Caroline Nowlan
Center for Astrophysics | Harvard & Smithsonian
Xiong Liu, Kelly Chance, Gonzalo González Abad, Chris Chan Miller, Heesung Chong, John Davis, Jean Fitzmaurice, Weizhen Hou, John Houck, Raid Suleiman, Junsung Park, Huiqun Wang, Aaron Naeger, James Carr, Barron Henderson, Luke Valin, James Szykman, Jerry Ziemke and the TEMPO Team
CEOS AC-VC Meeting
October 15, 2024

## Slide 2: Tropospheric Emissions: Monitoring of Pollution
Hourly daytime air pollution measurements over North America
NASA’s first Earth Venture Instrument (EVI), selected in 2012
Led by Smithsonian Astrophysical Observatory (SAO) in partnership with NASA LaRC
Geostationary orbit
→ High temporal resolution
→ High spatial resolution
Baseline data products:
  NO2, HCHO, O3 (total and profile)
Credit: NASA’s Scientific Visualization Studio

## Slide 3: TEMPO Timeline
Date | Details
7 April 2023 | Launch
June-July 2023 | TEMPO power on + dry-out, cool down, etc.
2 August 2023 | First light
19 October 2023 | Nominal operations
June 2025 | Baseline mission ends
September 2026 | First extended mission ends
Public Release | Date | Details
V01 | February 2024 | Limited 3 weeks released
V02 | February 2024 | Level 1 (spectra) released
V03 | May 2024 | L1 updated, Level 2/3 NO2, HCHO, total O3
V04 | June 2025 | Release ozone profile, update L1 + trace gases

## Slide 4: TEMPO Products
4
Level | Product | Developer
L1 | Irradiance NRT | SAO
 | Radiance NRT | SAO
 | Radiance (twilight – city lights) | SAO
L2 | Clouds NRT | SAO
 | NO2 NRT | SAO
 | HCHO NRT | SAO
 | O3 (total) | SAO
 | O3 (profile) | SAO
 | TEMPO/GOES-R synergy aerosol product NRT | NOAA
 | C2H2O2 | SAO
 | H2O | SAO
 | BrO | SAO
 | SO2 NRT | NASA GSFC
 | UVAOD | NASA GSFC
 | Aerosol layer height | U. Iowa
 | UVB | SAO/NASA GSFC
NRT Products
Satellite Needs Working Group Cycle 3
Enhanced Products
Satellite Needs Working Group Cycle 4
Research Products
  Ocean color
  Vegetation
  SIF
  City lights/lighting types
  HNO2
  IO
  NO3
  Surface albedo
  Surface concentrations
  Emissions
Baseline Products

## Slide 5: Using TEMPO Data
TEMPO data is publicly available through NASA’s Atmospheric Science Data Center
V3 download metrics (May-Sept 2024)
  782 TB
  48M files
  1M+ image requests (Worldview etc.)
NASA Webinar recording for new users: https://youtu.be/meySKqVuVT0?si=uiLTRXsgtKIGS_OT

## Slide 6: Trace Gas Validation
HCHO
NO2
[Credit: Barron Henderson, Luke Valin, Jim Szykman]
* TROPOMI comparisons are for Pandora locations + ozone non-attainment areas
Pandora
Pandora
TROPOMI
TROPOMI

## Slide 7: NO2 and Hurricane Helene
Before Helene
After Helene
[Credit: Aaron Naeger]
Decreases seen in NO2 in Savannah (GA), Jacksonville (FL), Raleigh-Durham (NC)

## Slide 8: July 2024 Formaldehyde
08 -12 UTC
12 -16 UTC
18 -20 UTC
20 -24 UTC
[Credit: Gonzalo González Abad]
Notes: Update with real Worldview data

## Slide 9: Total Ozone Validation
[Credit: Jerry Ziemke]

## Slide 10: Summary and Outlook
TEMPO operations are nominal
NO2, HCHO, total O3 publicly available
Expect validation report soon and trace gas upgrade from “beta” to “provisional” status
Priorities for V04:
  Radiances  improve absolute calibration, include polarization correction
  NO2, HCHO, cloud  improve surface albedo, cloud fraction bias, HCHO background correction, NO2 de-striping
  Total O3  latitude-dependent bias
  Continued development and release of O3 profile product
Near real-time products expected middle of 2025
Many more TEMPO products to come!
Acknowledgements: Funding from NASA (TEMPO, NNL13AA09C; SNWG TEMPO NRT, 80MSFC24CA004)