## Slide 1: Validation and support of space-based measurements with the Pandonia Global Network of ground-based spectrometers Thomas Hanisco1, Nader Abuhassan1,2,3, Stefano Casadio4, Alexander Cede1,3,5, Limseok Chang6, Angelika Dehn4, Barry Lefer7, Elena Lind1,Apoorva Pandey1,2, Bryan Place1,3, Alberto Redondas8, James Szykman9, Martin Tiefengraber5, Luke Valin9, Michel van Roozendael10, and Jonas von Bismarck4 1NASA Goddard Space Flight Center, Greenbelt, Maryland, USA 2University of Maryland Baltimore County, Maryland, USA 3SciGlob, Columbia, MD, USA 4Earth Observation Ground Segment Department, ESA / ESRIN, Frascati, Italy 5LuftBlick, Innsbruck, Austria 6National Institute of Environmental Research, Incheon, Korea 7NASA Headquarters, Washington, DC, USA 8AEMET- Meteorological State Agency, Spain 9EPA Research Triangle Park, Charllotte, NC, USA 10BIRA-IASB, Brussels, Belgium
15-October, 2024
CEOS AC-VC meeting

## Slide 2: Pandonia Global Network: Reference measurements of O3, NO2, and HCHO
Calibration and Quality Assurance:
  Laboratory and Field calibration of instruments
Network operation
  Remote monitoring and repair of instruments
Retrieval
  Production of O3, NO2 and HCHO Columns/Profiles
The PGN operates 175+ Pandora instruments
https://www.pandonia-global-network.org/
Thomas.Hanisco@nasa.gov, alexander.cede@luftblick.at

## Slide 3: Instrumentation
Pandora is a ground-based sun/sky/moon viewing spectrometer system
The sensor head (light collector) is mounted on a 2-axis tracker.
Sun/sky/moon-light is directed to the input of a ccd spectrometer with a fiber optic cable.
Control electronics for semi-autonomous operation in all-weather conditions
Pixels (wavelength) and Counts (intensity) are used to derive trace gas abundance
Dual-axis
tracker
Head
Sensor
Electronics
Enclosure
Fiber Optic Cable

## Slide 4: Pandora measurements
Direct sun: mostly BEER’s Law.
Total absorption used to derive the column abundance between the instrument and the top of atmosphere
MAX-DOAS: multiple angle BEER’s Law
Differential measurements used to derive the abundance at multiple elevations

## Slide 5: Motivation
NASA Satellites measure sunlight reflected from the earth’s surface and scattered from the atmosphere. This is complicated and requires assumptions (a priori) that are not always correct. Even harder with Geostationary!
Pandora provides direct sun with lower sensitivity to scattered light.
MAX-DOAS profiles can be used to validate the a priori assumptions.

## Slide 6
Pandonia Global Network
            175 Official instruments
            Unofficial
            Adding 30/year
TEMPO
SENTINEL-4
GEMS
Notes: Buenos Aires and Rivadiva, Antarctica Trollhausen, Ann Marie Fjaera NILU

## Slide 7
Notes: Added Actris not up to date

## Slide 8
8
8
8
PGN Real Time Data: BlickV http://blickv.pandonia-global-network.org/
All products are available for download on BlickV.
Quality assured total column NO2 and O3 are archived at the EVDC.
“Out of the Box” MAX-DOAS products provided without a field calibration.
Stan State - 248

## Slide 9: Data quality
Direct sun NO2 and O3 are “validation quality”. These products have been validated with airborne (DISCOVER-AQ), balloon (O3 sonde), and ground remote (Brewers). High quality data is on the EVDC.
Profiles (MAX-DOAS) of NO2 and HCHO and direct sun HCHO are not fully understood.
NO2
HCHO

## Slide 10: Validation of MAX-DOAS products: NO2
Bryan Place NASA/SciGlob
Airborne, balloon and ground-based in situ comparisons to MAX-DOAS NO2.
Measurements of NO2 columns are robust but our understanding of the spatial distribution needs improvement.

## Slide 11: Validation of MAX-DOAS products: HCHO
Apoorva Pandey, Poster 49
Altitude (m)
HCHO partial column (mol/m2)
NASA (SARP) and EPA (ALEGROS) airborne in situ profiles over Pandora sites in 2024. More flights planned for 2025.
MAX-DOAS Consistently agrees well with the in situ

## Slide 12: Expansion programs
Leverage other agencies and objectives
  For example, the United Nations UNESCO funded 23 instruments to be managed by KOICA and NIER in southeast ASIA.
EPA 25+ instruments
NASA IPMSI – 13 instruments
NASA Satellite needs Working Group (SNWG) - Hard to reach rural and developing nation sites
  10 US department of Agriculture rural sites
  10 US State Department embassy locations
NOAA starting investment with interest for GEO-XO.
  Installed at Essex, Maryland MDE site in June 2024
Notes: Shobha Kondragunta at NOAA Bojan Bokov at Eumetsat

## Slide 13: Increasing Participation in Minority Serving Institutions (IPMSI)
Pandoras added in 2023-2024 at 13 institutions
Expand in areas with limited measurement resources
Create a cohort of motivated PI’s with 5 years funding
90+ instruments in the TEMPO FOV

## Slide 14: Colocated Pandora and Cimels
Tuba City, AZ
Whittier, CA
New Orleans, LA
Chesapeake Bay Bridge
Chicago, IL
Langley, VA

## Slide 15: SNWG: Produce localized NO2 forecasts by combining PANDORA observations with GEOS model output
Pandora observations
GEOS-CF model output + machine learning
Adapt ML method developed for surface observations (Christoph Keller et al., ACP 2021)
Method is limited to locations with at least 1 year of historical data
PGN +
GEOS_CF trop columns -> Surface concentration
PI Emma Knowland, GMAO

## Slide 16: Instrumentation & Technology
Delrin -> Nylon in sensor head. Complete
Upgraded tracker. Complete
  Still working on trackers with brakes
Upgraded sensor head cables on all new instruments/repairs.
New optical diffusers in all new instruments/repairs.
Dehumidifier in spectrometer box
  Humidity is still #1 failure mode
  All new NASA instruments have the dehumidifier
Custom spectrometer development through NASA SBIR
  Low stray light
  Temperature controlled detector
  Fiber adapter
New PAN-C all in one in GSFC lab for calibration
Electrolytic membrane dehumidifier
SciGlob NASA SBIR Ph-II Spectrometer prototype

## Slide 17
THANKS!
Pan-C NASA SBIR
Optical NO2 Sonde
(HCHO and O3 in development)
20 x 25 x 4 cm, 1 kg, 6W
100 ppt/s
Bailey et al., AMT, https://doi.org/10.5194/amt-17-5903-2024