## Slide 1
AC-VC#20 meeting, Maryland, USA (15 Oct 2024)
Antje Inness (ECMWF)
Uptake of satellite data in the CAMS system

## Slide 2: CAMS Information Flow
Earth Observation from satellite (>75 instruments) and in-situ (regulatory and research)
CAMS main operational data assimilation and modelling systems
CAMS users
Applications
Policy products
IFS 40km (oper) / 80km (rean) Globe
11-member ensemble
10km Europe
Two global 5-day forecasts daily
atmosphere.copernicus.eu

## Slide 3: Satellite data and types used in NRT by CAMS
 | O3 |  |  |  |  | CO |  |  | NO2 |  | SO2 |  | AOD |  |  |  | CH4 |  |  | CO2 |  | 
Satellite | AURA |  | Metop BC | S-NPP & NOAA 20 | Sentinel 5p | Metop BC | TERRA | Sentinel 5p | Metop BC | Sentinel 5p | Metop BC | Sentinel 5p | AQUA & TERRA | Metop BC | S-NPP & NOAA-20 | Sentinel-3 | GOSAT | Metop BC | Sentinel 5p | GOSAT | Metop BC | OCO-2
Instrument | MLS | OMI | GOME-2 | OMPS | TropOMI | IASI | MOPITT | TropOMI | GOME-2 | TropOMI | GOME-2 | TropOMI | MODIS | PMAP | VIIRS | SLSTR | TANSO | IASI | TropOMI | TANSO | IASI | OCO-2
Type | Strat Profiles | Total Columns | Total Columns | Layers | Total Columns | Total Columns | Total Columns | Total Columns | Tropospheric Columns | Tropospheric Columns | Total Columns | Ttotal Columns | AOD | AOD | AOD | AOD | Total Columns | Total Columns | Total Columns | Total Columns | Total Columns | Total columns

## Slide 4: Observation data flow at ECMWF
EUMETCast
internet
GTS
Acquisition (ECPDS)
Ingestion & processing
(SAPP)
Analysis & forecast
(Atos supercomputer)
Data storage (DHS)
Notes: SAPP: scalable acquisition and pre-processing system

## Slide 5: Observation data flow
EUMETCast
internet
GTS
Acquisition (ECPDS)
Ingestion & processing
(SAPP)
Analysis & forecast
(CCA/CCB)
Data storage (DHS)
Converter: Read S4 data and convert into BUFR
Include the S4 BUFR data into CAMS model
S4 monitoring statistics and feedback to retrieval teams
For this to be implemented we need
useful test data
ATBD/ User Guide etc

## Slide 6: CAMS analysis window and cut-off times
Observation cut-off
00Z analysis window
15
03
00
Time
(UTC hours)
07
1st minimisation
2nd minimisation
Observation cut-off
12Z analysis window
03
15
12
Time
(UTC hours)
19
1st minimisation
2nd minimisation
CAMS runs two 12-hour assimilation windows, with observation cut-off times at 07 UTC and 19 UTC (4 hours)
Timely data provision important for NRT use

## Slide 7: Timeliness of data (Example Tropomi O3)
00Z analysis window
15
03
00
Time
(UTC hours)
07
Observation cut-off
12Z analysis window
03
15
12
Time
(UTC hours)
19
Observation cut-off
Timeliness of observations is important
Observations received within 4 hours of sensing time are guaranteed to be included in the 12-hour analysis window
Arrival time – sensing time
2.5 hours

## Slide 8: Monitoring of data wiht the CAMS DA system
CAMS DA system is a powerful tool to monitor the quality of data
  Looking at departures (e.g. obs – model) can highlight problems
  Global statistics are built up quickly
  CAMS system as reference frame to compare data from different instruments
New data are monitored passively first
  Departures are calculated but data do not influence analysis
  => information about quality of data and potential issues before using the data
  => feedback to producers (e.g. ESA, Eumetsat,…) on the data quality
Assimilation tests follow if the data are of good quality
Can help Cal/Val activities of future missions (e.g. Sentinel-4, Sentinel-5, Altius,…)
observation
Model equivalent of observation (observation operator applied to model data)

## Slide 9: Examples of monitoring plots
Evaluate observations and departures (obs-model)
Timeseries (area-mean and Hovmoeller plots)
Geographical plots
Scatter plots
Histograms
Timeseries
Histograms
Maps
Scatter plots
Hovmoeller plots

## Slide 10: Maps of analysis departures: TROPOMI O3
Feb-April 2018
Sep-Nov 2018
Shown are obs – analysis TCO3
Early S5P TCO3 NRT data in 2018
Looking at departures allowed CAMS to identify problems in the data related to the surface albedo climatology used in the NRT retrievals
The retrieval has since been improved
Inness et al., 2019, ACP https://doi.org/10.5194/acp-19-3939-2019
TROPOMI TCO3 analysis departures:
dep = obs - analysis
[DU]
[DU]

## Slide 11: Timeseries of TROPOMI O3 departures
90-70N
Departures
Stdv(dep)
Obs, an, fg
Numbers
TROPOMI TCO3 Algorithm upgrade to V2.1.3 on 16 July 2020
Area averaged timeseries 1-28 July 2020
Monitoring of TROPOMI TCO3 data shows reduced bias at high northern latitudes after upgrade.
Benefit of assimilation system:
  Departures show differences that are not clearly visible in absolute values
  We can build up statistics quickly and globally

## Slide 12: Scatterplots: TROPOMI COBRA SO2 data
Andep vs Lat
Andep vs CC
Andep vs CTP
Andep vs SOE
Obs vs SOE
No noticeable issues related to cloud cover and cloud top pressure
Larger andep and obs at low SOE and swath edges
Use only data with SOE>30 and rows 26-424: in line with Theys et al. (2021) plots
Andep vs scanPos

## Slide 13: Area averaged timeseries: IASI CO
Looking at departures helps us to assess impact of newly assimilated data
IASI TCCO departures are reduced if TROPOMI CO data are assimilated too
Good agreement between IASI-B and IASI-C
Time
Without TROPOMI
With TROPOMI

## Slide 14: Timeseries: GOME-2 NO2 retrievals
Monitoring allows us to check consistency between retrievals from different instruments
Here: GOME-2C NO2 values are higher than GOME-2AB and give different departures
This is more visible in the plot of departures than in the absolute obs values
Unit: 1015 molec/cm2
GOME-2B and GOME-2C
GOME-2A and GOME-2C
Departures
Obs, an, fg

## Slide 15: CAMS can help in CAL/VAL activities
Retrieval teams
L1b data
L2 data
CAMS analysis and monitoring tools
Statistics and plots
Feedback
Good data
Assimilation tests
NRT assimilation
CAMS analyses and forecasts
Downstream services and users

## Slide 16: CAMS satellite monitoring page
https://atmosphere.copernicus.eu/charts/packages/cams_monitoring/
Monitoring plots are
routinely displayed on the CAMS website
give us and the data producers timely information about any changes in the data

## Slide 17: Recommendations
What works well | What does not work well
Easy-to-use quality flag e.g. TROPOMI qa-flags are great | Complicated qa-instructions or bad observations that are not flagged properly. e.g. reprocessed IASI CO data are very difficult to handle
Good documentation: PUM, ATDB, validation reports | No or bad documentation
Information about obs errors, averaging kernels, a-priori | No information
All information in one file | E.g. IASI CO/ SO2 data require input from CO/SO2 files and L2 files
Netcdf, HDF5, BUFR format. Preferable to have many small files, rather than huge daily files. Consistent variable formats, missing values definitions. | BUFR format that does not contain all the information we need and was finalised years in advance
Data access: can use sftp, http, S3. Files grouped by days make acquisition easier | Random file/directory names
Consistent reprocessed datasets for use in reanalysis (e.g. NO2 from several instruments) | Inconsistencies between retrievals from different instruments
Plan for NRT data delivery | No NRT data delivery planned
Early pre-launch test data Data available asap after launch, e.g. during commissioning phase | No pre-launch test data No access to early data after launch
Notes: if they use netcdf, the variables should be consistent, if the variable is float the max min etc and other attributes should have to proper type to avoid

## Slide 18: Summary
The CAMS data assimilation system is a powerful tool to provide feedback on data quality
New data are monitored first and only assimilated once quality is established
Departures (obs – model) provide useful information about data quality
Valuable feedback to data providers
Early provision of test data and ATBD/PUM important to allow CAMS to be ready for new data
Timely delivery of data important for NRT use (<3-4 hours)
Monitoring plots available on CAMS website:
  https://atmosphere.copernicus.eu/charts/packages/cams_monitoring/

## Slide 19: The Atmosphere Data Store (ADS)
All CAMS data are freely available: https://ads.atmosphere.copernicus.eu/
Documentation of atmospheric composition in IFS:
https://www.ecmwf.int/en/elibrary/81374-ifs-documentation-cy48r1-part-viii-atmospheric-composition
Validation reports from:
https://atmosphere.copernicus.eu/quality-assurance
Copernicus EU
www.copernicus.eu
atmosphere.copernicus.eu
Copernicus EU
Copernicus ECMWF
@copernicusecmwf
Copernicus ECMWF
@CopernicusEU
@CopernicusECMWF