## Slide 1: Multi-model multi-constituent chemical (MOMO-Chem) data assimilation for city-to-global scale atmospheric composition and emission analysis
Copyright 2024, California Institute of Technology. Government sponsorship acknowledged.
Kazuyuki Miyazaki
NASA Jet Propulsion Laboratory, California Institute of Technology , USA
Kevin Bowman (JPL), Longtao Wu (JPL), Takashi Sekiya (JAMSTEC), Dylan Jones (Univ. Toronto), Helen Worden (NCAR), Henk Eskes (KNMI), Pieter Rijsdijk (KNMI), Mukesh Rai (JPL), Vivienne Payne (JPL), Nathaniel Livesey (JPL), Emanuele Emili (BSC), Antje Inness (ECMWF), Zhen Qu (NCSU), Brad Pierce (Univ. of Wisconsin-Madison), William Chen (NCAR), Vincent Huijnen (KNMI), Gerbrand Koren (Utrecht Univ.), Rajesh Kumar (NCAR), Pablo Saide (UCLA)

## Slide 2
Oxidation capacity (OH)
↓
CH4
Long-lived GHGs
AQ-GHG co-emissions
↓
CO2
MOMO-Chem Tropospheric Chemistry Reanalysis (TCR-3)
Miyazaki et al.,
In prep.
(updated from Miyazaki et al., 2020)

## Slide 3: MOMO-Chem contribute to NASA’s current and future missions
Broad communities
Top-down emissions (NOx,CO,SO2,Isopren)
Attribution
TROPESS new
satellite products
High-resolution DA
GEO+LEO AQ integration
AQ-GHG synergy
Earth Science to Action
New generation
chemical reanalysis
Aircraft campaigns (ASIA-AQ)
Support policy decisions
Health & Climate impacts
9 papers using MOMO-Chem and TROPESS data in TOAR-2
Satellite assessment paper lead
- IGAC GEIA, AMIGO, TOAR-2
- ISSI GEO AQ
NASA chemDA
CEOS-AC-VC
WMO observing system impact
OSSEs mission formation
GEMS, TEMPO
Explore class missions
CMS-flux, GOSAT-GW,
OCO-2/3, CO2M
We do science!
(not operational or engineering)

## Slide 4: Chemical reanalysis Focus Working Group
Co-leads: Kazuyuki Miyazaki, Dylan Jones, Helen Worden
Evaluate current chemical reanalysis products to assess their potential (Jones et al.).
Assesses the relative importance of individual observations (e.g., ozone vs precursor) to improve ozone analyses and help to design observing systems (Sekiya et al.)
Evaluate representativeness of FT ground-based ozone measurements (Miyazaki et al.).
Human health impact assessment (Wang et al)
ML downscaling and bias correction (Miyazaki et al)
Co-leads: Daan Hubert, Kazuyuki Miyazaki
Satellite ozone assessment paper
Provide present day maps, long-term changes, and attributions of tropospheric ozone
Evaluate agreements between satellite records and harmonized data products.
APARC Reanalysis Intercomparison (A-RIP)

## Slide 5
Reanalysis | Area | Resolution | Scheme
CAMS (A. Inness) | GLOBAL | T255 | 4D-Var
GEOS-CHEM (Z. Qu) | GLOBAL | 2°x2.5° | 4D-Var
TCR2 (K. Miyazaki) | GLOBAL | 1.125°x1.125° | EnKF
CAQRA (X. Tang) | CHINA | 15 km x 15 km | EnKF
CMAQ-GSI (R.Kumar) | US, Asia | 12 km x 12 km | 3D-Var
500 hPa ozone
U.S.
India
Toward further development of chemical reanalysis and observing systems
CAMS
TCR-2
GEOS-Chem
Jones et al. (in prep)
Chemical reanalysis intercomparisons

## Slide 6
2005-2018 surface ozone linear trends
Jones et al. (in prep)
Further improvements in DA settings, temporal consistency, enhanced constrains on surface pollutants

## Slide 7: Representative errors of ground-based observations
Occur when the atmospheric state is not uniformly and frequently sampled and lead to spurious signals in trend analysis. In regions where variability is dominated by short-term and/or small-scale variations, limited sampling may lead to a large random sampling error.
What are the spatial & temporal representative scales of
individual ground-based stations and networks?
TOC temporal correlations between individual stations and remote locations using chemical reanalysis
Miyazaki et al. (in prep)

## Slide 8
Toward effective observing system design to better capture regional-global scale ozone variations
Miyazaki et al. (in prep)

## Slide 9: Global anthropogenic emissions over 19 years
Top-down NOx (TgN/yr)
MOMO-Chem
Bottom-up CO2 (GtC/yr)
Le Quéré (2020)
Europe & USA ↓
China ↑
China ↓
India ↑
COVID
Recovery & India ↑
Updated from Laughner et al 2021 (PNAS)
and Miyazaki et al. 2021 (Sci Adv)
NOx emissions
2023 - 2019
Higher, India, W China, SE USA
Lower: Europe, NE China

## Slide 10
Hunga Tonga–Hunga
Australian fires
Canadian fires
?
?
Zonal mean O3
at 500 hPa
from MOMO-Chem
Anomaly from 2019
2020: The tropospheric ozone burden declined by 6TgO3 (∼2%)
2021-early2023: Continued low ozone in NH?
COVID
Updated from Miyazaki et al. 2021 (Sci Adv)

## Slide 11: Global high-resolution DA in MOMO-Chem
TCR-2 (1.1°)
GCHP (0.25°)
Surface ozone
Effective DA of high-resolution obs (GEO, in situ + LEO)
Evaluation of DA uncertainty due to model errors
City-to-global scale seamless analysis
GCHP (0.25°)
TEMPO
TCR-2 (1.1°)
Tropospheric NO2 column over LA
Local time (Hour)
GCHP
TEMPO
TCR-2
0
5
10
15
20
GEO+LEO will enable seamless local to global scale analysis and improve diurnal emissions while improving background chemical conditions and long-range transport

## Slide 12
OmF
Spread of NOx scale factor
GCHP-EnKF TROPOMI data assimilation

## Slide 13: Trace gas and AOD simultaneous DA
Sekiya et al. (2023 & in prep)
Primary aerosols
SO2,NO2,(NH3)
AOD
Precursor emissions
Trace gases and AOD observations provide independent information on the relative changes in directly primary aerosols and secondary inorganic aerosols

## Slide 14
Sekiya et al. (in prep)
Δ Sulfate
Trace gas + AOD DA
Trace gas DA
AOD DA
Δ PM2.5
Combined DA provide better agreements with independent aerosol species and PM2.5 observations
Optimized speciation aerosol emission information support more detailed policy decision
Enhanced constrained by the modern satellites (TROPOMI+VIIRS) than the previous gen (OMI+MODIS)

## Slide 15: Summary
Combined use of multi-scale multi-component DA in MOMO-Chem advance AQ and climate sciences and contribute to NASA’s missions.
Current & future applications: Satellites (GOSAT-GW, CO2M, GEMS, TEMPO, GEO-XO, Sentinel-4), aircraft missions (ASIA-AQ), scientific focuses (AQ+GHG, trace gas + aerosol interactions, OH, wildfires, VOCs), techniques (DA+ML).
Contributions/collaborations: Explore class missions, Schmidt Futures FETCH4 (Co-I), IGAC AMIGO (SC), IGAC TOAR-2 (Lead: Chemical reanalysis WG & satellite assessment report), ISSI (GEO AQ summary paper), JEDI, WMO observing system impacts, CEOS-AC-VC, TRACER-1 (NASA Ames regional reanalysis), JPL TROPESS (new satellite products)
NASA funded projects: AST (PI, Decadal reanalysis), ACMAP (PI, MOMO-Chem), ESUSPI (PI, GOSAT-GW), Earth to Action for Air Quality (PI), JPL ML-AQ (PI), HAQAST (LBC), CMS-Flux (CO2-CO-NOx), NPP (VOCs), ACMAP (trace gas atmospheric river)