## Slide 1: JPSS Aerosol Update
Hongqing Liu, Istvan Laszlo, Shobha Kondragunta,
and NOAA/NESDIS/STAR Aerosol Team
CEOS AC-VC-20 Meeting
October 15th - 18th, 2024
NOAA Center for Weather and Climate Prediction in College Park, MD, USA

## Slide 2: JPSS AOD Algorithm
Retrieves AOD from multispectral, single-look, unpolarized reflectance at pixel level (750m)
Separate retrievals over land and water
  Surface reflectance
    Calculated over water
    Spectral relationship prescribed over land
  Aerosol Optical Depth
    Match the TOA reflectance at the primary channel (M3 over land, M7 over water)
  Aerosol model
    Selected based on the minimum residual

## Slide 3: Availability of JPSS AOD Product
Operational JPSS VIIRS AOD are available from NOAA Comprehensive Large Array-data Stewardship System (CLASS) (https://www.aev.class.noaa.gov/)
  S-NPP AOD available from July 06, 2017;
  NOAA-20 AOD available from March 07, 2019
  NOAA-21 AOD available from July 24, 2023
Past two years data also available at NOAA Open Data Dissemination (NODD)
  https://noaa-nesdis-snpp-pds.s3.amazonaws.com/index.html#VIIRS-JRR-AOD/
  https://noaa-nesdis-n20-pds.s3.amazonaws.com/index.html#VIIRS-JRR-AOD/
  https://noaa-nesdis-n21-pds.s3.amazonaws.com/index.html#VIIRS-JRR-AOD/

## Slide 4: Global Images
NRT images available at the JSTAR Mapper https://www.star.nesdis.noaa.gov/mapper

## Slide 5: Validation over Land
Performances of the three VIIRS retrievals are similar: small negative bias of -0.01 to -0.02; RMSE is about 0.1
Larger uncertainty and underestimation at high AODs.

## Slide 6: Validation over Water
More accurate than retrievals over land
Performances of the three VIIRS retrievals are similar: small bias around 0.01; RMSE is about 0.06

## Slide 7: Time Series

## Slide 8: Reprocessed AOD Products
Reprocessed the historical VIIRS AOD on
  SNPP: 2012-2022; NOAA20:2018-2022
  Used reprocessed VIIRS SDR
Data are available at Amazon Simple Storage Service (S3 buckets)
  Level-2 AOD data
    https://noaa-jpss.s3.amazonaws.com/index.html#SNPP/VIIRS/SNPP_VIIRS_Aerosol_Optical_Depth_EDR_Reprocessed/
    https://noaa-nesdis-n20-pds.s3.amazonaws.com/index.html#reprocessed/VIIRS-JRR-AOD_R/
  Gridded AOD data
    https://noaa-jpss.s3.amazonaws.com/index.html#SNPP/VIIRS/SNPP_VIIRS_Aerosol_Optical_Depth_Gridded_Reprocessed/
    https://noaa-jpss.s3.amazonaws.com/index.html#NOAA20/VIIRS/NOAA20_VIIRS_Aerosol_Optical_Depth_Gridded_Reprocessed/
More information from the START Atmospheric Composition Product Training website: https://www.star.nesdis.noaa.gov/atmospheric-composition-training/satellite_data.php#satellite_data_archives

## Slide 9: Validation of the Reprocessed AOD
Performances are similar to the operational VIIRS AOD

## Slide 10: Time Series of the Reprocessed AOD

## Slide 11: Application (PM2.5)
More details in Michael’s presentation “Satellite perspectives to changing federal standards for PM2.5” (15:30 - 15:45 today)

## Slide 12: Future Plans
Current issues
  Candidate aerosol models are not globally representative
  Dynamic model selection favors dust and smoke
  Underestimation over Africa and India
Future updates – implement operationally
  Expanded candidate aerosol models derived from AERONET
  Updated spectral surface reflectance relationships
  Adjust the model selection scheme

## Slide 13: Preliminary Results
One-year (2023) test with SNPP/NOAA20/NOAA21 AOD retrievals over dark land
SNPP
NOAA20
NOAA21
Over Land
Over Land
Over Land
SNPP
NOAA20
NOAA21