## Slide 1: Over view of the aerosol assimilation activities with the JEDI system
J. Barré1, S.-W. Wei1,2, S. Lu1,2, M. Abdi-Oskouei1, C. Martin3, Y. Wang3, B. Huang4, C. Dang1, V. Buchard-Marchand5, A. DaSilva5, H. Wang3, Y. Tang6, S. Ha7, B. Ménétrier8 and all JCSDA
1UCAR, Joint Center for Center for Satellite Data Assimilation
7State University of New York at Albany
3NOAA, NWS, NCEP, Environmental Modeling Center
4NOAA, OAR, Global Systems Laboratory
5NASA, GSFC, Global Modeling and Assimilation Office
6George Mason University
7NSF, NCAR, Microscale Mesoscale Meteorology
8Norwegian Meteorological Institute

## Slide 2
Coupled DA with AC
Air quality
& scales
Emissions
& fluxes
JCSDA Atmospheric COMPOsition – Research Elements
Enhance Coupled Data assimilation with NWP:
Aerosols – Clouds - Radiation
Stratospheric Ozone
AQ - GHG
L1 DA
Extend DA for fluxes and emission constraint:
Anthropogenic emissions
Fires
Vegetation
Chemical reactions
Facilitate high resolution data assimilation:
New sensors i.e. TEMPO, GEMS, S4, (GeoXO)
Novel geometries, stretched and refined grids
Scalability
Surface observations/ field campaigns
JCSDA
COMPO

## Slide 3
JCSDA Atmospheric COMPOsition – Core and In-Kind
JCSDA COMPO core team
DA capability development and demonstration
NOAA NWS
Operational integration in UFS
NOAA OAR –Research specific Elements for COMPO in UFS
NASA GMAO –Near Real time integration in GEOS
NCAR
MPAS integration &
Science
U. Albany
Evaluation products
George Mason Univ.
Regional AQ research
Morgan State Univ.
GEOS-CF integration & Science
Colorado State Univ.
JEDI training

## Slide 4
JEDI: moving towards coupled DA
State for MOM6
4DEnVar
4DVar
State for MPAS
Uses
Implements
FSOI
Abstract Layer (OOPS)
State
x
Generic Algorithms
Abstract Interfaces
Covariance
B
LETKF
UFO
Specific Implementations
Generic Implementations
IODA
State for FV3
VADER, ATLAS
Coupled State
JEDI - Design Principles and Notional Status
SABER
HDF5
ODB
BUFR
…
ROPP
RTTOV
CRTM
Diffusion
Spectral
BUMP
Generic code eliminates duplication of development, testing and maintenance effort, across teams & Earth-system components.
JEDI design cleanly separates the concepts of:
DA algorithms
model specifics
observation specifics
Abstract interfaces are used by DA algorithms and implemented by specific models and observations.
…
Notes: Separate (as cleanly as possible) the concepts of data assimilation algorithms from the estimated model state specifics and from the observation specifics.
Most (Gaussian) DA algorithms can be written using concepts of x, y, H, M, B, R, without knowing what grid x is distributed on, how many different channels y can contain, and whether M is atmospheric, land, or coupled model.
Key is defining ”interfaces” that are used by DA algorithms and implemented by specific models and specific observations.

## Slide 5
Specific: Air Quality and global Atmospheric Composition interfaces
Dycore/grid: FV3 – stretch grid
Actively supported JEDI atmospheric composition modelling configurations for Aerosol DA
Dycore/grid: FV3 – nested domain
Dycore/grid: MPAS – refined grid
Chemistry: CMAQ
Aerosol Scheme: GOCART-2G
Aerosol Scheme: GOCART-2G in dev.
Current NOAA UFS-Chem
NASA GEOS
Future NOAA UFS-Chem
JEDI Status: Tested and used with JEDI for global and regional AQ application (pre-operational)
JEDI Status: Tested and used with JEDI for global AQ application – preliminary tests with stretch grid
JEDI Status: Tested and used with JEDI for NWP applications – ongoing activity to develop JEDI-MPAS for atmospheric composition
Aerosol Scheme: GOCART & CMAQ

## Slide 6: AOD observation operators in JEDI
UFO
AOD CRTM
AOD Ext
Requires mass mixing ratios in control vector
Requires aerosols extinctions at given wavelength in control vector
Not prognostic variables: require the reverse computation from extinction to mass mixing ratios
Prognostic variables: analyses can be used as is for forecast initial condition
Computationally expensive:
Depending on aerosol scheme and univariate vs multi variate choices
More scalable:
Only one control variable per wavelength
Requirement at NOAA
Requirement at NASA

## Slide 7
  Aerosols:
  VIIRS NPP AOD and L1b in development
  VIIRS NOAA 20,21 AOD and L1b in development
  MODIS Aqua AOD
  MODIS Terra AOD
  Aeronet
  AirNow – PM2.5
  PACE AOD in development
  TEMPO AOD??
Tested and/or Assimilated aerosol observation products in JEDI
VIIRS NPP AOD
MODIS AQUA

## Slide 8: Operational Global Aerosol DA at NOAA NCEP
GOCART - aerosol scheme from NASA included in UFS
GEFS target: C384 (25km), prognostic aerosols in some/all members
Analysis resolution C384L127 (~0.25 deg); background resolution C1152L127 (~9km)
3DVar FGAT with 3-hourly backgrounds
VIIRS EPS 550nm AOD from S-NPP, N20, N21
Difference of absolute error against CAMS (VarBC (sulfate) - CTRL)
Positive: VarBC has smaller error
Negative: CTRL has smaller error
Example of pre-operational fine tunning: JEDI Variational Bias Correction to correct differences between satellite platforms
Lead: NOAA/NCEP/EMC – Support JCSDA

## Slide 9
Monthly mean bias and R2
Jan. 2018 – Mar. 2019
Jul. 2020 – Aug. 2021
Bias
R2
Reanalysis shows significantly improved agreement with AERONET AOD.
Early - NOAA global Aerosol ReAnalysis (NARA)
MODEL: Unified Forecast System - Aerosols (UFS-Aerosols, based on NASA’s GOCART2G)
OBSERVATIONS: NOAA/NESDIS 550 nm Aerosol Optical Depth (AOD) retrievals from S-NPP VIIRS instruments
DA SYSTEM: Ensemble-Variational based with JEDI
Early Reanalysis exercise: from 2018 to 2022
Lead: JCSDA - NOAA/OAR/GSL
Wei et al., 2024

## Slide 10: NOAA/OAR - NOAA regional air quality DA
Lead: NOAA/OAR/GSL and GMU – Support: JCSDA
Integration of PM2.5 and AOD data assimilation and forecasting cycling capabilities into the NOAA AQM workflow.
With guidance form JCSDA a set of variables transforms to compute PM2.5 and AOD (using CRTM) have been implemented in the JEDI code to perform aerosol DA with the UFS CMAQ
CMAQ has many variables we need to condense this information to make it scalable for DA
The DA works well O-A is much improved compared to the O-B.

## Slide 11: NSF NCAR MPAS for atmospheric composition using JEDI
A new system development of MPAS-GOCART2G using JEDI to assimilate NASA PACE AOD retrievals
Instrument/Source | Measurements
PACE OCI | AOD (440 and 550 nm)
MODIS | AOD (550 nm)
VIIRS | AOD (550 nm)
PACE HARP2, SPEXone | AOD (550 nm, when available)
This collaborative project between UCP-JCSDA and NCAR will leverage from previous DA efforts on AOD observations and also in weather with MPAS
Lead: NCAR in collaboration with JCSDA
    Planning stage:
    Add full gas-phase chemistry to MPAS-A through the Model Independent Chemistry Module (MICM)

## Slide 12: Using L1 satellite data for aerosol assimilation
BC1
OC1
DU5
SS5
Looking at channel vs altitude Jacobians: access to size and speciation information
First tests done with VIIRS-NPP
L1b reflectance products:
11 channels
Frontier work to 1. reduce gaps between NWP and AQ DA, 2. improve aerosol DA
Lead: JCSDA

## Slide 13: Evaluation work leveraging existing JEDI UFO capability
JEDI generic simplified interface for evaluation:
  It allows users leverage existing operators in UFO to simulate observations from model states (forecasts) with any projections supported by the atlas library.
  Can use all UFO functionalities: ColumnRetrieval, CRTM, RTTOV, Radar, etc.
Lead: U. Albany and JCSDA
Period: 2019 July (FIREx-AQ)
Model background: GEFS-Aerosols (6 hourly outputs in Gaussian grids, N384)
Observation: NOAA EPS VIIRS AOD (Suomi-NPP)
Operator: AOD CRTM
H(x)
Obs