## Slide 1
Satellite perspectives to changing Federal standards for PM2.5
Michael Cheeseman, Shobha Kondragunta, Hai Zhang, Pubu Ciren
Disclaimer: The scientific results and conclusions, as well as any views or opinions expressed
herein, are those of the author(s) and do not necessarily reflect those of NOAA or
the Department of Commerce.

## Slide 2: EPA amended federal standards for PM2.5
In 2024, the US EPA updated the National Ambient Air Quality Standards (NAAQS) for annual average PM2.5 from 12 µg m-3 to 9 µg m-3
The EPA estimates that 99% of counties will be in attainment by 2032
Source: U.S. Environmental Protection Agency (EPA), Proposed Decision for the Reconsideration of the National Ambient Air Quality Standards for Particulate Matter (PM)

## Slide 3: The Exceptional Events Rule (EER)
Pollution levels can often exceed the NAAQS due to unusual and naturally occurring events (exceptional events) that cannot reasonably be controlled by state regulations:

## Slide 4: The Exceptional Events Rule (EER)
Pollution levels can often exceed the NAAQS due to unusual and naturally occurring events (exceptional events) that cannot reasonably be controlled by state regulations:
  Wildfires
  Dust storms
  Volcanic emissions
(Image credit: EUMeTrain)

## Slide 5: The Exceptional Events Rule (EER)
Pollution levels can often exceed the NAAQS due to unusual and naturally occurring events (exceptional events) that cannot reasonably be controlled by state regulations:
  Wildfires
  Dust storms
  Volcanic emissions
In these cases, states can take advantage of the Exceptional Events Rule (EER) and avoid being classified as nonattainment.

## Slide 6: Landscape fires are becoming an increasingly important source of PM2.5 in the US
See Ford et al. (2018), slide courtesy of Bonne Ford

## Slide 7: Exceptional Events Reports (EERs) have significant resource costs
A single EER for a wildfire can require tens of thousands of dollars and hundreds of working hours for local agencies.
Reducing the NAAQs will likely lead to an increase in EERs and some agencies argue those resources would be better spent on reducing local air pollution.
New York city smoke from Canadian fire in June 2023
https://www.nbcnewyork.com/local/wildfire-smoke-photos-in-nyc-show-apocalyptic-sepia-landscape/4405485/

## Slide 8: Visible Infrared Imaging Radiometer Suite (VIIRS) Aerosol Products from JPSS series

## Slide 9: Translating satellite AOD, smoke, and dust retrievals to PM2.5

## Slide 10: VIIRs smoke/dust-free PM2.5 shows many counties in excess of the new NAAQs during the 2019-2021 period
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 11: VIIRs smoke/dust-free PM2.5 shows many counties in excess of the new NAAQs during the 2019-2021 period
Increase from 1.6 million people to 65 million people above the NAAQs during 2019-2021
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 12: VIIRs smoke/dust-free PM2.5 shows many counties in excess of the new NAAQs during the 2019-2021 period
Southeastern exceedances may be driven by combination of smoke/dust transport, sulfate aerosols, and secondary organic aerosol (SOAs) formation.
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 13: Using HMS smoke information leads to similar results in southeastern US but a decrease in the West

## Slide 14: Including smoke/dust events indicates a significant increase in NAAQs exceedances
Notes: Southeastern US exceedances may be driven by combination of local sources and optically thin transported smoke/dust that isn’t captured

## Slide 15: Thus, smoke/dust events will likely drive increased demand for counties to produce EERs, especially in Western US
Number of counties that would require EERs (VIIRS smoke + dust mask, 2019-2021)

## Slide 16: HMS indicates an even greater number of EERs during the 2019-2021 period
Number of counties that would require EERs (HMS smoke + VIIRS dust mask, 2019-2021)

## Slide 17: VIIRS aids in identifying areas most impacted by acute PM2.5 concentrations
<1
5
10
20
> 30
Number of days with hazardous PM2.5
Background/Anthropogenic PM2.5
VIIRS-identified Smoke PM2.5

## Slide 18: Racial/ethnic data indicates that there is some disparity in acute episodes of smoke/dust-free PM2.5

## Slide 19: Racial/ethnic data indicates that there is some disparity in acute episodes of smoke/dust-free PM2.5

## Slide 20: Conclusions
VIIRS observations indicate a large population increase across many counties that will exceed the new annual PM2.5 NAAQS, even in the absence of smoke/dust.
  The Southeastern US may be driven by anthropogenic emissions of SO2 and NOx that will be diminished by 2032 due to regulations.
  However, if biogenic emissions and transported smoke/dust also play a major role, this region may continue to be in exceedance of the new NAAQs.
The increasing number landscape fires and reduced annual NAAQS may lead to a large increase in Exceptional Events Reports, which require significant man-hours and analysis to complete.
VIIRS-derived PM indicates disparities in acute exposure for both anthropogenic and smoke/dust sources.

## Slide 21: Supplemental Slides

## Slide 22: VIIRS smoke/dust retrievals are especially useful for thicker smoke plumes in the West

## Slide 23: What happens when PM2.5 concentrations exceed the NAAQS?
If a county is in nonattainment, the state must create a State Implementation Plan (SIP):
New York city smoke from Canadian fire in June 2023
https://www.nbcnewyork.com/local/wildfire-smoke-photos-in-nyc-show-apocalyptic-sepia-landscape/4405485/

## Slide 24: What happens when PM2.5 concentrations exceed the NAAQS?
If a county is in nonattainment, the state must create a State Implementation Plan (SIP):
  Show that the state has adequate air quality management program to implement NAAQS
New York city smoke from Canadian fire in June 2023
https://www.nbcnewyork.com/local/wildfire-smoke-photos-in-nyc-show-apocalyptic-sepia-landscape/4405485/

## Slide 25: What happens when PM2.5 concentrations exceed the NAAQS?
If a county is in nonattainment, the state must create a State Implementation Plan (SIP):
  Show that the state has adequate air quality management program to implement NAAQS
  Provides state-adopted control measures in order to reach and maintain air pollutant concentrations below the NAAQS
New York city smoke from Canadian fire in June 2023
https://www.nbcnewyork.com/local/wildfire-smoke-photos-in-nyc-show-apocalyptic-sepia-landscape/4405485/

## Slide 26: How does smoke/dust impact daily air quality disparities across the US?
<1
1-5
5-10
15-20
10-15
> 20
Number of daily air quality alerts due to
Background/Anthropogenic PM2.5 (2020)
Number of daily air quality alerts due to
Total PM2.5 (2020)
Air quality alert: daily PM2.5 > 35 μg m-3

## Slide 27: Racial/ethnic data indicates that there is some disparity in daily air quality alerts from Total PM2.5

## Slide 28: Background/anthropogenic PM2.5 shows even larger disparities

## Slide 29: Low-fire year (2019) shows very few daily PM2.5 air quality alerts
<1
1-5
5-10
15-20
10-15
> 20
Number of daily air quality alerts due to Total PM2.5

## Slide 30: Hispanics still have proportionally higher number of daily air quality alerts

## Slide 31: VIIRS captures acute smoke contributions to daily hazardous PM2.5