## Slide 1
Itziar Irakulis-Loitxate, Javier Gorroño, Manuel Montesino, Gonzalo Mateo-García, Luis Guanter
October 2024
Discussion on Characterizing POD for Facility Scale
Emissions Estimates
The International Methane Emissions Observatory

## Slide 2
UNEP’s IMEO
interconnects better data with targeted action
The International Methane Emissions Observatory exists to provide open, reliable, and actionable data to those that can act to reduce methane emissions
Methane Science
OGMP 2.0
Actionable Data
MARS

## Slide 3
IMEO’s MARS uses satellites to provide rapid, actionable data to stakeholders
METHANE
ALERT
RESPONSE
SYSTEM
Detect and Attribute
Notify and Engage Stakeholders
Stakeholders Take Action
Track, Learn, Collaborate, Improve
Requirements for notification:
High-resolution plume
Recent plume
O&G emission (coal emissions soon)

## Slide 4
Data to Action Tapping into the methane data revolution
Methane Science
MSI
OGMP 2.0
Actionable Data
MARS
Beta Version

## Slide 5
Jacob et al., ACP, 2022 (edited)
Area flux mappers:
  Spatial sampling ~1-10 km
  TROPOMI: 7 km/pixel, global daily coverage, >10 t/h emissions, difficult attribution to sources
  A number of other missions coming up soon
  Point source imagers:
  Spatial sampling ~30 m
  Allow attribution to sources and lower detection limits (300-10,000 kg/h)
  Two classes of satellite missions
    Spectrometers (PRISMA, EnMAP, EMIT): medium sensitivity, sporadic acquisitions, require tasking/limited to some latitudes
    Multispectral imagers (S-2/Landsat): low sensitivity, but “monitoring” with frequent and global coverage
The diverse ecosystem of methane-sensitive missions

## Slide 6
IMEO public portal with all detected plumes and hot spots
In the portal we show the plumes but not the days without plumes
Users: both experts and non-experts (journalists, NGO, governments, industry,...) in satellites and/or methane.
Requests for:
  No-plume days
  Frequency of emission/persistence of a leak
  Estimate of the total amount of methane emitted (requires knowing the duration of the emission)
  Detection limit of the satellites

## Slide 7
  No plume No emission
Internally we keep with the “no plume observed” data
Without the proper expertise, the data can be easily misinterpreted.
The danger of giving non-plume data

## Slide 8
Vaughan et al., 2024 (in preprint) https://arxiv.org/html/2408.04745v1
In order to give a more comprehensive understanding of the emission frequency we would like to provide the emission time series per source
The days without plume need further context
Minimum Detection Limit (MDL): Lowest emission flux rate for a set of conditions to provide a correct quantification at a given level of probability
Proposed solution

## Slide 9
DEFINITION
Minimum Detection Limit (MDL) – Lowest emission flux rate for a set of conditions to provide a correct quantification at a given level of probability
Conditions:
Observation conditions – illumination, wind speeds and turbulence, landscape
Instrument capabilities – spectral and spatial resolutions, Signal-to-Noise ratio
Algorithm performance – transmission artefacts and detection algorithms
Correct quantification – when the true Q is within the confidence interval (tied to quantification)
Frequency at which the system provided the right quantification:
Q50 – flux rate at which the system provides the right quantification 50% of the times
Q90 – flux rate at which the system provides the right quantification 90% of the times
Emission flux rate (Q):
kg/h – combines CH4 sensitivity and spatial resolution
Based in simulations

## Slide 10
ALGORITHM

## Slide 11
PRELIMINARY RESULTS
Q50 – 9081 kg/h
Q90 – 14933 kg/h
Q50 – 1812 kg/h
Q90 – 3249 kg/h
Detections and quantifications
Target image
PoD
Q50 – flowrate at which the system provides the right quantification 50% of the times
Q90 – flowrate at which the system provides the right quantification 90% of the times

## Slide 12
Goal: provide the time series and the data for each non-plume day with an estimated MDL
The first tests are already running
First tests:
  With multispectral data
  Using standard wind
  Simulate the plume in the centre of the image
  Processing time 3-6 minutes
There is a trade-off between processing time and scope of validation: more simulations with more flux rates and plume variability, more processing time.
Next versions adapted to other satellites and with different winds
Implementation

## Slide 13
Thank you !
itziar.irakulisloitxate@un.org
Itziar Irakulis Loitxate
MARS Remote Sensing Lead