## Slide 1: CEOS Carbon Task Force Report – Atmospheres Chapter
David Crisp, OCO-2 Science Team Leader
Jet Propulsion Laboratory, California Institute of Technology
June 2014
Copyright 2014 California Institute of Technology. Government sponsorship acknowledged.
10th CEOS Atmospheric Composition Constellation Meeting (ACC-10)

## Slide 2: GEO Carbon Strategy
The GEO Carbon Strategy states:
“a key reason for our lack of understanding of the global carbon cycle is the dearth of global observations,”
and calls for
“an increased, improved and coordinated observing system for observing the carbon cycle as a prerequisite to gaining that understanding.”
The Committee on Earth Observation Satellites (CEOS) is well positioned to meet this challenge and provide needed coordination for the space-based observations called for in the GEO Carbon Strategy.

## Slide 3: CEOS Response to the GEO Carbon Strategy
CEOS established a Carbon Task Force (CTF) to coordinate the response from the space agencies to the GEO Carbon Strategy.
  Take into account information requirements of both the UNFCCC and IPCC and consider how future satellite missions will support them
  Also take account of, and be consistent with, the GCOS and GEO Implementation Plans.
  Help definition of next generation missions for individual agencies (provide a long-term outlook, 2013-2028).
  Provide a basis for systematic observation and reporting of progress towards satisfying society’s carbon information needs
CEOS Strategy for Carbon Observations from Space

## Slide 4: The Natural Carbon Cycle
Land Biosphere
Ocean
330 Gt CO2
340 Gt CO2
440 Gt CO2
450 Gt CO2

## Slide 5: Atmospheric Carbon Dioxide
Source: NOAA Earth System Research Laboratory Global Monitoring Division
Fossil Fuel use and other human activities are now adding more than 39 billion tons of carbon dioxide to the atmosphere each year

## Slide 6: Fossil Fuel CO2 Emissions: Top Emitters
The most rapid growth is happening in the Developing World
Source: CDIAC Data; Le Quéré et al 2013; Global Carbon Project 2013
2
0
6
4
10
8
Billions of Tons of CO2 / Year
Notes: Fossil fuel combustion and other human activities are now adding more than 35 billion tons of carbon dioxide to the atmosphere each year. The U.S. and Europe were once the largest emitters, but have been recently overtaken by China.
Note, here carbon emissions are expressed in “Billions of tons of carbon per year.” When a fossil fuel is burned, each carbon atom is “oxidized” with two Oxygen atoms, to produce a CO2 molecule. Because a mole (6.02 x 1023 atoms) of carbon has a molecular weight of 12, and a mole of oxygen has a molecular weight of 16, the molecular weight of CO2 is 44, which is 3.7 times as large as that of carbon. Each ton of fossil fuel carbon therefore add 3.7 tons of CO2 the atmosphere.

## Slide 7: Processes Regulate the CO2
10
0
30
20
40
Billions of Tons of CO2 / Year
1
We don’t know.
Total Emissions
Atmospheric Grown Rate
Source: CDIAC Data; NOAA/ESRL Data; Le Quéré et al 2013; Global Carbon Project 2013
    What natural processes absorb half of the CO2 emitted by human activities?
    Why does the amount of CO2 absorbed change from year to year?
    Will this change in the future, as the climate changes?
Notes: The green bars show the number of tons of carbon added to the atmosphere each year from fossil fuel combustion.
The blue bars show the amount of carbon dioxide that accumulates in the atmosphere. The rest is apparently absorbed by the land biosphere and oceans.

## Slide 8: In Summary, for CO2 …
Fossil Fuel combustion and other human activities are rapidly increasing the atmosphere CO2 concentration
Natural “sinks” in the land biosphere and ocean are currently absorbing about half of the CO2 emitted by human activities
The nature, location, and processes controlling these natural CO2 sinks are unknown
CO2measurements from the ground-based network provide an accurate description of the global atmospheric CO2 budget and its rate of increase, but do not have the resolution or coverage needed to quantify its sources or sinks

## Slide 9: Methane (CH4) is Also Increasing
The atmospheric abundance of CH4, the second most abundant well-mixed greenhouse gas, has grown by 150% since the beginning of the industrial age
CH4 is less abundant than CO2, but more efficient as a greenhouse gas, such that it is now contributing about 60% as much greenhouse warming as CO2
Recent changes in the atmospheric CH4 budget are controlled by a diverse array of natural and human sources (wetlands, livestock fossil fuel) and natural sinks, that are less well understood than those for CO2
Because it is also an abundant, long-lived gas, CH4 poses measurement challenges similar to those for CO2

## Slide 10: CH4 Sources and Sinks
Anthropogenic Sources
Natural Sinks
Natural Sources
Source: Global Carbon Project 2013
Tarasova and Butler, GeoCarbon 2013

## Slide 11: Tracking Sources and Sinks of Long-Lived Greenhouse Gases is Challenging

## Slide 12: In Summary …
Space-based measurements of CO2, CH4, and other greenhouse gases will complement those from the ground based network with dramatically improved resolution and coverage
However, these measurements must have unprecedented accuracy (0.25%) to resolve the small variations in these gases associated with their sources and sinks
The world’s spacefaring nations are now implementing a range of innovative systems to address this increasingly urgent need

## Slide 13: The Promise and Challenge for Space Based CO2 Measurements
Spatial coverage
  Observations over both land and ocean
Temporal resolution and sampling
  Daily/Weekly sampling needed to resolve CO2 weather
  Monthly measurements required over > 1 year to resolve seasonal and inter-annual variability in CO2
Spatial resolution and sampling
  Sensitivity to point sources scales with area of footprint
  Small measurement footprints enhance sensitivity to point sources and reduce data losses due to clouds
Primary Challenge: Precision and accuracy
  High precision required to resolve small (0.2-0.3%) variations in CO2 associated with sources and sinks
  High accuracy essential to avoid regional-scale biases

## Slide 14: Thermal Infrared Observations of CO2
Thermal IR observations (AIRS, TES, IASI, CriS) measure CO2 in the middle troposphere
  Provide global maps of CO2 at altitudes where it is most effective as a greenhouse gas
  Provide limited information about surface sources and sinks of CO2
AIRS July 2003 CO2
378 ppm
AIRS JULY 2008 CO2 (ppm)
388 ppm
Metop IASI
Aqua AIRS

## Slide 15: Remote Sensing of CO2 using Reflected Sunlight: The Pioneers
SCIAMACHY (2002-2012) – 1st NIR/SWIR CO2 / CH4 sensor
  Regional-scale maps of CO2 and CH4 over continents on seasonal time scales
GOSAT (2009 - ?) - Optimized for spectral coverage
  Combination of high spectral resolution over broad spectral range yields high sensitivity to CO2, CH4, and chlorophyll fluorescence
  OCO-2 (2014) - Optimized for XCO2 sensitivity, resolution, and coverage
  Optically fast, high resolution spectrometer with agile pointing (glint, nadir, target), small (3 km2) footprint and rapid sampling (106 samples/day)

## Slide 16: Remote Sensing of CO2 using Reflected Sunlight: The Next Generation
TanSat (2016) - First Chinese greenhouse gas satellite
  Uses same O2 and CO2 bands and similar orbit as OCO-2
  Cloud & Aerosol Imager: 0.38, 0.67, 0.87, 1.38 and 1.61μm channels
OCO-3 (2017) - OCO-2 spare instrument, to be deployed on ISS
  First solar CO2 sensor to fly in a low inclination, precessing orbit
GOSAT-2 (2018) – High precision CO2, CH4, CO, and NO2
  Improved precision (0.5 ppm), spatial resolution, and range of ocean glint observations expected to improve coverage
CNES MicroCarb (2019) – high sensitivity at low cost
  Flies in the A-Train, providing data continuity for OCO-2
  ~1/2 to 1/3 of the size (and cost) of OCO-2, with similar sensitivity
ESA CarbonSat (2022) – CO2 & CH4
  high spatial resolution (2 km x 3 km), over a broad (~200 km) swath

## Slide 17
Allow full-column greenhouse gas measurements day and night and at high latitudes.
MERLIN (2019): First CH4 LIDAR (IPDA)
  Science focus: Precise (1-2%) XCH4 retrievals for studies of wetland emissions, inter-hemispheric gradients and continental scale annual CH4 budgets
  Orbit: 6AM/6PM, 28-day repeat
ASCENDS* (2022+): First CO2 LIDAR
  Precise (0.3%) global measurements of XCO2, over days, nights, including winter high latitude regions to quantify continental and oceanic CO2 sources and sinks
  Should provide many useful soundings in partially cloudy regions because of near vertical sounding
Planned Active Greenhouse Gas Missions
*Proposed Mission - Pre-decisional - for Planning and Discussion Purposes Only
Notes: The first generation active CO2 sensors are still on the drawing boards.
Active LIDAR instrument concepts like those being considered for ASCENDS cannot provide the sensitivity or coverage of passive solar NIR sensors over most of the sunlit hemisphere, but can return data at night as well as during the day.
These systems are currently being tested in the laboratory and in aircraft. The first space-based deployment is still a few years off.

## Slide 18: OCO-2 is Part of a Growing International Constellation of Greenhouse Gas Satellites
The Evolving Atmospheric CO2 Constellation
*Proposed Mission - Pre-decisional - for Planning and Discussion Purposes Only
*
*
Notes: And OCO-2 is not the only greenhouse gas monitoring satellite. Several nations have started to build similar satellites that will be launched over the next few years.
If we can combine the measurements from all of these satellites, we can learn much more about the natural and human processes that are controlling the buildup of greenhouse gases in our atmosphere.

## Slide 19: Exploiting the Benefits of Multiple Missions
Space-based remote sensing observations hold substantial promise for future long-term monitoring of greenhouse gases
  These measurements will complement existing ground-based data with increased spatial coverage and sampling density
Over the next decade, a succession of missions with a range of CO2 and CH4 measurement capabilities will be deployed in LEO
  Include near polar, sun synchronous orbits with morning and afternoon mean local times, and low inclination, precessing orbits (OCO-3/ISS)
  Because there is little overlap between the missions, each one is a critical link in a chain that must be successfully deployed to ensure a continuous climate data record.
Measurements from Geosynchronous obit (GEO) would also be valuable for studying the diurnal cycles of CO2 and CH4
  There are no plans to collect precise CO2 measurements from GEO
Much greater benefits could be realized if these missions could be coordinated and their data products can be combined

## Slide 20: Examples of Collaborative Cal/Val Activities
Pre Launch:
Cross calibration of pre-launch radiometric standards
Exchange of gas absorption coefficient and solar databases
Algorithm development / intercomparison
Validation system development (TCCON, AirCore, Other)
Dual/multi-Satellite OSSE’s – what do you gain with truly coordinated observations
Post Launch:
Cross calibration of solar / lunar / Earth (vicarious calibration) observations
Cross validation: TCCON, AirCore, Tower, etc.
Algorithm implementation/intercomparison
Intercomparisons of flux inversions

## Slide 21: Thank You for Your Attention Questions?