## Slide 1: Hourly atmospheric pollution from geostationary Earth orbit
PI: Kelly Chance, Smithsonian Astrophysical Observatory
Instrument Development: Ball Aerospace
Project Management: NASA LaRC
Other Institutions: NASA GSFC, NOAA, EPA, NCAR, Harvard, UC Berkeley, St. Louis U, U Alabama Huntsville, U Nebraska
International collaboration: Korea, Europe, Canada, Mexico
Selected Nov. 2012 as NASA’s first Earth Venture Instrument
  Instrument delivery September 2017
  NASA will arrange hosting on commercial geostationary communications satellite with launch expected NET 11/2018
Provides hourly daylight observations to capture rapidly varying emissions & chemistry important for air quality
  UV/visible grating spectrometer to measure key elements in tropospheric ozone and aerosol pollution
  Exploits extensive measurement heritage from LEO missions
  Distinguishes boundary layer from free tropospheric & stratospheric ozone
Aligned with Earth Science Decadal Survey recommendations
  Makes many of the GEO-CAPE atmosphere measurements
  Responds to the phased implementation recommendation of GEO-CAPE mission design team
  North American component of an international constellation for air quality observations

## Slide 2: Typical TEMPO-range spectra (from ESA GOME-1)

## Slide 3: TEMPO footprint, ground sample distance and field of regard
Each 2.1 km × 4.7 km pixel is a 2K element spectrum from 290-740 nm
GEO platform selected by NASA for viewing Greater North America
2.1 km × 4.7
__________

## Slide 4: TEMPO footprint (GEO at 100º W)
For GEO at 80ºW, pixel size at 36.5ºN, 100ºW is 2.2 km × 5.2 km.
Location | N/S (km) | E/W (km) | GSA (km2)
36.5oN, 100oW | 2.11 | 4.65 | 9.8
Washington, DC | 2.37 | 5.36 | 11.9
Seattle | 2.99 | 5.46 | 14.9
Los Angeles | 2.09 | 5.04 | 10.2
Boston | 2.71 | 5.90 | 14.1
Miami | 1.83 | 5.04 | 9.0
Mexico City | 1.65 | 4.54 | 7.5
Canadian tar sands | 3.94 | 5.05 | 19.2
Assumes 2000 N/S pixels |  |  | 

## Slide 5
Species/Products | Required Precision | Temporal Revisit
0-2 km O3 Selected Scenes, Baseline only | 10 ppbv | 2 hour
Tropospheric O3 | 10 ppbv | 1 hour
Total O3 | 3% | 1 hour
Tropospheric NO2 | 1.0 × 1015 molecules cm-2 | 1 hour
Tropospheric H2CO | 1.0 × 1016 molecules cm-2 | 3 hour
*Tropospheric SO2 | 1.0 × 1016 molecules cm-2 | 3 hour
*Tropospheric C2H2O2 | 4.0 × 1014 molecules cm-2 | 3 hour
*Aerosol Optical Depth | 0.10 | 1 hour
Minimal set of products sufficient for constraining air quality
Field of Regard (FOR) is Greater North America, depending on host satellite selected:
  At least 19°N to 57.5°N near 100°W
  At least 67°W to 125°W near 42°N
Data products at urban-regional spatial scales
  Baseline ≤ 60 km2 at center of FOR
  Capability for retrieval at native pixel resolution (approx. 2.1 km x 4.7 km) when SNR allows
Geolocation uncertainty of less than 4 km
Temporal scales to resolve diurnal changes in pollutant distributions
Mission duration, subject to instrument availability
  Baseline 20 months
  Threshold 12 months
*Implementation of SO2, C2H2O2, and aerosol algorithms is deferred until after successful instrument PDR
Likely ~October 2015
No impact on instrument design capability
All products still ready for launch once approved
Baseline and threshold
data products

## Slide 6: TEMPO Summary
TEMPO is a pathfinder for NASA
  The first mission under the stringently cost-capped Earth Venture Instrument program
  First use of a competitively selected commercial host satellite
Currently on-schedule and on-budget
  Passed System Requirements Review and Mission Definition Review in November 2013
  Passed KDP-B April 2014, now in Phase B
  PDR scheduled for late July 2014
Commercial satellite host selection and Instrument CDR summer 2015
  TEMPO operating longitude and launch date are not known until after host selection
Instrument delivery 11/2017 for launch no earlier than 11/2018

## Slide 7: Sentinel-4 in the Context of Copernicus
  Copernicus Programme
  Services Component (European Commission)
In-situ Component (European Environmental Agency)
Space Component (European Space Agency): Sentinels + contributing missions
www.copernicus.eu
  Copernicus Atmosphere Service
Protocol compliance monitoring: ozone layer (Montreal, …), air quality (Göteborg, …), climate (Kyoto, …), emission verification
Near-real-time services: Local air quality, health warning, aviation routing
Assessments: Improve understanding of processes, validate chemical transport models, ground measurement networks
Pre-operational: http://atmosphere.copernicus.eu
Uses observations from current satellites,
in the future also from Sentinel-4, -5, -5P, …
Notes: 7

## Slide 8
Sentinel-4/UVN Instrument
Spatial Sampling: 8 km at 45°N
Coverage: Europe + part of Sahara
Repeat Cycle: 1 hour
Low sensitivity to polarisation (1%)
Low level of spectral features (0.05%)
High radiometric accuracy: 3% (2%, goal)
Band | Wavelength range [nm] | Spectral resolution [nm] | Spectral sampling ratio
UV | 305 - 400 | 0.5 | 3
VIS | 400 – 500 | 0.5 | 3
NIR | 750 – 775 | 0.12 | 3
OZA: Observation Zenith Angle
GCA: Geo Coverage Area; RA: Reference Area
Key Parameter | Estimated Value
Mass | ≈ 200 kg
Power (Obs.) | ≈ 180 W (average)
Data Rate | 29 Mbps (average)

## Slide 9: Sentinel-4/UVN Development
Development Tasks
  S4/UVN instrument
  Level-1b Prototype Processor
Status
  Preliminary Design Review completed
  Phase C: Detailed Design
  currently Phase C/D price conversion
Flight Acceptance Review expected in 2021
EUMETSAT will operate S4/UVN and process the mission data
  in the MTG ground segment

## Slide 10: Sentinel-4 Level-2 Products
Product | Application |  |  | Comment
 | Air Quality | Climate | Surface UV | 
O3 total & tropospheric column | X |  | X | 
O3 enhanced sensitivity to lower troposphere | X |  | X | Synergy with infrared data from IRS
NO2 total & trop. column | X |  |  | 
SO2 total column | X |  |  | Also for volcanic eruption monitoring
CHOCHO total column | X |  |  | By-product
CH2O total column | X |  |  | 
Aerosol extinction coeff. profile, column optical depth / type / index | X | X |  | Also for volcanic eruption monitoring Also auxiliary for other S4 products Synergy with imager data from FCI
Cloud optical thickness, fraction, altitude |  |  | X | Mainly auxiliary for other S4 products Synergy with imager data from FCI
Surface reflectance daily map |  |  | X | Mainly auxiliary for other S4 products

## Slide 11: Sentinel-4 Level-2 Processor Development
Invitation To Tender AO7845
  Published on EMITS http://emits.sso.esa.int
  Proposal submission until 18 July 2014
Tasks
  Algorithm and Processor Concept Development building on heritage and pre-development studies (AERORPO, SURMACED)
  Prototyping and Operational Processor Development
  System Integration & Verification and Mission Commissioning Support
  Performance Monitoring Support Functions/Elements
Project time frame
  kick-off 2014
  to end of commissioning (Launch+12m)

## Slide 12
AROMAT
Airborne ROmanian Measurements of Aerosols and Trace gases
Aims: test new systems (aircraft + UAV, in-situ), prepare S5p validation, investigate consistency and complementarity of different approaches
Targets: high pollution levels and strong gradients of NO2, SO2 and aerosol in power plant exhaust plumes and urban area
Partners: BIRA (Belgium), KNMI (Holland),
IUP-Bremen (Germany), ISS-Berlin (Germany)
Ugal (Romania), INOE (Romania), RRA, (Romania)
Instrumentation: AirMAP (Cessna) + SWING system (UAV) + in-situ NO2 (Ballon) + Ground
Campaign Targets
Bucharest
Romania
Power plants

## Slide 13
UV/VIS: Nadir
Column obs. to surface
uvSCOPE: 460-490nm
APOLLO: 305-505nm
ISS Orbit
MWI: Limb 2D Tomographic Obs.
Above UT
(300+600 GHz)
Air quality missions in Japan
Mission | Launch* | - O3, NO2, SO2, AAI (Absorption Aerosol Index) - Vertical res.: 3km in the troposphere - Horizontal res.: 1x1km – 2x2km - Coverage: 50S-50N * Target launch year (The selection process is still under evaluation)
uvSCOPE (UV ) | 2017 | 
APOLLO-Anu (UV + MW) | 2018 | 
GMAP-Asia (UV+ TIR + MW) | No plan | 
  UV/VIS+MW Averaging kernel for O3
  Degree of freedom for Boundary layer ozone

## Slide 14: Next Activities: Harmonization to improve data product quality and usage
During 2013, the CEOS ACC AQ Constellation leads developed recommendations for harmonization to mutually improve data quality and facilitate widespread use of the data products (see next slide)
Includes LEO and GEO: LEO observations are a common transfer standard to link the GEO observations
Already seeing progress
  Sharing instrument requirements, which is influencing instrument specifications and should ultimately improve harmonization of data products
  Advocating open data policy (including L1B) with common formats to facilitate broad usage
  Sharing L1B and L2 format specifications to easily exchange data
  Establishment of new GSICS UV-Vis subgroup (see L. Flynn talk at 9:00 tomorrow)

## Slide 15: Open Data Policy and Common Cal/Val Standards: Recommendations
  Apply best practices (lessons learned) for UV-Vis spectrometer calibration, characterization, and validation
    Share calibration/characterization plans and invite cross participation in reviews of such plans
    Develop longer term recommendations for common post-launch cal/val strategies (e.g. supersite instrumentation round-robins, joint airborne campaigns)
  Radiometric consistency
    Pre-launch: highest priority is per-instrument calibration/characterization as completely as possible (common absolute radiance calibration is secondary)
    Post-launch: more work needed on approaches (eg LEO vicarious intercalibration or Earth scenes)
  Sharing and consistency of data products (format, content, metadata)
    Share specification documents
    Share instrument characterization/calibration databases and Level 1-b data, in a common format, to allow wide application of algorithms to all datasets
    Identify and produce common constellation data products (may differ from standard products)
  Consistency in retrieval algorithms
    Cross participation in ATBD reviews
    Jointly improve retrieval algorithms by conducting inter-comparisons on common radiances
  Consistency of spectroscopy
  Support scientific collaboration

## Slide 16: Concluding thoughts and the year ahead
It has been a busy and successful year for the AQ Constellation mission teams
Data harmonization activities have started and will need constant attention
  Mission leads have been sharing specifications
  Pre-launch instrument characterization requirements necessarily vary by instrument
    GEMS and TEMPO should have very similar pre-launch characterization, due to having the same builder and enveloped requirements
  GSICS UV-Vis working group is off to a good start
Tentative upcoming airborne field campaigns offer potential for early S-5P cal/val and ongoing collaborative GEO mission preparation
  AROMAT Romania 2015, 2016 (ESA)
  KORUS-AQ Korea 2016 (Korea NIER, US NASA & NSF)
  Consider establishing an AQ Constellation Geophysical Validation Document before the geostationary mission specific requirements are written by the respective agencies
We look forward to a dedicated session next year in ACC-11
  Algorithm and processor development, vicarious inter-calibration, common validation, etc. etc.
Atmospheric Composition Constellation Meeting ACC-10
College Park, MD, 4-5 June 2014

## Slide 17: Backup

## Slide 18: Intent and Scope of the CEOS Activity
Conduct international collaborative activities to improve preparation for, and capabilities of, planned air quality missions
Identify policy-relevant science and environmental services that would be enabled by common observations from each mission
  Improved emissions, at common confidence levels, over the industrialized Northern Hemisphere
  Improved air quality forecasts and assimilation systems
  Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution (LRTAP)
  Include the low-Earth-orbit missions and observations expected to be operating in the 2018-2022 period: critical to the constellation objectives
  Hourly observations over source and receptor regions are linked by ~daily LEO observations over oceans and intermediate regions
Include those climate aspects that are interrelated with AQ
  Short-lived climate forcers (O3, aerosols)
  AQ/climate co-benefits
May 2011: Position paper and its 7 recommendations endorsed by CEOS
  A Geostationary Satellite Constellation for Observing Global Air Quality: An International Path Forward http://www.ceos.org/images/ACC/AC_Geo_Position_Paper_v4.pdf

## Slide 19: Near-Term Recommendations (Within 3 Years)
Coordinate one or two key people per mission to be part of mutual mission science or advisory teams with a focus on common science and collaborative data products.
  Points of contact for each mission have been named
Facilitate scientific collaboration on retrieval algorithms and chemical Observing System Simulation Experiment (OSSE) studies. Organize a workshop on air quality OSSE activities.
  “Cooperation to define, conduct, and analyze common OSSE scenarios… align and extend ongoing regional studies and systematically incorporate them into global studies.”
  CEOS/MACC-II International OSSE Workshop held 22-24 October 2012 at ECMWF http://www.ecmwf.int/newsevents/meetings/workshops/2012/OSSE/
Coordinate societal benefit assessment of satellite air quality observations, leveraging recent GCOS and GEO health community of practice efforts
  Requires interaction with economists and health effects communities
✔
✔
http://www.ceos.org/images/ACC/AC_Geo_Position_Paper_v4.pdf

## Slide 20: Longer Term Recommendations
Agree on an open data policy for AQ-relevant data and support establishment of common cal/val standards
  Data sharing protocol should include Level 1-B data to enable reprocessing of all data with common algorithms
  Initial workshop to compare cal/val plans and identify collaborative opportunities
Organize a workshop on AQ model intercomparison
  The ongoing Air Quality Modelling Evaluation International Initiative (AQMEII) has already made much progress among European and North American groups
Undertake best efforts to overlap planned GEO AQ missions by at least 1 year
  Given the expected 2018-2019 launches of S4, GEMS, and TEMPO, this will be achieved for the baseline products beginning with the first-generation missions!
  The existence of these missions is enabling stronger international collaborations
Support evaluation of strategies for extending coverage, including possible approaches for common instrumentation
✔
✔
http://www.ceos.org/images/ACC/AC_Geo_Position_Paper_v4.pdf

## Slide 21: Lessons learned from UV spectrometer experience
Calibration and characterization are very instrument dependent
  We cannot dictate common calibration practices for instruments of different design, but can share techniques
  Standardize the “outcome” of calibrations, not the actual calibration procedure
We always wish we had more pre-launch characterization data
  Always have to sub-sample the sensor spatial and spectral domains
  The more sparse the sub-sampling, the harder it is to diagnose unexpected on-orbit performance
  The amount of sampling often gets scaled back to reduce cost
  We should at least recommend where to not cut corners
One opinion: “With LEO instruments, we used to do a lot of common inter-calibration. Now everyone does calibration so well that we may not need to focus so much on inter-calibration anymore.”
Others?