## Slide 1
EUMETSAT GHG Activities CEOS ACC Meeting #10, 4/5 June 2014

## Slide 2: Atmospheric Composition Services: Greenhouse Gases
Metop IASI
EPS-SG UVNS (Sentinel-5) EPS-SG IAS

## Slide 3: Atmospheric Composition Services: Greenhouse Gases
Metop IASI CH4 (&CO2)
Two studies on-going with the scientific community for assessment for assessment of the feasibility of operational implementation of state of the art retrievals
Artificial Neural Net, Crevoisier et al., LMD
Optimal Estimation Method, Siddans et al., RAL
EPS-SG IAS & Sentinel-5
CH4 products envisaged

## Slide 4
EUMETSAT Polar System Second Generation (EPS-SG):
IAS (IASI-NG) (~2020)

## Slide 5: IASI-NG Instrument
    IASI-NG will be jointly provided by CNES and EUMETSAT as a CFI instrument
    IASI-NG will be an interferometer-type instrument with performance improved by a factor of 4 with respect to the previous generation
    Covering the spectral range 645 cm-1 (15.5 µm) and 2760 cm-1 (3.6 µm), with 4 different spectral bands/detectors, and a spectral resolution of 0.25 cm-1 sampled at 0.125 cm-1
    New optical concept, based on a Mertz interferometer (with self-apodization compensation)
    Internal imager allows for the very accurate co-registration with Metimage
    On-board spectral and radiometric calibration sources

## Slide 6: Committed List of Products
Infra-red Atmospheric Sounding (IAS) Processing Chain |  |  |  |  |  | 
Product | Dev | Continuity | Coverage | Resolution | NRT | Accuracy
Temperature profile | C | YES | global regional | Pixel | YES | LT, MT: 0.8 K UT, S: 1.2 K
Water vapour profile | C | YES | global regional | Pixel | YES | LT: 5 % MT, UT: 7 % S: 20 %
Cloud detection and fractional coverage from VII and IAS | C | YES | global regional | IAS Pixel | YES | 10 %
Cloud top phase | C | YES | global regional | Cloudy pixel | YES | 10 %
Cloud top height /pressure | C | YES | global regional | Cloudy pixel | YES | 0.2 km
Cloud drop effective radius at cloud top (by-product) | C | NO | global regional | Cloudy pixel | YES | 5 µm
Surface temperature (sea) | C | YES | global regional | Clear pixel | YES | 0.3 K
Surface temperature (land, ice) | C | YES | global regional | Clear pixel | YES | 1 K
Water vapour total column from IAS and MWS | C | YES | global regional | MWS Pixel | YES | 5 %
Cloud liquid water path from MWS and IAS | C | YES | global regional | Pixel | YES | 5 %
Volcanic ash | C | NO | global regional | Clear pixel | YES | detection

## Slide 7: Committed List of Products
Infra-red Atmospheric Sounding (IAS) Processing Chain |  |  |  |  |  | 
Product | Dev | Continuity | Coverage | Resolution | NRT | Accuracy
Carbon monoxide profile | O3M | NO | global regional | Clear or partly cloudy pixel | YES | 3 km LT: 30 % MT: 25 % HT, S: 20 %
Carbon monoxide partial column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | 10 %
Methane partial column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | LT: 12 % S: 30 %
Nitric acid partial column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | 20 %
Nitrous oxide total column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | 10 %
Ammonia total column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | 20 %
Ozone profile | O3M | YES | global regional | Clear or partly cloudy pixel | YES | LT,MT, UT: 20 % S: 10 %
Ozone total column | O3M | YES | global regional | Clear or partly cloudy pixel | YES | 5 %
Sulphur dioxide total column | O3M | NO | global regional | Clear or partly cloudy pixel | YES | 50 %

## Slide 8
MTG-S1( 2021) and MTG-S2
Infrared Sounder (IRS)

## Slide 9: The IRS mission and instrument
    The IRS products are vertical temperature and humidity profiles (L2) over the Earth disc, with 30 minutes refresh rate over Europe.
    They are obtained by processing spectral (L1) data.
    The IRS is an imaging spectrometer, based on a Michelson interferometer.
    2000 spectral samples for every spatial sample.
The IRS is designed and built by Kayser-Threde (Munich).
LWIR
MWIR

## Slide 10: IRS performance parameters and budgets
    Main performance parameters (L1):
      Spatial resolution: 4 km
      split in two non contiguous bands:
        680 cm-1 to 1210 cm-1 (LWIR band)
        1600 cm-1 to 2250 cm-1 (MWIR band)
      Spectral resolution: 0.625 cm-1
      NEdT: around 0.2 K
      Repeat cycle:
        Earth disk: 1 hour
        Europe: 30 min

## Slide 11: List of IRS L2 data products
L2 data product description
Atmospheric temperature profile
Atmospheric humidity profile
Surface state product: Surface properties (temperature, emissivity, pressure)
L2 data products in NetCDF-4