## Slide 1: Status of ACC Air Quality Constellation Activities
Jay Al-Saadi (NASA)
Kelly Chance (SAO)
Yasuko Kasai (NICT)
Jhoon Kim (Yonsei University)
Pepijn Veefkind (KNMI)
Ben Veihelmann (ESA)
Claus Zehner (ESA)
Atmospheric Composition Constellation Meeting ACC-10
College Park, MD, 4-5 June 2014

## Slide 2: Geostationary Air Quality Constellation Coordination: Background (circa 2009-2011)
Geostationary orbit provides “continuous” observations (many times per day) but a single geostationary satellite can view only a portion of the globe.
Several countries and space agencies are planning to launch geostationary satellites in the 2018-2019 time frame to obtain air quality measurements.
NASA GEO-CAPE NOAA GOES R/S
ESA, Eumetsat Sentinel-4 + MTG
KARI, ME GEMS JAXA GMAP-ASIA
http://www.ceos.org/images/ACC/AC_Geo_Position_Paper_v4.pdf
These missions share common objectives yet individually are restricted to regional relevance. Harmonization through a constellation framework will provide a global perspective otherwise impossible to achieve.
Such an integrated global observing system for atmospheric composition is key to abatement strategies for air quality as laid down in various international protocols and conventions (IGACO, GEO, WMO GAW).

## Slide 3: The Sentinel Missions for Copernicus Atmosphere Services
GEOstationary (GEO)
Hourly revisit time over Europe
Mainly air quality
Diurnal cycle of tropospheric composition
Sentinel-4 (on MTG-S)
Low Earth Orbit (LEO)
Daily revisit time global coverage
Climate, air quality, ozone & UV
Tropospheric & stratospheric composition
Sentinel-5 (on MetOp-SG)
Sentinel-5 Precursor (dedicated platform)

## Slide 4: Global pollution monitoring constellation: Tropospheric chemistry missions funded for launch 2016–2021
Sentinel-5P
(once per day)
TEMPO
(hourly)
Sentinel-4
(hourly)
GEMS
(hourly)
Courtesy Jhoon Kim,
Andreas Richter
Policy-relevant science and environmental services enabled by common observations
Improved emissions, at common confidence levels, over industrialized Northern Hemisphere
Improved air quality forecasts and assimilation systems
Improved assessment, e.g., observations to support United Nations Convention on Long Range Transboundary Air Pollution

## Slide 5: Funded tropospheric chemistry mission parameters (as of 5/2014)
 | Europe Sentinel 4 | USA TEMPO | Korea GEMS | Europe Sentinel 5 Precursor TROPOMI
Orbit | Geostationary | Geostationary | Geostationary | Low-Earth
Domain | Europe and surrounding | North America | Asia-Pacific | Global
Revisit | 1 hour | 1 hour | 1 hour | 1 day
Status | Detailed Design, Phase C | Instrument PDR July 2014 | Instrument PDR complete | Instrument delivery 2015
Launch | 2021 (Flight Acceptance Review first instrument) | No earlier than 11/2018 | 2018 | Early 2016
Payload | UV-Vis-NIR 305-500, 750-775 nm | UV-Vis 290-490, 540-740 nm | UV-Vis 300-500 nm | UV-Vis-NIR-SWIR 270-500, 675-775, 2305-2385 nm
Products | O3, NO2, SO2, HCHO, AAI, AOD, height-resolved aerosol | O3, trop. O3, 0-2km O3, NO2, HCHO, SO2, CHOCHO, AOD, AAI | O3, NO2, SO2, HCHO, AOD | O3, NO2, SO2, HCHO, AAI, AOD, height-resolved aerosol, CO, CH4
Spatial Sampling | 8 km x 8 km at 45N | 2.1 km N/S x 4.7 km E/W @35N | 3.5 km N/S x 8 km E/W @38N | 7 km x 7 km nadir
Nominal product resolution | 8.9 km N/S x 11.7 km E/W @40N | 8.4 km N/S x 4.7 km E/W or better @35N (with 100W orbit) | 7 km N/S x 8 km E/W @38N (gas), 3.5 km N/S x 8 km E/W @38N (aerosol) | 7 km x 7 km nadir
Notes | Two instruments in sequence on MTG-S; use TIR sounder on MTG-S (expected sensitivity to O3 and CO). Synergy with imager on MTG-I w.r.t. aerosol and clouds. | GEO-CAPE precursor or initial component of GEO-CAPE. Synergy with GOES-R/S ABI w.r.t. aerosol and clouds. | Synergy with AMI and GOCI-2 instruments w.r.t. aerosol and clouds. | In formation with S-NPP for synergy w.r.t. clouds and O3.
Notes: The limitation of GEO view is the lack of a global perspective
This can be mitigated through international cooperation to form a constellation from GEO
Timing and payloads demonstrate that threshold capability is ready
N. America-Europe-Asia covers the three primary economic/population/emissions regions

## Slide 12: Overview and Status of GEMS
Jhoon Kim,
GEMS Team
Yonsei University

## Slide 13: GEO-KOMPSAT-2B GEMS (Geostationary Environment Monitoring Spectrometer)
Launch: 2018 (planned)
GEMS Specification
 | Specification
Lifetime | 10 yrs
Spatial coverage | 5000 km x 5000 km (5o S ~ 45o N)
Longitude | 128.2 E
Duty cycle | 8 times / 1 day
Spatial resolution | 7 km (NS) x 8 km (EW) @ Seoul (gas) 3.5 km (NS) x 8 km (EW) (aerosol )
Spectral coverage | 300 – 500 nm
Spectral resolution | 0.6 nm (3 samples)
Products | O3, NO2, SO2, HCHO, aerosol, cloud, surface reflectance
2A Sat. : AMI
2B Sat. : GEMS, GOCI-2
(Twin Satellite)

## Slide 14: GEMS Design
Step-and-stare UV-Visible imaging spectrometer scanning at least 8 x per day in 30 minutes
Daily solar and dark calibration
Images coadded at each position + mirror move back < 30 minutes
Scanning Schmidt telescope and Offner spectrometer
Diffusers for on-orbit solar calibration and onboard LED light source
2-axis scan mechanism with gyro feed capability
Redundant electronics for 10-year lifetime

## Slide 15: Projected FOV & GSD NS GSD @ Seoul : 7.0km
Projected FOV
Region of interest
For clear sector method
Normal operation

## Slide 16: Status of GEMS Mission
GEO-KOMPSAT-2 Program
  SRR in Apr., 2012; SDR in Feb. 2014
Budget
  GEMS Program passed Mid-term review on Dec. 4, 2013, and now is in Main Phase till launch. (* Launch : Dec., 2018)
Prime Contractor
  Selection of main contractor for GEMS Joint Development with KARI on May 13th, 2013
  (International Contractor: Ball Aerospace & Technologies Corp.)
  * AMI contract with ITT; GOCI-2 contract with Astrium
GEMS Design reviews
  SDR finished in October 28-29, 2013
  PDR finished in March, 2014
  CDR planned in 2015
Changes in Environment
  Air quality forecast in operation since 2013 by NIER/ME
     GEMS to be an operational sat. (e.g. data assimilation of model with sat. data)
  CEOS ACC for GEO AQ (TEMPO over N. America and S-4 over Europe)
  ‘KORUS-AQ’ airborne campaign planned in 2016 (airborne GEMS considered)

## Slide 17: GEMS Summary
GEMS is now in main phase, after PDR in 2014 and planned to be launched in Dec., 2018.
GEMS is expected to provide information on trace gas and aerosol with their precursors in high spatial and temporal resolution
  O3 NO2 HCHO SO2 AOD/AI/AEH, (possibly CHOCHO, BrO)
  Clouds, surface reflectance, UV radiation.
The predicted performance of trace gases from the initial design of GEMS satisfies the product accuracy requirements of NO2, HCHO, O3. Meanwhile, the estimated accuracy of SO2 product requires the increase of SNR by spatial coadding (lowering resolution), longer observation time, or reduced E-W scan range (or more frequent operation).
The data assimilation between CTM and GEMS data is important with the air quality forecast in operation.
Collaboration with Team of TROPOMI, Sentinel-4 & TEMPO is desirable in calibration, algorithm development and application.