## Slide 1
The Support to Aviation Control Service (SACS)
Atmospheric Composition Constellation Meeting
Washington, June 2014
N. Theys (1), H. Brenot (1), L. Clarisse (2), J. van Gent (1), R. van der A(3), M. Van Roozendael(1), P.-F. Coheur (2), D. Hurtmans (2), C. Clerbaux (2,4), K. Stebel(5) , F. Prata(5), C. Zehner (6)
(1) BIRA-IASB, Brussels, Belgium.
(2) ULB, Brussels, Belgium.
(3) KNMI, De Bilt, The Netherlands.
(4) LATMOS-IPSL, Paris, France.
(5) NILU, Kjeller, Norway
(6) ESA-ESRIN, Frascati, Italy.

## Slide 2
Overview
SACS: system overview, satellite data
Warning system for volcanic plumes of
SO2 and/or ash
Future improvements of SACS
Link with the VAST project (ESA)
Ash plume from Eyjafjallajökull

## Slide 3
The objective of SACS is –with respect to volcanic SO2 and ash.:
Deliver in near-real time space observations
Provide near-real time notifications (email and webbased)
Provide access to archive data
>> Useful for operational and research applications
SACS is an ESA project
Hosted by BIRA-IASB
Number of subscribed users : 215
Volcanic Ash Advisory Centres
Volcanic Observatories
Research and Meteorological institutions,
Universities, scientists
Flight captains
Airlines Companies
VAST project

## Slide 4
Support to Aviation Control Service (SACS)
SACS first phase
(TEMIS, PROMOTE)
SACS second phase
SACS second phase
SCIAMACHY, OMI, GOME-2
UV-visible
IASI, AIRS
Infrared
SACS first phase
SCIAMACHY, OMI, GOME-2
UV-visible sat. sounders
2006
2009
2010
2012
April 2012:
Multi-sensors SO2 warning system
2014
SACS2
October 2013:
Multi-sensors ash warning system
SACS2
SCIAMACHY, OMI, GOME-2 (A&B)
IASI (A&B), MODIS
Improved SO2 and ash products

## Slide 5
Constellation of satellite instruments

## Slide 6
Satellite data: research and operational products
Instruments | Data type | Data availability | Overpass time | Resol. (km²) | Participants | Data products
SCIAMACHY (ENVISAT) | UV/visible | 2004/04  2012/04 | 10:00 | 30x60 | BIRA KNMI | SO2 vertical columns absorbing aerosol index
GOME-2 (MetOp-A) | UV/visible | 2007/01 present | 09:30 | 40x80 /40x40 | DLR BIRA KNMI | SO2 vertical columns SO2 plume height absorbing aerosol index
GOME-2 (MetOp-B) | UV/visible | 2012/12 present | 09:00 | 40x80 | DLR KNMI | SO2 vertical columns absorbing aerosol index
OMI (Aura) | UV/visible | 2004/09 present | 13:30 | 13x24 | KNMI | SO2 vertical columns absorbing aerosol index
IASI (MetOp-A) | Infrared | 2007/10 present | 09:30 21:30 | 12x12 | ULB | SO2 index and columns ash indicator
IASI (MetOp-B) | Infrared | 2013/01 present | 09:00 21:00 | 12x12 | ULB | SO2 index and columns ash indicator
AIRS (Aqua) | Infrared | 2002/09 present | 01:30 13:30 | 15x15 | NILU ULB | SO2 columns ash indicator
Near-real time  delay: 1-4 hours

## Slide 7
Grímsvötn eruption May 2011 (Iceland)

## Slide 8
Aerosol/Ash products
Grímsvötn eruption May 2011 (Iceland)

## Slide 9
http://sacs.aeronomie.be
period
sounder
data
region

## Slide 10
Simultaneous eruptions of Nabro and Puyehue
Warning system

## Slide 11
Eruption of Eyjafjallajoküll
Warning system
SO2
Ash

## Slide 12
System optimized to avoid false notifications (e.g., anthropogenic SO2) – success rate: >95%
Main features
One e-mail is sent per 12 hours and per 30°x30° predefined region (first instrument to detect SO2).
Multi-sensors SO2 notification system
After a notification, all other warnings (confirmation during the next 12h) are available
through the webpage.
SO2-based warning system.
Multi-sensors SO2 warning system

## Slide 13
SO2 notification service
Bezymianny eruption
November 2012
Multi-sensors SO2 warning system

## Slide 14
First overpass : AIRS, 1h46 after the start of the eruption.
SACS e-mail warning: 4h23 after the start of the eruption.
Recent warning: Paluweh eruption

## Slide 15
Selective detection of ash
Absorbing aerosol index products are sensitive to all types of absorbing aerosols  not to be used in an alert system

## Slide 16
Selective detection of ash
High-spectral resolution measurements at TIR wavelengths allows the ash absorption to be discriminated from other absorbing aerosols
Classification of spectral signatures
Clarisse et al., ACP, 2013

## Slide 17
  New notification system selective for the detection of ash
  using IASI-A, IASI-B and AIRS
Operationnal since October 2013
Extensive tests on historical data; no major eruptions missed.
false notifications ~1% and misses (small puffs) <1% (but compromise on sensitivity)
Multi-sensors ash warning system

## Slide 18
Recent event: Kliuchevskoi eruption

## Slide 19
First overpass : AIRS, 1h11 after the start of the eruption.
SACS notification send: 3h10 after the start of the eruption.
Recent notification: Kelut eruption

## Slide 20
Jetstar 114: flight Perth-Jakarta
.
Jakarta
.
Perth
19:00 UTC  02:00 UTC

## Slide 21
Warning system

## Slide 22
Warning system
SO2
Ash

## Slide 23
Recent eruption: Sangeang api
Ash plume height :
15-20 km

## Slide 24
Future improvements of SACS
Continuous development of the warning system
2. Improvement of the ash monitoring capability of SACS
3. Include new sensors, e.g. OMPS and CrIS onboard Suomi-NPP
4. NRT retrievals of SO2 plume height
Clarisse et al., ACP, 2014
Nabro eruption, June 2011

## Slide 25: Volcanic Ash Strategic-initiative Team
The project has been established to improve the quality and use of EO based observations in numerical atmospheric dispersion models for the purpose of assisting global aviation.
VAST - http://vast.nilu.no/ is coordinated by F. Prata (NILU)

## Slide 26
Establishment of an operational LIDAR network in Ireland (national co-funding)
Establishment of a database for historic eruptions (satellite, ground-based, airborne, modeling data), include data from SACS and SMASH
Development of an operational demonstration volcanic ash forecasting service (FLEXPART open source code)
Improve the quality of EO data for volcanic ash monitoring;
focus on SEVIRI (NRT - fred.nilu.no/sat), AIRS and AATSR (historical cases)
User workshop and update of existing user requirements
Improved dispersion modelling (FLEXPART, SILAM and WRF-Chem, Ensemble) and eruption source terms (inverse modeling)

## Slide 27
More information
Support to Aviation Control Service
http://sacs.aeronomie.be
theys@aeronomie.be or sacs@aeronomie.be
Paper on SACS: Brenot et al., in Nat. Hazards Earth Syst. Sci.