## Slide 1: MEthane Remote sensing LIdar missioN MERLIN Mission Overview CEOS Atmospheric Composition Constellation (ACC) 4. – 5. June 2014 College Park, MD, United States D. Loyola (MF-ATP) B. Millet (CNES), M. Alpers (DLR Space Admin.) P. Flamant (CNRS-LMD), G. Ehret (DLR-IPA)

## Slide 2
Overarching Scientific Goal
A better understanding of the Global Methane Cycle and the nature of the processes which govern the exchange of methane between biosphere and atmosphere.
Mission Objectives
Primary
  High accurate space-borne measurements of the spatial and temporal variability of atmospheric CH4 for determination of CH4 fluxes (emissions) on the Earth surface
Secondary (tentatively)
Surface properties & Vegetation
Contribution to cloud/aerosol data base
Method
IPDA-Lidar for XCH4
  Integrated-Path Differential Absorption (IPDA) Lidar in the near IR using pulsed laser transmitter and rang-gated receiver in nadir-viewing mode
Fluxes
  Inverse models converting XCH4 into CH4 fluxes (emissions) & errors

## Slide 3
Measurement Precision & Bias on Methane Column-Weighted Dry-Air Mixing Ratio or (XCH4)
MERLIN
design goal
Notes: This table shows the Observational Requirements for MERLIN which have been derived by the SAG.
It’s important to note that MERLIN is a Micro-Sat Class mission with limited resources in terms of laser average power and telescope receiver area which basically limits SNR and with that the measurement precision.
The envisaged precision of 1% , however, would be sufficient for flux inversion calculations on a spatial scale of 500 km on a monthly basis if the observations on a 50 km scale are uncorrelated and can be aggregated as input for the flux inversion model.
This methode requires a very low systematic error which should be on order of magnitude smaller than the that of the precision value.
Compared to passive missions such high accuracy of better than 3 ppb (or >0.2% on the 500 km length scale for the integrated fluxes is outstanding and therefore justifies such a mission like MERLIN

## Slide 4
  MERLIN Measurement Method:
  Integrated-Path Differential Absorption (IPDA) Lidar
Methane line spectrum

## Slide 5: MERLIN system architecture
Payload Operation Centre
Earth Terminals
Command & Control
Centre
Payload Data
Processing & Delivery
Exchange
Command
Telemetry
Launcher
Users
Scientific Processing
Expertise
Exchange
Payload
Expertise
Payload
Commanding & Monitoring
Control Ground Segment
Payload Ground Segment
Satellite
(Platform – Payload)
Payload Data
Delivery
Numerical System Simulator

## Slide 6: MERLIN main parameters
Radiators
Star Tracker
Optical Head
Laser Emitter
Laser Transmission
Telescope
Receiving
Telescope
Satellite platform: MYRIADE Evolutions
  Satellite mass: 400 kg
    Payload mass allocation: 119 kg
    Satellite power: >400 W
    Payload power allocation: 150 W
  Satellite GPS: 2 sensors
  Satellite star tracker: 2 opt. heads
Payload: Methane IPDA LIDAR
  XCH4 absorption line: 1.645 mm
  Laser emitter type: Nd:YAG pumped OPO
  OPO pulse energy: 9 mJ
  Laser pulse repetition
  frequency PRF: 20 Hz
  Receiving telescope size: 69 cm
  Detector: APD pin diode
Orbit: Sun synchr. polar LEO
  LTAN: 06:00h or 18:00h
  Height: 500 km

## Slide 7: MERLIN mission status
  Development status: Phase B
  SRR successfully passed in Nov. 2013
  Satellite PDR: Intended for June 2015
  Payload PDR: Intended for September 2015
  Launch:
    Intended launcher: SOYUZ (ASAP, inner position)
    Intended launch location: Kourou
    Intended launch date: end of 2019
  Contacts:
    Bruno Millet (CNES): Bruno.Millet@cnes.fr
    Matthias Alpers (DLR): Matthias.Alpers@dlr.de