## Slide 1: The NASA Orbiting Carbon Observatory – 2 (OCO-2) Mission Status
David Crisp, OCO-2 Science Team Leader
and the OCO-2 Science Team
Jet Propulsion Laboratory, California Institute of Technology
June 2014
Copyright 2014 California Institute of Technology. Government sponsorship acknowledged.
10th CEOS Atmospheric Composition Constellation Meeting (ACC-10)

## Slide 2: Global Measurements from Space are Essential for Monitoring the Climate
To understand and predict our changing climate, we must:
  Monitor human activities that can affect our environment
  Understand how natural processes will respond to these changes
We can only manage what we can measure
High resolution, space-based measurements are needed to discriminate its sources & sinks.
NOAA/ESRL
Precise ground-based measurements describe global CO2 trends.

## Slide 3: The Pioneers: GOSAT and OCO
GOSAT launched successfully on 23 January 2009
OCO was lost a month later when its launch system failed
24 Feb 2009
Space based measurements provide new tools for measuring CO2
Notes: The two missions eventually had very similar launch dates. GOSAT was successfully launched in January, 2009.
One month later, we tried to launch OCO, but the launch vehicle malfunctioned, and the spacecraft was lost.

## Slide 4: Processing the Data from OCO-2: The ACOS/GOSAT Collaboration
Notes: This slide has 3 time steps illustrating the primary areas of collaboration between ACOS and GOSAT.
Before the sun rose on the day OCO was lost, Hamazaki-san invited the OCO science team to join the GOSAT analysis effort. NASA responded by reformulating the OCO science team as the Atmospheric CO2 Observations from Space (ACOS) team, and the collaboration continued. The primary areas of focus of this collaboration included vicarious calibration activities in Railroad Valley, Nevada, Retrieval algorithm development, and Data product validation and screening. A tremendous amount was learned in all three areas.

## Slide 5: Producing Global Estimates of CO2: The ACOS GOSAT B3.4 XCO2 Product
400
380
Jul 2009
Aug 2009
Sep 2009
Oct 2009
Nov2009
Dec2009
Jan 2010
Feb 2010
Mar 2010
Apr 2010
May 2010
Jun 2010
Notes: We are also deriving global maps of CO2, and providing them to the global science community, along side the product produced by our Japanese partners. Both teams have benefited from this collaboration.

## Slide 6: The Next Step - The NASA Orbiting Carbon Observatory-2 (OCO-2) Mission

## Slide 7: The OCO-2 Mission Architecture
Data Transmitted to NASA NEN and SN
Delta-II Launch Vehicle
Dedicated Spacecraft Bus
3-Channel Grating Spectrometer
Data Product Generation
Formation Flying in the A-Train Constellation
Notes: The original plan was to build a “carbon copy” of OCO, and have it ready for launch by February 2013
Like OCO, OCO-2 carried a single instrument on a dedicated spacecraft bus, that was to be carried into space on a dedicated launch vehicle.
It was to fly at the head of “Afternoon Constellation”, a series of satellites that flies in formation at a mean altitude of 705 km (440 miles) above the Earth.
It was to transmit it data to a ground station in Alaska, and were supposed to process these data at the Jet Propulsion Laboratory in Pasadena, California, and deliver them to NASA, for distribution to the science community.

## Slide 8: The OCO Instrument – Optimized for Sensitivity
3 imaging grating spectrometers record reflected sunlight at high spectral resolution
Resolving Power 17,000 - 20,000
High Signal-to-Noise Ratio
Collects 24 soundings per second while over the sunlit hemisphere (1 million soundings per day)
O2 A-Band
CO2 1.61m Band
CO2 2.06 m Band
Notes: The instrument is a 3-channel, imaging grating spectrometer
It is designed to record high resolution spectra of reflected sunlight in two near infrared carbon dioxide bands, and in the molecular oxygen “A-band” at 760 nm.
This instrument records 24 sounding each second, producing almost 1 million observations of CO2 over the sunlit hemisphere of Earth each day. This almost 100 times as much data as GOSAT collects.

## Slide 9: Verifying End-to-End Instrument Performance during Pre-Flight testing
Observations of the sun with the flight instrument taken during TVAC tests provide an end-to-end verification of the instrument performance.
1.6 m CO2
21 April 2012
TCCON
FTS
OCO-2
FTS
TV Chamber
with
Flight Instrument
Heliostat
Notes: The pre-launch instrument testing included direct observations of carbon dioxide and molecular oxygen absorption in the Earth’s atmosphere, like those to be collected in space.
We used a precise ground based instrument as a reference in these experiments. The two instruments produced very similar estimates of atmospheric carbon dioxide.
In fact, on 20 April 2012, we made simultaneous observations of atmospheric CO2 using the OCO-2 instrument, the reference instrument, and the GOSAT instrument, which was flying over Los Angeles on that day.

## Slide 10
Observatory Integration & Test Activities
Notes: The instrument was then delivered to Orbital Sciences, in Gilbert Arizona, where it was integrated with the spacecraft. The entire system was then tested as a unit.

## Slide 11: On Track for 01 July 2014 Launch
Credit: Steve Greenberg, JPL
The Mobile Service Tower [left] and Fixed Umbilical Tower [right] at SLC-2W (Space Launch Complex 2 West), Vandenberg Air Force Base, CA
Credit: NASA
The business end of one of three
Series 40 Graphite Epoxy Motors that will more than double the total thrust of the vehicle to 0.5M lbf at launch
Credit: NASA

## Slide 12: Post-Launch Critical Events
Fairing Ejection
Separation
Solar Array Deployment
Sun Acquisition

## Slide 13: Nominal Early Operations Schedule
T + 45d – Nominal End of In Orbit Checkout (IOC)
T + 135d – First Public Release of L1b data (calibrated spectra)
T+0d
T + 30d
T + 60d
T + 90d
Assent
Insertion Orbit Engineering Checkout
T + 120d
First update to dark subtraction (no temperature corrections)
First update to gain degradation (weather over Railroad Valley permitting)
First Temperature corrected dark subtraction
First Update to SNR model
First Update to Dispersion
First Update to Pointing Vectors
First update to bad pixel map in flight
Nominal data collection (i.e. 16 days nadir / 16 days glint)
Operational Orbit Engineering Checkout

## Slide 14: Inserting Into the A-Train
OCO-2 will fly at the head of the 705-km Afternoon Constellation (A-Train), but has changed it flight path to share the ground track with CloudSat and CALIPSO, which is 217 km East of the AQUA (WRS-2 Standard) track.
Notes: Once in orbit, we will join the “Afternoon Constellation” or “A-Train” as it is called.
This constellation currently includes 6 satellites that measure a range of whether and climate properties, including atmospheric and surface temperatures, surface cover, clouds, aerosols (hazes), and a stratospheric gases, including ozone.

## Slide 15: On-orbit Calibration Operations
Routine Calibration (every orbit)
Solar Calibration
  Observe sun through a solar diffuser
Lamp Calibration
  Observe illuminated diffuse target
Dark/Bias calibration: Lamps off
Special Calibration Activities
Solar Doppler calibration (semi-annual)
  Observe sun through entire daylight orbit to calibrate ILS
Lunar calibration required for absolute and relative pointing (monthly)
  Verifies instrument-star tracker alignment
  Radiometric calibration check
Star Tracker FOV
Instrument
Boresight
q
Lunar Calibration
CAL(Solar)
Science
Routine
Calibration

## Slide 16: Routine Operations: Sampling the Earth
The OCO-2 Orbit:
  705 km altitude
  98.2 inclination
  16-day ground track repeat
  1:30 PM Equator Crossing time
  98.8 minute orbit period
    14.57 Orbits/day
Latitude Coverage
  Nadir: +85o Solar zenith angle
  Glint: +81o Solar zenith angle
Resolution
  ~25 longitude offset between consecutive orbits
  1.5 longitude offset between orbit tracks after16-days
OCO-2 will collect about 1 million soundings each day along a narrow track.
OCO-2 is a SAMPLING system, not a MAPPING system.

## Slide 17: The OCO-2 Retrieval Algorithm
Instrument Model
Spectral + Polarization
Forward Radiative Transfer Model
Spectra + Jacobians
Inverse Model
Compare obs. & simulated spectra
Update State Vector
Final State
Diagnostics
converged
not converged
Gas Cross Sections
Cloud & Aerosol Optical Properties
Simulated Spectrum
Spectral Residual
Apriori + Covariance
State Vector First Guess
Altitude
Aerosol
Mixing Ratio
CO2
aer
Temp.
T
Altitude
aer
Aerosol
Mixing Ratio
CO2
T
Temp.
Viewing geometry
Full-res Spectrum
Jacobians
GOSAT Data have provided a critical validation of the OCO-2 Algorithm

## Slide 18: Conclusions
OCO-2 is scheduled to launch from Vandenberg Air Force Base, at 2:56:44 AM PDT on 1 July 2014
  Preparations for the OCO-2 launch are progressing on schedule
  Next step: Observatory is scheduled for installation on the launch vehicle on 10 June
A launch ready version of the OCO-2 Retrieval Algorithm has been delivered and is being tested using GOSAT data
  The ACOS/GOSAT collaboration provided valuable insight and a critical validation of the OCO-2 algorithm
If all goes as planned, we could start delivering
  Level 1B products as early as late November 2014
  Level 2 products as early as February 2015

## Slide 19: Thank You for Your Attention Questions?