## Slide 1: “NOAA NO2 Project Report” S. Kondragunta, C. Trevor Beck, L. E. Flynn NOAA/NESDIS Center for Satellite Applications and Research
<number>

## Slide 2: Summary of Accomplishments
<number>
CEOS ACC NO2 project facilitated a multi institutional collaboration
  NOAA is the recipient of GOME-2 L1B files from EUMETSAT (NOAA-EUMETSAT Initial Joint Polar Satellite System Agreement)
  OMI NO2 algorithms successfully adapted for GOME-2 by NOAA
  EPA is working with NASA to establish ground monitoring station to provide routine measurements of NO2 for GOME-2 and OMI validation
Primary Applications
  EPA AIRNOW system being enhanced with routine ingestion of GOME-2 and OMI NO2 data for air quality forecasting applications (NASA funded activity)
  NOAA National Weather Service using the data offline to investigate events when operational ozone forecast is a bust
  Extending the trend analysis for NOx emissions
Data Availability
  Near real time and historic data processed with the same algorithm as OMI, 2007 - present

## Slide 3: GOME-2 NO2 Operational Product
GOME-2 Product is available to users in pre-operational mode. Product was to become operational in March 2010 but IT system freeze for security reasons delayed the plan.
  Data access via http://www.osdpd.noaa.gov
Slant columns agree well with OMI based on Simultaneous Nadir Overpass (SNO) analysis (~2%)
Tropospheric NO2 retrievals depend on air mass factors (AMF) which are computed using standard profile used by OMI algorithm. Work underway, in collaboration with NASA and Dallhousie university to update this.
Preliminary comparisons with in situ measurements (Data from EPA/NASA-LaRC) shows a low bias in GOME-2 retrievals.

## Slide 4
<number>
July 2007
July 2008
July 2009
Regional trend analysis of OMI NO2 in the U.S. by Ken Pickering extended using GOME-2 for 2009. OMI and GOME-2 data were remapped to 0.25o grid prior to the analysis. Screening of data for bad pixels is identical between the NASA and NOAA software except the native pixel resolution. Diurnal differences not accounted for.
GOME-2
GOME-2

## Slide 5: Summer Seasonal Mean Tropospheric NO2
<number>
GOME-2
OMI
Seasonal Mean
Seasonal Mean (Weekdays)
Seasonal Mean (Weekends)
Seasonal Mean
Seasonal Mean (Weekdays)
Seasonal Mean (Weekends)
Notes: This slide shows seasonal mean tropospheric NO2 as observed by GOME-2 with local time of 10 AM (+/- 20 min)and OMI with a local time of about 1 PM (+/- 20 min). Spatial patterns in observed NO2 between GOME-2 and OMI are similar for weekdays and weekends and combined data. GOME-2 values are higher than OMI in all three cases. However, both satellites show urban source regions well. The difference in NO2 between weekday and weekend is quite remarkable, especially in the northeast.

## Slide 6: Modeled and Measured Diurnal Variation of NO2 in the U.S. Ozone Non-Attainment Areas
<number>
Notes: We wanted to look at the specific diurnal variation in NO2 in the ozone non-attainment regions to see how well the model is capturing the observed diurnal variations. Several factors such as emissions, production/loss mechanisms contribute towards diurnal variation. But the late evening peak is due to loss rate decreasing. These figures show weekday (in red) and weekend (in blue) CMAQ diurnal curves. On top of the curves for their specific observing time periods, GOME-2 and OMI data are overlaid. Square is OMI and closed circle is OMI. Except for the Houston area curves, for the other three locations there is a good agreement between satellite observations and model predictions. As observed in the maps before, Texas NO2 values in the model are higher than observations.

## Slide 7: Observed and Modeled Weekday/Weekend Differnce in Tropospheric NO2
<number>
GOME-2
OMI
CMAQ at 10 LST
CMAQ at 13 LST
Notes: Figures in this slide show weekday/weekend difference in NO2. Top left is for GOME-2, bottom left is for OMI, top right is for CMAQ at 10 LST (GOME-2 time) and bottom right is for CMAQ at 13 LST (OMI time). GOME-2 shows a very large weekday/weekend difference compared to CMAQ. GOME-2 shows differences in the West Virginia, Tennessee, Ohio, and in general the whole mid-western region whereas CMAQ does not really show much of a weekday/weekend difference. OMI also shows weekday/weekend difference in NO2 but not as large as GOME-2. That is because between GOME-2 and OMI observing time period, NO2 values decrease and this is well captured in observations. Again, CMAQ NO2 for this observation time period does not show a big weekday/weekend differences like OMI.

## Slide 8: Ongoing Activities
<number>
Plan to compare GOME-2 NO2 with University of Maryland aircraft data,
NOAA modeling group that looked at the U.S. power plant emissions using OMI/SCIA NO2 data (Kim et al., JGR, 2009) to use GOME-2 NO2 data in assessing WRF-Chem emissions,
Work with NOAA modeling group (Daewon Byun) in using GOME-2 and OMI NO2 data to update model emissions,
As part of EPA AIRNOW project, GOME-2 NO2 to be provided to Dalhousie university (Randal Martin) for analysis and assessment,
NASA (Ken Pickering) to extend OMI trend analysis using GOME-2 NO2 data,
Coordinate with NASA on OMI algorithm updates and changes for GOME-2 implementation,
Work underway to publish GOME-2 NO2 CMAQ comparisons

## Slide 9: Conclusions
<number>
Documentation
  multiple NOAA internal documents on algorithm and code are prepared and available. Report on GOME-2 vs. CMAQ NO2 comparison work is under preparation.
Results
  Demonstrated that NO2 data from two polar-orbiting (GOME-2 and OMI) satellites can be used to evaluate diurnal variation in an air quality model.
  Spatial and temporal patterns observed in GOME-2 and OMI are consistent with our understanding of NO2 chemistry.
  Diurnal variation in observed NO2 consistent with CMAQ model including the non-attainment areas except:
    Texas region and northwest
  Weekday/weekend differences are stronger in observations (both GOME-2 and OMI) compared to CMAQ model.