## Slide 1
The French-German Climate Monitoring Initiative
CH4 Remote Sensing LIDAR Mission

## Slide 2: Overall context
Background for a French-German “Climate Monitoring initiative”
  Development of a joint mission proposal addressing the most important climate questions and to present it to the community on the occasion of COP-15 (Copenhagen, 8.-15.12.09)
Boundary conditions
  Innovative mission, should not be redundant with other European initiative
  High scientific value
  Demonstrator of a potential series of future operational missions (e.g. monitoring of international agreements of GHGs)
  Cost target: total around 120 M€, equally shared
  Launch date objective: planned 2014

## Slide 3: Why is it important to measure atmospheric GHGs for climate predictions?
Global average radiative forcing (RF) in 2005 with respect to 1750 for CO2, CH4, N2O and other important agents and mechanisms, together with the typical geographical extent (spatial scale) of the forcing and the assessed level of scientific understanding.

## Slide 4: Scientific Background
Atmospheric concentration of methane and corresponding radiative forcing over the last 10,000 years taken from ice core and atmospheric samples (red lines)
© IPCC, 2007
CH4 is second most abundant anthropogenic greenhouse gas with a Global Warming Potential (GWP) that is 25 times larger than that of CO2
Strongest change in concentration due to human activities led to doubling of its abundance since pre-industrial times whilst CO2 increased by 30%, "only"
Anthropogenic emissions from gas leaks and incomplete combustions are much more uncertain than man-made emissions of CO2
The climate impact of the reservoir of CH4 in Arctic permafrost is an important unknown in modelling future climate

## Slide 5: Scientific Justification
Increases in Anthropogenic Sources?
Decreased Chemical Loss Rate?
Fires?
Increased Wetland Emissions (including arctic & tropical forest)?
CH4 “Burp” from Permafrost Decomposition, Hydrates or Clathrates? (time bomb is starting to go off)

## Slide 6: Research Objectives and Challenges
  Global carbon cycle and climate change
  The F-G mission will measure the spatial and temporal gradients of atmospheric CH4 with high precision and unprecedented accuracy to constrain emissions from anthropogenic and natural sources significantly better than with the current observational network
  Kyoto protocol and emission inventories
  The mission will contribute to an independent verification of the national emission inventory with respect to methane as formulated in the Kyoto Protocol

## Slide 7: Observational Method: Determination of CH4 fluxes by DIAL* Measurements & Inverse Modelling
Result: True regional CH4 fluxes through minimizing the distance between measurement and simulation
DIAL measurement of CH4
Global distribution of CH4
Simulated concentrations using a priori CH4 fluxes
Forward simulation
Inverse modelling
comparison between measurement and model
*DIAL = Differential Absorption Lidar

## Slide 8: Mission Uniqueness: Breakthrough in Data Quality
Active instrument much less sensitive to biases than passive instruments
pulsed DIAL permits to distinguish between the contribution from surface and atmospheric scattering layers
allows to sound in cloud holes and through thin cirrus layers
enables measurements at day and night time (high latitude coverage)
F.-M. Breon (pers. Comm)
GOSAT
A-SCOPE
Scattering
layer
SPACE-CH4
cloudy boundary layer
A-SCOPE
MERLIN

## Slide 9: Mission Architecture Overview
Mission
Elements
Flight Operations Segment
Flight Operation Control Centre
Payload Data Ground Segment:
Data Acquisition Station
Processing and Archiving Element
Ancillary Data :
Numerical Weather Prediction (NWP) Centres
Cal / Val measurements, Airborne Campaigns
GROUND SEGMENT
USER SEGMENT:
Climate Modelling/Research Centres
LAUNCHER
SUBJECT:
Column-weighted dry air mixing ratio of CH4
Vegetation canopy height Cloud boundaries
Latitude range ±80°
SPACE SEGMENT:
Platform MYRIADE
Payload CH4 DIAL
3 year lifetime
ORBIT:
Sun-Synchronous
450-650 km, LTDN tbd (not critical
repeat cycle tbd (not critical)

## Slide 10: User Communities interested in CH4 data
Scientific Programmes
GCOS, WCRP, and IGBP
Organizations
France: IPSL = LMD, LSCE, LATMOS (Climate study, Tropospheric Chemistry, Inverse Modelling, Assimilation, + ONERA and others
Germany: DLR (Climate study, Tropospheric Chemistry), MPI für Biogeochemie (Jena), Carbon Cycle modelling; University (Jena), Atmosphere/Biosphere Interaction; MPI für Chemie (Mainz), Fires&Tropospheric Chemistry; Alfred Wegener Institute (Kiel), Permafrost; IFM-GEOMAR (Kiel) Gas Hydrates and others
EU: ECMWF (Reading), data assimilation; EC-JRC (Ispra, Italien), Inverse Modelling, Univ. Utrecht (Netherlands), Inverse Modelling
Global: NASA-GSFC-GMAO (USA), Assimilation & Inverse Modelling; Harvard Univ. (USA), Assimilation & Inverse Modelling; NOAA (USA), Carbon Cycle modelling; NIES (Japan), Inverse Modeling
User Readiness
Very high. Inverse modelling methods are already developed for the current missions SCIAMACHY, AIRS, IASI, and GOSAT

## Slide 11: Technical heritage
Large number of mission elements are space qualified
The mission will benefit from development of
  Complete Airborne Lidar CHARM-F, kick-off Oct’09
  EQM of Laser-Transmitter (most critical item), kick-off Nov’09
MYRIADE platform space proven, e.g. Demeter, Parasol
Joint heritage by common studies on Wind Lidar projects (ADM-Aeolus, Airborne WIND)
 Due to the technical heritage and the joint preparatory work the mission can be realised in a short timeframe and with low budget

## Slide 12: Technical Summary
Mass: 80kg Instrument + 100kg Platform = 180kg
Lifetime: 3 years
Launch date: planned 2014
Launcher: VEGA as baseline, if qualification and reliability proven in time (backup tbd)
Platform: MYRIADE
Instrument: CH4 DiAL, pressurized N:YAG pumped OPO
Orbit: 450-650km
Power: 60-80W
Data rate: 300kBps
Dimension: 60x60x80 cm3
Products: column integrated CH4, Canopy height, Cloud boundaries

## Slide 13: Programmatic Summary
DLR provides CH4 Lidar instrument, CNES provides the platform (and its control centre)
Overall mission cost estimate: ~120 Mio. € (w/o science activities), equally shared
Planned launch date: 2014
Joint agency management and science teams
Next step:
Phase 0/A to consolidate feasibility

## Slide 14: Conclusion
The French-German CH4 mission will be worldwide the first active optical greenhouse gas monitoring instrument in space
It will contribute to verify the anthropogenic methane emissions which are banned by the Kyoto Protocol
It will pave the way to a new generation of active optical sensors with a large application potential within the well established Global Climate Observing System (GCOS) from WMO
Active optical instruments like the CH4 mission in space will become an indispensable observational tool for reliable climate prediction and verification of future climate conventions on greenhouse gas reduction