## Slide 1
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Status / Scope of Sentinels 4&5
Jörg Langen, Paul Ingmann, Ben Veihelmann
ESA, Mission Science Division

## Slide 2
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Global Monitoring for Environment and Security (GMES) – the European contribution to GEOSS
Services Component – led by EC
  Produces information services in response to European policy priorities in environment and security
  Relies on data from in-situ and space component
In-situ component – led by EEA
  Observations mostly within national responsibility, with coordination at European level
Space Component – led by ESA
  Sentinels - EO missions developed specifically for GMES
  Contributing Missions - EO missions built for purposes other than GMES but offering part of their capacity to GMES
<number>
Notes: <number>

## Slide 3
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
GMES dedicated missions: Sentinels
Sentinel 1 – SAR imaging
All weather, day/night applications, interferometry
Sentinel 2 – Multispectral imaging
Land applications: urban, forest, agriculture,.. Continuity of Landsat, SPOT
Sentinel 3 – Ocean and global land monitoring
Wide-swath ocean color, vegetation, sea/land surface temperature, altimetry
Sentinel 4 – Geostationary atmospheric
Atmospheric composition monitoring
Sentinel 5 – Low-Earth orbit atmospheric
Atmospheric composition monitoring
(S5 Precursor launch in 2014)
2011
2012
2012
2017+
2019+
<number>
Notes: <number>

## Slide 4
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Development of Sentinel 4 and 5 missions (1/2)
Starting point (2002): 5 GMES Sentinel missions of which 1 GEO and 1 LEO for atmospheric composition.
“Capacity” study (2003-5): top-down approach. Identified environmental themes, operational usage categories. Extensive survey of geophysical observation requirements.
Climate protocol monitoring and air quality applications to be combined in single mission, due to strong thematic coupling and large overlap in requirements. Basic stratospheric ozone monitoring possibly included.
Additional limb mission needed to cover UTLS climate and ozone applications. Operational applications and instrument selection premature.
Started industrial system studies on nadir mission with preliminary requirements; extensive simulations on orbit options:
    1 GEO + 1 sun-synch LEO
    3-4 inclined LEO
    3-4 sun-synch LEO

## Slide 5
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Development of Sentinel 4 and 5 missions (2/2)
“Camelot” study (2007-9): Mapping of geophysical requirements to radiometric, spectral and spatial requirements; orbit trade-off accounting for sampling statistics, cloud interference and accuracy requirements.
Orbit scenario selected:
  Sentinel 4: 1 GEO (UVN instrument added to Eumetsat MTG sounder platform, usage of existing TIR sounder capabilities)
  Sentinel 5: 1 sun-synch LEO at 9.30h (UVNS instrument added to Eumetsat post-EPS, combined met-chem IR sounder, usage of multi-spectral imager, usage of polarisation imager if implemented)
Rationale:
  cost (usage of existing platforms, non-redundant scheme for GEO)
  synergy with meteorological observations
  high diurnal observation frequency over Europe

## Slide 6
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Geographical coverage requirements
Ozone Layer & global
Surface UV radiation
threshold : Europe + surrounding areas
(e.g. monitoring of EC directives and national AQ legislation, short-term air quality forecast)
Air Quality target : global (monitoring, assessment and forecast of global air quality, the oxidising capacity, and the quantification of continental in/outflow)
Africa not strictly in scope of GMES AQ requirements –
temporal and spatial resolution considered more important than target geographical coverage.
Climate global

## Slide 7
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Sentinel 5 precursor
Rationale:
Continuity of CO and CH4 data with PBL sensitivity (Sciamachy)
Continuity in high spatial resolution (OMI)
Start into diurnal AQ observations (2nd local time: 13.30h)
Scope:
UVN spectrometer as Sentinel 5
2.3 micron band (CO, CH4)
The CH4 data product from this mission would benefit strongly from an efficient cooperation with NPP/NPOESS if flying concurrently.

## Slide 8: Summary of Observation Requirements UV-Vis-NIR-SWIR Bands
Sentinel-4
Sentinel-5
Sentinel-5p

## Slide 9: Summary of Observation Requirements TIR Bands
Sentinel-5
Sentinel-4
Using IRS

## Slide 10
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Programmatic status
Sentinel 5 precursor approved and funded (NL co-funding)
system phase A/B1 kickoff soon, instrument activities ongoing, launch 2014
Sentinel 4 approved and funded by ESA ministerial council
phase A/B1 running in competition, launch 2018
final approval of MTG-S by Eumetsat expected 2010/11
Sentinel 5 preparatory activities approved
phase A to start 2010, launch ≥ 2018
final approval and funding expected 2011/12 (ESA and Eumetsat)

## Slide 11
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Scope of possible international cooperation / harmonisation
Objectives and requirements
limited possibilities for S5, closed for S4 and S5p
Retrieval algorithms and OSSEs
open in principle. General methodology maybe more promising field than implementation (the latter instrument-specific for retrieval, and also scene-specific for OSSEs).
Data quality and access
Large mutual benefit!
International cooperation has large potential for LEO missions:
Long range transport of pollutants; climate aspects
Detailed observations on partner’s “terrain”
“ground truth” for GEO data

## Slide 12
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
CO2
CO2 Kyoto protocol verification mission out of reach
Random and systematic measurement error requirements
Uncertainties of inverse modelling (transport PBL – free troposphere)
Uncertainties in modelling of natural surface fluxes
CO2 mission on total surface fluxes
Data available from AIRS, Sciamachy, IASI. ECMWF/MACC: confidence not good enough for data assimilation or inverse modelling. Only ground data shown to improve carbon budget.
Awaiting demonstration of operational benefit before investing in long-term observation system.

## Slide 13
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
CH4
Direct retrieval: high sensitivity to cloud and aerosol
Calibration of AMF using CO2 (1.6 m band): sensitivity to assumed CO2 abundance
Combination of 1.6 and 2.3 m bands required for high quality product
Sentinel-5 precursor : 2.3 m band
Sentinel-5 : 1.6 and 2.3 m bands

## Slide 14
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Thank you!

## Slide 15
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Local time of Sentinel 5 precursor orbit
MRD follows advice from Camelot study:
  early afternoon orbit most suitable for continuation of the long term record of short-lived tropospheric species, which has been started in 2004 with OMI at a local time of 13:45h;
  synergistic exploitation of simultaneous measurements form NPOESS 13:30h platform possible: CRIS IR data and stratospheric ozone profiles by OMPS-limb, as well as cloud data from imager;
  early afternoon provides better observation conditions in solar channels than late afternoon, due to more favourable solar zenith angles (see next slide).

## Slide 16
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
useful data in solar range for SZA < 80° (ref. TRAQ, Camelot)
late afternoon (17.30h) implies summer only mission of UVNS

## Slide 17
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Sentinels 4&5 are to support GMES atmospheric services:
Core services
standard operational products and information services providing direct support to European policy and information on global issues
Sustained public funding (EU & Member States)
Pilot service “GMES Atmospheric Service (GAS)”: EU FP7 activity “MACC” to start in June
precursor / development activities: GEMS (EU FP6 Integrated Project), PROMOTE (ESA GMES Service Element)
Downstream services
targeted services that address specific user requirements, or trans-national, national, regional or local problems
EU not directly driving the service and not responsible for service requirements
use core service data as input
call to be issued
precursor / development activities: PROMOTE, national developments

## Slide 18
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Core Service components
Air quality
• integrated global and European air quality analysis;
• integrated global and European air quality forecast;
• historic records of Global and European atmospheric composition.
Climate forcing
• improved and sustained monitoring of the state of the climate system (surface and upper air meteorology and composition) and its variability;
• integrated global, European and regional concentration fields of key greenhouse gases (CO2, CH4 and related tracers) enabling determination of sources and sinks.
Stratospheric ozone and solar radiation
• improved and sustained monitoring of the current status and trends in stratospheric ozone depletion and ozone depleting gases;
• routine provision of updated ozone, UV and solar radiation maps and forecasts;
• historic European UV and solar radiation records and mapping.

## Slide 19
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Examples of downstream services
Air quality
• local air quality forecasts, e.g. as input to traffic regulation
• Improved air-quality-related alerts and forecasts for health services supporting vulnerable communities (COPD, asthma, pollen-induced allergies)
• daily compliance with air-quality legislation (threshold exceedance warning)
• support to development of effective air pollution abatement measures through proper apportionment of sources and assessment of impacts (human exposure) etc.
• forecasts for extreme events involving the combined effects of heat stress, high UV-B exposure and poor air quality.
Climate change
• information for quick response to extreme weather events and natural catastrophes
• identification, assessment and monitoring of regional/local sources and sinks of greenhouse gases and pollutants and related tracers in support of emission and sink verification and mitigation policy.
Stratospheric ozone and solar radiation
• surface UV-radiation monitoring and forecasting;
personalized skin-type specific UV information

## Slide 20
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Mapping of services to
Level 2 data products
(simplified)
GEMS:
prototype core service
PROMOTE:
prototype downstream services
X – target product
x – auxiliary product

## Slide 21
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Environmental themes, data usage, services
Environmental Theme
Data usage
Ozone Layer &
Surface UV radiation *)
Air Quality
Climate
Protocol monitoring
UNEP Vienna Convention; Montreal and subs. Protocols
CFC emission verification
Stratospheric ozone, halogen and surface UV distribution and trend monitoring
UN/ECE CLRTAP; EMEP / Göteborg Protocol; EC directives EAP / CAFE
AQ emission verification
AQ distribution and trend monitoring
UNFCCC Rio Convention; Kyoto Protocol; Climate policy EU
GHG and aerosol emission verification
GHG/aerosol distribution and trend monitoring
Near real time services
Stratospheric composition and surface UV forecast
NWP assimilation and (re-) analysis
Local Air Quality (BL); Health warnings (BL)
Chemical Weather (BL/FT)
Aviation routing (UT)
NWP assimilation and (re-) analysis
Climate monitoring
Climate model validation
Assessment
(lower priority for operational mission)
Long-term global data records
WMO Ozone assessments
Stratospheric chemistry and transport processes;
UV radiative transport processes
Halogen source attribution
UV health & biological effects
Long-term global, regional, and local data records
UNEP, EEA assessments
Regional & local boundary layer AQ processes; Tropospheric chemistry and long-range transport processes
AQ source attribution
AQ Health and safety effects
Long-term global data records
IPCC assessments
Earth System, climate, rad. forcing processes; UTLS transport-chemistry processes
Forcing agents source attribution
Socio-economic climate effects
 | A | B | C
1 | A1 | B1 | C1
2 | A2 | B2 | C2
3 | A3 | B3 | C3

## Slide 22
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Comprehensive set of related observational requirements established in ESA “CAPACITY” study
for each environmental theme
for each application type
self-consistent
sufficiently complete to perform trade-offs between space mission concepts
following an integrated observation strategy (IGACO) considering ground, airborne and space observations and assimilation / models
using information from existing reviews and ongoing activities

## Slide 23
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Observational requirements – example: AQ NRT satellite
 | A | B | C
1 | A1 | B1 | C1
2 | A2 | B2 | C2
3 | A3 | B3 | C3

## Slide 24
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Assessment of existing and planned missions (1/2)
A. Research missions
Envisat, Aura, Odin, Scisat, Mopitt, Gosat – all ongoing
    Wealth of data for science
    Advanced stratospheric component
    Pathfinders for tropospheric applications
    Main deficiencies:
    Temporal resolution, horizontal sampling / coverage in nadir
    Vertical resolution in limb
    All expected to stop ≤ 2014, no definitive new plans.

## Slide 25
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Assessment of existing and planned missions (2/2)
B. Operational missions
MetOp ongoing GOME-2, IASI
NPP / NPOESS 2012 / OMPS, CRIS
MTG-S 2018 IRS
post-EPS 2018/20 IRS
Asia ?
    stratospheric ozone monitoring well covered
    some contribution to NWP
    some contributions to tropospheric applications
    Main deficiencies:
    horizontal resolution in UV-VIS/NIR
    temporal resolution

## Slide 26
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
  High temporal and spatial resolution space-based measurements of tropospheric (PBL) composition for application to air quality
  Climate gases (CO2, CH4 and precursor CO) and aerosol monitoring with sensitivity to the PBL
  High vertical resolution measurements in the UT/LS region for ozone and climate applications
Main gaps in current / planned operational system
 | A | B | C
1 | A1 | B1 | C1
2 | A2 | B2 | C2
3 | A3 | B3 | C3
 | A | B | C
1 | A1 | B1 | C1
2 | A2 | B2 | C2
3 | A3 | B3 | C3
 | A | B | C
1 | A1 | B1 | C1
2 | A2 | B2 | C2
3 | A3 | B3 | C3

## Slide 27
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Mission concept for ozone and climate applications in the UTLS
Instrumentation options:
either mm-wave or mid-IR limb-sounder
System: sun-synchronous LEO platform
Maturation of operational application to be pursued.
Choice of instrument type open.
Mission to be considered after clarification of these points.

## Slide 28
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Option | Latitude range [deg] | Longitude range [deg] | Revisit time | Implementation option
a 1 b | 30 - 65 N | 30 W - 45 E @ 40 N | 0.5 - 1 h solar ch. 0.5 - 2 h thermal ch. | 1 GEO
 | All | All | 24 h @ fixed L.T. | 1 SSO
2 | 30 - 60 N & 30 - 60 S | All | 2 h | Constellation of drifting LEO
 | 30 N - 30 S | All | 6 h | 
3 | All | All | 4 h | Constellation of SSO
System trade-off for climate protocol monitoring and air quality
1. Air quality and climate protocol monitoring missions can be combined due to large overlap of requirements (CO2 excluded).
2. System concept driven by air quality geographical coverage and time resolution requirements.Trade-off between geographical coverage and temporal sampling:

## Slide 29
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Option 1: 1 GEO + 1 LEO in sun-synchronous orbit
cost prohibitive for stand-alone realisation →
only possible as additional payloads on MTG and post-EPS
+ high temporal and spatial sampling over Europe and around
+ least variation in observation geometries → facilitates data usage
- no redundancy: two MTG-Sounder platforms for 15 years
- incompliant with GEO thermal IR requirements (O3, CO profiles)
- no PBL-sensitive CO measurement at high temporal resolution
- no multi-directional polarisation imaging
- pointing and co-registration difficult
focus on European air quality, also stratospheric ozone monitoring

## Slide 30
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Option 2: Constellation of 3-4 LEO satellites in drifting orbit
+ high temporal sampling over most of the polluted areas globally
+ favourable redundancy concept (all satellites identical)
- misses polar ozone
→ relying on NPOESS or future S5 limb-sounding component
- misses CH4 from melting permafrost
→ relying on NPOESS / post-EPS
- impact of non-sunsynch orbit on platform and payload concept
Higher orbits (~1000km) would improve spatio-temporal coverage but are prohibited by radiation environment and decrease in radiometric sensitivity
focus on quasi-global air quality – high population density
Courtesy:
P. Veefkind

## Slide 31
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Option 3: Constellation of 3 LEO satellites in sun-synch orbit
+ full global coverage
+ maturity
+ highest synergy with meteorological measurements
- temporal resolution less favourable for air quality
(however improving with increasing latitude)
Climate, air quality and stratospheric ozone monitoring

## Slide 32
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Mission concept for climate protocol monitoring (lower troposphere) and air quality applications
Instrumentation:
UV-VIS-NIR-SWIR spectrometer for O3, NO2, SO2, H2CO, CH4, CO, aerosol
thermal IR sounder for O3, CO and CH4 profiles and HNO3 + others
cloud imager
System: 1 GEO platform (Europe) and 1 sun-synchronous LEO platform.
Selection of system concept
Option 1 has been selected
lowest cost
synergy with meteorological payload through implementation on Eumetsat platforms
highest diurnal sampling frequency over Europe

## Slide 33
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Implementation of S4&5 on Eumetsat platforms
Sentinel 4 will be a realised as
  addition of a UVN spectrometer on the MTG-S platforms;
  utilisation of TIR data from the IR sounder onboard the same platforms; and
  utilisation of imager data from the MTG-I platforms.
Sentinel 5 will consist of
  a UVNS spectrometer embarked on the post-EPS platforms;
  utilisation of the EUMETSAT post-EPS IR sounder which addresses requirements for both meteorology and atmospheric chemistry (the latter consistent with the Sentinel 5 IR sounding requirements);
  utilisation of post-EPS imager data;
  utilisation of multi-directional polarisation imager if implemented.

## Slide 34
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Requirements for Sentinel 5 precursor
Requirements are those of S5, except
Local time (see above)
fly in loose formation with NPP
(synergy with imager, OMPS-limb, CRIS)
Thermal IR part is dropped, considering
  availability of IASI data,
  the transitional nature of the precursor mission,
  programmatic constraints.

## Slide 35
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Some results of Camelot study (1)
Camelot consortium: KNMI, RAL, U. Leicester, SRON, FMI, BIRA-IASB, CNR-IFAC, U. Köln, Noveltis
Ozone
Both UV and TIR have limited sensitivity to PBL
Combination of a posteriori covariances promises ~30-50% precision in PBL ( := 0-2km layer)
Averaging kernel for “PBL” extends to ~7km altitude
Iterative synergistic retrieval remains to be demonstrated
Observation of diurnal variation in PBL challenging
NO2
Strong benefit from O2-A band in cloudy conditions
Good correlation OMI / ground-based (where expected)
Observed diurnal variation convolved with PBL dynamics (Av. Kernel)

## Slide 36
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Some results of Camelot study (2)
CH4
Direct retrieval: high sensitivity to cloud and aerosol
Calibration of AMF using CO2 (1.6 m band): sensitivity to assumed CO2 abundance
Combination of 1.6 and 2.3 m bands required
(implementation on Sentinel 5)
Aerosol
Proper characterisation of aerosol requires multi-spectral, multi-directional, multi-polarisation imager (3MI)
UV and SWIR channels desirable in 3MI

## Slide 37
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Some results of Camelot study (3)
Thermal IR
Drastic change of requirements following IASI success:
From 2-3 narrow bands (O3, CO [,HNO3]) to wide-band instrument
Target species: O3, CO, HNO3, CH4, H2O, NH3, CH3OH, PAN, volcanic SO4, C2H4, C2H2, HCN, CFC-11, CFC-12
spectral resolution 0.075 – 0.3 cm-1 unapodised
Implementation in combined meteo – chem instrument on post-EPS

## Slide 38
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Some results of Camelot study (4)
Sampling statistics for orbit configurations
based on SEVIRI cloud statistics
taking account of retrieval sensitivity to cloud statistics and observation geometry
Comparing retrieval accuracies to requirements
Results shown are observation probabilities per 24h for
  Tropospheric ozone column from UV
  London (51°N)
  10km pixel size (GEO), 10km sub-satellite pixel size (LEO)
  30km field of regard
and should be seen as examples.

## Slide 39
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Probability of at least 1 cloud free observation
Probability
Jan Mar May Jul Sep Nov
9:30 Sun-synchronous
9:30+13:30 Sun-synchronous
9:30 Sun-synch
9:30+13:30 Sun-synch
9:30+13:30+15:30 Sun-synch
9:30+13:30+17:30 Sun-synch
9:30+13:30+Geo
4x Non-sun-synch (inc.55)
Notes: <number>

## Slide 40
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Probability of at least 1 observation meeting user requirement (20%)
Probaility
Jan Mar May Jul Sep Nov
9:30 Sun-synch
9:30+13:30 Sun-synch
9:30+13:30+15:30 Sun-synch
9:30+13:30+17:30 Sun-synch
9:30+13:30+Geo
4x Non-sun-synch (inc.55)
Notes: <number>

## Slide 41
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Number of hours with observation meeting requirement during day,
  If at least one cloud free observation obtained during the day
Number of hours
Jan Mar May Jul Sep Nov
9:30 Sun-synch
9:30+13:30 Sun-synch
9:30+13:30+15:30 Sun-synch
9:30+13:30+17:30 Sun-synch
9:30+13:30+Geo
4x Non-sun-synch (inc.55)
Number of Observations
Notes: <number>

## Slide 42: Sentinel-4
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Applications: monitoring changes in the atmospheric composition (e.g. ozone, NO2, SO2, BrO, formaldehyde and aerosol) at high temporal resolution (1 hour) troposphere variability
Narrow field spectrometer covering UV (305-400 nm), visible (400-500 nm) and near-IR (750-775 nm) bands
Spatial sampling 8 km (over Europe) and spectral resolution between 0.12 nm and 0.5 nm (depending on band)
Geostationary orbit, at 0o longitude
Embarked on MTG-S and operated by EUMETSAT
GEO atmospheric composition mission

## Slide 43: Sentinel-5
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Applications: monitoring changes in the atmospheric composition (e.g. ozone, NO2, SO2, BrO, CO, CH4 formaldehyde and aerosol) at high temporal (daily) resolution troposphere variability
LEO UVNS instrument with bands: UV1, UV2, VIS123 and SWIR-1 and SWIR-3. Option also to include SWIR 2 channel.
Spatial resolution 15 x 15 km2 (UV1) 5 x 5 km2 (UV2/VIS/NIR/SWIR)
Low Earth orbit (reference altitude of about 817 km)
Sentinel-5 embarked on post-EPS and operated by EUMETSAT
LEO atmospheric composition mission
Flight direction
Nadir
IRS
Flight direction
Nadir
IRS
UVNS
Implementation
example

## Slide 44: Sentinel 5 precursor
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
1. Continuity of data 2014 – 2020 (Envisat/Aura – Sentinel 5)
spatial resolution
CO and CH4 with PBL sensitivity
2. Transition to operational scheme
Afternoon orbit required for AQ forecast (Metop: 9:30h).
Use synergy S5 precursor – Metop to start into observation of diurnal variation, as needed for AQ monitoring. (Will be picked up by S4 later).
improved radiometric sensitivity
3. Implementation
UV-VIS-NIR-SWIR spectrometer on dedicated platform, flying in loose formation with NPP (13:30h)

## Slide 45: Sentinel-5 Precursor
<number>
ACC-5, CSA - Montreal, 30-31 March 2010
Applications: monitoring changes in the atmospheric composition (e.g. ozone, NO2, SO2, BrO, CO, CH4 formaldehyde and aerosol) at high temporal (daily) resolution tropospheric variability
LEO UVNS instrument with priority bands in the UV12, VIS123, NIR and SWIR.
Spatial resolution 21 x 28 km2 (UV1) 7 x 7 km2 (UV2/VIS/NIR/SWIR)
Low Earth orbit (reference altitude 828 km)
Sentinel-5 precursor shall fill data gap (2013-2019) in critical data streams between Envisat/Sciamachy, Aura/OMI and Sentinel-5 embarked on post-EPS
LEO atmospheric composition mission
UV1
UV2
VIS12
VIS3-NIR
SWIR3
SWIR module
UVN module
SWIR calibration unit
UVN calibration unit