## Slide 1: Global Environmental Monitoring (from Jhoon Kim ACC-4 presentation, Frascati, IT, June 2008)
Constellation of GEO Mission to study Air Quality
GEO-CAPE
(America)
GMES
(Europe)
MP-GEO
(Asia Pacific)
Constellation synergy
Improving spatial and temporal coverage
Monitoring globalized pollutants
sharing data and science
supporting QA and CAL/VAL of instruments
EPA
ME
Notes: <number>

## Slide 2: Global Observations from Geostationary Vantage Point: International Cooperation Required
Americas: NASA, NOAA
Europe and Africa: ESA, Eumetsat
Asia and Australia: KARI, JAXA
Geostationary orbit offers the potential for “continuous” (or many times per day) observation within the satellite field of view
Continuous global Earth observations can be provided by a constellation of at least 3 geostationary satellites positioned appropriately around the globe
  Precedent in operational meteorological agencies for aerosol and fire detection: NOAA GOES, Eumetsat MSG, JMA MTSAT
Unique considerations of geostationary access
  Orbit slots allocated by international agreement and are acquired ~years in advance of launch
  Relatively expensive cost to orbit because of high altitude
Because of these considerations, Instruments of Opportunity are of particular interest for geostationary (on Government or commercial satellites)
Notes: <number>

## Slide 3: The Geostationary Coastal and Air Pollution Events (Geo-CAPE) Mission
Jay Al-Saadi & Paula Bontempi Program Scientists, NASA Headquarters
And the entire Geo-CAPE Science Working Group
CEOS Atmospheric Composition Constellation Meeting (ACC-5) 30-31 March, 2010, CSA, Montreal, Canada

## Slide 4
Notes: <number>

## Slide 5: Why Geo-CAPE? From Decadal Survey…
Next generation “Earth Science and Applications from Space”: High-time-resolved (~hourly) observations of atmospheric composition and coastal ocean biochemistry/physics
  Air Quality goals include:
    Satisfy basic research and operational needs related to air-quality assessment and forecasting
    Emission of O3 and aerosol precursors, including human and natural sources
  Coastal Ocean goals include:
    Quantify response of marine ecosystems to short-term physical events
    Monitor biotic and abiotic material in transient surface features
  Synergy: measurements of aerosols from the air-quality instrument can be used to correct aerosol contamination of the high-resolution coastal ocean imager
Suggested instrumentation has strong low-Earth-orbit space heritage and high level of technology readiness; 2015 launch would be feasible
  MOPITT, SBUV, GOME, SCIAMACHY, OMI, SeaWiFS, MODIS
Notes: <number>
, such as river plumes and tidal fronts
, such as oil spills, waste disposal, and harmful algal blooms
to support air-program management and public health
That’s about it for decadal survey summary.

## Slide 6: Decadal Survey “Notional” GEO-CAPE Mission
Geosynchronous orbit near 80W with notional payload of 3 instruments
  Wide area UV-Visible spectrometer, <10km nadir resolution, hourly, 45S to 50N (O3, NO2, CH2O, SO2, aerosol)
  Wide area IR correlation radiometer for CO mapping with capability to distinguish between near-surface and free-troposphere
  High spatial resolution (250m) steerable event-imaging spectrometer
The 2 wide-area instruments together provide systematic/continuous air quality observations
The high-resolution event imager provides targetable/episodic observations
  This is the coastal ocean color instrument but also capable of atmospheric observations
Estimated mission cost ~$550M (NRC) ~$1.1B (NASA)
Notes: <number>
, such as river plumes and tidal fronts
, such as oil spills, waste disposal, and harmful algal blooms
to support air-program management and public health
That’s about it for decadal survey summary.

## Slide 7: Geo-CAPE Mission Status
Systematic NASA implementation of Decadal Survey: Tier-1 Missions, then Tier-2 Missions, then Tier-3
All Tier-2 missions are in pre Phase-A and preparing for potential transition to Phase A
  Advanced technology development and maturation funded separately through NASA ESTO program
  Science Working Groups funded at ~$2M /yr each FY09-10
    ~60 participants including NASA, NOAA, EPA, University
    Science objectives and instrument requirements
    Mission concepts, observing strategies, and key partnerships
Based on current budget guidance, estimated Tier-2 mission launch dates are 2018-2022
Notes: <number>

## Slide 8
Geo-CAPE Atmosphere Science Traceability Matrix: Science Questions define measurement objectives which establish instrument requirements
What are the temporal and spatial variations of emissions of gases and aerosols that are important for air quality and climate?
How do physical, chemical, and dynamical processes determine tropospheric composition and air quality over scales ranging from urban to continental, diurnally to seasonally?
How does air pollution drive climate forcing and how does climate change affect air quality on a continental scale?
How do we improve air quality forecasts and assessments for societal benefit?
How does regional and intercontinental transport affect local and regional air quality?
How do episodic events, such as wild fires, dust outbreaks, and volcanic eruptions, affect atmospheric composition and air quality?

## Slide 9: Geo-CAPE Atmosphere Science Traceability Matrix (Version 2010/03/26)

## Slide 10: GEO-CAPE Atmosphere Measurement Requirements (Version 2010/03/26)
Threshold measurements (minimum mission, ~2017 planning):
  O3, NO2, SO2, hourly for SZA<70, and CO hourly day and night, at 4km horizontal spatial footprint at nadir
  AOD hourly at 2 km
Baseline measurements (desired mission, ~2020 planning):
  O3, NO2, CO, SO2, HCHO, CH4, NH3, CHOCHO, different sampling frequencies, 4km horizontal spatial footprint size at nadir
  AOD, AAOD, AI, aerosol optical centroid height (AOCH), cloud detection, hourly for SZA<70 and 1 km horizontal spatial footprint size at nadir
Baseline measurements require addition of Thermal IR instrument; multi-spectral retrievals using wavelength combinations from UV through TIR are being systematically evaluated
Primary focus now on systematic observation of North America land and coastlines
  Other “Regions of Interest” from the fine spatial resolution instrument, e.g., South America

## Slide 11: GEO-CAPE Pre-Phase A Plan for Threshold Mission (target 2017 launch) v2010.03.26
Threshold Requirements Development
Host S/C
Orbit coverage
Analysis
Instrument Conceptual
Design
UV-Vis Spectrometer
IR-GFCR (or equiv)
UV-SWIR
Commercial Comm Sat
GOES-S
Military or other classified
Foreign
*Contact the spacecraft sponsor (company, NOAA, appropriate other US government entity). Obtain interface specifications if available and identify accommodation resources (mass, power, data rate, pointing knowledge and stability, dimensions, unobstructed fields of view (optical & thermal) ) available for a hosted payload. Conduct accommodations studies on each instrument for those options that appear viable. The accommodations studies should take roughly 1 day in an MDL or Team X for each host spacecraft once the interface information and a CAD file are available. Note that Geo Quick Ride RFI responses indicate mass available on commercial spacecraft is around 100 kg.
Identify target host launch dates and instrument delivery date requirements. Develop grass roots schedule for instrument(s) development based on known subsystem/component lead times to evaluate the feasibility of the delivery date
Host spacecraft identification and evaluation*
Schedule
Development
Cost Estimate
Dedicated spacecraft Design
April
November
June
Notes: <number>

## Slide 12: GEO-CAPE Pre-Phase A Plan for Baseline Mission (target 2020 launch) v2010.03.26
Host S/C
Orbit coverage
Analysis
Instrument Conceptual
Design
Host spacecraft identification and evaluation
Schedule
Development
Cost Estimate
Baseline Requirements Development
April
November
June
Dedicated spacecraft Design
Payload Option 1
UV-Vis spectrometer (atmosphere) NIR-SWIR (GFCR or TIMS) (atmosphere) TIR (FTS, FPI) (atmosphere) UV-SWIR fine spatial (grating or prism or FTS?) (ocean)
Payload Option 2
Panchromatic FTS (atmosphere) UV-SWIR fine spatial (grating or prism or FTS?) (ocean)
Payload Option 3
Panchromatic FTS (atmosphere and ocean)
Conduct Team–X or MDL studies using the instrument payload options defined to the left
Time: 1 week for each run (scheduling may be difficult)
Cost: approximately $100K each
Same as previous slide

## Slide 13: Geo-CAPE Mission Architecture and Observing Strategies
Concept: Systematic medium-resolution and targetable episodic high-resolution observations
  Regular (~hourly) medium-resolution (5-8 km) continental viewing for atmospheric composition
  High-resolution (300-375 m) regional viewing for coastal waters and targeted special/ episodic events
Both Dedicated and Distributed mission concepts are now being considered, to possibly include instruments of opportunity on non-NASA satellites
  Appears feasible for the systematic (autonomous) and episodic (interactive) instruments to be on different platforms if needed
  Provide revolutionary Earth observations as soon as possible (i.e., contemporaneous with partner missions) while continuing maturation of advanced instrumentation concepts
Continuous
scan of polluted regions
Programmable high-resolution observations
Washington, DC imaged with 5-km pixels.
Notes: <number>
Basic framework for HQ mission studies.

## Slide 14: Backup

## Slide 15: NASA Advanced Technology Investments
NASA Earth Science Technology Office (ESTO) plans and funds investments to further support the research areas, observations, and notional missions recommended in the Decadal Survey: http://esto.nasa.gov/adv_planning_ds.html
Advanced instrumentation development and maturation programs:
  Advanced Component Technologies (ACT)
    Component and subsystem level technologies
    3 GEO-CAPE relevant projects selected in 2008 solicitation
  Instrument Incubator Program (IIP)
    Assessment of instrument concepts in ground, aircraft, or engineering model demonstrations
    7 Geo-CAPE relevant projects funded over the past decade, 2 of them in the most recent solicitation (2007)
      4 different IR concepts (CO, O3, potentially other gases)
      1 UV-Visible concept (O3, NO2, SO2, HCHO, aerosol)
      2 hyper/multi spectral concepts (many atmosphere species; ocean color and other products)
Notes: <number>

## Slide 16
GEO-CAPE will significantly improve observational capability in 4 key areas:
High-temporal resolution measurements to capture changes in pollutant distributions due to changing photochemistry, emissions and meteorology
High-spatial resolution measurements to access the city scale with continuous full-coverage of North America
Exploitation of multispectral observations to improve information content in the vertical profile
Development of an integrated measurement system for atmospheric composition science and applications in conjunction with observations from the ground-based, suborbital and satellite platforms of US and international partners

## Slide 17: GEO-CAPE Mission Study Issues
Science Requirements
  Vertical resolution within the troposphere: Is BL sensitivity a satellite measurement science requirement (e.g., through multi-wavelength retrievals) or part of a broader integrated observing system?
  Need to better define the atmospheric correction requirements for coastal ocean color retrievals
Observing strategy
  Systematic vs episodic
Mission cost
  Advanced instrumentation concepts may offer reduced mass and improved capability, but at higher mission risk or later launch date
  Potential for “hosted payloads” on other geostationary platforms may offer reduced cost
  Common instrument development for contemporaneous international geostationary missions can reduce cost and improve science
Notes: <number>

## Slide 18: Geo-CAPE and Future NOAA GOES Platforms
Future GOES platforms are particularly compelling synergistic options for part or all of GEO-CAPE
  Value to GOES
    Addition of UV wavelengths will significantly improve aerosol information, e.g., can infer absorption and composition
    Hourly OMI-like ozone column complements IR ozone retrieval (jet stream/turbulence location)
    Trace gas observations for improving air quality forecast guidance
    Cost sharing/ risk reduction of Coastal Waters Imager: NASA matures advanced instrumentation, e.g. hyperspectral Visible-TIR
  Value to GEO-CAPE
    Coincident cloud and met observations will significantly improve the atmospheric chemistry and ocean color data products
    Coincident lightning mapper and fire detection data will fundamentally improve utility of satellite trace gas observations
    Lower cost to NASA (launch and platform cost savings)
European and Korean satellite programs are now planning air quality and ocean color measurements within the operational meteorological framework (GEO and LEO)

## Slide 19: Building the Science Traceability Matrix
Flow from objectives
to requirements
Trace requirements
to their objectives

## Slide 20: Global Observations: International Cooperation
Americas: NASA, NOAA
Europe and Africa: ESA, CNES
Asia and Australia: KARI, JAXA
Figure courtesy Doreen Neil, NASA
Continuous global observations can be provided by a constellation of at least 3 geostationary satellites
Harmonization of currently planned geostationary missions would enable an integrated global observing system fulfilling the visions of GEO/GEOSS and IGOS Atmospheric Chemistry and Coastal themes
  ESA Sentinel 4 on MTG, 2017 (AQ)
  MEST/ME MP-GeoSat, 2017 (AQ, OC)
  NASA GEO-CAPE, 2020? (AQ, OC)
  CNES OCAPI ???? (OC)
The US component of this global constellation could be effectively achieved by coordinating GEO-CAPE to align with planned ESA and MEST/ME missions
  Cost must fit within NASA Earth Science mission budget profiles
Notes: <number>