## Slide 1
The potential of MTG-IRS to detect high pollution events
at urban and regional scales
Aim
The study investigates the capability of IRS onboard MTG to detect enhanced levels of carbon monoxide (CO) and ozone (O3) at local and regional scales, in particular over Europe.
People involved
Cathy Clerbaux, Anne Boynard (SA/IPSL- CNRS, Paris)
Pierre Coheur, Oliver Scharf
(ULB, Brussels)
Some slides extracted
from a former study

## Slide 2
>> Detection of pollution peaks with IR instruments
Controlled pollutants are O3, CO, NO2, SO2, PM;
  Ozone: peaks in the afternoon. Alert levels exceeded several days per year. Current prediction scores around 50%.
  CO: Alert levels exceeded only when big fire events occur.
All controlled pollutants but ozone are continuously decreasing above Europe;
- O3 and CO (and SO2-volcano) are measured by TIR;
Thermal contrast is high during the day and during the spring/summer, over land.
  Ozone/IASI: Profiles retrievable but low sensitivity near the ground.
  CO/MOPITT and IASI: Cities can be seen if favorable thermal contrast. Fires are easy to be detected because it is a large signal.

## Slide 3
 | IRS/MTG | TIR GEO S4
Species | O3, CO | O3, CO, (HNO3)
Spatial res. | 4 x 4 km2 | 5 x 5-15 x 15 km2 (G -T)
Nedt @280K | 0.2 (O3) , 0.85 (CO) | 0.05 - 0.15 (G -T)
OPD Spectral res. (unapodized) | 0.8 cm 0.75 cm-1 | 4 - 2 cm (G -T) 0.15 - 0.3 cm-1
Compared specifications of the proposed
IRS/MTG and TIR/S4 missions
IASI= ~TIR S4 threshold
Notes: 0.85 K >>>>> 6 10-7 en radiance
0.2 K >>>> 2.45 10-6 en radiance

## Slide 4
Spectral resolution and sampling
MOPD  sampling  FWHM of non-apodized ILS
0.8 cm  0.625 cm-1  0.75cm-1  IRS-MTG
 4.0 cm  0.125 cm-1  0.15cm-1  Sentinel 4 (goal)
 2.0 cm  0.250 cm-1  0.30cm-1  Sentinel 4 (Threshold)
Radiometric noise
NEDT (of 280K blackbody)  NESR
0.20 K  2.45 10-8 W/cm2 sr cm-1  IRS-MTG
 0.05 K  6.08 10-9 W/cm2 sr cm-1  Sentinel 4 (goal)
 0.10 K  1.22 10-8 W/cm2 sr cm-1
IRS-MTG
Sentinel 4 (goal)
Sentinel 4
(threshold)
IRS-MTG IRS3: OPD = 0.8 cm NEDT = 0.2K
Results for ozone
A. Sensitivity analyses

## Slide 5
MTG-IRS
Sentinel 4 (FWHM threshold)
Sentinel 4 ( FWHM goal)
DOFS
Varying spectral resolution and noise
= 0.96; T = 0 K
Summary
Results for ozone
A. Sensitivity analyses
a priori variability
MTG-IRS
PBL (0-2 km) column
LT (0-6 km) column
a priori variability
MTG-IRS
MOPD=0.8 cm (IRS-MTG)
MOPD = 2.0 cm (Sentinel 4 threshold)
MOPD = 4.0 cm (Sentinel 4 goal)

## Slide 6
Vertical sensitivity from the ground to about 40 km but low sensitivity to the surface
DOFS around 3.5  single information in the troposphere
Errors range from 20 to 40 % on individual levels above 2 km while errors in the PBL are close to the a priori variability.
Error on the tropospheric column is around 15 %
Improving noise and/or spectral resolution (IRS-MTG vs. Sentinel 4) improves retrieval performances in the lower troposphere.
Impact of thermal contrast (T=Tground-Tatm@surface): Impact is in the lower troposphere. The error on the tropospheric column reaches ~ 10 % for positive values of T
Despite a priori far from the target:
Significant improvement with respect to a priori over the entire troposphere.
Errors around 12 % on the tropospheric column for vanishing thermal constrast decrease to 5 % for T values of 5 K or larger.
Similarly PBL errors decrease to 50 % for T values of 5 K or larger.
Diurnal variations are hardly reproduced for the case analyzed here (retrieval errors being of the order of the diurnal variability). Sentinel 4 goal closest to the truth in PBL.
Conclusions of Part II: Sensitivity analyses - retrieval experiments
B. Retrieval experiments
A. Sensitivity analyses
Ozone retrievals from IRS-MTG

## Slide 7
Spectral resolution and sampling
MOPD  sampling  FWHM of non-apodized ILS
0.8 cm  0.625 cm-1  0.75cm-1  IRS-MTG
 4.0 cm  0.125 cm-1  0.15cm-1  Sentinel 4 (goal)
2.0 cm  0.250 cm-1  0.30cm-1
1.0 cm  0.500 cm-1  0.60cm-1  Sentinel 4 (Threshold)
Radiometric noise
NEDT (of 280K blackbody)  NESR
0.85 K  6.12 10-9 W/cm2 sr cm-1  IRS-MTG
 0.05 K  3.60 10-10 W/cm2 sr cm-1  Sentinel 4 (goal)
 0.15 K  1.08 10-9 W/cm2 sr cm-1
IRS-MTG
Sentinel 4 (goal)
Sentinel 4
(threshold)
IRS-MTG IRS7: OPD = 0.8 cm NEDT = 0.85K
A. Sensitivity analyses
Results for carbon monoxide

## Slide 8
10%
MTG-IRS
Sentinel 4 threshold
a priori variability
DOFS
Total column error
Varying spectral resolution and noise
= 0.96; T = 0 K
NeDT 0.85 K
NeDT 0.15 K
NeDT 0.05 K
Sentinel 4 goal
MTG-IRS
Sentinel 4 threshold
Sentinel 4 goal
DOFS of 1 for MTG-IRS
Up to 3 for Sentinel 4 - goal
13 % on total CO column for MTG-IRS
Down to 5 % for Sentinel 4 - goal
A. Sensitivity analyses
Summary
Results for carbon monoxide

## Slide 9
a priori variability
LT (0-6 km) column
a priori variability
Trop. (0-12 km) column
UT (6-12 km) column
a priori variability
a priori variability
PBL (0-2 km) column
MOPD=0.8 cm (IRS-MTG)
MOPD = 2.0 cm (Sentinel 4 threshold)
MOPD = 4.0 cm (Sentinel 4 goal)
Varying spectral resolution and noise
= 0.96; T = 0 K
10%
MTG-IRS
Sentinel 4 threshold
Sentinel 4 goal
20%
MTG-IRS
Sentinel 4 threshold
Sentinel 4 goal
A. Sensitivity analyses
Summary
Results for carbon monoxide

## Slide 10
DOFS is 1  only a total (tropospheric) column can be retrieved by MTG-IRS
Error on the CO tropospheric column is ~15 %.
Sentinel 4 – threshold improves slightly upon the vertical sensitivity and the errors
Sentinel 4- goal allows retrieving vertically resolved profiles of CO (DOFS up to 3). For that instrument tropospheric (0-12 km) and PBL (0-2 km) column errors are around 5% and 20% respectively
Impact of thermal contrast (T=Tground-Tatm@surface): Impact is in the lower troposphere.
The error on the tropospheric decreases below 10 % for high positive values (+5 K) of T
Conclusions of Part II: Sensitivity analyses - retrieval experiments
Carbon monoxide retrievals from IRS-MTG
A. Sensitivity analyses

## Slide 11
General conclusions
CO and O3 pollution events in Europe are occurring in summer + daytime (O3)
Thermal contrast is higher during day and summer, over land
Current instruments show an improved sensitivity towards the surface when there is a thermal contrast
IRS has a limited sensitivity for the PBL but is able to provide more measurements including in the afternoon
IRS-S4 provides improved measurements in terms of accuracy and vertical information/sensitivity

## Slide 12
General conclusions
Will IRS/MTG be able to detect pollution events ?
Yes, because extreme events generally occur over land/during
day when thermal contrast (and hence instrumental sensitivity) is high
Is IRS/MTG the instrument we would like to have to perform TIR chemistry measurement from a geo?
No, because of limited vertical sensitivity and accuracy, in particular in the boundary layer
Is IRS/MTG able to detect the diurnal variability for O3 et CO?
Probably not, because of limited sensitivity and low diurnal variability
Will the complementarity with UVN-S4 will help to improve O3 ?
Yes, because of different vertical sensitivity a combined retrieval
will provide an improved product

## Slide 13
O3
NO2
CO
PM2.5
SO2
IRS
S4-UVN
+ VOC + NOy + H2O + …
Diurnal and day-to-day variations of key trace gases
and fine particulate matter
Introduction: Air quality

## Slide 14
Number of exceedance days of the threshold value for the information to the public
CO
O3
Years 2003, 2004 et 2005 (49 days over limit) | All pollutants + all regions | Ozone Paris | Ozone Suburb | Dioxyde d'azote Paris
Event forecasted | 63% | 45% | 68% | 33%
Un-detected event | 29% | 26% | 31% | 28%
False alarm | 37% | 55% | 29% | 67%
Courstesy to Air Parif - http://www.airparif.asso.fr/pages/prevision/intro
Introduction: Air quality

## Slide 15
MOPITT CO China
[Clerbaux et al, GRL, 2008]

## Slide 16
Fires in Greece, 25 August 2007
Credit D. Hurtmans, S. Turquety (ULB, SA)
IASI CO
Smoke plume (meteosat data)
Turquety, ACP, 2009