## Slide 1
Chemical and Aerosol Sounding Satellite (CASS)
Presentation to CEOS ACC-5
Atmospheric Composition Constellation Meeting
30 March 2010
Thomas Piekutowski
Director, Earth and Solar System Sciences
Notes: 1

## Slide 2: Background
CASS is a gap-filling mission to continue climate-quality solar occultation measurements of stratospheric and upper tropospheric composition with the proven ACE-FTS and SAGE III instruments. It is meant to continue the long series of solar occultation measurements after SCISAT and until NASA launches the Global Atmospheric Composition Mission (GACM) in 2025+.
CASS is meant to be built and launched quickly, with minimal time spent on technology development.
Continued occultation measurements are strongly endorsed by the:
  International Ozone Commission,
  CEOS Atmospheric Composition Constellation Data Gaps Report,
  NAS Decadal Survey for Earth Science (USA),
  20th Meeting of the Parties to the Montreal Protocol,
  ESA’s CAPACITY report.

## Slide 3: Proposed CASS Instruments
Atmospheric Chemistry Experiment - Fourier Transform Spectrometer (ACE-FTS) similar to the one on SCISAT, with corrections of known shortcomings (internal reflections on imagers, beam-splitter coating spectral cut-off ) and modifications to improve pointing knowledge (will help with retrieval of CO2 profiles).
Stratospheric Aerosol and Gas Experiment instrument from storage at Langley. SAGE III is a UV-Vis-NIR spectrometer that makes measurements with solar and lunar occultation and with limb scattering.
Both of these instruments have proven science value, robust performance of flight hardware and well developed data retrieval algorithms.

## Slide 4: CEOS-ACC Gaps Report Rec #2
CSA should consider plans to develop an ACE-II instrument. The current ACE instrument on SCISAT has provided unique and critical high resolution trace gas measurements for improved understanding on atmospheric chemistry processes and their climate links. A follow-on ACE-II instrument would benefit from existing ACE science and data infrastructure, thereby minimizing cost to CEOS agencies.
In addition, NASA should concurrently consider a flight opportunity for the SAGE-III instrument (in storage) for aerosol and ozone profiles. It is believed that climate cannot be adequately addressed with only nadir aerosol optical depth due to uncertainty in height distributions whereas the combination of these missions would address those issues.

## Slide 5: CASS Partnership Scenarios (autumn 2009)
Scenario 1: CSA provides FTS and related science operations. NASA provides SAGE-III, related science operations, spacecraft, AIT, launch and satellite operations.
Scenario 2: CSA provides FTS and related science operations, spacecraft, AIT and satellite operations. NASA provides launch, SAGE-III and related science operations.
Each instrument team performs their own data retrievals, data distribution and preservation.
February 2010: NASA will assess flight of SAGE-III on ISS ~2013

## Slide 6: CASS – Current Status
Exchanging information with NASA about the assessments each is performing.
CSA awarded an Accommodation Study (Dec 2009 – June 2010) with Bristol Aerospace including:
  Bristol MAC-200 Bus layout
  Mass & Power budgets (Polar Panel concept)
  Data Management and Communication Assessment
  Pointing assessment of spacecraft and instruments
  Launch options
  Nominal Spacecraft concept of Operations
  TRL Levels and Risk Assessment
  Mission costs and options

## Slide 7: Current Status cont.
CSA awarded a Feasibility Study (Dec 2009 – June 2010) with ABB Bomen including:
  Review and resource components for rebuilding and ACE “As-is”
  Review and propose costs of minor improvements identified in SciSat-1 project. Extend wavelength range to 4500 cm-1 with SNR > 100 for better retrievals of HF, CO
  Study improvements of sun tracker to reach 5 km altitude.
  Study ways to improve pointing knowledge.
  Determine cost, schedule and risks.

## Slide 8: Alternate Considerations
NASA is considering flying SAGE-III on ISS by 2013
CSA will likely assess ISS as platform for ACE-FTS (work not yet begun)

## Slide 10: Backup Slides