## Slide 1
Status/Scope of Japanese Geostationary Satellite
Shuji Kawakami (kawakami.shuji@jaxa.jp)
Earth Observation Research Center
Japan Aerospace Exploration Agency
(JAXA/EORC)
Notes: <number>

## Slide 2
<number>
Disasters
Energy
Climate
Water
Health
Weather
Ecosystems
Agriculture
Biodiversity
GEOSS and Japan’s priority (Global Earth Observation System of Systems)
Japan’s 3 priority areas among 9 GEOSS societal benefits:
  Reduction and Prevention of Disasters
  Climate change, including Water-cycle variation
  Global warming and Carbon cycle change
Special focus on Asia-Pacific Region
9 Societal Benefit Areas
Notes: <number>

## Slide 3
<number>
Long-Term Plan of JAXA Earth Observation
Targets |  | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Disasters & Resources |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Climate Change & Water Water Cycle |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Climate Change |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Greenhouse gases |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Phase A
On orbit
Extension
Mission status
[Land and Disaster monitoring]
GPM/DPR
Aqua/AMSR-E
GCOM-C1/ SGLI
[Vegetation, aerosol, cloud, SST, ocean color]
[Cloud and Aerosol 3D structure]
[CO2, Methane]
TRMM/PR
GCOM-W1/ AMSR2
[Wind, SST , Water vapor]
Phase B~
[Precipitation]
[CO2, Methane]
GCOM-W2
GOSAT-2
ALOS-3 Optical
ALOS-2 SAR
ALOS/PALSAR
ALOS/PRISM AVNIR2
ALOS
EarthCARE/CPR
GCOM-C2
GOSAT
TRMM
Pre-Phase A
AQUA
250m, multi-angle, polarization
<number>
Geostationary Satellite
Air Quality/Climate Change/Meteorology
Notes: <number>

## Slide 4
Increase of Anthropogenic Emissions of NOx in Asia
Akimoto, Science, 2003.
Ohara, Akimoto, et al. ACP, 2007.
Increased by a factor of 3 in Asian total (×4 in China)
REAS: 1980-2003
1970-2000
Asian Emission is Overwhelming
after 2000
Needs of Geostationary Satellite for Air Pollution in Asia
From Dr H. Akimoto’s AGU presentation
Notes: <number>

## Slide 5
・ Surface observation sites for continuous measurement of air quality are very scarce.
・ Observational data are not necessarily open to public in many countries except for international network sites.
● Ozone Sonde ● Surface Ozone
WMO/GAW Ozone Stations
EANET Stations: wet 55/gas, aerosol 44
However, -----
From Dr H. Akimoto’s AGU presentation
Notes: <number>

## Slide 6
Scientific Requirement of Air Quality
■Region：Asia; Japan and East China
■Temporal&IFOV：hourly & 10 km
■Two Instruments on Geostationary satellite
UV/Vis Spectrometer for O3, NO2
Thermal infrared Imaging FTS for Ozone/CO/Temperature/Humidity
The scopes are Air Quality, Climate Change and Meteorology.
Currently Unnamed
To observe temporal and spatial distributions of ozone, aerosols and
their precursors in Asia
To identify emission sources, transport and photochemical processes
To serve for atmospheric environment policy by clarifying atmospheric
environment issues in each region and transboundary air pollution
To aim for accurate chemical weather forecasting by data assimilation
From Dr H. Akimoto’s AGU presentation
Notes: <number>

## Slide 7
Background of JAXA Geostationary Air Quality and Meteolorogy Satellite
2010 Study of key technology of an imaging FTS
..........
2013? Phase C/D
2017? Launch
Japan Society of Atmospheric Chemistry：Committee on Atmospheric Environment Observation Satellite (Leader: Dr. H. Akimoto)
Feasibility Study WG@the committee above Science Requirement Team (SRT) Simulations and Sensitivity Study Team (S3T）
JAXA： Committee for Discussion on Geostationary Atmospheric Observation Mission
2006
2007
2008
JAXA： Communication with Japan Meteorological Agency, etc
JAXA：MDR (Mission Definition Review) on 24th December
2009
for next generation of Met. Sat. not operation
Notes: <number>

## Slide 8
 | UV/VIS | Thermal IR
L1 products | Radiance | BrightnessTemp.
L2 products (research products) | O3, NO2, (SO2, HCHO, Aerosol(AOT)) | O3 (upper/lower Trop.) , CO, (HNO3), H2O, Temp.
Diurnal Observation | Daytime only (hourly) | Day and Night (hourly)
Observation Area | Japan and East China (4000 km×4000 km) | Full disk
Spectral Domain | 280-600 nm [753-784 nm (O2-A)] | 700-1200 cm-1 1600-2250 cm-1
Spectral Resolution (sampling interval) | <0.6nm(0.1nm@310-600 nm) [<0.12 nm (O2-A)] | 0.6 cm-1
IFOV | 40 km (280-310 nm) 10 km (310-600 nm) | less than 10 km (4km)
S/N (requirement to instr.) | 350@500 nm、500@330 nm | 0.23K(SN290)@1030cm-1 0.85K(SN30)@2160cm-1
Notes: <number>

## Slide 9
Mission Study Status
Requirements
  Air Quality: Baseline requirements from
    Commisson for Discussion on Geostationary Atmospheric Observation Mission
    this requirements based on originally proposed by Japan Society of Atmospheric Chemistry：Committee on Atmospheric Environment Observation Satellite
  Meteorology: Baseline requirements from
    WMO GOS-2009 and communication with Japan Meteorological Agency
Status
  Measurement, instrument and retrieval requirements have been defined at MDR, but it’s still preliminary level and refining is necessary.
  Study of instrumentation will be made in 2010. Especially key technology on imaging FTS
Notes: <number>

## Slide 10
Organizations’ needs which presented at JAXA MDR
Ministry of Environment(http://www.env.go.jp)
National Institute for Environmental Studies(http://www.nies.go.jp)
  Contribution to better public service on Air Quality
  Tropospheric Ozone/PM2.5/Kosa(yellow sand dust)
Japan Meteorological Agency(http://www.jma.go.jp)
  Weather forcasts
  Vertical profiles of Temperature and wator vapor with higher frequency and higher vertical resolution
Meteorological Research Institute(http://www.mri-jma.go.jp)
    Contribution to improvement of public service on Environmental Meteorology(Air pollution, Kosa)
    Tropospheric Ozone/NO2/Aerosols
Japan Petroleum Energy Center (http://www.pecj.or.jp)
  JATOP:Japan Auto-Oil Program
    Utilization and improvement of air quality model
National Maritime Research Institute (http://www.nmri.go.jp)
  Ocean Environment: Air Quality over coasts/oceans : NO2/SO2 from ships
Notes: <number>

## Slide 11
Mission Study Issues in 2010 (Action Items of the MDR)
  To merge Ministry and Agency’s further needs into the requirement
    Studies for SO2 and aerosols (especially PM2.5) are needed
Listen to requirements from users in Asia
Imaging FTS
  Study of key technology of Imaging FTS
  Calibration/data processing
Notes: <number>

## Slide 12
Summary
Overview of Japanese Geostationary Satellite Mission (Currently Unnamed)
The scopes are Air Quality/Meteorology/ Climate Change
Geosynchronous orbit with two instruments
  UV/Vis Spectrometer for O3, NO2
  Thermal infrared Imaging FTS for Temperature/Humidity/Ozone/CO
  Observation area: Asia; Japan and East China
  frequency: hourly
In 2010 Study of key technology of Imaging FTS
Notes: <number>