## Slide 1: NASA’s plans for Orbiting Carbon Observatory – 2
Ken Jucks and Rich Eckman
NASA
March 31, 2010

## Slide 2: Executive Summary
The Orbiting Carbon Observatory (OCO-2) is designed to demonstrate a unique measurement technique to improve our understanding of the global carbon cycle by returning space-based measurements of atmospheric carbon dioxide (CO2) with the sensitivity and sampling density required quantify regional scale carbon sources and sinks and characterize their interannual variability.
  The management of atmospheric CO2 is an important science policy issue for the 21st Century
  OCO will provide a proof-of-concept of how space borne technologies can monitor greenhouse gas emissions
OCO was delivered to VAFB to be launched in 25 February 2009 but the launch vehicle failed to deliver the Observatory to orbit
In the President’s FY11 budget, there is language and funds to rebuild OCO.
OCO-2 was approved by NASA on February 24, 2010 to enter mission formulation

## Slide 3: OCO-2 Is Designed to Revolutionize Global Carbon Cycle Science
Current measurement networks are unable to deliver the observations needed to close the carbon budget, resulting in a “missing sink” corresponding to about half of the annual fossil fuel emissions
Fundamental questions:
  Where is the missing sink?
    land or ocean?
    when does it occur?
  Why does the sink strength vary dramatically from year to year?
  Will the nature, location and strength of CO2 sinks change in the future?
Annual fossil fuel emissions, the major anthropogenic CO2 source, increase smoothly over time.
The accumulation rate of atmospheric CO2 varies dramatically from year to year due to variation in the fundamental processes responsible for land and ocean sinks.
  OCO-2 is designed to deliver the observations needed to characterize CO2 sources and sinks
    No other existing or planned satellite sensor will match OCO’s capabilities

## Slide 4: Why Precise Space-based CO2 Measurements are Needed
R. Kawa, personal communication (2009)
Simulated global XCO2:
North-South gradients ~ 3-8 ppm
East-West gradients < 2 ppm
Regional gradients ~1 ppm
Scale lengths: Land ~100 km, Ocean ~1000 km

## Slide 5: Orbiting Carbon Observatory-2 Measures Reflected Solar Radiances
OCO-2’s small footprint maximizes the probability of observing scenes clear enough to sense the entire column
OCO-2 measures reflected solar radiances to maximize sensitivity to surface CO2
Notes: OCO is designed to provide the data needed to find the missing pieces of the carbon puzzle (sinks)

## Slide 6: The OCO-2 Instrument
3 co-bore-sighted, high resolution, grating spectrometers
  O2 0.765 m A-band
  CO2 1.61 m band
  CO2 2.06 m band
Resolving Power> 20,000
Optically fast: f/1.8 (high SNR)
Footprint size: 1.29 x 2.25 km @ nadir
Swath: 0.8 (10.6 km at nadir)
Mass: 140 kg
Power: ~105 W
Advantages
  Most sensitive to near surface CO2
  Can “target” off-track locations
  No limited-life components
  Ideal for long-term monitoring
  2-8 year lifetime.
Collimator
Slit
Grating
Relay
Optics
Telescope/
Recolimator
Detector
Light
Trap
Polarizer
Beamsplitter
&Pre-Filter
Cold
Filter
Camera
Notes: <number>

## Slide 7: GOSAT provides key experience for OCO-2
While designed around different instruments, both GOSAT and OCO-2 have wavelength regions in common with differences in sensitivity (SNR).
GOSAT baseline: SNR ~300 for 30% albedo, 30 deg SZA
OCO baseline: SNR ~300 for 5% albedo, 60 de SZA
Collaboration with Japanese GOSAT has provided OCO/ACOS team with data to test retrieval algorithms and validation approach developed for OCO.
GOSAT
OCO-2

## Slide 8: OCO-2 vs. GOSAT: Global Sampling Strategies
3-day global repeat cycle
FOVs spaced 160 km apart in 5-point raster
Glint obs limited to ±35 deg
Near Surface Winds
High Altitude Winds
16-day global repeat cycle
Contiguous sampling along track
Adjacent orbits 150 km apart
Global Glint obs
Point and stare Target mode

## Slide 9: Latest OCO/ACOS Results Using GOSAT Data
Global Mean (ppm): 376.53
North (20-60o)
Mean: 376.34
STD : 6.74
South (20-60o)
Mean: 376.94
STD: 3.82

## Slide 10: Interhemispheric CO2 gradients
OCO-2 will provide the precision and accuracy to determine the trends and gradients seen in CO2 by highly precise and accurate aircraft measurements (HIAPER series of aircraft flights).
S. Wofsy, private communication, 2009

## Slide 11: Programmatic Status
In the FY10 budget NASA has been directed to fund OCO-2 not less than $50M. This and residual project funds have been used to purchase long lead items for a new instrument.
FY11 President’s Budget identifies a funding profile for OCO-2:
On February 24, 2010, NASA authorized the project to begin mission formulation
  Critical Design Review planned for August 2010
  Authorization to Proceed (Key Decision Point C) planned for October 1, 2010
  Launch Readiness Date of Feb 2013
The new budget also for a complete set of spares to build a new instrument as a “Mission of Opportunity”.
OCO-2 and potential OCO-MoO will be followed by the ASCENDS mission.
Notes: <number>