## Slide 1
7th CEOS Atmospheric Composition Constellation Meeting
Washington Area, USA
21-22 June 2011
Lessons learnt from the validation
of GOME Total Ozone Columns
Jean-Christopher LAMBERT
Belgian Institute for Space Aeronomy (IASB-BIRA)
j-c.lambert@aeronomy.be
Presented by Michel Van Roozendael (IASB-BIRA)
Committee on Earth Observation Satellites

## Slide 2
History of GOME validation at IASB-BIRA
Lessons, questions and recommendations
Validation in the maturation process of GOME Data Processor
Metrology of a data comparison – Smoothing errors
Conclusion
7th CEOS Atmospheric Composition Constellation Meeting, Washington Area, USA, 21-22 June 2011
Lessons learnt from the validation
of GOME Total Ozone Columns

## Slide 3: History of IASB-BIRA validation support to GOME Data Processor (GDP) development
GDP Version | Time Frame | Major Milestones and Deliverables
1.15 | 1995 | First orbits - Report at DLR meeting
1.20/21 | Jan. 1996 | ESRIN workshop + ESA WPP-108
1.40/50/60 | Spring 1996 | val + 2 workshops at DLR
2.0 | 1996-1997 | val + QO3OS + ERS symp. + ESA SP-414 + J. Atmos. Sci. 1999
2.3/2.4 | 1998-2000 | val + ESAMS + WPP-161 + ESA EOQ + COSPAR + Adv. Space Res. 2000 + QO3OS
2.7 | 2000-2002 | val + Issl. Zemli iz Kosmosa 2003
3.0 | 2002-2004 | val + Envisat Symp. + Appl. Optics 2005
4.0/4.1 | 2004-2006 | val + 2 JGR 2007
5.0 | 2006-2011 | val + 2 JGR 2011 + work on GODFIT prototype
Note: val = meeting(s) + Technical Note

## Slide 4: Lessons learnt, questions and recommendations
Goal: To determine the fitness of satellite O3 column data for intended use(s). Usually done by comparison with reference data: Brewer, Dobson, NDACC/UVVIS, other satellites.
User requirements:
  Bias and precision estimates => How can we determine them from comparisons? Can we determine them? => See metrology of a data comparison.
  Global ozone assessments (e.g. 60°N-60°S average anomaly): How representative are validation results based on a single station? Are global networks representative of the global atmosphere? Any SAT or GB error dependence on time, latitude, temperature…? How meaningful is a global average of discrepancies with respect to reference data? How meaningful is a SAT vs. GB correlation coefficient?
  Polar processes: Any dependence on SZA, on temperature, on surface albedo, on PSCs…?
  Ozone/climate links: Long-term stability, short term variability?
In brief: Validation results should go beyond a mean difference.

## Slide 5: Lessons learnt, questions and recommendations
A 3-month commissioning phase is not long enough to enable detection of major cyclic errors: dependence on SZA, temperature etc. At least one year of data is required.
Validation of bias and stability at the « 1% level » is a challenge, considering:
  The error budget of a data comparison in a variable and structured atmosphere
  The known uncertainties in GB measurements and known discrepancies between existing GB networks
  The continuity and actual quality of archived ground-based data
Information content aspects can play an important role. E.g., understanding of smoothing errors can be critical for a proper interpretation of comparison results. Understanding of what the algorithm retrieves exactly is also vital: e.g., what do we retrieve exactly as information on clouds by looking at the O2 A band (SWIR) and at PMD readings in three different spectral ranges? Are effective CF and CTH estimates representative of the cloud effect on an ozone retrieval in the Huggins band?

## Slide 6: Lessons learnt, questions and recommendations
Several validation activities (with appropriate effort) should be considered:
  Test case validation in support to algorithm development
  Delta validation after algorithm improvement, new XS and albedo databases, new cloud algorithm etc. on a dedicated delta validation set of orbits and reference data
  After reprocessing with an improved algorithm, detailed validation of the entire data record, before public release
  In routine, as a monitoring task
Bidirectional and sustained collaboration between algorithm developers and validators (and users) is essential. Development, validation and use of the data are three very different types of activities requiring different expertise.
Validation is usually not the most exciting and best funded part of the work. But it is essential. For GOME, GDP developments from early V 2.6/2.7 to current V 5.0 have been supported by appropriate validation programmes. “Routine” long-term validation is not envisaged, fortunately there are regularly major reprocessings with validation support.

## Slide 7: Role of validation in the maturation process of GDP
GDP 1.20
1995
GDP 2.0
1996
GDP 2.7 / 3.0 / 4.0
1999 / 2003 / 2006
GDP 5.0
2011
RTS

## Slide 8: Role of validation in the maturation process of GDP

## Slide 9
Lambert et al., Adv. Space. Res. 2000
Role of validation in the maturation process of GDP

## Slide 10: Delta validation of improvement between GDP 4.21 and 5.0
Midnight Sun
Mid morning
Midnight Sun
Mid morning

## Slide 11: SZA is OK? => Then cloud effects can be detected.

## Slide 12: SZA is OK? => Then cloud effects can be detected.

## Slide 13: Metrology of a data comparison Error budget
1. Errors due to measurement noise of the individual measurement systems: S1N and S2N
2. Uncertainties associated with the forward and inverse models and parameters: S1M and S2M
3. Comparison errors due to differences in smoothing of atmospheric variability:
. vertical smoothing: SSV = (A1V - A2V ) SV (A1V - A2V )T
. horizontal smoothing: SSH = (A1H - A2H) SH (A1H - A2H)T
. temporal smoothing: SSt = (A1t - A2t) St (A1t - A2t)T
4. Comparison errors due to differences in sampling of atmospheric structures, often called errors due to vertical/horizontal/temporal mismatch:
. vertical sampling: SdO3/dz
. horizontal sampling: SdO3/dH
. temporal sampling: SdO3/dt

## Slide 14
Metrology of a data comparison
Air masses probed by GOME, SCIAMACHY and NDACC instruments
in the vertical and horizontal dimensions

## Slide 15
Smoothing by GOME-2: O3 column
Vandenbussche et al., 2011

## Slide 16: Horizontal smoothing by GOME-2
West
West
East
East
Scatterer
to satellite
Sun to
scatterer
Vandenbussche et al., 2011

## Slide 17: Horizontal smoothing by NDACC/UVVIS
Dobson, Brewer, FTIR
DOAS, SAOZ

## Slide 18: Smoothing error for ozone column measurements – Ground-based zenith-sky observation at twilight
Tarawa (Kiribati, 1°N / 173°E)
Dumont d’Urville (French Antarctica, 66°S / 140°E)
Kerguelen (Indian Ocean, 49°S / 70°E)

## Slide 19: Conclusion
Lessons have been learnt and recommendations drawn from 15 years of GOME validation and support to GDP maturation.
Validation must encompass studies of several dependences and look at statistics with care.
In many cases validation needs to abandon the idea that we are comparing true vertical columns. Differences in 2D/3D smoothing of atmospheric gradients can explain a large part of the scatter in the comparison results, and sometimes also biases (in case of permanent gradients).
Generic validation protocols exist for atmospheric data and services (PROMOTE, MACC, Ozone-cci PVP etc.) Starting from them, CEOS WGCV might wish to develop an illustrative validation protocol for satellite ozone column and profile data.