## Slide 1: Atmospheric Composition Constellation Meeting (ACC-7) 21-22 June 2011, Columbia, MD, USA
The merged Weighting Function DOAS (WFDOAS) total ozone data set derived from GOME, SCIAMACHY, and GOME-2 (1995-present)
M. Weber, S. Dikty, W. Chehade, G. Kiesewetter, A. Serdyuchenko, C. von Savigny, and J. P. Burrows
Institute of Environmental Physics (IUP),
University Bremen (UB)
www.iup.physik.uni-bremen.de/UVSAT weber@uni-bremen.de
Notes: <number>

## Slide 2: Releavnt ozone research at IUP
IUP University of Bremen:
  PI and lead scientist (J. P. Burrows) for SCIAMACHY and GOME1
  UV/VIS/NIR satellite retrievals (limb/occultation, nadir)
  Remote sensing from ground/ship (DOAS, MAXDOAS, etc.)
  radiation transfer modelling
  chemical transport modelling and data assimilation
  laboratory spectroscopy (absorption cross-section)

## Slide 3: Ozone data sets at IUP
Ozone data sets created by IUP-UB for science and WMO UNEP Assessments:
  WFDOAS total ozone (see this talk) 1995 to present
  SCIAMACHY limb ozone profiles (global,10-70 km, 3 km vertical resolution, horizontal resolution 240x400km, von Savigny et al., 2005, Sonkaew et al., 2009) 2002-present
  Vertical profiles from nadir sounding GOME, SCIAMACHY, GOME-2 in prepation 1995 to present
  SCIAMACHY occultation profiles (solar: NH latitudes, lunar: SH) 2002 to present
  total ozone columns from BREDOM DOAS ground network
  www.iup.uni-bremen.de/sciamachy/dataproducts/index.html www.iup.uni-bremen.de/doas

## Slide 4: Ozone data sets at IUP
Data assimilation (Kiesewetter et al., JGR, 2010)
  sequential assimilation of SBUV v8 partial columns (10/1978 – 12/2007 so far)
  Bremen 3D CTM and ERA-Interim/ERA-40
  good agreement with observed total columns
  contact: gregor@iup.physik.uni-bremen.de
New ozone absorption cross-sections (Serdyuchenko et al.)
  Echelle (UV) and FTS (VIS) measurements
  10 temperatures (193-293K), 220-1000 nm
  high spectral resolution: 0.003 nm
  precision: 2%
  release: late summer
Updated ozone x-section
  reanalysed SCIAMACHY FM (Bogumil et al. 2003)
and GOME-2 FM3 data (Gür et al., 2005)
    improvements in the Huggins band
  release: late summer

## Slide 5: WFDOAS total ozone retrieval
Major features of the iterative WFDOAS retrieval (Coldewey-Egbers et al. 2005, Weber et al., 2005):
  Direct fitting (no lookup tables, radiative transfer part of retrieval)
  includes ozone temperature fit (shift in temperature profile)
  improved treatment of rotational Raman scattering on air molecules (Ring effect) properly accounting for the varying ozone filling-in
  cloud retrieval/correction using SACURA (Kokhanovsky et al. 2005) or FRESCO (Koelemeijer et al. 2001) cloud retrievals in the oxygen A-band
  albedo retrieved at 378 nm (LER method)
after Lee et al., 2008

## Slide 6: WFDOAS data sets
Data sets:
  GOME1/ERS-2: 1995-present (lost global coverage after 2003)
    global coverage: ~3 days, large ground pixel: 320 x 40 km2
  SCIAMACHY/ENVISAT: 2002-present
    limb and nadir alternating, global coverage ~6 days
  GOME-2/METOP-A: 2007-present
    wide swath, daily coverage ~1 day, small ground pixel: 80 x 40 km2
  GOME-2/METOP-B: to be launched in April 2012
  GOME-2/METOP-C: ~2016
GOME1 is the „gold standard“ for
the European satellite total ozone
record
www.iup.physik.uni-bremen.de/gome

## Slide 7: WFDOAS validation with respect to Brewer/Dobson
Dobson
+0.8%
Brewer
+0.6%
0.0%
-1.0%
-0.6%
-1.8%
GOME-2
GOME1
SCIAMACHY
collocation criteria: <300 km

## Slide 8: WFDOAS vs. Brewer Hohenpeissenberg (47°N)
biases between satellites:
  1-2%
trends:
  SCIAMACHY: -1%/decade until ~2010
GOME1
GOME-2
SCIAMACHY
collocation criteria: <300 km

## Slide 9: GOME minus Brewer timeseries
Trends:
  GOME stable
  SCIAMACHY:
    -4%/decade until ~2007
    -1%/decade until ~2010 (trend slowdown)
    seen with all algorithms used (ESA, BIRA, KNMI, see Lerot et al 2009)
  GOME-2
    no trend
    jump of -1% after September 2009, due to detector heatup?
Biases between satellites:1-2%
Notes: Note : in the SCIA comparison it seems that SCIAMACHY minus Brewers is slightly positive lately. This is not seen in the Dobson comparison, but the validation slide shows a 1% difference when comparing with Dobsons and Brewers (SCIA, GOME2), but only 0.2% for GOME when comparing to brewers and dobsons, separately (see two slides earlier).
<number>

## Slide 10: Merging strategy for GOME/SCIAMACHY/GOME-2
Merging strategy:
  Use GOME1 as reference („gold standard“)
  Determine corrections (factor, linear trend) from GOME/satellite ratio time series using monthly means, 1°x1.25° binned data
    multiplicative correction
  SCIAMACHY
    factor + linear trend
  GOME2
    factor only

## Slide 11: Corrected data sets
  Merged GSG data: GOME (1995/07-2003/05), SCIAMACHY (2003/06-2006/12), GOME-2 (2007/01-present)  use satellite with best global coverage
  Remaining issue (under investigation):
    bias between SCIAMACHY and GOME-2 after 2009/10?
      SCIAMACHY: instrumental trend slow down since ~2009
      GOME-2: jump by ~-1% after decontamination/detector heatup in September 2009
Notes: Note: the GSG merged data (solid points) are not exactly identical to GOME and adjusted SCIA/GOME2 - reason is that for each data set (original, adjusted, and merged) the seasonality may differ due to different time periods fitted.
<number>

## Slide 12: GSG merged data set: global anomalies
Science:
  extreme conditions within last decade (climate related?):
    split ozone hole in 2002, WMO 2007), record size ozone hole in 2006, very high NH ozone in 2010, Steinbrecht et al., 2011), record Arctic ozone loss in 2011
record Arctic
ozone loss 2011
very high NH ozone 2010
record size ozone hole 2006
split ozone hole 2002
QBO
Notes: QBO east leads to more planetary waves in extratropics and perturbed vortex (high ozone transport, low chemical ozone loss at high latitudes). This happened in 2010, that yera showed also an extreme b´negative AO index (arctic oscillation). In spring 2011 we had the oposite, QBO west phase, little wave activity and strong chemical ozone loss in the Arctic. In 2002, a major stratopheric war
<number>

## Slide 13: Long-term ozone trends
Ozone trends:
  WOUDC
  SBUV/TOMS/OMI (Mod V8)
  GSG data set
GSG merged total ozone data:
www.iup.uni-bremen.de/gome/wfdoas
Weber et al., 2011

## Slide 14: Conclusion
  A merged WFDOAS total ozone data set is available
    GSG data set (1995-present)
  WFDOAS overpass data (uncorrected data) for NDACC/WOUDC stations available
    www.iup.uni-bremen.de/gome/wfdoas
  Important issues when merging data sets:
    justification of the reference data set (GOME1 stable in comparison to ground)
      GOME1 although working excellently and yielding ~40% coverage is to be de-commissioned by ESA this summer (:-(.
    overlap periods between instruments are available (not an issue here since all instruments GOME/SCIA/GOME-2 are still operating)
    Bias/ratio and trend (linear)correction is fairly straight forward
      are multiplicative or additive corrections better?
    more challenging: changes in instrumental trends with time (SCIAMACHY?), sudden jumps in the data record (GOME-2?)
      requires good knowledge of instrument status and calibration changes