## Slide 1: Monitoring the Atmospheric Carbon Cycle from Space David Crisp (JPL) Ray Nassar (Environment Canada) March 29, 2012
Copyright 2012 California Institute of Technology. Government sponsorship acknowledged.
Carbon Task Force Meeting

## Slide 2: The Atmospheric Carbon Cycle
YOU ARE HERE

## Slide 3: Global Measurements from Space are Essential for Monitoring Atmospheric CO2
To limit the rate of atmospheric carbon dioxide buildup, we must
  Control emissions associated with human activities
  Understand & exploit natural processes that absorb carbon dioxide
We can only manage what we can measure
Plumes from medium-sized power plants (4 MtC/yr) elevate XCO2 levels by ~2 ppm for 10’s of km downwind [Yang and Fung, 2010].
These variations are superimposed on a background of “CO2 weather”

## Slide 4: Requirement: High Precision
CO2 sources and sinks must be inferred from small spatial variations in the (387 ±5 ppm) background CO2 distribution
The largest CO2 variations occur near surface
Space based NIR observations constrain column averaged CO2, XCO2
XCO2 must be measured with a precision of < 1 ppm on regional scales to resolve the small variations associated with sources and sinks
372
380
Small spatial gradients in XCO2 verified by pole-to-pole aircraft data [Wofsy et al. 2010]

## Slide 5: Requirement: Spatial Resolution
A Small Footprint:
Increases sensitivity to CO2 point sources
  Minimum measureable CO2 flux is inversely proportional to footprint size
Increases probability of recording cloud free soundings in partially cloudy regions
Reduces biases associated with optical path length uncertainties over rough topography
2011/06/22
OCO-Nadir
GOSAT
OCO-Glint
2011/06/19
2011/06/25

## Slide 6: Requirement: Spatial Coverage
Ground based measurements - greater precision and sensitivity to CO2 near the surface, where sources and sinks are located.
Space-based measurements – improve spatial coverage & resolution.
Source/Sink models - assimilate space and ground-based data to provide global insight into CO2 sources and sinks

## Slide 7: Requirement: Coverage of Oceans and Continents
  The ocean covers 70% of the Earth and absorb/emit 10 times more CO2 than all human activities combined
  Coverage of the oceans is essential to minimize errors from CO2 transport in and out of the observed domain
Near IR solar measurements of CO2 over the ocean are challenging
Typical nadir reflectances: 0.5 to 1%
Most of the sunlight is reflected into a narrow range of angles, producing the familiar “glint” spot
Glint and nadir measurements can be combined to optimize sensitivity over both oceans and continents
OCO single sounding random errors for nadir and glint [Baker et al. ACPD, 2008].
3-5 ppm
<0.4 ppm

## Slide 8: Pioneering Missions: Thermal Infrared Observations of CO2
Thermal IR observations (AIRS, TES, IASI, CriS) measure CO2 in the middle troposphere
  Provide global maps of CO2 at altitudes where it is most effective as a greenhouse gas
  Provide limited information about surface sources and sinks of CO2
AIRS July 2003 CO2
378 ppm
AIRS JULY 2008 CO2 (ppm)
388 ppm
Metop IASI
Aqua AIRS

## Slide 9: Pioneering Missions: Full-Column CO2 Measurements using Reflected Sunlight
SCIAMACHY (2002)
  Demonstrated capability, providing regional scale maps of CO2 and CH4 over continents on seasonal time scales
  Limited precision (3-6 ppm), large footprint (18,00 km2), and lack of ocean coverage limited impact on carbon cycle science
GOSAT (2009) -Optimized for spectral and spatial coverage
  Collects 10,000 soundings every day over land and ocean
    10-15% are sufficiently cloud free for CO2 and CH4 retrievals
    Observations of the glint spot within 20°of sub-solar latitude have adequate SNR to allow XCO2 retrievals over the ocean at these latitudes
  Precision requirement is 1% (3-4 ppm), but typical values near 0.5%.
    Adequate to resolve regional-scale XCO2 variations at monthly intervals
  OCO-2 (2014) - Optimized for XCO2 sensitivity and spatial resolution
  Collects up to 106 measurements each day over a narrow swath
    Smaller footprint ensures that >20% all soundings are cloud free
  1 ppm (0.3%) precision adequate to detect weak sources & sinks

## Slide 10: Planned Passive Solar Greenhouse Gas Missions *
TanSat (2015) - First Chinese greenhouse gas satellite
  Uses same O2 and CO2 bands a OCO-2
  Cloud and Aerosol Imager: 0.38, 0.67, 0.87, 1.38 and 1.61μm channels
OCO-3 (2017) - OCO-2 Spare parts instrument, flying on ISS
  First solar CO2 instrument to fly in a low inclination, precessing orbit
GOSAT-2 (2017) – The next step, following GOSAT
  Improved resolution and expanded coverage of the ocean glint spot
  May add a channel near 2.3 µm to measure CO
ESA CarbonSat (2018) – CO2 and CH4 over a broad swath
  Combines high precision and resolution of OCO with a broad swath (160 to 500 km) to yield complete coverage of sunlit hemisphere weekly
CNES MicroCarb (2018) – high sensitivity at low cost
  Flies in the A-Train, providing data continuity for OCO-2
  ~1/2 to 1/3 of the size (and cost) of OCO-2, with similar sensitivity.
    Enables constellations of low-cost CO2 monitoring satellites
*This information based on my notes from the GOSAT-2 Workshop

## Slide 11
Allow full-column greenhouse gas measurements day and night and at high latitudes.
MERLIN (2016): First CH4 LIDAR (IPDA)
  Science focus: Precise (1-2%) XCH4 retrievals for studies of wetland emissions, inter-hemispheric gradients and continental scale annual CH4 budgets
  Orbit: 6AM/6PM, 28-day repeat
ASCENDS (2021): First CO2 LIDAR
  Precise (0.3%) global measurements of XCO2, over days, nights, including winter high latitude regions to quantify continental and oceanic CO2 sources and sinks
  May include a passive (2.3/4.6 µm CO channel
Planned Active Greenhouse Gas Missions*
*Based on notes from the 5th DIAL Remote Sensing Workshop
Notes: The first generation active CO2 sensors are still on the drawing boards.
Active LIDAR instrument concepts like those being considered for ASCENDS cannot provide the sensitivity or coverage of passive solar NIR sensors over most of the sunlit hemisphere, but can return data at night as well as during the day.
These systems are currently being tested in the laboratory and in aircraft. The first space-based deployment is still a few years off.

## Slide 12
Incomplete and not updated with latest mission timelines!
Figure 15, page 28

## Slide 13: Carbon Task Force CO2 and CH4 Missions with near-surface sensitivity
Near-surface sensitivity (NIR or lidar) is needed for source/sink estimation, although TIR measurements (not shown) can be combined with NIR or lidar, yielding vertical resolution.
Moving forward there are abundant TIR observations (IASI, HIRS, etc.) but potentially a NIR data gap without continuation of SCIAMACHY or GOSAT

## Slide 14: GHG Constellations
LEO
Global coverage over many days with one satellite
Multiple satellites needed to achieve continuous observations at one location (depending on swath width)
Lower launch cost per single satellite
Lower risk of spatially-dependent biases in dataset
GEO
Temporally continuous observing over limited area
Weaker signal at large distance, but longer integration times are possible to reduce noise
3 or more satellites needed for full longitudinal coverage
Maximum latitude range of ~55°S-55°N, so must add HEO satellites for continuous coverage of latitudes poleward of ~55°S/N
Moving forward, we also need to have more than one satellite at a time for increased spatial and temporal sampling. LEO and GEO missions each have pros/cons for building a constellation.
There are advantages to combining LEO and GEO due to their complementary nature (as done with missions for operational weather forecasting) when designing an ideal GHG observing system.

## Slide 15: Collaborative Cal/Val Activities
Development / Pre Launch:
Cross calibration of pre-launch radiometric standards
Exchange of gas absorption coefficient and solar databases
Algorithm development/intercomparison
Validation system development (TCCON + Tsukuba FTS?)
Dual/multi-Satellite OSSE’s – what do you gain with truly coordinated observations
Operations / Post Launch:
Cross calibration of solar/lunar/Earth observations
Cross validation: TCCON (possibly adding a validation campaign or two)
Algorithm implementation/intercomparison
Intercomparisons of flux inversions

## Slide 16: Conclusions
Space-based remote sensing observations hold substantial promise for future long-term monitoring of CO2 and other greenhouse gases
The principal advantages of space based measurements include:
  Spatial coverage (especially over oceans and tropical land)
  Sampling density (needed to resolve CO2 weather)
The principal challenge is the need for high precision
To reach their full potential, space based CO2 measurements must be validated against surface measurements to ensure their accuracy.
  The TCCON network is providing the transfer standard
Just as for weather forecasting, a coordinated global network of surface and space-based CO2 monitoring systems as well as sophisticated models that can assimilate these data are needed to provide insight into the processes controlling atmospheric CO2