## Slide 1: CARD4L and the Product Family Specifications (PFS)
LSI-VC-10 Teleconference #1

## Slide 2: Overview
CARD4L assessment progress (Matt for Medhavy)
Consider endorsement of the new Aquatic Reflectance CARD4L PFS [for decision]
SAR & Lidar PFS updates [for information] (Ake Rosenqvist)
  Normalised Radar Backscatter & Polarimetric Radar annual revisions
  Geocoded SLC, Interferometric Radar & LiDAR development status
Status of in-development PFS [for information]
  Nightlight Radiance (Brian)
Hear from participants on the latest plans regarding CARD4L assessment and production [for information]
  KARI, JAXA, ESA, ISRO, NASA, DLR, CSA,,,,, others.

## Slide 3: CARD4L Assessment Progress
v5.0 USGS SR and ST assessments are nearing completion, awaiting response from a panel member
ESA Sentinel-2 SR submission (at Threshold level) has now been received. A quick turnaround assessment is planned, as no review panel is being assembled for this partial assessment.
Element 84 Sentinel-2 SR: further questions have been sent back to Element 84. The assessment is for threshold and partial target.
The DLR EnMap review (simulated products provided) is underway.
INPE and KARI are planning to initiate self-assessments / peer reviews

## Slide 4: Aquatic Reflectance PFS
Christopher Barnes
CEOS LSI-VC, USGS/KBR

## Slide 5: Aquatic Reflectance PFS
Coordinated by: Andreia Siqueira (GA) & Chris Barnes (USGS/KBR)
Development began in March 2020 with endorsement targeted for LSI-VC-10
Applies to data collected by multispectral and hyperspectral sensors operating in the VIS/NIR/SWIR wavelengths over coastal and inland water bodies
Using the Surface Reflectance PFS as a baseline, GEO-Aquawatch, Water-ForCE and subject matter experts around the world met virtually to review/modify and/or generate new Threshold and Target requirements
  Technical Lead: Arnold Dekker (SatDek)

## Slide 6: Aquatic Reflectance PFS
Requirements summary of changes:
  General Metadata (17/17)
  No requirement changes
  Per-Pixel Metadata (13/20)
  1 requirement modified
    Sea/Lake/River Ice Mask
  10 new requirements identified
    Adjacency Effects
    Altitude (ASL)
    Bidirectional Reflectance Distribution Function
    Deep/Shallow Water
    Floating Vegetation/Surface Scum Mask
    Optically Deep or Optically Shallow Assessment
    Sky Glint Mask
    Sun Glint
    Turbid Water Flag
    Whitecap/Foam Mask

## Slide 7: Aquatic Reflectance PFS
Requirements summary of changes continued:
  Radiometric and Atmospheric Corrections (6/15)
  1 requirement modified
    Atmospheric Reflectance Correction
  10 new requirements identified
    Adjacency Effects Correction
    Bidirectional Reflectance Distribution Function
    Floating Vegetation/Surface Scum Correction
  Geometric Corrections (1/1)
  No requirement changes
~80% of the Aquatic Reflectance PFS requirements correspond with Surface Reflectance PFS requirements
    Other Trace Gaseous Absorption Corrections
    Sky Glint Correction
    Sun Glint Correction
    Surface Reflected Vegetation Spectral Correction
    Turbid Water Correction
    Whitecap and Foam Correction

## Slide 8: Aquatic Reflectance PFS
Next steps:
  Seeking Aquatic Reflectance PFS Version 1.0 review and endorsement at LSI-VC-10
  Make Version 1.0 available from the CARD4L website to solicit community feedback
  USGS intends to conduct an informal self-assessment evaluation against its Landsat 8 Provisional Aquatic Reflectance Product
Landsat 8 Provisional Aquatic Reflectance Product. OLI Band 2 (Blue band) San Francisco Bay, CA.

## Slide 9: Radar and Lidar PFS
Ake Rosenqvist JAXA/soloEO

## Slide 10
CARD4L SAR & LiDAR
Current status
Completed 2019 & 2020, Annual rev. 2021
Normalised Radar Backscatter (NRB)
Polarimetric Radar (POL)
Under development:
Geocoded SLC (GSLC)
Interferometric Radar (INSAR)
New under consideration:
Multi-mission NRB
To be revived:
Lidar Terrain & Canopy Height
Notes: To date, there are 4 CARD4L products specifications for SAR products:
Normalised Radar Backscatter (NRB), which is a backscatter-only product (as the name indicates) and it doesn’t contain any phase information. It is the most basic and commonly used radar product, suitable also for users with little or no experience of SAR data.
Polarimetric Radar (POL), aimed at users interested in exploring radar polarimetry
Geocoded SLC (GSLC), which are specs for geocoded complex data, aimed to help non-SAR experts to do InSAR applications.
Interferometric Radar (INSAR) - specifications for interferometric products using two or more SAR images as input
I will provide a brief description of the 4 SAR specifications in the following slides.
The endorsed specification documents are available for public download at CEOS.org/ARD

## Slide 11: CARD4L SAR
CARD4L NRB sample (Processing: Z-S Zhou, CSIRO)
Radar Measurements (RTC γ0)
VV VH
Per-Pixel Metadata
Local Inc Angle
Scattering Area
Sigma-to-Gamma
Data Mask
Ellipsoid Inc Angle
Noise Power
Normalised Radar Backscatter expressed as Gamma-0 (γ0), with Radiometric Terrain Correction (terrain flattening) applied.
NRB structure is used as basis for all SAR PFSs.
NRB endorsed at LSI-VC-7 (2019). 2nd annual revision planned for LSI-VC-10 (today), but postponed to resolve outstanding issue w.r.t. Geometric Accuracy (item 4.3)
Normalised Radar Backscatter (NRB)
Notes: Starting with the CARD4L Normalised Radar Backscatter (NRB), this is an example of what a CARD4L NRB product should comprise of:
The actual sensor measurement data (in this example, the radar backscatter images, provided as Radiometrically Terrain Corrected Gamma-0 for each polarisation band)
General metadata, with all relevant information about the data take, processing steps, geometry and radiometry of the product, provided in a format that is both machine-readable and readable by humans (e.g XML, Json, YAML)
Per pixel metadata – which are image data of the same geometry as the measurement data, including for example, Data/No-Data Mask image, Local incidence angle and scattering area image. Depending on the data provider, the per-pixel metadata may be selected on demand by the user, or (for pre-processed products) consist of a fixed selection.

## Slide 12: Ionospheric effects on SAR geolocation accuracy
Ionosphere
Refraction of microwave signals
Longer
wavelengths
X C S L P
3 5 9 23 69
Band
λ [cm]
Shorter wavelengths
Refraction of microwave signals passing the ionosphere, resulting in a shift in range (cross-track) direction and uncertainty in absolute geolocation.
Geolocation error in turn affects accuracy of Radiometric Terrain Correction
Magnitude of range displacement function of radar wavelength and Ionosphere total electron content (TEC).
Refraction increasing with increasing radar wavelength.
Notes: A number satellite data providers are working to develop CARD4L compliant SAR products to include in their product catalogues. We will hear from a few of them here today in the following presentations.
Thank you for your attention.

## Slide 13
Geometric Terrain Correction (GTC)
0 DEM shift
RTC geolocation displacement test (ALOS-2 PALSAR-2 stripmap 10m)

## Slide 14
Radiometric Terrain Correction (RTC)
0 DEM shift
RTC geolocation displacement test (ALOS-2 PALSAR-2 stripmap 10m)

## Slide 15
Radiometric Terrain Correction (RTC)
1 px shift N and E
RTC geolocation displacement test (ALOS-2 PALSAR-2 stripmap 10m)

## Slide 16
Radiometric Terrain Correction (RTC)
2 px shift N and E
RTC geolocation displacement test (ALOS-2 PALSAR-2 stripmap 10m)

## Slide 17
Radiometric Terrain Correction (RTC)
Radiometric Terrain Correction (RTC)
3 px shift N and E
RTC geolocation displacement test (ALOS-2 PALSAR-2 stripmap 10m)

## Slide 18: Ionospheric effects on SAR geolocation accuracy
Study initiated by CARD4L SAR team to assess impact
Assessing a range of CEOS mission data
  ALOS/ALOS-2, Sentinel-1, Radarsat-1/2, RCM, NovaSAR.
  (SAOCOM, TSX, CSK, if available)
Over a range of geographical areas with different topography and land cover
Aim to complete study in June.
Question: Can endorsement be foreseen between LSI-VC meetings, or will it have to wait until LSI-VC-11 (Sept?)
Example: PALSAR-2 geometric uncertainty.
Note EW (range) > NS (azimuth)
Notes: A number satellite data providers are working to develop CARD4L compliant SAR products to include in their product catalogues. We will hear from a few of them here today in the following presentations.
Thank you for your attention.

## Slide 19: CARD4L SAR
RADARSAT-2 (MDA) Processing: F. Charbonneau (NRCan)
Polarimetric Radar (POL)
PFS development led by NRCan, CSIRO & JPL
CARD4L POL covers two product types:
  Polarimetric Decomposition
  Polarimetric Covariance Matrix
POL structure mirrors that of the NRB, with the exception of the measurement data (🡪)
Endorsed at LSI-VC-9 (2020). Annual revision planned for LSI-VC-10, but postponed until NRB Geometric Accuracy requirement agreed upon.
Notes: Polarimetric Radar (POL) – objective to make radar polarimetry accessible
to enable users to explore
CARD4L POL covers two product types:
  The first one is Polarimetric Decomposition product – which is comparable to the standard backscatter product, but where the polarimetric information has been enhanced – for instance to separate different scattering mechanisms from each other – by the use of various decomposition techniques. Which decompositions to include is not prescribed in the CARD4L specification, but for Data Providers to decide. which ones to offer to users (e.g. Eigen value; Pauli, Freeman-D; Yamaguchi, etc.)
  The second POL product is the Polarimetric Covariance Matrix, which is a set of complex images from which the full polarimetric phase and amplitude can be derived. It is for a bit more advanced users, and can be applied for e.g. polarimetric time-series analysis and Pol-InSAR applications
The CARD4L POL structure is based on NRB, with similar requirements for geometric and radiometric accuracy, and general and per-pixel metadata.

## Slide 20: CARD4L SAR
Polarimetric Radar (POL) - – Polarimetric decomposition
Provides information about scattering mechanisms
Brings out the colour in radar ;-)
ALOS-2 Polarimetric Processing: Y. Yamaguchi (Niigata Univ.)
Cape Lopez Bay, Gabon Niger delta, Nigeria Iguazu, Brazil/Argentina
Notes: Polarimetric Radar (POL) – objective to make radar polarimetry accessible
to enable users to explore
CARD4L POL covers two product types:
  The first one is Polarimetric Decomposition product – which is comparable to the standard backscatter product, but where the polarimetric information has been enhanced – for instance to separate different scattering mechanisms from each other – by the use of various decomposition techniques. Which decompositions to include is not prescribed in the CARD4L specification, but for Data Providers to decide. which ones to offer to users (e.g. Eigen value; Pauli, Freeman-D; Yamaguchi, etc.)
  The second POL product is the Polarimetric Covariance Matrix, which is a set of complex images from which the full polarimetric phase and amplitude can be derived. It is for a bit more advanced users, and can be applied for e.g. polarimetric time-series analysis and Pol-InSAR applications
The CARD4L POL structure is based on NRB, with similar requirements for geometric and radiometric accuracy, and general and per-pixel metadata.

## Slide 21
Geocoded Single-Look Complex (GSLC)
PFS development led by Stanford Univ. and JPL.
Single Look Complex (SLC) is the base Level-1 SAR image product. It comprises information about the received radar amplitude and phase, provided in range/Doppler (slant range) geometry
The CARD4L GSLC product describes the complex radar reflectivity on the surface with all propagational phases removed, so that the amplitude and phase values represent properties of the surface and not the instrument
GSLC data are presented in a common, often user-defined, ground based coordinate system (e.g. UTM, geogr. coord.), rather than in radar slant range coordinates, to facilitate use by non-radar-specialists.
Aim to submit for endorsement at LSI-VC-11.
Stack of geocoded SLC images
(Zebker et al, 2018)
CARD4L SAR
Notes: Single Look Complex (SLC) is the standard Level-1 SAR image product. It comprises information about the amplitude and phase of the received radar energy, provided as a complex number.
SLC are given in slant range geometry and require additional processing software and a fair amount of radar expert knowledge to be used.
The CARD4L GSLC product on the other hand, is an enhanced pre-processed version of the SLC, that describes the complex radar signal at each point on the ground surface with all average propagational phases removed, so that the amplitude and phase values represent properties of the ground surface, without influence by the radar instrument
CARD4L GSLC products are presented in a common geographical coordinate system – such as e.g. UTM - rather than in slant range radar coordinates, to facilitate use by non-radar-specialists
The CARD4L GSLC product specification is still under development and we expect it to be completed within the next few months.

## Slide 22
Sentinel 1 interferometric products (Geoscience Australia team)
CARD4L SAR
Interferometric Radar (INSAR)
PFS development led by Geoscience Australia
A suite of three products generated by InSAR processing of two images captured of the same geographic area at different times:
  Wrapped interferogram: Image of differential phase signals between two SLC images
  Unwrapped interferogram: Image of differential phase signals where the wrapped fringes are summed (“unwrapped”) to give a continuous phase signal across the image
  Interferometric coherence: Image of phase coherence between the two images.
Aim to submit for endorsement at LSI-VC-12
Notes: CARD4L INSAR product specifies a suite of three products generated by InSAR processing of two observations of the same geographic area at different times:
  Wrapped interferogram is an image showing the differential phase signals between the two complex images. The signal is ‘wrapped’ in quantities of 2*πι radians, giving an image with ‘fringes’.
  The Unwrapped interferogram is an image where the wrapped fringes have been added up to give a continuous phase signal across the image. There are different approaches to do this unwrapping and CARD4L does not prescribe which methods to use.
  Interferometric coherence is an image of phase coherence between two SLC images.
The CARD4L INSAR product specification also is still under development, and expected to be completed in the second half of 2021

## Slide 23
ICESat-2 photon height
(Amazon river transects at dry and wet season)
CARD4L LiDAR
LiDAR Terrain and Canopy Top Height
Lidar measurements of vegetation canopy structure and height. GEDI and ICESat-2 launched in 2018 + MOLI targeted for 2024. Plan to develop CARD4L for LiDAR well received by mission teams.
New CARD4L subgroup on LiDAR launched in 2019
Group members representing 3 spaceborne LiDAR missions + science users
Target PFS: Terrain & Canopy Top Height
Progress in 2020 slow ...
Attempt to revive activity in 2021, depending on interest from LiDAR mission group and users.
Notes: CARD4L INSAR product specifies a suite of three products generated by InSAR processing of two observations of the same geographic area at different times:
  Wrapped interferogram is an image showing the differential phase signals between the two complex images. The signal is ‘wrapped’ in quantities of 2*πι radians, giving an image with ‘fringes’.
  The Unwrapped interferogram is an image where the wrapped fringes have been added up to give a continuous phase signal across the image. There are different approaches to do this unwrapping and CARD4L does not prescribe which methods to use.
  Interferometric coherence is an image of phase coherence between two SLC images.
The CARD4L INSAR product specification also is still under development, and expected to be completed in the second half of 2021

## Slide 24: CARD4L SAR - Outreach
JAXA
CARD4L SAR Outreach
CARD4L SAR Webinar (Feb 2021)
  150 participants from 40+ countries
  300+ views on CEOS YouTube Channel (www.youtube.com/watch?v=Pe-7WXle-EI)
WGCV SAR meeting (Oct 2020)
  Special CARD4L session
AGU 2020 Fall meeting (Town Hall Panel)
ARD2020 Symp (Nov 2020)
CARD4L SAR Uptake
CARD4L SAR Educational Resources
Guidance document to be developed, starting in mid 2021
”Easy to understand” descriptions for data providers and (non-expert) users on what the CARD4L SAR products and per-pixel metadata represent and how they can be used.
DE-Africa
CSIRO

## Slide 25: Nighttime Lights Surface Radiance PFS
Brian Killough CEOS SEO, NASA

## Slide 26: Summary of PFS Plans
Coordinated by Brian Killough (CEOS SEO, NASA) with detailed support from Miguel Roman (NASA, USRA) and Zhousen Wang (NASA GSFC).
Development began in Oct 2020 with endorsement planned for LSI-VC-11 (later 2021).
Working with a team of ~20 people (NASA, NOAA, CEOS) to develop the PFS.
Applies to data collected by nighttime light sensors operating in the VIS/NIR wavelengths. Resolutions are in the order of 10m to 1km.
Uses the surface reflectance PFS as a baseline with several modifications and additions.

## Slide 27: Summary of PFS Plans
There have been a number of revisions by team members. The current version (0.4) is nearing completion.
~ 80% of the Nighttime Light Surface Radiance PFS requirements correspond to the Surface Reflectance PFS requirements.
  Per-Pixel Metadata - replaced solar with lunar (radiance and viewing angles) and , added brightness temperature and solar zenith angle.
  Atmospheric Corrections - removed aerosol, water vapor and ozone corrections. Added general atmospheric scattering, lunar radiance corrections and stray light corrections.
Several important paper references have also been added to the document.

## Slide 28: Next Steps
Seeking Nighttime Light Surface Radiance PFS version 1.0 review and endorsement at LSI-VC-11.
Make version 1.0 available from the CARD4L website to solicit community feedback.
Identify a specific dataset example (e.g. NASA's Black Marble) to conduct a self-assessment against the PFS and later consider full CARD4L review and approval.

## Slide 29: Agency Updates: CARD4L Assessment and Production

## Slide 30: KARI

## Slide 31
2021. 5. 12
Korea Aerospace Research Institute
Image Data System Development Division
Study on CARD4L Compliance of KOMPSAT-3 & 3A Products

## Slide 32: Experiments for achieving CARD4L
Current K3/K3A data does not meet CARD4L PFS even Threshold requirement.
Technical challenges to CARD4L specifications for current K3/K3A data
  Per-pixel metadata
    Pixel-level cloud/cloud shadow detections
  Surface reflectance measurements
    Atmospheric corrections
  Geometric Correction
    Sub-pixel accuracy : less than 0.5 Pixel rRMSE
We performed experiments to see if CARD4L on K3/K3A is feasible
  Experiments about three major technical components above

## Slide 33: Cloud Detection
Surface Reflectance
Final Corrected Image
(B/G/R/N/P)
K3, K3A
L1R or L1G
(B/G/R/N)
Atmospheric Correction
Cloud Detection [1]
Cloud Shadow
Candidate area Detection [2]
Cloud Shadow Detection [3]
Per-Pixel Data
Cloud shadow candidate altitude: 1~3km
[1] Qing Zhang and Chunxiz Xizo, Cloud Detection of RGB Color Aerial Photographs by progressive Refinement Scheme, IEEE, November 2014
[2] Victor J.D. Tsai, A Comparative Study on Shadow Compensation of Color Aerial Images in Invariant Color Models, IEEE, June 2006
[3] Tianxing Wang and 3 others, Effect of Solar-Cloud-Satellite Geometry on Land Surface Shortwave Radiation Derived from Remotely Sensed Data, RemoteSens, July 2017
Flow Chart
Atmospheric Corrections

## Slide 34: Atmospheric Corrections
Verifications
  Reference: RadCalNet Data on Railroad Valley Playa (USA)
    Provided by CEOS
    Providing surface reflectance, AOT @ 550nm, Water vapor, Ozone, etc.
  Data for cross-check: Surface reflectance using AERONET + OTB tool
    Developed by Hansung Univ.
— : RadCalNet — : Hansung — : KARI

## Slide 35: Cloud Detection
Results

## Slide 36
Zuunmod : K3 (3) K3A (4)
Geometric Accuracy Check for ARD

## Slide 37: Geometric Accuracy Check process
L1G Image : Original & APC (Auto Precision Correction)* Image)
Down-sampling : 1x, 2x, 3x, 4x, 8x
GeoCorrection QA : Video comparison through video matching
*Auto Precision Correction (APC) : Translation model (Offset model)
Perform 4-corner coordinate shift without performing L1G resampling
Reference Map : Google Map

## Slide 39: Conclusion
We assessed compliance of K-3/3A (KOMPSAT-3/3A) level 1 products with CARD4L-SR PFS. Since the K-3/3A is high-resolution satellite, many requirements are still challenging.
To investigate whether CARD4L on K3/K3A is feasible, we performed experimental tests on cloud/cloud shadow detection and atmospheric corrections and geometric correction requirements.
We obtained promising results to comply CARD4L requirements for cloud/cloud shadow detection and atmospheric corrections. However, Geometric Correction requirement (Sub-pixel accuracy : less than 0.5 Pixel rRMSE) is almost impossible to meet for K3 / K3A original resolution.
- Down sampling image (about 5 m resolution) for K3 /K3A show the possibility to meet the CARD4L requirements.

## Slide 40: JAXA

## Slide 41
JAXA mission and
CARD4L product development update
Takeo Tadono, JAXA EORC
Ake Rosenqvist, soloEO/JAXA
LSI-VC-10 #1 – May 12, 2021

## Slide 42: ALOS-2 mission status
ALOS-2 payload performance nominal – No geometric, radiometric or polarimetric anomalies have been observed
ALOS-2 in extended mission phase since May 2019
Observation duty cycle reduced to 30% (from 50%) to conserve mission resources
  Observations in Fine Beam Stripmap mode limited to one single global coverage per year (target)
  Observations in 50 m ScanSAR mode proceed without reduction. Regional observations every 3 cycles (42-day repeat, 9 obs/year). Focus on pan-tropics and crustal deformation areas.

## Slide 43: ALOS-4 mission development status
ALOS-4 PALSAR-3 to provide continuation and enhanced performance of ALOS-2 PALSAR-2. Key improvements include wider swath and observation capacity in both dual- and full polarimetric modes.
Currently in Phase D – Proto-Flight Model (PFM) manufacturing and tests
Launch shifted – now foreseen within JFY 2022 (2022/04-2023/03)
Operations to commence 6 months after launch (3 mo check-out, 3 mo Cal/Val)
Global observation strategy under development
Joint operations with ALOS-2 planned until ALOS-2 EOL
Joint A-2/A-4 operations

## Slide 44: ALOS-4 mission development status
ALOS-4 PALSAR-3 to provide continuation and enhanced performance of ALOS-2 PALSAR-2. Key improvements include wider swath and observation capacity in both dual- and full polarimetric modes.
Currently in Phase D – Proto-Flight Model (PFM) manufacturing and tests
Launch planned within JFY 2022 (2022/04-2023/03)
Operations to commence 6 months after launch (3 mo check-out, 3 mo Cal/Val)
Joint operations with ALOS-2 foreseen
PALSAR-3 antenna PFS tests

## Slide 45: ALOS-4 mission development status

## Slide 46
CARD4L product development update
LSI-VC-10 #1 – May 12, 2021

## Slide 47: JAXA Annual Global 25 m Mosaics
Processing/Re-processing schedule
Completed: 2019 & 2020 PALSAR-2
2021 Q2-Q3: 2015, 2016, 2017, 2018 PALSAR-2
Q3-Q4: 2007, 2008, 2009, 2010 PALSAR-1
TBC: 1993-1998 JERS-1
Q4: PALSAR-2 Quad-pol mosaic (NEW)
New mosaic features:
Improved geometric accuracy
Single-year data only (i.e. no gap-filling from other years in case of missing data)
GeoTiff format
and... CARD4L NRB compliant!!
New!

## Slide 48: Mosaics – CARD4L self-assessment
Measurement data:
        HH & HV gamma-0 (γ0) backscatter
        Geometric & Radiometric Terrain Correction
Per-pixel metadata:
        Local incidence angle image
        Observation date image
        Mask image (valid data; no-data; lay-over; radar shadow; water)
General metadata:
        CARD4L formatted XML
Format
        GeoTiff
Global PALSAR Mosaics:
“Analysis-Ready”
– but not CARD4L (yet)
HH γ0 backscatter HV γ0 backscatter
Local incidence angle Observation date
Mask image CARD4L XML header
Notes: The mosaic products can be referred to as “analysis-ready”, however they do not YET fully comply with the CARD4L NRB standards.
The mosaics are provided in 1x1 degree tiles, in geographic lat/long coordinates, and comprise the following data layers:
Measurement data:
        The HH & HV polarisation images are given as gamma-nought backscatter
        They have been subject to full Geometric & Radiometric Terrain Correction
There are 3 Per-pixel metadata images included:
        Local incidence angle image
        Observation date image, which indicates on a per-pixel basis, the corresponding observation date
        And a Mask image, with information about valid data; no-data; radar shadow and lay-over; and water surfaces)
The General metadata is the key point of non-compliance with the CARD4L standards, as it presently only consists of a simple ENVI header.
The file format is generic raw, with the backscatter data provided as 16 bit Unsigned Integer

## Slide 49: Mosaics – CARD4L self-assessment
  CARD4L NRB v5.0 :
  Self-assessment completed
  Target compliance with v5.0 except two items:
    Scattering Area (per-pixel metadata)
    Geometric Accuracy
  Awaiting update to NRB. Outstanding issues foreseen to be resolved.
Notes: JAXA EORC is currently undertaking a major reprocessing effort of all global mosaic data, and that presented a perfect opportunity to assure that the new products are fully CARD4L compliant
The re-processed mosaics will feature
improved geometric accuracy
They will be composed of data from the year in question only, in order to maintain the temporal integrity of the mosaics. This is important for instance when using the data for change analysis
The mosaics will be provided in GeoTiff format to accommodate direct ingestion in standard GIS software such as QGIS or ARC-GIS
Processing/Re-processing schedule
The 2019 & 2020 PALSAR-2 are being processed as we speak, with public release in late March or April
The 2015 through 18 PALSAR-2 mosaics are scheduled for the 2nd and 3rd quarter of this year
All PALSAR-1 mosaics are to be re-processed in the second half of this year
And in collaboration with the ESA CCI Biomass project, reprocessing of all historical JERS-1 data is also planned
At the end of the year, a new mosaic product consisting of all fully polarimetricl data acquired with ALOS-2 is planned. This is very exciting and we hope this product will stimulate new SAR polarimetry applications. This also presents a potential opportunity to assure compliance with the CARD4L Polarimetric Radar (POL) specifications.
CARD4L self-assessment of the mosaic products is ongoing, including the development of complete general metadata information.
the aim is to achieve at least threshold compliance with the CARD4L Normalised Radar Backscatter (NRB) specifications
The target is to submit the assessment for review by CEOS WG CalVal in mid 2021

## Slide 50: Standard products – CARD4L NRB target
 |  | CY 2020 |  |  |  | CY 2021 |  |  | 
 |  | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec | 1Q Jan Mar | 2Q Apr Jun | 3Q Jul Sept | 4Q Oct Dec
ALOS | AVNIR-2 (10 m) |  |  |  |  |  |  |  | 
 | PALSAR FBS, FBD (10 m) |  |  |  |  |  |  |  | 
ALOS-2 | PALSAR-2 ScanSAR * (25m) |  |  |  |  |  |  |  | 
Processing
Processing
Data Processing
Global
Distribution (Public open)
Data Distribution (Public open)
Global (L2.2)
Japan (L1.1, L2.1)
* Production of ALOS-2 ScanSAR L2.2 (RTC) to start before the end of 2021. Software tool for conversion to CARD4L NRB product level to be provided
Japan(L2.2)
Scene-based standard products:
Reprocessing of ALOS and ALOS-2 archives by JAXA Super Computer (JSS2/JSS3) ongoing

## Slide 51
Thank you
LSI-VC-10 #1 – May 12, 2021

## Slide 52: ESA

## Slide 53: ESA Update on ARD
Ferran Gascon, Copernicus Sentinel-2 Mission Manager
and CEOS LSI-VC ESA representative
CEOS LSI-VC#10
12 May 2021

## Slide 54: VH-RODA 2021 Workshop

## Slide 55: VH-RODA / Session on Institutional & Commercial ARD
Definition of Analysis Ready Data (ARD)
  Institutional sector well advanced with:
    CARD4L specifications defined for 5 product families,
    additional CARD4L specifications in the pipeline,
    CEOS-endorsed terminology and
    interest in developing CEOS ARD specifications for non-land applications.
  Commercial sector brought additional concepts/thoughts like:
    ARS (Analysis Ready Services), going beyond the notion of product that limits the range of downstream applications, or
    the need to move towards product Levels 4 and 5.
Commercial space involvement
  General consensus that sensor agnostic, standardised and easy-to-use products are interesting for non-expert users.
  Commercial sector is showing some support to CEOS-lead CARD4L initiative (2 commercial products under certification: Sinergise Sentinel-1 and Element 84 Sentinel-2).
  Need to reinforce CEOS-led initiatives to promote ARD in general and CARD4L in particular (e.g. in venues like ARD workshop, JACIE, VH-RODA) to foster adoption of CARD4L by the commercial sector.
  Need to reinforce the promotion of the benefits brought by existing and future CARD4L products in the general effort towards facilitating missions inter-operability + advantage of being first movers.

## Slide 56
Process initiated to certify Sentinel-2 Level-2A products.
Sentinel-2 products expected to be compliant CARD4L requirements soon, after full activation of geometric refinement and inclusion of a DOI (Digital Object Identifier) in the metadata.
S2 Analysis Ready Data (ARD) – Level-2A

## Slide 57
Improvement of geometric performances since 30 March 2021:
      Absolute geolocation accuracy from 11m improved to 8 m (CE95).
      Multi-temporal co-registration accuracy from 12m improved to 5 m (CE95).
Copyright: contains modified Copernicus Sentinel data (2020), processed with Sentinel Hub EO Browser
Greenhouses in Egypt's former desert
Copyright: New China TV
Not Refined Geometry
Refined Geometry
Sentinel-2 Towards CARD4L compliance

## Slide 58
Collection 1 will be generated reprocessing full S2 archive for both Level-1C (TOA reflectance) and Level-2A (surface reflectance and cloud mask) products.
Reprocessing campaign foreseen to start during Q4 2021.
Collection 1 available to users by second half 2022.
Collection 1 will feature several improvements on both Level-1C and Level-2A products.
Collection 1 targets CARD4L compliance for Level-2A products (currently only DOI inclusion is missing).
Towards Sentinel-2 Collection 1

## Slide 59: S2 - Landsat Interoperability
  Geometry :
    S2 GRI (Global Reference Image)
    Copernicus DEM (Digital Elevation Model)
    DEMIX (DEMs Intercomparison eXercise)
    DGGS (Discrete Global Grid System)
  Top-Of-Atmosphere Radiometry :
    Sensor inter-comparison using an integrating sphere
    S2 “inspired” by Landsat-8 bands
    Absolute radiometry inter-comparison
  Surface Reflectance and Cloud Mask:
    ACIX (Atmospheric Correction Intercomparison eXercise)
    CMIX (Cloud Mask Intercomparison eXercise)
    CARD4L [ http://ceos.org/ard ]
  Harmonised and Fused Products
    Sen2Like

## Slide 60: VC-19-05: Open-source library for surface reflectance product generation
Sen2Llike software available in open-source at: https://github.com/senbox-org/sen2like
Sen2Like pilot productions provided to several teams (Copernicus Services, Szantoi et al., Labahn et al., Roy et al., Schaaf et al.).
Pilot productions also available to LSI-VC members.
Sen2Like being compared with NASA HLS.
Sen2Cor will become also available also in open-source on GitHub during Q3 2021.
Sen2Cor new release in open-source will support both Sentinel-2 and Landsat.

## Slide 61
“As far as we know, Timelapse in Google Earth is the largest video on the planet, of our planet. And creating it required out-of-this-world collaboration. This work was possible because of the U.S. government and European Union’s commitments to open and accessible data. Not to mention their herculean efforts to launch rockets, rovers, satellites and astronauts into space in the spirit of knowledge and exploration. Timelapse in Google Earth simply wouldn’t have been possible without NASA and USGS Landsat program, the world’s first (and longest-running) civilian Earth observation program, and the European Union’s Copernicus program with its Sentinel satellites.”
Google statement:
https://blog.google/products/earth/timelapse-in-google-earth/
Landsat + Sentinel-2 in Google Earth Timelapse
Notes: One of the most comprehensive pictures of our changing planet is now available to the public.
24 million satellite images from Sentinel-2 and Landsat from the past 37 years have been embedded into a new layer of Google Earth.

## Slide 62
Columbia Glacier (Alaska)
Thank you
Notes: Columbia Glacier in Alaska
Sentinel-2 image acquired in August 2019. On top of the image we have annotated historical glacier calving front lines from 1986 using data from Landsat and Sentinel-2.
Main result : The glacier has been retreating of about 20 km in 33 years (1986-2019)

## Slide 63: ISRO

## Slide 64: CARD4L and Product family specification(PFS): Assessment and Production: RS2/2A Products-NRSC/ISRO LSI-VC-10 : 12 May 2021
T. Radhika, NRSC, ISRO

## Slide 65
Objective
Design an approach to generate Analysis Ready Data (ARD) set using IRS sensors data.
Currently we propose to generate ARD sets from Resourcesat-2 series (RS2/RS2A)
ARD (Surface Reflectance Family) product includes temporal sets in compliance with CARD4L product family specs..
Top of Atmosphere (TA) reflectance (reflectance calculated “at sensor,” not atmospherically corrected)
Surface Reflectance (SR) (atmospherically corrected)
Pixel Quality Assessment (QA) (common and sensor specific quality bands included)
General meta data
Quality meta data
From relevant/similar sensors

## Slide 66
Resourcesat-2/ 2A:
The Resourcesat-2(RS-2) satellite was launched by the Indian Space Research Organization (ISRO) on April-2011, followed by Resourcesat-2A(RS-2A) on Dec-2016, to ensure systematic and repetitive coverage of the earth’s surface to provide data for integrated land and water resource management.
 | AWiFS | LISS-3 | LISS-4
No of Bands | 4 | 4 | 3
Spectral Band2 (µ) | 0.52 – 0.59 (green) | 0.52 – 0.59 (green) | 0.52 – 0.59 (green)
Spectral Band3 (µ) | 0.62 – 0.68 (red) | 1.55 – 1.70 (SWIR) | 1.55 – 1.70 (SWIR)
Spectral Band4 (µ) | 0.77 – 0.86 (NIR) | 0.77 – 0.86 (NIR) | 0.77 – 0.86 (NIR)
Spectral Band5 (µ) | 1.55 – 1.70 (SWIR) | 1.55 – 1.70 (SWIR) | -
Resolution (m) | 56 | 24 | 5.8
Swath (km) | 740 | 140 | 70
Revisit period (days) | 5 | 24 | 5

## Slide 67
Status of RS2/2A Data products :CARD4L framework
  Expertise in realizing Ortho- Surface reflectance(SR) products
  Thorough Validation carried out with Insitu measurements - varied reflectance features , ISRO-CAL sites and with OLI
  RS-2/2A SR product is in good agreement with OLI with R2 > 95 % for R2A and R2 ~ 90 % for R2
  Geometric Accuracy : better than a pixel (CE90)
  QA band with cloud and cloud shadow
  Variation of SR values is more on Aquatic features

## Slide 68
PFS assessment
Threshold : 9/10, Target 7/17
Threshold : 5/7, Target 5/11
Threshold : 4/4, Target 4/6
Threshold : 0/1, Target 0/1

## Slide 69
Way Forward ..
  AOD data pre-Processing
  Deriving Per pixel uncertainty in terms of geometry and radiometry
  Land/water, Snow/Ice and Terrain shadow mask
  Measurement Normalization
  Subpixel accuracy over all types of terrains
Thank you..
Collaboration to overcome Challenges
  Process exchange on Atmospheric data handling : High variations in neighbouring AOD values
  Process exchange for Non- availability of AOD data over Himalayan region and AOD from LS8 .
  Exchange of RS2/2A SR products and Reports .

## Slide 70: Analysis Ready Satellite Data at NASA
Christopher Lynnes

## Slide 71: DLR: EnMAP ARD / CARD4L Metadata
Martin Bachmann et al., DLR
for the EnMAP Ground Segment

## Slide 72: Wrap-up
LSI-VC Leads