## Slide 1: LSI-VC-14 2023 KARI’s works on ARD
Chiho KANG, KARI
Agenda Item 2.3
LSI-VC-14 2023, ESA/ESRIN
10th - 12th October 2023

## Slide 2
KARI’s LEO Missions
LEO
Working
Not Working
Under Development
KOMPSAT-1
1999
EO 6.6m
KOMPSAT-2
2006
EO 1m
KOMPSAT-3
2012
EO 0.7m
KOMPSAT-3A
2015
EO 0.55m
KOMPSAT-5
2013
SAR 1m
KOMPSAT-7
2024
EO 0.3m
KOMPSAT-6
2024
SAR 0.5m
CAS500-1
2019
EO 0.5m
CAS500-2
2025
EO 0.5m
KOMPSAT-7A
2025
EO 0.3m
"Development of over 170 satellites, launch of more that 40 domestic launch vehicles (~2031)”
National Space Committee (2021)

## Slide 3
KARI’s Works on ARD (1/18)
Surface Reflectance (1/8)
  Major characteristics of KOMPSAT-3 & KOMPSAT-3A systems
Property | KOMPSAT-3 | KOMPSAT-3A
Orbit | Sun-Synchronous | Sun-Synchronous
Altitude (km) | 685.13 | 528
Inclination () | 98.14 | 97.5
MLTAN | 13:30 | 13:30
Bandwidth (nm) | PAN: 450 – 900 MS1 (B): 450 – 520 MS2 (G): 520 – 600 MS3 (R): 630 – 690 MS4 (NIR): 760 – 900 | PAN: 450 – 900 MS1 (B): 450 – 520 MS2 (G): 520 – 600 MS3 (R): 630 – 690 MS4 (NIR): 760 – 900
GSD (m, @nadir) | 0.5 (PAN) / 2.0 (MS) | 0.4 (PAN) / 1.6 (MS)
Data Quantization (bit/pixel) | 14 | 14
Swath (km, @nadir) | 16 | 13
Geolocation Accuracy (m) | 19.96 (RMSE), < 30.3 (CE90) | 7.86 (RMSE), < 11.2 (CE90)
Map Projection / Datum | UTM / WGS84 | UTM / WGS84
Product Format | GeoTIFF | GeoTIFF
KOMPSAT-3
KOMPSAT-3A

## Slide 4
KARI’s Works on ARD (2/18)
Surface Reflectance (2/8)
  KOMPSAT-3 & KOMPSAT-3A product level
Level | Description
1R | Corrected for radiometric and sensor distortions Difference of relative radiometric response between detectors is corrected. Internal detector geometry and mis-registrations between detectors are corrected.
1O | Ortho-ready Corrected for radiometric and sensor distortions Corrected for geometric distortions and projected to UTM. Optical distortions and terrain effects are corrected using average height over the region. The final product is projected to UTM coordinate.
1G | Corrected for radiometric and sensor distortions Corrected for geometric distortions and projected to UTM. Optical distortions and terrain effects are corrected a coarse digital elevation model (DEM), SRTM DEM The final product is projected to UTM coordinate.

## Slide 5
Surface Reflectance (3/8)
  The CARD4L-SR (Surface Reflectance) specification
KARI’s EO missions provide high resolution imagery. Considering our experiences, we feel that it is very difficult to
        Assess physical properties (e.g. surface reflectance) for every pixel properly even with coarse accuracy
        Achieve the sub-pixel accuracy of PFS, i.e. 0.5 pixel rRMSE
We have focused on checking if the ARD product based on high resolution EO imagery, especially using KOMPSAT-3/3A imagery, can meet the threshold requirement for the CARD4L-SR.
KARI’s Works on ARD (3/18)

## Slide 6
Surface Reflectance (4/8)
  Feasibility Study: Atmospheric correction
KARI’s Works on ARD (4/18)
Procedure for Atmospheric correction
Atmosphere
  MODIS DB
    AOD/O3/WV
Radiation Transfer Model
  MODTRAN
Result
  Reflectance close to the reference value
    RadCalNet

## Slide 7
Surface Reflectance (5/8)
  Feasibility Study: Assessment of registration accuracy (1/2)
KARI’s Works on ARD (5/18)
Procedure for Qualifying Geolocation Accuracy
Methods
  rRMSE/CEP
    For matched points
Image matching

## Slide 8
Surface Reflectance (6/8)
  Feasibility Study: Assessment of registration accuracy (2/2)
KARI’s Works on ARD (6/18)
Spatial Resolution Vs. Registration Accuracy
Test data
  Down-scaled datasets
    1/2/4/8
Result
  8-Down-scaled datasets meet the threshold of “4.1 Geometric Correction” in CARD4L-SR.
    ~16m spatial resolution

## Slide 9
Surface Reflectance (7/8)
  Feasibility Study: Cloud detection for “Per-Pixel Metadata” generation (1/2)
KARI’s Works on ARD (7/18)
Procedure for Cloud Detection
Characteristics of cloudy pixels
  Mass of pixels
  Brighter than neighborhood pixels
  Lower saturation/hue in HSI space
  Lower texture details
Classification
  No data
  Cloud
  Cloud Shadow
  Earth’s Surface

## Slide 10
Surface Reflectance (8/8)
  Feasibility Study: Cloud detection for “Per-Pixel Metadata” generation (2/2)
KARI’s Works on ARD (8/18)
Cloud Detection & Classification
Results
  Detection accuracy
    Cloud: ~80%
    Cloud shadow: ~ 70%
 | No data (DN: 1)
 | Cloud (DN: 4)
 | Cloud Shadow (DN: 8)
 | Earth’s Surface (DN: 8)

## Slide 11
KARI’s Works on ARD (9/18)
Normalized Radar Backscatter (1/5)
  Major characteristics of KOMPSAT-5 system
Property | KOMPSAT-5
Orbit | Sun-Synchronous
Altitude (km) | 550
Inclination () | 97.06
MLTAN | 6:00
Repeat Cycle (days) | 28
Operation Mode (Resolution (m), Swath (km)) | Stripmap (3, 30) Spotlight (1, 5) ScanSAR (20, 100)
Center Frequency (GHz) | 9.66
Incidence Angle () | 20 – 55
Polarization | HH / HV / VH / VV
Geolocation Accuracy (m) | 4.82 (RMSE), 7.32 (CE90)
Map Projection / Datum | UTM / WGS84
Product Format | HDF5 / GeoTIFF

## Slide 12
KARI’s Works on ARD (10/18)
Normalized Radar Backscatter (2/5)
  KOMPSAT-5 product level
Level | Description
1A | Single Look Complex Slant Range / Azimuth (Zero-Doppler)
1C | Geocoded Ellipsoid Corrected UTM / GEOG, EGM96 EQPOT Surface
1D | Geocoded Terrain Corrected UTM / GEOG, DEM + EGM96 EQPOT Surface

## Slide 13
Normalized Radar Backscatter (3/5)
  Radiometric Terrain Correction (RTC)
  CARD4L-NRB
We have focused on implementing and applying RTC function to SAR imagery, especially using KOMPSAT-5 imagery, to meet the threshold requirement for the CARD4L-NRB.
KARI’s Works on ARD (11/18)

## Slide 14
Normalized Radar Backscatter (4/5)
  Radiometric Terrain Correction Test (1/2)
KARI’s Works on ARD (12/18)
Procedure for Radiometric Terrain Correction
SAR Backscatter Normalization Conventions
(D. Small, “Flattening Gamma: Radiometric Terrain Correction for SAR Imagery”, IEEE Transactions on Geoscience and Remote Sensing, Vol. 49, No.8, Aug. 2011)
DEM

## Slide 15
Normalized Radar Backscatter (5/5)
  Radiometric Terrain Correction Test (2/2)
KARI’s Works on ARD (13/18)
Result of Radiometric Terrain Correction Test

## Slide 16
System Preliminary Design (1/4)
  ARD processing system
KARI’s Works on ARD (14/18)
ARD Product
ARD Processing
Optical · SAR
Image
ARD NRB Processing
ARD
Processing
Image (SR, NRB)
Image
Pixel-Metadata
Metadata
Per-pixel Metadata
ARD Metadata
L0 Data
KOMPSAT Product
K3/3A
Level
Processor
K5
Level
Processor
K3/3A 1R/1G
K5 L1A
ARD SR Processing

## Slide 17
System Preliminary Design (2/4)
  ARD product
KARI’s Works on ARD (15/18)
Sensors
Product Families
K-ARD Products
KOMPSAT Optical
CARD4L PRODUCT FAMILY
Surface Reflectance
General Metadata
Quality Metadata
Measurement Calibration
Geometric Calibration
KOMPSAT SAR
General ARD Metadata
Surface reflectance - Image
Thumbnail
Pixel Metadata – Cloud Mask
Pixel Metadata – QR(Quality Assessment)
TCI(True Color Image)

## Slide 18
System Preliminary Design (3/4)
  ARD processing software: SR
KARI’s Works on ARD (16/18)

## Slide 19
System Preliminary Design (4/4)
  ARD processing software: NRB
KARI’s Works on ARD (17/18)

## Slide 20
Near Term Activities
  Preliminary Design for ARD processing Software: ~’23/12
  Detailed Design for ARD processing Software: ~’24/12
KARI’s Works on ARD (18/18)

## Slide 21: Thank You!
LSI-VC-14 2023, ESA/ESRIN
10th - 12th October 2023