## Slide 1
20-21 March, 2017
Takeo Tadono1, Masanobu Shimada1,2, and Ake Rosenqvist3
1 Earth Observation Research Center (EORC)
Japan Aerospace Exploration Agency (JAXA)
2 Tokyo Denki University, Japan
3 SoloEO, Japan
JAXA’s Analysis Ready Data (ARD)
JERS-1, ALOS, ALOS-2, and Future
CEOS LSI-VC #3 Meeting, ESA ESRIN, Frascati, Italy

## Slide 2: Contents
JAXA’s EO Status
  History of L-band SARs: JERS-1, ALOS, ALOS-2, and future
Analysis Ready Data (ARD) Production Status
  Case study for forest observations “GFOI”
Description of SAR ARD
Summary

## Slide 3: JAXA’s EO Satellites
JAXA’s Past, Current and Future Satellite/Sensor Activities
GCOM-C
SHIZUKU
(GCOM-W)
GPM/DPR
DAICHI (ALOS)
IBUKI (GOSAT)
(JFY2008)
(JFY2013)
(JFY2012)
(JFY2014)
ALOS-2
(JFY2018)
Earth CARE/CPR
(JFY2017)
GOSAT-2
(JFY2018)
TRMM/PR
JERS-1
MOS-1
ADEOS-II
(JFY1991)
(JFY2002)
(JFY1986)
(JFY1997)
(JFY2005)
Aqua/AMSR-E
(JFY2002)
Advanced Optical Satellite
(JFY2020)
Advanced SAR Satellite
(JFY2020)

## Slide 4: Japanese Earth Resources Satellite-1 (JERS-1, “FUYO”)
Japanese Earth Resources Satellite-1 (JERS-1)
Feb. 1992 - Oct. 1998
Launcher: H-I
Orbit: Sun-Shyncronous
Altitude: 568 km
Inclination: 98°
Revisit: 44 days
Weight: 1,340 kg
SAR
L-band (1.275 GHz)
HH
Resolution: 18 m
Swath: 75 km
OPS (Optical Sensor)
VNIR (Visible and Near Infrared Radiometer) 3ch,
SWIR (Short Wavelength Infrared Radiometer) 4ch,
18×24 m, 75 km

## Slide 5: Advanced Land Observing Satellite (ALOS, “DAICHI”)
PRISM can acquire triplet stereo imageries by nadir-, forward-, and backward-radiometers with 2.5 m spatial resolution in 35 km swath.
PRISM
PALSAR
AVNIR-2
Operation
24 Jan. 2006 by H-2A Rocket #8
12 May 2011 Mission ended
~22 Apr. 2011: Low Load Mode (LLM)
> 1,934 days=5.3 years > 12 mil. scenes
Objectives
  Cartography (1/25,000 scale)
  Regional environmental monitoring
  Disaster monitoring, etc.
PRISM
Panchromatic Remote sensing
Instrument for Stereo Mapping
AVNIR-2
Advanced Visible and Near-Infrared Radiometer type 2
PALSAR
Phased Array type L-band
Synthetic Aperture Radar
AVNIR-2 can observe with 10 m resolution in 70 km swath, and it can be changed the observation area by pointing capability within +/-44 deg. in across track.
PALSAR can acquire the data in not only daytime but also nighttime as well as cloudy and rainy whether conditions.

## Slide 6: ALOS PALSAR
Phased Array type L-band Synthetic Aperture Radar
L-band (1.27 GHz)
Fine Resolution Mode
8.0-60.0 deg.
HH or VV / HH+HV or VV+VH
7.0-44.3m / 14.0-88.6m
40-70km / 40-70km
ScanSAR Mode
18.0-43.0 deg.
HH or VV / 100m / 250-350km
Polarimetric Mode
8.0-30.0 deg.
HH + HV + VH + VV
24.1-88.6m / 20-60km

## Slide 7: Advanced Land Observing Satellite-2 (ALOS-2, “DAICHI-2”)
Orbit | Orbit |  | Sun-Synchronous Sub-Recurrent (Repeat cycle: 14 days)
 | Altitude |  | 628 km (at Equator)
 | Local sun time |  | 12:00 (noon) at Equator (Descending)
Design Life |  |  | 5 years (target: 7 years)
Launch |  | Date | May 24, 2014
 |  | Rocket | H-IIA FY24
Satellite |  | Mass | Approx. 2 ton
 |  | Paddle | Dual wing solar paddle
Mission data transmit |  |  | Direct and via. DRTS
SAR |  |  | L-band (1.2 GHz range)
Mode | Spotlight |  | Resolution: 1-3 m, Swath: 25 km
 | Stripmap |  | Resolution: 3 / 6 / 10 m Swath: 50 / 50 / 70 km
 | ScanSAR |  | Resolution: 100 / 60 m Swath: 350 / 490 km
The compact infrared camera (CIRC) and SPAISE2 for detecting ships are carried as a technology demonstration payload.
Overview of ALOS-2 (Daichi-2)
L-band Synthetic Aperture Radar-2
（PALSAR-2）
Flight
Earth
X
Y
Z
16.5m
10m
3.7m

## Slide 8: Advanced Land Observing Satellite-2 (ALOS-2, “DAICHI-2”)
Incidence angle: 8-70 deg.
70°
8°
350 or 490km
25 km x 25km
70°
50 or 70km
Observable area
Approx. 1,160 km
ScanSAR
Swath: 350 or 490 km
Spotlight
Swath: 25 km
Stripmap
Swath: 50 or 70 km
Continuity from ALOS/PALSAR
8°
PALSAR-2 Observation Geometry.
New observation mode
Flight direction
Un-observable area
80 km
Nadir
同一地点を連続観測
Flight direction

## Slide 9: History of Japanese L-band SARs
JERS-1 SAR
1992 - 1998
ALOS PALSAR
2006 - 2011
ALOS-2 PALSAR-2
2014 -
Resolution:
18 m
10 m / 100 m
3 m / 100 m
Swath width:
Polarization:
75 km
70 km / 350 km
50 km / 490 km
Single
Single, Dual, Quad
Single, Dual, Quad
Transmit power:
~1.5 kW
~2 kW
~6.1 kW
Obs. direction:
Right
Right
Right or Left

## Slide 10: Definition of ARD
The definition of the Analysis Ready Data (ARD) is depends on the application as well as the objective.
E.g., “the Global Forest Observations Initiative” (GFOI)*:
1) Radiometry (Information Units - comparable through time and across sensors): Atmosphere, solar illumination and viewing angle corrected, and cross-calibrated;
  a. Optical: Absolute calibration and surface reflectance:
    i. Landsat TM, Landsat ETM+, Landsat OLI/TIRS, SPOT 1-5, Sentinel-2
    ii. Caveats: Spectral band differences must be accounted for when comparing multiple sensors. The differences between Landsat and Sentinel-2 bands can be significant (see figure). Differences exist for most bands and differences may increase when bands are used to create derived products such as indices. Most time series algorithms do not currently accommodate spectral differences.
  b. SAR: Backscatter correction:
    i. Absolute calibration (calibration constant supplied by data provider)
    ii. Radiometric correction for topography by DEM
    iii. Normalisation of cross-track (near-far range) incidence angle variation
    iv. JERS-1/ALOS/ALOS-2 PALSAR global mosaics provide an example of analysis ready Radar data.
* Global Data Flow Study for the Global Forest Observations Initiative (GFOI), Ver. 0.11,24 Nov. 2015.

## Slide 11: Definition of ARD
2) Geometry (Optical and SAR): Geolocation - pixels need to be aligned with a common origin and spatially nested;
  a. Orthorectification, coregistration, reprojection: Image to image registration accuracy, resampling method, pixel origin, and projection must be known
  b. Caveats: The miss-registration to a reference database should be kept below a half pixel, preferably below a quarter pixel. If different reference databases exist then the errors will be a function of both individual errors. The resampling algorithm, the number of times resampled and map projection all will impact the comparability of the data through time. Miss-registration will be reflected in the data values.
3) Data organization - users must be provided efficient access to a defined structure of tiled data. Pixel-level metadata identifying clouds, shadows, shadow/layover (for SAR) and sensor artifacts are also best provided by space agencies.
  a. Provenance, quality and cloud metadata
  b. Data reformatting and reorganization: for example, Data Cube. Data should be stored on line so direct access to the data is possible and tools must be available to extract spatial, spectral and temporal subsets of the data.
4) Methodologies
  a. Earth Observation variables (e.g., NDVI, greenness, bareness, wetness)
  b. Cloud-free Mosaics (e.g., annual, seasonal, monthly)
  c. Classification and change detection (e.g., Continuous Change Detection and Classification)
  d. Classification
  e. Validation and update of existing classification
* Global Data Flow Study for the Global Forest Observations Initiative (GFOI), Ver. 0.11,24 Nov. 2015.

## Slide 12: JAXA’s SAR ARD Productions
One examples for generating a mosaic image
SLC generation, Ortho-rectification+
Slope correction
Multiple raw data
Multiple ortho generations
Pre-processing (Multiple path processing):
Mosaic (processing)
DEM preparation
Flowchart of producing a mosaic product.

## Slide 13: JAXA’s SAR ARD Productions
Download: JAXA’s SAR ARD (analysis ready Data), available from the web site:
http://www.eorc.jaxa.jp/ALOS/en/palsar_fnf/fnf_index.htm
Contents:
  Satellite: JERS-1/SAR (1996), ALOS/PALSAR (2007-2010), and ALOS-2/ PALSAR-2 (2015-)
  Frequency: Annual summer data (June-September)
  Data: gamma-zero image and forest/non-forest (FNF), ancillary data (local incidence, mask, etc.), spaced in 0.8 arcsec (approx. 25 m) and averaged in 100 m, ortho-rectified, and slope corrected
  Geometric accuracy: 10 m
  Expression: 2 byte data (unsigned short integer) for amplitude image
  Area: Global Land
  Download unit: 1 x 1 deg. or 5 x 5
  degrees in lat/long unit
Access:
  Free of charge
  E-mail registered

## Slide 14: JAXA’s SAR ARD Productions
JERS-1 25 m global mosaic dataset (HH): 1992 - 1998

## Slide 15: JAXA’s SAR ARD Productions
ALOS PALSAR 25 m global mosaic dataset (HH, HV): 2007 - 2010
Global 25 m mosaic (Ortho+slope correction)
Global 25m Forest/non-forest map

## Slide 16: JAXA’s SAR ARD Productions
ALOS-2 PALSAR-2 25 m global mosaic dataset (HH, HV): 2015 -
Global 25 m mosaic (Ortho+slope correction)
Global 25m Forest/non-forest map

## Slide 17: JAXA’s SAR ARD Productions
Online registration for download : JERS-1, ALOS PALSAR, ALOS-2 PALSAR-2 25 m global mosaic datasets open release:
http://www.eorc.jaxa.jp/ALOS/en/palsar_fnf/registration.htm
User ID and Password are sent to registored e-mail address automatically

## Slide 18: JAXA’s SAR ARD Productions
Browse of FNF can be confirmed after login and select preferred dataset:

## Slide 19: JAXA’s SAR ARD Productions
Download the dataset in 5 x 5 degrees or individual 1 x 1 deg. tile:
Bulk download of data
over 5 x 5 degrees region (25 tiles)
Click on a tile in the grid to download the individual 1 x 1 deg tile

## Slide 20: Contents of SAR ARD
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Backscatter image (HH)
Radar backscatter, normalised for incidence angle ( go = so/cosqi )
Radiometric and geometric corrections for topography
16 bits (Unsigned INT)
ENVI header information

## Slide 21: Contents of SAR ARD
PALSAR and PALSAR-2 25 m global mosaic dataset:
Backscatter image (HV)
Radar backscatter, normalised for incidence angle ( go = so/cosqi )
Radiometric and geometric corrections for topography
16 bits (Unsigned INT)
ENVI header information

## Slide 22: Contents of SAR ARD
PALSAR and PALSAR-2 25 m global mosaic dataset:
Backscatter image
Faulse color composite
R: HH
G: HV
B: HH/HV

## Slide 23: Contents of SAR ARD
DN=917
29/07/2008
DN=854
27/05/2008
DN=975
25/09/2008
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Observation date layer
Data layer showing the acquisition date for each pixel in the image
Date = [Launch date] + DN
11/2/1992 for JERS-1,
24/1/2006 for ALOS, and
24/5/2014 for ALOS-2
16 bits (Unsigned INT)

## Slide 24: Contents of SAR ARD
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Incidence angle layer
Layer with local incidence angle for each pixel
8 bits

## Slide 25: Contents of SAR ARD
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Mask information layer
Ocean and no-data areas: layover and shadow
8 bits

## Slide 26: Contents of SAR ARD
PALSAR and PALSAR-2 25 m global mosaic dataset:
Forest and Non-Forest Classification
8 bits

## Slide 27: Contents of SAR ARD
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Specifications and ancillary information (for PALSAR)

## Slide 28: Contents of SAR ARD
PALSAR, PALSAR-2, and JERS-1 25 m global mosaic dataset:
Specifications and ancillary information (for PALSAR)

## Slide 29: FNF Spatial and Temporal Change
Comparison between PALSAR and PALSAR-2 (JERS-1 in future):
PALSAR-2 2015
PALSAR 2010
South America
(Brazil)
●: Forest
●: Non-Forest
●: Deforestation
●: Reforestation
FNF change 2015-2010
0 30km

## Slide 30: FNF Spatial and Temporal Change
PALSAR-2 2015
PALSAR 2010
South America
(Brazil)
●: Forest
●: Non-Forest
●: Deforestation
●: Reforestation
FNF change 2015-2010
0 10km

## Slide 31: FNF Spatial and Temporal Change
PALSAR-2 2015
PALSAR 2010
●: Forest
●: Non-Forest
●: Deforestation
●: Reforestation
0 5km
FNF change 2015-2010
South America
(Brazil)

## Slide 32: Future Missions
Hazard Map
High Precise 1/25,000 Map
© GSI
Advanced Optical Satellite
Advanced SAR Satellite
Estimate situation of magma chamber under the ground and faulting
Take a decision for evacuation
Observation
Modeling
Magma Chamber
Crucial Deformation
Rising Magma
© GSI

## Slide 33: Summary
JAXA’s ARD production and release status reported:
  L-band SARs: JERS-1, ALOS, ALOS-2. Hope in the future
ALOS-2/PALSAR-2 operation very well and global data acquisitions ongoing with the excellent performance (high resolution, low noise level, polarimetry) to monitor the earth environment.
Optical image ARD: Global ortho-rectified ALOS AVNIR-2
JAXA will continue to produce the high level products.