## Slide 1
Land Products and Applications by ISRO
Bimal K. Bhattacharya
Head, Agriculture and Land Ecosystem Division (AED)
Biological and Planetary Sciences and Applications Group (BPSG)
Earth and Planetary Sciences and Applications Area (EPSA)
Space Applications Centre, ISRO, Ahmedabad 380015, Gujarat, India
Ahmedabad Earth Station
Satellite Payload Development
Payload definition and development, application research
Remote Sensing
Communication
Navigation
Other centres
NRSC, Hyderabad
Data reception, dissemination
Airborne survey, disaster
Geospatial applications
IIRS, Dehradun
Training & Academic outreach
LSI – VC 5th meeting during 21 -23 Feb., 2018 in Tokyo, Japan

## Slide 2: Electro-Optical (EO) and Microwave payloads for Earth Observations
Meteorology
Land resources
Cartography
Resourcesat series
Three tier imaging
Cartosat series
Sub meter resolution
INSAT-3D series
7 channel Imager
19 channel sounder
Synthetic Aperture Radar (SAR)
RISAT-1 C-band

## Slide 3
Examples of Three-tier Observations from Resourcesat satellites
AWiFS: 56m (5 day)
LISS-III: 24m (24 day)
LISS-IV: 5.8 m
Advanced Wide Field Sensor
Linear Imaging Self-scanner
False Color Composites from multi-spectral bands
(Green, Red, Near-infrared)
Cartosat - 1

## Slide 4
Backscatter signature of Synthetic Aperture Radar

## Slide 5: Scheme for Atmospheric Correction of Resourcesat-2 AWiFS data (SACRS2)

## Slide 6: Validation of SACRS2-derived reflectance with 6S-derived and in-situ reflectance
Comparison of surface reflectances (s) in four spectral bands derived using the SACRS2 scheme and 6SV model for the RS2 AWiFS data over various land covers.
Validation of SACRS2 reflectance with the in-situ measurements
over Bareja, Kutchh, Hoshangabad sites.

## Slide 7: Software package developed: SACRS2-AWiFS

## Slide 8: SACRS2 Model Released on MOSDAC site
SACRS2 software released on MOSDAC site

## Slide 9: SACRS2 module included in IGIS V2 software

## Slide 10: Model takes raw Digital Number file of RS2-AWiFS as input and provides radiance, TOA reflectance and Surface Reflectance as outputs based upon atmospheric and viewing geometry parameters
SACRS2 module included in IGIS V2

## Slide 11
NDVI product from
Oceansat-2 Ocean Color Monitor during January
Ku band scatterometer back scattering coefficient (sigma-0) in Vertical polarization data from SCATSAT1 over the globe
Some Ocean monitoring sensors useful for Land studies
Ocean monitoring satellites have global coverage
It has 1-2 day repeativity, but have moderate to coarser resolution
Useful for quick assessment and modelling
Oceansat-2 Ocean Color Monitor

## Slide 12
Operational Weather products from Meteorological satellites (INSAT)
Meteorology
Vegetation & snow
Radiometer (Kalpana - 1)
Optical band
Thermal band
Imager (INSAT 3D)
Multi-spectral
(CCD : INSAT 3A)
Geophysical / biophysical products (Rainfall, LST, insolation, forest fire)
at MOSDAC (www.mosdac.gov.in) from Kalpana-1, INSAT 3A, INSAT 3D & 3DR
Daily Solar radiation
Land surface temperature (LST)
SWIR band
MIR band
Coarser (8 km)
Finer (1 km)
4 km
Rainfall
Forest Fire

## Slide 14: Examples of crop inventory
Chart: NDVI Vs Time (Madhya Pradesh)
| 42665 | 42675 | 42694 | 42723 | 42747 | 42766 | 42776 | 42785 | 42790 | 42800 | 42816
pulses | 0.28327 | 0.15772 | 0.14073 | 0.16399 | 0.28088 | 0.36974 | 0.38628 | 0.43758 | 0.38562 | 0.30588 | 0.22267
wheat | 0.52053 | 0.29286 | 0.13774 | 0.12693 | 0.30888 | 0.47195 | 0.55257 | 0.63455 | 0.57019 | 0.513 | 0.42968
mustard | 0.17088 | 0.08944 | 0.26167 | 0.47812 | 0.53193 | 0.4766 | 0.34135 | 0.30014 | 0.2027 | 0.1288 | 0.11029
Chart: NDVI Vs Time (Maharashtra)
| 42665 | 42684 | 42713 | 42732 | 42756 | 42775 | 42785 | 42799 | 42816
pulses | 0.26974 | 0.24287 | 0.25812 | 0.34968 | 0.37749 | 0.37661 | 0.34876 | 0.33737 | 0.20671
wheat | 0.37626 | 0.2897 | 0.21874 | 0.30271 | 0.39789 | 0.44829 | 0.45206 | 0.42309 | 0.2408
rabi sorghum | 0.21352 | 0.30475 | 0.43277 | 0.48594 | 0.37485 | 0.27867 | 0.20098 | 0.21907 | 0.11866
cotton | 0.37748 | 0.33856 | 0.27353 | 0.24996 | 0.22152 | 0.25323 | 0.22638 | 0.27904 | 0.20289

## Slide 15
Horticultural crop inventory and Geo-spatial Applications
Geospatial support for site suitability in zoom land of north-east
Agricultural fallow and prospect of horticultual intensification
Bhiwani District,
Haryana
Primarily with LISS-III & LISS-IV

## Slide 16
Three-date FCC of
9 May, 3 June, 28 June 2016
of MRS RISAT-1
Three-date FCC of
27 April, 22 May,16 June, 2016
of MRS RISAT-1
Jute growing areas in Nagaon district, Assam
Jute growing areas from RISAT-1 Synthetic Aperture Radar data

## Slide 17: Crop yield modelling using LEO-GEO satellite data
Modelling framework
Wheat yield (tha-1)
Mustard yield (tha-1)

## Slide 18
Sowing suitability based on crop vigour and surface soil moisture
Satellite-based Value-added Agro-met Products for farmers advisories
4th Week, June
1st Week, July
2nd Week, July
3rd Week, July
4th Week, July
Kharif Sowing Suitability from
Space based observations

## Slide 19
Alpine tree-line shift
Forest dynamics and carbon sequestration
East coast delta of India

## Slide 20
Climate and Agro-ecosystem Interaction : Process Studies through Fluxes
NEE of CO2

## Slide 21
High-resolution ET modelling using thermal remote sensing and surface energy balance
Using Landsat 8 data

## Slide 22
ISRO – JPL AVIRIS-NG Airborne Hyperspectral Campaign over India : Phase – I results
Airborne hyperspectral campaign with AVIRIS-NG instrument was carried out over 57 sites in India during December 2015 – March 2016 (Phase – I) covering seven science themes : Agriculture & ecosystem, Geology, Urban, Coastal –Ocean, River and Inland Water, Snow & Glacier, Atmosphere
Both airborne L1 and L2, ground-truth data have been archived in VEDAS and being disseminated to Indian researchers. Hands-on training has also been provided to academia.

## Slide 23
Future ISRO EO missions
OCEANSAT-3/ 3A/3B Global missions with 13 channel OCM, Ku-band Scatterometer, Hyperspectral sesnor are also in pipeline

## Slide 24
International and Global missions during 2021 - 2023
Indo – French : ISRO-CNES thermal infrared mission
TRISHNA : Thermal InfRed Imaging Satellite for High-resolution Natural resource Assessment
Five-channel VNIR suite 3-day revisit, 60m spatial resolution
Single-channel SWIR
Four-channel thermal Infrared
Major science objective : Terrestrial Ecosystem Stress and Water use

## Slide 25
2009
2010
SAR FCC (July, Aug, Sep 2010)
Kharif rice:Bangladesh using C band SAR data
Rabi crops: Pakistan using multi date AWiFS data
Towards Global Initiatives
Queries
How ISRO can revive the role in Geo-GLAM ?
How framework of Analysis-Ready-Data (ARD) can be implemented with Resourcesat series and other future sensors ?
How ISRO can become part of GFOI ?