## Slide 1: Session 2: CARD4L Product Family Specification (10:00-10:45)
Geoscience Australia/European Space Agency/University of Leicester
SLI-VC6 Meeting
JRC, Ispra
5th September 2018
Committee on Earth Observation Satellites

## Slide 2
Overall PFS status
  Initial PFS
  Under development Radar PFS
Proposed steps to take us through to the endorsement of revisions in early 2019
PFS updates - discussion
  Surface Temperature updates for discussion
  Discussion to resolve the issue regarding the choice between land surface temperature and surface brightness temperature as the basis of the associated PFS.
Presentation Outline

## Slide 3
Product Family Specifications – Current Status
Initial Product Family Specifications
  Surface Reflectance:
    PFS doc v3.0 currently being validated/tested by ESA (S2) & USGS (Landsat) (link)
  Surface Temperature:
    LBT PFS doc v3.1 was/has been validated by ESA (S3) & USGS (Landsat) (link)
    LST PFS doc V0.1 circulated (16/08) (link)
  Radar Backscatter:
    PFS doc v3.2 (final) circulated to LSIVC list (22/08) (link)
    Upcoming validation by JAXA (ALOS mosaics)

## Slide 4
Under development PFSs for Radar products (link)
  Polarimetric covariance – Francois Charbonneau (NRCan/RNCan)
  Polarimetric decomposition – Marco Lavalle/Bruce Chapman (JPL), Takeo Tadono/Ake Rosenquvist (JAXA) and Zheng-Shu Zhou (CSIRO)
  INSAR LOS – Medhavy Thankappan (Geoscience Australia)
  INSAR Coherence – Ben Lewis (Geoscience Australia) and Nuno Miranda (ESA)
  Geocoded SLC – Bruce Chapman (JPL)
Product Family Specifications – Current Status
Oct/Nov 2018
Drafts open for review
Dec 2018
Jul 2018
SAR ARD definition Team created
Jun 2018
Additional PFS proposed
Aug 2018
1st PFS Drafts received
Sep 2018
PFS Drafts presented at LSIVC6
First versions finalized
SAR ARD definition Team disbanded
Feb 2019
Final versions presented/LSIVC7
Feb 2018
SAR ARD definition Team proposed/LSIVC5
Jan 2019

## Slide 5
PFSs – Overall Chronology
Chronology | Surface Reflectance | Surface Temperature (LBT) | Radar Backscatter | Additional Radar PFS
Mar 2017 | Draft Zero created |  |  | -
Apr-Jul 2017 | Various revisions to the document structure Edits to reflect feedback from a number of agencies & experts |  |  | -
Aug 2017 | Documents circulated to LSI-VC list |  |  | -
Sep 2017 | Feedback from ESA incorporated |  |  | -
Dec 2017 | Teleconferences |  |  | -
Jan 2018 | Feedback from Teleconferences included/Document circulated to LSIVC list |  |  | -
Feb 2018 | Outcomes presented at LSI-VC5 meeting |  |  | SAR ARD definition Team proposed
Apr-Jul 2018 | Self-assessment process/ESA (S2)/USGS (Landsat) | Self-assessment process/USGS (Landsat)/U.Leicester/ESA (S3) | ESA, JAXA & GA Feedback incorporated | SAR ARD definition Team Created First Team Teleconference Additional Radar PFS proposed
Aug 2018 | Self-assessment process/ESA (S2)/USGS (Landsat) | Draft LST created (based on LBT) and circulated to experts | SAR ARD definition Team feedback incorporated/Final document circulated to LSI-VC | Second Team Teleconference Drafts Zero created for: 1) Polarimetric covariance, 2) Polarimetric decomposition, 3) INSAR LOS, 4) INSAR Coherence and 5) Geocoded SLC specs

## Slide 6
Proposed PFS Future Steps
PFSs/Month
Sep 2018
Oct 2018
Dec 2018
Jan 2019
Feb 2019
Onwards
Surface Reflectance
Self-assessment process/ESA (S2)/USGS (Landsat)
Surface Temperature
Discuss updates/LSIVC6
Radar Backscatter
Present latest version at LSIVC6
Self-assessment process (JAXA)
Additional Radar PFS
Drafts presented at LSIVC6
Drafts open for review
First versions finalized
SAR ARD definition Team disbanded
Nov 2018
Self-assessment process (USGS)
Present refined SR/ST/RB versions at LSIVC7
for endorsement/present additional RADAR PFS
PFSs Stability
Updates will be carried out as necessary but no more than once a year
Documents circulated to the LSIVC list
Incorporate user survey
and Planets workshop Feedback
Feedback from WGCV
Feedback from ESA/USGS/JAXA/GA
self-assessment incorporated
Notes: Establish a maintenance plan

## Slide 7
Item | Assemssment to Threshold | Assemssment to Target | Comment/proposed updates
1.1 Traceability | N/A | SL_2_LST is validated against numerous in situ sites. One of these (Gobabeb, Namibia) has participated in the FRM4STS Project and can be classified as an FRM station since its instrumentation have been compared against SI traceable blackbodies | Traceability is a key metric for product maturity and thus there may be a case for upgrading to “threshold” level. This is particularly pertinent for climate studies.
1.2 Metadata machine readability | Metadata for SL_2_LST is stored in individual netCDF datafiles specific to the observation variable and in the global XML wrapper for each product granule | Metadata conforms to CF convention | This raises a general query as to whether the PFS is too narrow in the requirements, and it should take account of the community established protocols for the observation family in question. For Surface Temperature the convention across domains is to adhere to the climate driven CF convention
1.3 Data collection time | Metadata for SL_2_LST is stored in the global XML wrapper for each product granule | SLSTR acquisition times per pixel is not available in a single field. Acquisition times per pixel can though be determined by reading in data from multiple variables in a product granule and applying a recipe provided in the product documentation | 
1.4 Geographical area | Metadata for SL_2_LST is stored in the global XML wrapper for each product granule in WGS84 coordinates | Full resolution locations of the detector FOV centre per pixel stored in both geodetic and Cartesian coordinates | 
1.5 Coordinate reference system | The Geodetic coordinate system is reference ellipsoid WGS84, but this is only listed in the ATBD documentation | As threshold | 
1.6 Map projection | No | No | This relates to the projection of the data onto a standard map projection for use by GIS software. This is a nice to have rather than an essential, and should be removed from the threshold level. This is a requirement that has originated from the optical domain and has no heritage in thermal missions
1.7 Geometric correction source | Geometric calibration ADF is listed in the XML wrapper for each product granule | The L1 product ATBD describes the correction methods | This is crucial information to increase product maturity
PFS Surface Temperature S3 Assessment

## Slide 8
Item | Assemssment to Threshold | Assemssment to Target | Comment/proposed updates
1.8 Geodetic accuracy | The Product Notice document reports the Geolocation Accuracy | The Product Notice document reports the Geolocation Accuracy rather than in the metadata. The accuracy is assessed with respect to Ground Control Points (GCPs) | 
1.9 Instrument | Metadata for SL_2_LST is stored in the global XML wrapper for each product granule | Although included in the CEOS Missions, Instruments and Measurements Database, there is no reference to this in the product metadata | 
1.10 Sensor calibration | Channel specific characterisation ADF defines non-linearity and general calibration parameters | As threshold, but without a DOI specified | We could add a link (or DOI reference) to the calibration parameters for the L1 data
1.11 Radiometric accuracy | The Product Notice document reports the Radiometric Accuracy. The Measurement Accuracy is stored in the global XML wrapper for each product granule | Radiometric Accuracy determined by intercomparison with reference desert sites. Details available from ESA online | 
1.12 Algorithms | Algorithms are only described in the L2 product ATBD | The algorithm is published in the peer-reviewed literature with a DOI but not referenced in the product metadata | We could add a link (or DOI reference) to the ATBD or the peer-reviewed manuscript
1.13 Ancillary data | Ancillary netCDF files are provided in the product package and identified in the global XML wrapper for each product granule | Each netCDF file is freely accessible to download as part of the product package (but without a DOI) | We could add a link (or DOI reference) to the ATBD
1.14 Processing chain provenance | Processing baseline and IPF / PUG versions are identified in the global XML wrapper for each product granule | These details are available online as product documentation rather than in the metadata | This is crucial information to increase product maturity
1.15 Data access | The Product Notice document reports the location from where the product can be retrieved rather than in the metadata | L1 data download can be automated through EUMETCAST | We should seek a DOI for the product
1.16 Overall data quality | Overall product quality is provided in the Cyclic Reports rather than in the product metadata | N/A | The is critical information for users to determine whether to use a product or not in their applications
PFS Surface Temperature S3 Assessment

## Slide 9
Item | Assemssment to Threshold | Assemssment to Target | Comment/proposed updates
2.1 Metadata machine readability | NetCDF is self-describing format that can easily be read by computer algorithm | Metadata conforms to CF convention | PFS should take account of the community established protocols for the observation family in question. For Surface Temperature the convention across domains is to adhere to the climate driven CF convention
2.2 No data | These are flagged in the confidence word in the SL_2_LST product | As threshold | 
2.3 Incomplete testing | Both the “confidence” word and the “exception” word in the SL_2_LST product contain a number of individual flags representing tests carried out on the data | As threshold | 
2.4 Saturation | The “exception” word in the SL_2_LST product contains a flag to indicate whether data is saturated | The “exception” word is determined on a per pixel basis | 
2.5 Cloud | The SL_2_LST product contains both a cloud word with all the individual “Basic” bit masks and a Bayes word which includes the “Probabilistic” mask over land | Both the “basic” and “probabilistic” cloud masks have been published in peer-reviewed journals with no DOIs are referenced in the product metadata | We could add a DOI reference to these papers
2.6 Cloud shadow | This is less of a quality indicator than other metadata since the LST observed by the satellite of surface in shadow would measure in theory the same as a ground-based radiometer | As threshold | This is not in the product; it should be a nice to have rather than a threshold. This would be an evolution to the product
2.7 Illumination and viewing geometry | Both the solar and satellite zenith and azimuth angles are included in the SL_2_LST product per tie point | The solar and satellite zenith and azimuth angles are included in the SL_2_LST product per tie point and can easily be determined per pixel with a recipe | There should be a threshold requirement for minimum geometry information since it is critical information to the users for numerous applications, and to assess algorithm performance with respect to validation and intercomparison
2.8 Snow/ice mask | Both a permanent and transient snow/ice mask is produced per pixel | The algorithm is published in the peer-reviewed literature with a DOI but not referenced in the product metadata | Useful information to enable users to understand gradients in temperature between pixels
PFS Surface Temperature S3 Assessment

## Slide 10
Item | Assemssment to Threshold | Assemssment to Target | Comment/proposed updates
3.1 Measurement | LST values represent the thermodynamic temperature of the land surface in Kelvin | SL_2_LST is validated against numerous in situ sites. One of these (Gobabeb, Namibia) has participated in the FRM4STS Project and can be classified as an FRM station since its instrumentation have been compared against SI traceable blackbodies | 
3.2 Corrections for atmosphere (and emissivity in the case of LST) | This is not at all relevant to the user community, and not something any of the current operational LST products provide | The surface emissivity algorithm / auxiliary data are published in the peer-reviewed literature with a DOI but not referenced in the product metadata | Discussion at the GlobTemperature Workshop with ~50 LST users led to the conclusion that no user would exploit this. We should urgently seek to remove this requirement
3.3 Measurement Uncertainty | This is provided per pixel for SL_2_LST. It is essential for many applications, and LST products without such data cannot be used in any climate related studies | A full uncertainty model consistent with CCI approaches has been proposed for implementation for SL_2_LST | This is an essential requirement, providing information on the product quality, and should be moved to threshold level
4.1 Geometric correction | Geolocation accuracy in the nadir for LST retrievals meets mission requirements | Geolocation is assessed against Ground Control Points (GCPs) | SLSTR pixels are ortho-geolocated. There should be additional requirement to the “threshold” to account for ortho-geolocation needs
PFS Surface Temperature S3 Assessment

## Slide 11
                Should LSIVC adopt two (2) PFSs? LBT and LST?
                Resolution at the LSIVC6 meeting: “”Just one PFS (LST) will be maintained by LSIVC””
LBT versus LST

## Slide 12
Thank you!