## Slide 1
ESA update
for LSI-VC
Ferran Gascon
LSI-VC-7, VNSC, Hanoi (Vietnam), 14-15 February 2019

## Slide 2
Sentinel-1 mission status
Wind field of Typhoon Mangkhut (11 Sep 2018)
SAR is the only sensor able to characterize extreme winds (greater than 70 m/s) at very high resolution
Sentinel-1A and Sentinel-1B mission operations  nominal
Sentinel-1 contribution to emergency activations, in particular from the Copernicus Emergency Management Service, continues to be very high, for flood monitoring in particular
A dedicated campaign aiming at demonstrating the monitoring of hurricanes over seas / oceans has been successfully conducted
Sentinel-1 is operated close to its full mission capacity (i.e. difficulty to accommodate additional observations)
A slight increase of the SAR operating time duty cycle constraint has started (outside 3-month eclipse season), mainly allowing to further stabilise the observation scenario
Copyright: Contains modified Copernicus Sentinel data (2018) / CLS-Ifremer

## Slide 3
Oil Spill North of Corsica, 8 September 2018
Copyright: Contains modified Copernicus Sentinel data (2018) / processed by ESA
Sentinel-1 mission status

## Slide 4
Nominal Sentinel-2 constellation operations with Sentinel-2A and Sentinel-2B.
Performing global and systematic acquisitions (5-day revisit) since 17 February 2018.
New core product (Level-2A surface reflectance) generated and distributed globally since 13 December 2018 (Europe since 28 March 2018).
Copernicus Sentinel-2 Mission Status

## Slide 5: Level-1C

## Slide 6: Level-2A

## Slide 7: Level-2A

## Slide 8: Revisit Time
5-day
10-day

## Slide 9
Indonesia Palu earthquake (28 September 2018) :
North – South ground displacement derived from Copernicus Sentinel-2 data
Copyright: Contains modified Copernicus Sentinel data (2018) / processed by V. Sotiris
Sentinel-2 mission status
Palu

## Slide 10: S2 Mission Next Steps
Band 11
B11
2019 Q1: Completion of the conversion of the archive into single-tile format.
2019 Q2: L2A on-demand service open to Copernicus Services.
2019 Q2: Start of the geometry-refined production using Global Reference Image (GRI).
2019 Q2: Usage of improved DEM for L1C and L2A productions.
2019 Q3-Q4: L2A on-demand service to all users.

## Slide 11
Sentinel-3A mission operations  nominal
New Level 2 synergy products released in October 2018
The definition and implementation of two new core data products, the Aerosol Optical Depth (AOD) and Fire Radiative Power (FRP) is on-going with sample products expected to be available in 2019.
Reprocessing activities are on-going:
For SRAL, a full mission reprocessing (starting from March 2016) has been completed for both the Land and the Marine products. The Land products release is scheduled for Q4 2018.
For SLSTR, Level 1 and 2 data reprocessing started in June 2018 and was completed in September 2018, including an updated cloud masking. The release is planned for Q4 2018.
For OLCI a full mission reprocessing from April 2016 has been carried out and made available to users in September 2018.
Land Surface Temperature, Central Europe, 13 October 2018
from Infra-Red 12µm channel of SLSTR sensor (1km resolution)
Baltic
Adriatic
Copyright: Contains modified Copernicus Sentinel data (2018)
Sentinel-3 mission status

## Slide 12
Sentinel-3B
Spacecraft and all instruments in nominal operational mode and functioning well
Tandem phase between S-3B and S3-A for cal/val
Sentinel-3 mission status
Launch
25 Apr
In Orbit Commissioning Review
28 Nov
2019 Q1
17 Oct
Routine Operations Readiness Review
Phase E2
S-3B nominal phase (140 deg.)
S-3B drift phase

## Slide 13
Copyright: Contains modified Copernicus Sentinel data (2018) / processed by BIRA–IASB/DLR
Sentinel-5 Precursor mission operations  nominal, with on-going ramp-up of data availability to users
First data released in July 2018:
Total Columns of Ozone (O3),
Nitrogen Dioxide (NO2),
Carbon Monoxide (CO),
Cloud & Aerosol information
New data released in October 2018:
Sulfur Dioxide (SO2, in NRT),
Formaldehyde (CH2O, in NRT)
S-5p Sulfur Dioxide (SO2) measurement, November 2017 – July 2018
Sulphur dioxide, which mainly comes from industrial processes and motor vehicle emissions, can result in breathing problems and is a precursor to acid rain
Sentinel-5 Precursor mission status

## Slide 14
Example of diffusion of information provided by Copernicus Sentinel-5p
Copyright: Contains modified Copernicus Sentinel data (2018) / processed by KNMI and Greenpeace
Nitrogen Dioxide (NO2) hotspots
https://unearthed.greenpeace.org/category/energy
Sentinel-5 Precursor mission status

## Slide 15: Data Distribution
Private companies re-distributing Sentinel products through free and pay-per-use schemes
International partners mirror sites disseminating towards own national communities
Collaborative mirror sites
Copernicus Data Hubs

## Slide 16: Data Distribution

## Slide 17
Hanoi, 13/02/2019

## Slide 18
Hanoi, 08/02/2019